## Slide 1
Cluster Simulation
via Neural Network
YiZhou Zhang, Tao Lin, WeiDong Li
zhangyz@ihep.ac.cn
30th Aug 2023

## Slide 2
Outline
1
Background
Cluster Reconstruction via Neural Network
2
Design
Cluster Reconstruction via Neural Network
3
Working progress
Cluster Reconstruction via Neural Network
2

## Slide 3
1
Background
Cluster Reconstruction via Neural Network
3
Requirements:
现有的模拟算法并不能模拟出粒子穿过感应器产生的感应簇。
Geant4模拟出的结果，只有模拟粒子穿过感应器的一个感应点。
Purpose：
根据粒子穿过感应器的真实响应感应簇，通过机器学习方法，训练出能够模拟产生感应簇的模型。
使用TestBeam的数据训练模型。
使用生成对抗网络。
Reference: R.M. Bianchi, “Event display of a 2-tau candidate in the ATLAS detector”
Reference: Acts Common Tracking Software https://acts.readthedocs.io/
感应簇
Geant4模拟

## Slide 4
Outline
1
Background
Cluster Reconstruction via Neural Network
2
Design
Cluster Reconstruction via Neural Network
3
Working progress
Cluster Reconstruction via Neural Network
4

## Slide 5
2
Design
Cluster Reconstruction via Neural Network
5
Overview
EDM4hep::
TrackerHit
CEPCSW
EDM4hep::
RawTimeSeries
.pt
TestBeam Data
Neural Network
Network Model
Wrapper
C++
Load_model()
predict()
libtorch
.so
Wrapped Functions

## Slide 6
2
Design
Cluster Reconstruction via Neural Network
6
Data Prepocessing
TestBeam Data
Neural Network
512 pixel
1024 pixel
(42,84)
(43,84)
16 pixel
16 pixel
(-0.5,0)
(0.5,0)
localize
round
(8,8)
(9,8)
Train the NN
using the data
Test Beam Data
The cluster of one hit at the plane.
Relative Coordinates of Geometric Centers
Put it at a 16*16 pic as the train data
.npy

## Slide 7
2
Design
Cluster Reconstruction via Neural Network
7
GAN
z
Generative model(DCNN)
Generated distribution
True data distribution
x
Image space
y
Discriminative model(DCNN)
Image space
16*16 pixel
(8,8)
(9,8)
16*16 pixel
Train data
after preprocessing
.npy
We use a standard DCGAN model
.pt
Save and Put
Generative Model into CEPCSW

## Slide 8
2
Design
Cluster Reconstruction via Neural Network
8
GAN
z
Generative model(DCNN)
Downsample
With a threshold
16*16 pixel * 25
(42,84)
(43,84)
(-0.5,0)
(0.5,0)
Local Coordinates
The cluster of one hit at the plane.
(42.5,84)
One hit at the plane
round
.pt

## Slide 9
Outline
1
Background
Cluster Reconstruction via Neural Network
2
Design
Cluster Reconstruction via Neural Network
3
Working progress
Cluster Reconstruction via Neural Network
9

## Slide 10
3
Working progress
Cluster Reconstruction via Neural Network
Overview
10
EDM4hep::
TrackerHit
CEPCSW
EDM4hep::
RawTimeSeries
.pt
TestBeam Data
Neural Network
Network Model
Wrapper
C++
Load_model()
predict()
libtorch
.so
Wrapped Functions
✔
✔
✔
TBD
Need to be improved!

## Slide 11
3
Working progress
Cluster Reconstruction via Neural Network
Predict in CEPCSW
11
CEPCSW
EDM4hep::
RawTimeSeries
Wrapper
C++
Load_model()
predict()
.so
Wrapped Functions
✔
✔
Run prediction
Save in a
RawTimeSeriesCollection
Encode in cellID

## Slide 12
3
Working progress
Cluster Reconstruction via Neural Network
DCGAN Train
12
Discriminator Loss
Generator Loss
基本符合预期。
Discriminator下降过快，考虑降低辨别器训练频率。

## Slide 13
3
Working progress
Cluster Reconstruction via Neural Network
DCGAN Predict
13
Predictor分布分析：
训练出来的预测分布，cluster偏小，大部分预测都是只有一个点。
DCGAN没能很好的学习到训练集分布。

## Slide 14
3
Working progress
Cluster Reconstruction via Neural Network
DCGAN Predict
14
训练数据分布统计：
从chip0-10，越靠后的plane，cluster越小

## Slide 15
3
Working progress
Cluster Reconstruction via Neural Network
Summary & future work
15
Summary
目标：根据粒子穿过感应器的真实响应感应簇，通过机器学习方法，训练出能够模拟产生感应簇的模型。
使用标准的DCGAN模型，以TestBeam Data为训练集，训练了能初步预测簇形状的模型。
将模型加入CEPCSW，能够成功运行预测算法，并生成储存相应的RawTimeSeries Collection的root文件。
Future Work
目前网络模型结果不甚理想，需要进一步优化模型（如使用FLOW模型）
目前模型的输入为隐空间的噪音，后续需要考虑加入其他输入（如：粒子入射角，能量，类型等）
CEPCSW部分需要加入geant4模拟（需要TB的几何信息），使整一个预测工作流程跑通。

## Slide 16
Thank You
YiZhou Zhang, Tao Lin, WeiDong Li
zhangyz@ihep.ac.cn
30th Aug 2023

## Slide 17
Backup