## Slide 1: Status and prospects of JUNO
Zeyuan Yu (IHEP)
On behalf of the JUNO collaboration
Feb. 19th, 2024
International Symposium on Neutrino Physics and Beyond, 2024

## Slide 2
Jiangmen Underground Neutrino Observatory
Leading term at JUNO
Leading term at Daya Bay
Sensitive to mass ordering
Daya Bay Far Hall
Key for NMO:
1、20 kton liquid scintillator detector
2、3% energy resolution at 1 MeV energy deposit
3、low background

## Slide 3
A multiple-purpose neutrino experiment
Neutrino oscillations, mass ordering (3-4 σ), precision measurement (<0.5%)
Astro-particle physics, supernovae neutrinos, geo and solar neutrinos

## Slide 4
JUNO collaboration
Country | Institute | Country | Institute | Country | Institute
Armenia | Yerevan Physics Institute | China | SYSU | Germany | U. Mainz
Belgium | Universite libre de Bruxelles | China | Tsinghua U. | Germany | U. Tuebingen
Brazil | PUC | China | UCAS | Italy | INFN Catania
Brazil | UEL | China | USTC | Italy | INFN di Frascati
Chile | PCUC | China | U. of South China | Italy | INFN-Ferrara
Chile | SAPHIR | China | Wu Yi U. | Italy | INFN-Milano
Chile | UNAB | China | Wuhan U. | Italy | INFN-Milano Bicocca
China | BISEE | China | Xi'an JT U. | Italy | INFN-Padova
China | Beijing Normal U. | China | Xiamen University | Italy | INFN-Perugia
China | CAGS | China | Zhengzhou U. | Italy | INFN-Roma 3
China | ChongQing University | China | NUDT | Pakistan | PINSTECH (PAEC)
China | CIAE | China | CUG-Beijing | Russia | INR Moscow
China | DGUT | China | ECUT-Nanchang City | Russia | JINR
China | Guangxi U. | China | CDUT-Chengdu | Russia | MSU
China | Harbin Institute of Technology | Czech | Charles U. | Slovakia | FMPICU
China | IHEP | Finland | University of Jyvaskyla | Taiwan-China | National Chiao-Tung U.
China | Jilin U. | France | IJCLab Orsay | Taiwan-China | National Taiwan U.
China | Jinan U. | France | LP2i Bordeaux | Taiwan-China | National United U.
China | Nanjing U. | France | CPPM Marseille | Thailand | NARIT
China | Nankai U. | France | IPHC Strasbourg | Thailand | PPRLCU
China | NCEPU | France | Subatech Nantes | Thailand | SUT
China | Pekin U. | Germany | RWTH Aachen U. | U.K. | U. Warwick
China | Shandong U. | Germany | TUM | USA | UMD-G
China | Shanghai JT U. | Germany | U. Hamburg | USA | UC Irvine
China | IGG-Beijing | Germany | FZJ-IKP |  | 
74 institutes and more than 700 collaborators

## Slide 5
JUNO site
Surface buildings/campus finished
Surface Assembly Building
LAB storage (5k ton)
Water purification
Computing
Power station
Cable train
Office/Dorm
Vertical and slope tunnels
1265 m w/ slope of 42%
Vertical tunnel: 563 m
Muon flux 0.004 Hz/m2
5

## Slide 6
JUNO detector and progresses
Stainless Steel structure
  Finished in June 2022
Acrylic panels
  All the panels are ready for shipping to onsite
  Starting from the top, 14/23 layers finished
20,012 20’’ PMTs + 25,600 3’’ PMTs
  Production and performance test done
  7,225 LPMTs and 9,293 SPMTs installed
Liquid scintillator
  Purification plants finished onsite construction
  Successfully joint commissioning in Nov. 2023
6

## Slide 7
JUNO detector progresses

## Slide 8
Central detector
Main difficulties overcome
  Acrylic transparency >96%, U/Th/K <1 ppt
  Fast bonding of 265 acrylic panels
  Mechanical precision for 3 mm PMT clearance
  Thermal expansion matching: 21oC  1oC
  Earthquake and liquid-solid coupling
arXiv: 2311.17314
8

## Slide 9
Photomultiplier Tubes
9
 | LPMT (20-inch) |  | SPMT (3-inch)
 | Hamamatsu | NNVT | HZC
Quantity | 5000 | 15012 | 25600
Charge Collection | Dynode | MCP | Dynode
Photon Detection Efficiency | 28.5% | 30.1% | 25%
Dynamic range for [0-10] MeV | [0, 100] PEs |  | [0, 2] PEs
Coverage | 75% |  | 3%
Reference | Eur.Phys.J.C 82 (2022) 12, 1168 |  | NIM.A 1005 (2021) 165347
All PMTs produced, tested, and instrumented with waterproof potting
PDE larger than required value 27%  expected energy resolution 2.9% @ 1MeV
Synergetic 20-inch and 3-inch PMT systems to ensure energy resolution and charge

## Slide 10
Photomultiplier Tubes
10
Clearance between PMTs: 3 mm  Assembly precision: < 1 mm
w/ protection cover (JINST 18 (2023) 02, P02013)
7,225 LPMTs and 9,293 SPMTs installed

## Slide 11
Liquid scintillator
11
2) Distillation for radiopurity
1) Al2O3 for optical
5000 m3 LAB tank
SS pipes to underground
Mixing PPO and bis-MSB
3) Water extraction to remove radioactive impurities
4) Gas stripping to remove Rn and O2
OSIRIS to monitor the LS quality
15%
85%
Water filling of OSIRIS finished a half month ago, LS run starts soon.
Filling strategies:
  Leakage (single component < 10-6 mbarL/s)
  Cleaning vessel before filling
  Clean environment
  Water/LS filling
Four purification plants to achieve target radio-purity 10−17 g/g U/Th and 20 m attenuation length

## Slide 12
Calibration
12
Cable system finished prototype test
1D, 2D, 3D scan systems with multiple calibration sources
JHEP 03 (2021) 004
Calibrate energy scale to better than 1% using gamma peaks and cosmogenic 12B beta spectrum

## Slide 13
Observing nuclear reactors, the Solar System, and the Milky Way at Jiangmen

## Slide 14
Event type | Rate [/day] | Relative rate uncertainty | Shape uncertainty
Reactor IBD signal | 60  47 | - | -
Geo-s | 1.1  1.2 | 30% | 5%
Accidental signals | 0.9  0.8 | 1% | negligible
Fast-n | 0.1 | 100% | 20%
Li/He | 1.6  0.8 | 20% | 10%
()O | 0.05 | 50% | 50%
Global reactors | 0  1.0 | 2% | 5%
Atmospheric | 0  0.16 | 50% | 50%
Event type | Rate [/day] | Relative rate uncertainty | Shape uncertainty
Reactor IBD signal | 60  47 | - | -
 | 1.1  1.2 | 30% | 5%
Accidental signals | 0.9  0.8 | 1% | negligible
Fast-n | 0.1 | 100% | 20%
 | 1.6  0.8 | 20% | 10%
 | 0.05 | 50% | 50%
Global reactors | 0  1.0 | 2% | 5%
 | 0  0.16 | 50% | 50%
JUNO physics book (J. Phys. G43:030401(2016))  updated analysis
Updates for the spectra and rates since JUNO (2016)
2 fewer reactor cores in Taishan
Better muon veto strategy
Improved energy resolution:
3.0% 1MeV  2.9% 1MeV
CPC 46 (2022) 12, 123001
More realistic estimate on signals and backgrounds
Slight less overburden
Lower radioactivity background based on latest measurements on material radiopurities
Reactor Antineutrino Oscillations

## Slide 15
Precision Oscillation Measurement
About one order of magnitude improvements in precision over existing constraints
Precision of sin2, , || < 0.5% in 6 years

## Slide 16
Neutrino Mass Ordering
JUNO NMO median sensitivity: 3σ (reactors only) @ ~6 yrs * 26.6 GWth exposure
Combined reactor+atmospheric neutrino analysis in progress: further improve the NMO sensitivity
 | Design * | Now
Thermal Power | 36 GWth | 26.6 GWth (26%)
Overburden | ~700 m | ~ 650 m
Muon flux in LS | 3 Hz | 4 Hz (33%)
Muon veto efficiency | 83% | 91.6% (11%)
Signal rate | 60 /day | 47.1 /day (22%)
Backgrounds | 3.75 /day | 4.11 /day (10%)
Energy resolution | 3% @ 1 MeV | 2.9% @ 1 MeV (3%)
Shape uncertainty | 1% | JUNO+TAO
3𝜎 NMO sens. exposure | < 6 yrs 35.8 GWth | ~ 6 yrs 26.6 GWth
 | Design * | Now
Thermal Power | 36 GWth | 
Overburden | ~700 m | ~ 650 m
Muon flux in LS | 3 Hz | 
Muon veto efficiency | 83% | 
Signal rate | 60 /day | 
Backgrounds | 3.75 /day | 
Energy resolution | 3% @ 1 MeV | 
Shape uncertainty | 1% | JUNO+TAO
3𝜎 NMO sens. exposure |  | 
* J. Phys. G 43:030401 (2016)
Preliminary

## Slide 17
Supernovae neutrinos
JCAP 10 (2022) 033
Nominal model
S/B ratio improved from 2 to 3.5
With the nominal model
3 in 3 years and 6 in 10 years
Diffuse supernova neutrino background
SN neutrinos of 30 M⊙ Nakazato mode
3 detection channels sensitive to all flavors
Excellent capability for early warning
220~400 kpc with 50% probability
10 ~ 30 ms for typical 10 kpc
JCAP 01 (2024) 057

## Slide 18
Solar and terrestrial neutrinos
JUNO will collect the largest dataset of geoneutrinos in about 1 year
Precision of total geoneutrino signal with Th/U ratio fixed: ~8% in 10 years
KamLAND ~15%, Borexino ~17%
JUNO could improve the measurement of solar ν’s

## Slide 19
JUNO-TAO
19
TAO CDR arXiv:2005.08745
An innovative apparatus
● ~94% coverage with SiPM (~50% PDE)
● Cooling to -50°C
● 1 ton fiducial volume / 2.8 tons of Gd-LS
● 44 m to the reactor core
Measurement of reactor anti-nu spectrum with no oscillations (within Taishan NPP building)
Rich Physics
●Sensitive to fine structure
● Model-independent reference spectrum for JUNO
● Improvement of nuclear databases
● Sensitive to sterile neutrino
Successful 1:1 prototype at IHEP, to be transported and assembled at Taishan NPP in 2024

## Slide 20
Future JUNO-0νββ upgrade
Critical R&D in progress
1、Te-loaded LS with high transparency, light yield and stability
2、Cosmogenic and 8B solar ν bkg rejection
3、Xenon enrichment w/ a company
Concept of the experiment
Te-LS
or
Xe-LS
JUNO offers an unique opportunity to search for 0νββ after completion of NMO measurements
Large target mass  100-ton scale isotope loading
Excellent clean LS shielding  low background
Energy resolution < 3% @ 1 MeV
 Potential to explore normal mass ordering parameter space of Majorana neutrino mass (SNOWMASS 2021)

## Slide 21
Summary
21
JUNO is designed to measure the Neutrino Mass Ordering
Rich physics program, future JUNO-0νββ
Construction close to completion, data taking with water starts in 2024
Short-baseline experiment TAO provides JUNO the reference spectrum and benchmark for nuclear database
Physics | Sensitivity
Neutrino Mass Ordering | 3σ in ~6 years by reactor neutrinos.
Precision Measurement | Precision of , , ¦¦ < 0.5% in 6 yrs
Supernova Burst (10 kpc) | ∼7300 of all-flavor neutrinos
DSNB | 3σ in 3 years
Solar Neutrino | 7Be, pep, CNO, and 8B neutrino fluxes depending on the LS radio-purity level
Nucleon Decays () | 9.61033 years (90% C.L.) in 10 yrs
Geo-neutrino | ∼400 per year, 8% measurement in 10 yrs
Physics | Sensitivity
Neutrino Mass Ordering | 3σ in ~6 years by reactor neutrinos.
Precision Measurement | 
Supernova Burst (10 kpc) | ∼7300 of all-flavor neutrinos
DSNB | 3σ in 3 years
Solar Neutrino | 7Be, pep, CNO, and 8B neutrino fluxes depending on the LS radio-purity level
Geo-neutrino | ∼400 per year, 8% measurement in 10 yrs

## Slide 22: Thanks!

## Slide 27
Energy Resolution
Change | Light yield in detector center [PEs/MeV] | Energy resolution | Reference
Previous estimation | 1345 | 3.0% 1MeV | JHEP03(2021)004
Photon Detection Efficiency (27%30%) | +11% | 2.9% @ 1MeV | arXiv: 2205.08629
New Central Detector Geometries | +3% |  | 
New PMT Optical Model | +8% |  | EPJC 82 329 (2022)
Change | Light yield in detector center [PEs/MeV] | Energy resolution | Reference
Previous estimation | 1345 |  | JHEP03(2021)004
Photon Detection Efficiency (27%30%) |  | 2.9% @ 1MeV | arXiv: 2205.08629
New Central Detector Geometries |  |  | 
New PMT Optical Model |  |  | EPJC 82 329 (2022)
Positron energy resolution is understood:
Scintillation quenching effect
  LS Birks constant from table-top measurements
Cherenkov radiation
  Cherenkov yield factor (refractive index & re-emission probability) is re-constrained with Daya Bay LS non-linearity
Detector uniformity and reconstruction
Photon statistics
Annihilation-induced s
Dark noise