## Slide 1
LIANG Tianjiao, Dongguan Branch
International Assessment
21st Sep,2023
CSNS Neutron Science

## Slide 2: Outline
Status and Progress of Neutron Science
Scientific Highlights
Neutron Technology R&D
CSNS-II Neutron Science
1
2
3
4

## Slide 3
General Status
  3 day-one neutron instruments + 8 cooperative instruments
  4 instruments open to users, other 7 instruments will open next year
  Target station operates at 140kW stably and safely
  Neutron Technologies R&D goes well: sample environments, neutron detector, optics, polarization, data analysis, target, moderator etc.
3

## Slide 4
Target Station Status
  Beam power increased from 20kW to 140kW
  The neutronic performance of the source (and moderators) is excellent
  Keep stable and safe operation, the failure time of target station is 316 hours in past five years
  Prompt recovery experience from failure
    Recovery of hydrogen pump failure: 50 hours
    Recovery of Target-2 failure: 170 hours
4

## Slide 5
5
GPPD:
  For most users to determine crystallographic and magnetic structures for general purposes
  Best resolution d/d ~ 0.14 %，Stress test upgrade completed
MR:
  Vertical sample geometry: solid film
  Reflectivity/diffraction/Polarizing analysis
  Best resolution Q/Q < 1%
SANS:
  Reliable SANS data between 0.005~1.4 Å-1
  Instrument Q resolution ~8% @ Å-1
Day-one Neutron Scattering Instruments

## Slide 6
Day-one Instruments Upgrade
  The residual stress measurement capability was upgraded for GPPD in 2021
  SANS upgrade during 2022-24 to expand Q range and improve electronics
  A range of sample environments are upgraded for MR and SANS
6

## Slide 7
North Instruments Hall
2018
2023
7

## Slide 8
Cooperative Instruments
8
BL05: High energy inelastic spectrometer (2020)
BL08: Engineering Material Diffractometer (2020)
BL09: High resolution Diffractometer (2021)
BL16: Multiple Physics Instrument (2018)
BL15: High Pressure Diffractometer (2021)
BL14: Very small angle neutron scattering(2020)
BL13: Energy resolved neutron imaging(2020)
BL11: Atmosphere Neutron Irradiation(2019)
BL16 open to user since Oct. 2021
BL05, 08, 11, 13, 14 under trail-operation or commissioning
BL09, 15 will finish construction this year
Total budget ~1B CNY
Limit to up to 30% beamtime for cooperative partner
with Shenzheng graduate school of Peking University
with Sun Yat-sen University
with Southern University of Science and Technology
with DongGuan University of Technology, and City U of HongKong
With Dongguan Center of Excellence for Advanced Materials
Funded by Guangdong Province
Funded by Guangdong Province
With China CEPREI Lab.

## Slide 9
Multi Physics Instrument (MPI)
  MPI was constructed as a total scattering diffractometer to measure both the Bragg and Diffuse Components. Open to user at Oct. 2021
Q: 0.1~50 Å -1
∆r ~0.1 Å
Flux : 3.0×107 n/cm2/s
Medium High Q resolution
ΔQ/Q : ~0.3%
9

## Slide 10
10
Atmospheric Neutron Irradiation
  The first neutron obtained 2022，under trial operation now
  Good spectra shape with JEDEC
  flux range:103-107 n/cm2/s (>10MeV)
  Collimated beam (1-10cm)
  Extended beam (80cm x 80cm)
  Aim to neutron single event effect test for semiconductors, electronic devices and integrated equipment used in aviation and ground.
  Industry user Research user

## Slide 11
Engineering Material Diffractometer & Energy Resolved Neutron Imaging
EMD (Under commissioning)
Built for Residual Stress Analysis, Texture Analysis, Industrial metallurgy and manufacturing process simulation.
Obtained first beam on Dec.29 2022, and launched day-one experiment on Apr. 28.
Neutron wavelength 0.5-6.0Å
resolution  d/d ~ 0.25 %
Gauge volume 2, 3, 4, 6mm
sample table 1.8x1.8m, 2ton
ERNI (Under commissioning)
Designed for Bragg edge imaging, Conventional neutron imaging,Grating imaging and Neutron diffraction.
Obtained first beam on Jan. 05 2023,
11
The field of view 200 mm x 200 mm
The spatial resolution <25 µm
The wavelength resolution <0.4%.

## Slide 12
Very Small Angle Neutron Scattering & High Energy Inelastic Spectrometer
VSANS (Under commissioning)
Study Structure-Property relationship on multiphase and multiscale in the field of biology, polymer, nano, giant and super molecular science.
Obtained First beam on Jan. 04 2023.
SANS and Polarized Mode: Qmin=0.002 Å-1
VSANS Mode: Qmin=0.0004 Å-1
Measurable Length Scale 3.2 Å−1.0 μm
HD(Under commissioning)
Study Dynamic properties : Lattice dynamics, Spin dynamics, Crystal field excitations, Spin-orbital couplin
Obtained First beam on Jan. 12 2023
12
Energy range : 10meV~1500 meV
Resolution: : 3%~10%
Detector coverage:
horizontal：-30˚～+60˚
vertical：-30˚～+30˚

## Slide 13
High-Resolution Diffractometer & High Pressure Diffractometer
  Detecting tiny structural changes complex crystal or magnetic structures in condensed matters physics.
Best resolution: <0.05%
d-range:0.1-25Å@6.25 Hz
Construction will be completed by the end of 2023
  High Pressure Powder Diffractometer applies for mineral, ceramics, hydrate, organics, Earth & Geology etc.
Resolution：~ 0.6%
Highest Pressure: 20Gpa
13

## Slide 14: Outline
Status and Progress of Neutron Science
Scientific Highlights
Neutron Technology R&D
CSNS-II Neutron Science
1
2
3
4

## Slide 15
15
User Service
Registration user: 5200+ (100+ abroad)
Ten rounds of proposal are called and completed, proposal approve rate of general user proposal : ~30%
More than 300 user publication
~10% international user proposal before Covid19
https://user.csns.ihep.ac.cn (in both Chinese and English）
General User Proposal Proposal Performed User Publication

## Slide 16
Research Areas
Chart: 
| Energy & Battery | Magnetism&Multiferroic | Metal&Alloy | Oxides Film | Spintronics | Polymer | Nano Composite | Biology | Superconductivity | Engineering | others
Sales | 64 | 27 | 32 | 15 | 11 | 17 | 15 | 3 | 7 | 12 | 11
University：～45%
Research institution：～49%
Industry：～6%
16

## Slide 17
Liu et.al. Science
2020, 368, 1347-1352
  Low-cost D&P steel with high yield strength (~2 GPa), excellent toughness , and good ductility was obtained by Prof. Huang Mingxin‘s team of Hongkong University.
  Important microscopic parameter information such as phase volume fraction and dislocation density was obtained through neutron diffraction @GPPD
Scientific Highlight: Metal & Alloy
17

## Slide 18
  Neutron Diffraction @ GPPD determines the fine structure of carbon dioxide in iron-containing mordenite, which has the record of high carbon dioxide uptakes. This work was supported by CSNS, BSRF and PALS of IHEP.
Zhou et.al. Science, 2021,373,315-320
Scientific Highlight: Catalyzer & MOF
18
Notes: positron annihilation lifetime spectrum

## Slide 19
  Long-range ordered porous carbon crystal (LOPC) achieved by Yanwu Zhu’s group of USTC. It is an new class of carbon-based crystal structures between graphite and C60 molecular.
F. Pan et.al., Nature 2023, 614, 95
Scientific Highlight: Carbon
@MPI accurately reveal the short and medium range ordered structures of Fullerene and 2H graphite.
19

## Slide 20
  The lanthanide all solid-state electrolyte material with good interface compatibility achieved by Hong-Bin Yao’s group of USTC.
  Combined refinement of TOF neutron data (@MPI) and synchrotron X-ray was conducted to acquire a more convincing crystal structure.
Y. Yin et.al., Nature 2023, 616, 77
Scientific Highlight: Battery
20

## Slide 21
Scientific Highlight: Magnetism
Polarized Neutron Reflection @MR is used to accurately measure the magnetic distribution and the spin structure within thin films.
Phys. Rev. Lett. 2022, 128, 167202
It is found @SANS that all of the disordered biskyrmions have their in-plane symmetry axis aligned along certain directions, governed by the magnetocrystalline anisotropy.
Adv. Mater. 2019, 1900264
21

## Slide 22
Scientific Highlight: Polymer and Drugs
J. Am. Chem. Soc. 2020, 142, 8473
The neutron data @SANS provides insight on the monomeric and integrated response capabilities of the Rotaxane dendrimers upon external stimulation in both solution (preparation) and film(application) state.
CCS Chem. 2022, 4, 1238
Advanced drug design usually involves the development of novel therapeutic agents but also proper spatial arrangement of these components. @SANS data reveals that the drugs can be effectively delivered and released.
22

## Slide 23
Physics Letters B, 2023, 839, 137832
Scientific Highlight: Neutron Physics
1-300MeV 232Th fission cross section measured (@Back-n)
Neutron ghost imaging is realized with a single-pixel detector (@testing beamline)
Science Bulletin 2021, 66, 133–138
23

## Slide 24: Industry Application
Before service
After service
Residual stress measurement of high-speed train wheels
Vehicle battery: inhomogeneity exists during charge and dis-charge
24

## Slide 25: Outline
Status and Progress of Neutron Science
Scientific Highlights
Neutron Technology R&D
CSNS-II Neutron Science
1
2
3
4

## Slide 26
Sample Environments
  More than 20 sets of SE equipment have been used online.
  At present, CSNS can provide the SE with temperature range of 0.3-1873K, 10GPa pressure, 9T magnetic field and some coupled fields for users.
  The necessary SE equipment optimization, research and development work is being carried out， such as Rheometer, Temperature Jumper, in-situ catalytic reactor.
26

## Slide 27
Neutron Detector & Electronics
  Develop advanced neutron detectors and readout electronics for CSNS and other neutron sources in China , Including detection physics, electronics, software, mechanics
  Several Labs for the detectors development and mass production
27

## Slide 28
Neutron Polarization, Optics and Chopper
Polarization
Off-situ and In-situ 3He neutron spin filter as neutron polarizer and analyzer
Customized neutron guide field and spin flipper based on beamline deployment
Guide
Glass base fabrication available
0.5m and 2m glass frames and assembly machines established
Chopper
Developed and manufactured 34 sets of choppers(T0, Disk, Fermi)
Very low vibrations:~0.14mm/s@50Hz
28

## Slide 29
Data Analysis
  Develops and supports the scientific data software for neutron instrumentations, including data reduction, data analysis, computer simulation, scientific application and data management systems.
29

## Slide 30
Cd decoupled material R&D
R&D of Moderator：New decouple material developed
B4C decoupled material R&D
Zr-W target plate
Zr-W erosion sample
Erosion experimental platform
R&D of Target，Ta claded W target and Zr claded W erosion experiment.
Target & Moderator R&D
30

## Slide 31
Post Irradiation Examination for Target
31
Ta coating detection
PIE of the target vessel material
Used target
Target cutting
Sample preparation
Equipment and testing platform for irradiated samples were developed, and joint commissioning is undergoing.
Prepare post irradiation examination of key materials on the used target

## Slide 32: Outline
Status and Progress of Neutron Science
Scientific Highlights
Neutron Technology R&D
CSNS-II Neutron Science
1
2
3
4

## Slide 33
CSNS II Target Station Upgrade
  Target plug replacement
  Moderator Reflector Plug replacement
  Heavy water cooling system upgrade
  Second cryogenic refrigerator and hydrogen loop
  Remote handling tool and storage of radioactive waste
  preliminary neutronic design and thermal hydraulic analysis completed. The key technology have been improved
33

## Slide 34
BL03: Liquid reflectometer
BL04: Cold inelastic Spectrometer
BL06: molecular vibration Spectrometer
BL08A: neutron technology test station
BL10: Backscattering
spectrometer
BL20: Polarized chopper spectrometer
BL19: Single crystal diffractometer
BL17: Quasi-elastic spectrometer
BL12: Neutron Physics & application
BL07: Reserve
BL10A: Reserve
CSNS II Neutron Instruments
  the instrument suite and instrument selection were reviewed by CSNS scientific and technical committee and CSNS international advisory committee.
34

## Slide 35: CSNS-II Instrument design
Liquid reflectometer
Neutron technology test station
Neutron physics and application
Cold inelastic spectrometer
35

## Slide 36: CSNS-II Instrument design
The physical designs of 9 neutron instruments have been completed primarily.
The performance optimization and engineering design of instruments are going forward,
The physical design
The instrument layout
BL17: Elastic Diffuse Scattering Spectrometer

## Slide 37
  Instruments and target station has been operated with high efficiency.
  The user demands is strong and the scientific output is significant.
  The construction, commissioning and operation of cooperative instruments are going forward as planning,
  The design and R&D for target station and instruments of CSNS-II keep improving.
  Challenges
  Human resource to adapt the operation, science application and CSNS II Project
  Original innovation technology and methods
  Many thanks for your review!
Summary and challenges
37