## Slide 1
Huachang Liu
Institute of High Energy Physics
Sep. 21, 2023
CSNS Accelerator
International assessment 2023

## Slide 2: Contents
1
2
Introduction of CSNS accelerator
Operation and beam power upgrading
3
Design and pre-research on CSNS-II
4
Summary

## Slide 3: Introduction
CSNS accelerator
China’s first high-energy/high-intensity proton accelerator
Beam Power on target [kW] | 100
Proton energy [GeV] | 1.6
Average beam current [μA] | 62.5
Pulse repetition rate [Hz] | 25
Linac energy [MeV] | 80
Linac type | DTL
Linac RF frequency [MHz] | 324
Macropulse. ave current [mA] | 15
Macropulse duty factor | 1.05
RCS circumference [m] | 228
RCS harmonic number | 2
RCS Acceptance [mm-mrad] | 540
Target | 1
Spectrometers | 3

## Slide 4: H- Linac Design
 | Ion Source | RFQ | DTL
Input Energy（MeV) |  | 0.05 | 3.0
Output Energy(MeV) | 0.05 | 3.0 | 80
Pulse Current (mA) | 20 | 15 | 15
RF frequency (MHz) |  | 324 | 324
Chop rate (%) |  | 50 | 50
Duty factor (%) | 1.3 | 1.05 | 1.05
Repetition rate (Hz) | 25 | 25 | 25

## Slide 5: RCS Design
Lattice of 4-fold symmetry, triplet
227.92m circumference
Four long straight sections for injection, acceleration, collimation and extraction
24 main dipoles with one power supply
48 main quadrupoles with 5 power supplies
Ceramic vacuum chambers for the AC & pulsed magnets
8 RF ferrite loaded cavities to provide 165 kV

## Slide 6: Operation and power upgrading
Over the past five years, while ensuring user operations, CSNS has steadily increased the target beam power and is currently operating at 140 kW, exceeding the design target by 40%.

## Slide 7: Operation
The target beam time and availability statistics
Highest availability
among similar international facilities！

## Slide 8: Challenges from Linac commissioning
Linac commissioning
1、Beam pulse: 100μs ->540 μs
2、Beam current: 10mA ->17mA
Challenges:
Beam loss <1W/m (~100mrem/hr@30cm)
Beam loss mechanism | Transmission improved | Beam loss mitigation
Beam halo/tails | 2~3% | Transverse matching: studying the effect of the fringe magnetic field, keeping beam equipartitioned, making phase advance smoothing, etc. Longitudinal matching: keeping the RFQ transmission>95%, optimizing buncher settings.
Ion source turn on/off transient | ~0.5% | About 20μs beam pulse is chopped with the LEBT chopper.
Linac beam transmission~100%, activation level<3.5mrem/hr@30cm

## Slide 9: Challenges from RCS commissioning
Beam power on target | Challenges | Solutions
50kW80kW | Too large beam size after painting, non-uniform beam distribution, large transverse coupling | By using the correlated painting instead of the anti-correlated painting
80kW100kW | Serious beam instability | Optimization of the tune and chromaticity
100kW125kW | Emittance increase caused by broken four-fold symmetry of the RCS; Large beam instability | Slight modification of injection system; installation of AC trim quadrupoles and AC sextupoles
125kW140kW | Strong space charge effects | Installation of a dual harmonic RF cavity

## Slide 10: CSNS-II accelerator
Space reserved for 300MeV SC Linac
500kW
beam power
Project Phase | I | II
Beam Power on target [kW] | 100 | 500
Proton energy [GeV] | 1.6 | 1.6
Average beam current [μA] | 62.5 | 312.5
Pulse repetition rate [Hz] | 25 | 25
Linac energy [MeV] | 80 | 300
Macropulse. ave current [mA] | 15 | 50
Macropulse duty factor | 1.05 | 1.5
New injection
Second harmonic MA system
The highest beam intensity among the same kind of RCS!

## Slide 11: Path to 500kW beam power
1. the first step
Linac（80MeV）+ RCS upgrade 150~200kW
  New dual harmonic RF system
  Adding AC trim quadrupoles, sextupoles and octupoles
2. the second step
Linac （300MeV+）+ upgraded RCS 500kW
  SC linac to 300MeV
  New injection region
  Upgrade the power supplies for the main magnets

## Slide 12: R&D for CSNS-II accelerator
1. Linac R&D 300MeV, 40mA+
Newly developed RF-driven H− ion source
Superconducting linac
RF power source
2. RCS R&D 500kW
  Beam dynamics
  High power MA loaded cavity
  New injection painting

## Slide 13: R&D : RF-Driven H- ion source
Facility | Op. Current (mA) | Duty Factor | RMS Emitt. (π.mm.mrad) | Life Time（month） | Availability | Structure
ISIS | >50 | 1.1% | 0.35 | 5 | 99.3% | Penning
SNS | >50 | 6% | 0.25 | 19 | 99.9% | In Antenna RF
J-PARC | 47 | 1.25% | 0.26 | 22 | 99.8% | In. Antenna RF
CSNS | 42 | 1.35% | <0.31 | >45 | 99.999% | Ext Antenna RF
The H- ion source was put into commissioning since Sep. 2021
Excellent performance with nearly 100% availability
External-antenna structure.
Silicon-nitride plasma chamber.
Concise and reliable ignition system
Innovations：

## Slide 14: R&D：Superconducting Linac
6-cell elliptical SRF cavities
Х8
Very stable linac beam energy ΔE<2MeV E=300±2MeV
High availability (>97%)

## Slide 15: R&D: Spoke cavity
Spoke cavity prototype
Two double spoke cavity prototypes have been fabricated and tested, the maximum Eacc reaches at 15 MV/m, and the Q is above 4E10 at 7.3MV/m.
Based on the experience gained in the prototyping，we improved the cavity design and process to enhance the performance further.
The prototype of DSR
The prototype of cavity
with vessle
Vertical testing data of the prototype
parameter | prototype | improved
Frequency(MHz) | 324 | 324
βopt | 0.5 | 0.5
Ep/Eacc | 4.1 | 3.44
Bp/Eacc(mT/(MV/m)^2) | 9.2 | 8.86
R/Q（Ω） | 410 | 401
G（Ω） | 120 | 118
Beam tube diameter（mm) | 50 | 50
Eacc(MV/m) | 7.3 | 9
The parameter of DSR

## Slide 16: R&D: elliptical cavity
648 MHz 6-cell elliptical Cavity
parameter | design
Frequency(MHz) | 648
TTF@βg | 0.7
βg | 0.62
Ep/Eacc | 2.53
Bp/Eacc(mT/(MV/m)2 | 5.45
R/Q（Ω） | 309
G（Ω） | 177
Beam tube diameter（mm) | 105/120
Cell-cell coupling（%） | 1.35
Eacc(MV/m) | 14
The mechanical design of coupler
The cryomodule structure
mechanical structure of ellipsoidal cavity
The design of the superconducting cavity, coupler, magnetic shield, and tuner has been completed.
The cryomodule is currently under design.
The cavity is currently being fabricated.
End cover

## Slide 17: R&D: RF power source
A separate power source for each cavity, to adjust power and phase
  300kW @ 324MHz * 20
  >500kW @ 648MHz * 24
Spoke cavity
Solid state amplifier, with 30% safety margin
Elliptical cavity
Klystron + solid modulator + circulator and load

## Slide 18: R&D：MA loaded cavity
Magnetic alloy loaded cavity
Test acceleration gradient > 50kV/m
Operation acceleration gradient > 40kV/m
Cavity impedance variation < 3%（>9600 hrs）
Frequency range 1-4MHz
A：25Hz/50% fundamental hormonic
B：25Hz/15% second hormonic
Cavity impedance variation <3%
2022.09 officially put into operation

## Slide 19
Painting injection scheme - New idea
New idea: chicane bump and horizontal painting bump are combined into one bump which make the chicane bump "move“. The horizontal painting is performed by using the position and angle scanning at the same time.
Peak temperature of the stripping foil can be greatly reduced.
Both correlated and anti-correlated painting can be performed.
The edge focusing effect of bump magnets is greatly reduced
The difficulty of large aperture of the injection port and transport line required by angular scanning is solved.
It saves a set of bump magnets and is easier to optimize the layout of the injection system.
Advantages:

## Slide 20: Beam dynamic challenges in the CSNS-II RCS
Challenges | Solutions
Emittance increases driven by space charge effects | Dual harmonic RF cavity system; Painting injection
Emittance increase caused by broken four-fold symmetry of the RCS | New injection system
Beam instability | Increasing chromaticity damping and octupole magnet damping; Installation of a beam feedback system; optimization of the tune
Large beam loss at the arc section | Installation of a momentum collimator system
Too small vertical acceptance of the circulating beam vacuum chamber at the Lambertson magnet inlet | New Lambertson magnet
Three dual harmonic RF cavity
The cryomodule structure
Notes: We have corresponding strategies to address these challenges

## Slide 21: Summary
IHEP has successfully built and operated China’s first high-energy & high-current proton accelerator
Thanks to the hard work of the accelerator team, CSNS has achieved an excellent performance compared to the similar facilities
CSNS-II project is ready for implementation with all crucial technologies and physics in place, following the completion of CSNS plus initial R&D research.

## Slide 22
Thank you for your attention!