## Slide 1
An efficient high power proton accelerator and its possible muon applications
WORKSHOP OF MELODY2023
Tianjue Zhang for the Cyclotron Team at CIAE
China Institute of Atomic Energy
Nov 4th, 2023

## Slide 5
1
General consideration and overall design
Plan of Talk
2
Beam dynamics and parallel computing
3
RF system & HTS magnet
4
Possible muon application
5
Summary

## Slide 6
Project Motivation
High energy and high current proton accelerators are widely applied in frontier research fields such as nuclear physics and particle physics, national economic fields such as medical application and advanced energy, and even national defense industry and national security
Proton accelerator with an average beam power of 5-10 MW is the world's dream machine for more than 30 years.
The MW class proton accelerators attracting institutions to continue research and tackle key problems.
★CIAE
★CIAE
High-power facilities in the world

## Slide 7
High Power Proton Accelerator:
Cyclotron, LINAC and RC Synchrotron
The average power of the three different types of constructed accelerators currently is from 0.2MW to 1.4MW
Institute | Facility | Energy (MeV) | Power (kW) | Current (uA) | Repetition rate (Hz) | Remark
RAL | ISIS | 800 | 200 | 250 | 30 | Short pulse
JAERI/KEK | J-PARC | 3000 | 1000 | 333 | 25 | Short pulse
ORNL | SNS | 1000 | 1400 | 1300 | 60 | Short pulse
LANL | LANSCE | 800 | 1000 | 1000 | 100 | Long pulse
PSI | SINQ | 590 | 1400 | 2400 | - | CW
TRIUMF | ISAC | 500 | 200 | 400 | - | CW
Europe | ESS | 2000 | 5000 | 2500 | 14 | Long pulse
RC Synchrotron
LINAC
Cyclotron
Current status for high power proton accelerator

## Slide 8
High Power Proton Accelerator:
Cyclotron, LINAC and RC Synchrotron
The average power of the three different types of constructed accelerators currently is from 0.2MW to 1.4MW
Institute | Facility | Energy (MeV) | Power (kW) | Current (uA) | Repetition rate (Hz) | Remark
RAL | ISIS | 800 | 200 | 250 | 30 | Short pulse
JAERI/KEK | J-PARC | 3000 | 1000 | 333 | 25 | Short pulse
ORNL | SNS | 1000 | 1400 | 1300 | 60 | Short pulse
LANL | LANSCE | 800 | 1000 | 1000 | 100 | Long pulse
PSI | SINQ | 590 | 1400 | 2400 | - | CW
TRIUMF | ISAC | 500 | 200 | 400 | - | CW
Europe | ESS | 2000 | 5000 | 2500 | 14 | Long pulse
CIAE | CYCIAE-2000 | 2000 | 6000 | 3000 | - | CW FFAG
RC Synchrotron
LINAC
Cyclotron
Current status for high power proton accelerator

## Slide 9
 | Cyclotron (Isochronous) | Linac | RCS | FFAG (Isochronous)
CW beam |  |  |  | 
FF magnets |  |  |  | 
Fixed RF |  |  |  | 
>1 GeV |  |  |  | 
The road map of higher power machine
L. Calabretta and Y. Ishi, Overview of FFAG, FFAG-2018： Energy limit：1 GeV
Current status for high power proton accelerator

## Slide 10
Energy efficiency
CW FFA with HTS magnets and high-Q RF cavity ≈ 30%
The energy efficiency of the PSI isochronous cyclotron is about 3 times of the other types.
To develop high average beam power, high power efficiency, and high cost-effective proton machine, the isochronous accelerator is a good technical route.
HTS magnet is used to replace the normal temperature magnet , and an RF cavity with Q value of 90000 to replace the 45000 cavity at PSI. Energy efficiency can be increased from PSI’s ~20% to 30%,
LINAC+RCS
SC LINAC
Basic Description of 2 GeV CW FFA –Energy efficiency
CYCLOTRON
Total power of PSI Cyclotron ~8 MW，1.4 MW proton beam, beam/grid efficiency: 18%, after upgrade: 24%
～8.6%
～3 %

## Slide 11
2011
800 MeV Ring Cyclotron Proposal
2014
2GeV FFA Conceptual Design
2018
2GeV Isochronous FFA Proposal
2019
Financial Support for Pre-research
Basic Description of 2 GeV CW FFA
Goal: 2GeV, 3mA, 6MW CW Proton Beam

## Slide 12
Realization of strong focusing in GeV-class FFA
Theory
Adjustment of peak field gradients in wide radial range.
In a synchrotron, particle orbits are fixed within a small radial range, and the tune is easily controlled, so the energy can reach higher levels than in a cyclotron.
In a cyclotron, hundreds of orbits change with energy increasement, which makes it more difficult to control the tune within certain range or manipulate it.
Synchrotron
Fixed orbits
Dipole
Quadrupole
Sextupole
Octupole
E.D. Courant, M.S. Livingston, H.S. Snyder, "The Strong-Focusing Synchrotron—A New High Energy Accelerator", Phys. Rev. 88 (5): 1190–1196 (1952).
Cyclotron
Thomas focusing
variable orbits
Dipole
Quadrupole
Sextupole
Octupole
1st order variable gap
2nd order variable gap
uniform gap
3rd order variable gap

## Slide 13
Realization of strong focusing in GeV-class FFA
Example
Adjustment of peak field gradients in wide radial range.
Effects of magnets such as quadrupole, hexapole, and octupole lenses to enhance vertical and radial focusing, compensate chromaticity, and handle resonance are realized by high order field equivalent.
Simple 1st order magnet
Work path optimization
Radial field
Transfer matrix
Twiss parameter
Oscillation frequency
Solving and
Octupole Component
No vertical motion and delta momentum equals dp
Nolinear effect
quadrupole
Dipole, distort Isochronism
Modulating the magnetic field gradient in a large radial range, provides additional focusing power and chromaticity matching effects, hit the energy limit of isochronous accelerators.

## Slide 14
Injection, extraction, and RF consideration
Extraction
Two methods for increasing the turn separation
Five RF cavities are added in addition to the original design of 10 RF cavities so that the energy gain per turn is up to 15 MeV. Thereby, the turn separation is increased from 10 mm to 15 mm, and can be further increased to about 30 mm by precession.
Septum
Septum

## Slide 15
Current limit
3 mA/6 MW beam could be expected very conservatively
Beam Intensity Estimation
Tune Shift Estimation
Taking into account relativistic effects for the high energy beam, the tune shift is 0.025 ~ 0.1 in high energy and low energy regions.
[2]
The beam intensity of ~5 mA for 10 MeV, and more than 10 mA for 15 MeV energy gain per turn. Such a high current limitation is also due to the big transverse acceptance of FFA.
[1]
Injection, extraction, and RF consideration
The 2GeV FFA machine has a potential to hit the aim of 10MW average beam power.
[1]
PSI scaling law
[2]
Dr. Richard Baartman, TRIUMF, Proc. of cyclotrons 2013

## Slide 16
RF system
High-Q RF cavitiy is crucial for stable operation.
Injection, extraction, and RF consideration
In the overall design, we still have five valleys with enough space, one for injection/extraction, and the rest for flattop cavities.
During the operation of this high power machine, in case of the worst case, two RF systems fail. Our solution is to improve the Q value of each main RF cavity in the design stage. Then we should be able to increase the voltage of each RF cavity by 20% to maintain the 15 MeV energy gain per turn.
We have completed the 1:4 scale RF cavity test, and the test result of Q value encourages this idea.
Layout of 2 GeV FFA

## Slide 17
1
General consideration and overall design
Plan of Talk
2
Beam dynamics and parallel computing
3
RF system & HTS magnet
4
Possible muon application
5
Summary

## Slide 18
Basic beam dynamics and resonance study
2GeV FFA tune diagram
Scheme 1
Scheme 3
Scheme 2
Parameters | Scheme 1 | Scheme 2 | Scheme 3
Extracted energy/GeV | 2 | 2 | 2
F magnet radius/m | 23.3~26.8 | 18.2 ~20.9 | 17.6~19.4
D magnet radius/m | 23.3~26.8 | 18.2 ~20.9 | 17.6~19.4
Focusing field/T | 1.5~2.7 | 1.56~2.62 | 1.57~2.66
Defocusing field/T | 1.0 ~2.4 | 1.77~2.51 | 1.15~2.31
Number of lattices | 10 | 10 | 10
RF frequency/MHz | 44.4 | 35.1 | 51.6
Cavity voltage/MeV | 1.2 | 1.5 | 1.5
Harmonic number | 26 | 16 | 22
Number of cavities | 10 | 15 | 15
Turn separation for the extraction/cm | 1.5 | 1.5 | 2
Field distribution
径向三阶调变磁场梯度
边缘场

## Slide 19
3Vr=10
4Vr=10
Stable region for Scheme 3
Stable region
10 cell lattice scheme is suitable for 2 GeV isochronous FFA
The physical parameters of the lattice scheme have been determined for all schemes and are proven to be feasible in engineering.
Analyze the phase space of 3rd and 4th inherent resonance during the 2GeV acceleration, and the large transverse phase space acceptance of the accelerator lays the foundation for higher current beam acceleration.
Basic beam dynamics and resonance study
Stable region for Scheme 2
4Vr=10
Energy = 800 MeV

## Slide 20
Basic beam dynamics and resonance study
The 𝜈r=2 resonance line will excite the overall oscillation of bunches, and bunches will be stretched longitudinally, resulting in increased energy dispersion.
By adjusting the phase of B2 properly, the beam can be centered.
Resonance Suppression Method
Resonances
𝜈r=2 would cause radial and longitudinal coupling effect.

## Slide 21
Resonances
10 cell lattice scheme is suitable for 2 GeV isochronous FFA
Basic beam dynamics and resonance study
Driving terms of the resonance excited by 3rd and lower order imperfection field are summarized, and the results ensures that the influence of the resonance excited by magnetic field is controllable.
Numerical simulation for resonance study
Resonance lines | Order | Driving term | Energy (MeV)
vr=3 | 1 |  | 1850~2000
2vr=5 | 2 |  | 1280
vr-vz=0 | 2 |  | 1120
vr+vz=5 | 2 |  | 1640
vr+2vz=7 | 3 |  | 1390
vr-2vz=-2 | 3 |  | 1250
2vr-vz=2 | 3 |  | 1030
2vr+vz=8 | 3 |  | 1730
3vr=7 | 3 |  | 1160
Resonance lines | Order | Driving term | Energy (MeV)
vr=3 | 1 |  | 1850~2000
2vr=5 | 2 |  | 1280
vr-vz=0 | 2 |  | 1120
vr+vz=5 | 2 |  | 1640
vr+2vz=7 | 3 |  | 1390
vr-2vz=-2 | 3 |  | 1250
2vr-vz=2 | 3 |  | 1030
2vr+vz=8 | 3 |  | 1730
3vr=7 | 3 |  | 1160

## Slide 22
Resonances
10 cell lattice scheme is suitable for 2 GeV isochronous FFA
Resonance study – Scheme 3
Although we introduce large driving terms, the radial and axial beam size are not significantly blown up. Radial resonance lines which mainly destruct the radial beam envelope are shown from plot (a) to (c).
Simulation with imperfection
But some of them are not mentioned, like Vr-Vz=1. Sextupole resonance of Vr-2Vz=0, and the octupole sum resonance of 2Vr+2Vz=10 should be very strong.
Vr-2Vz=0
Walkinshow resonance, off-center ~3 cm
2Vr+2Vz=10

## Slide 23
Extraction
Three options for beam extraction (1)
Possible solutions for extraction
Septum
Septum
(1) Half-integer resonance extraction
The requirement for magnetic field error is too challenging in engineering.
Option 1: Crossing through the 𝜈r=3 integer resonance, and utilizing one of half-integer resonances for extraction.
The Vr=3 resonance is the most serious resonance line affecting the beam current. The third harmonic of 1 Gs will cause the beam envelope to increase by 2~3 times
Half-integer resonance extraction is a relatively mature scheme in isochronous circular accelerators, and the turn separation is doubled. But the introduction of half-integer resonance in 2 GeV FFA needs to pass through 𝜈r=3 integer resonance first.
Scheme 1
Scheme 3
Scheme 2

## Slide 24
Extraction
Three options for beam extraction (2)
Option 2: Avoiding and utilizing the 𝜈r =3 integer resonance, introducing harmonic magnetic field for precession extraction.
It is beneficial to arrange injection and extraction components based long drifts. And the number of cavities is increased from 10 to 15, and turn separation is enlarged from 10 mm to 15 mm.
Adjusting the working path of the extraction area, and controlling 𝜈r≈3 resonance to drive radial oscillation. Turn separation generated by precession can be increased to more than 30 mm.
Energy gain
nonlinear resonance
Precession due to integer resonance
Septum
Vr
Vz
Cavity
Long drift
Integer resonance and precession extraction
Longitudinal defocusing phase and reasoance precession leads to beam envelope growth
Possible solutions for extraction

## Slide 25
Extraction
Three options for beam extraction (2)
Septum
In order to avoid crossing the resonance 𝜈𝑟=𝟑, there is a certain phase shift with RF system near extraction region.
The phase width and energy dispersion of the beam increase during extraction, which causes the beam envelope increases to a certain amount during precession extraction.
Possible solutions for extraction
Extraction
Three options for beam extraction (3)
Septum
The emittance of the injected beam is selected as 2.2 mm*mrad, the phase width is ±3°, the beam envelope is about 2.5 cm.
It can be seen that placing the ESD at a position with a radius of 1899.5 cm is conducive to a high-efficiency extraction
Partical distribution on radial probe

## Slide 26
Parallel computing and code opimization
Parallel computing
Software development and algorithm optimization
Adaptive mesh refinement (AMR) is within OPAL code.
AMR in OPAL (Left) and the large domain size in radial and longitudinal direction for the case of FFA (Right).
AMR Flow chart after modification
Start
end
Yes
Yes
The modified algorithm deletes the domain mapping process and changes the grassroots area 𝛺0 according to the change of the boundary value of bunches.

## Slide 27
Parallel computing and code opimization
brings about an increase in the overall time spent
Parallel computing
Software development and algorithm optimization
Simulation time comparison
Simulation result comparison
When the time other modules cost is not changed, time spent on solving the poisson equation accounts for the majority of numerical simulation.
Before modification
After modification
The results of the newly developed algorithm AMR_NEW are more close to FFT.
Emmitance
RMS size
Beam location
 | MX/Y/Z | Total/s | Regrid/s | Solve/s | Map/s
AMR | 32/32/4 | 228.6 | 0.84 | 220.2 | 0.035
AMR_NEW | 32/32/4 | 115.5 | 3.16 | 103.22 | 0.02
Better performance for the case with large domain size in radial and longitudinal direction

## Slide 28
The followings are the compared results with and without the space charge effect, with and without flattop cavity in more detail.
Parallel computing and code opimization
6 mA, 16382 macro particles, without flat-top cavity
3 mA, 16382 macro particles, without flat-top cavity
0 mA, 16382 macro particles, without flat-top cavity
6 mA, 16382 macro particles, with flat-top cavity
The followings are the compared results with and without the space charge effect, with and without flattop cavity in more detail.
Initial conditions:
Emittance is 2 𝜋 mm⋅mrad
Phase width is 3°
Beam size ~2cm, turn separation up to 3cm.
The amplitude and phase of 3rd harmonic flat-top cavity need to be improved. And with neighbouring bubnches effect, cleaner extraction is expected.

## Slide 29
1
General consideration and overall design
Plan of Talk
2
Beam dynamics and parallel computing
3
RF system & HTS magnet
4
Possible muon application
5
Summary

## Slide 30
RF system
Specification and Key parameters
RF system Design
Layout of 2 GeV FFA
10 to 15 sets of accelerating Cavities are needed. Each cavity runs at a 1MW power level, providing ~1MV acc. Voltage, and is loaded with ~600kW beam.
Main & Auxiliary Cavity: for acceleration
Flat-top cavities are discovered to be essential in multi-bunch beam simulation. The basic idea is to absorb or dump power from the beam. The massive beam power is why 3 to 5 cavities are needed. The phase of each cavity should be aligned to the fundamental.
Flat-top Cavity: essential for a better beam

## Slide 31
RF SubSystem Design
A three-stage amplification chain is needed to drive the cavities. The first two are solid-state amplifiers up to 100kW. The last one is tetrode based, capable of providing 1.5MW RF Power.
The RF system will start with self-excitation mode. Later on, the cavities phase will be locked to an external reference for beam acceleration. A full digital Low-level RF controller will be used.
Heavy beam loading is a challenge to the stability
of the Main RF, and even more difficult for Flat-top system
Amplifier
The 1.5MW Tetrode will be driven by a 100kW solid-state Amp.

## Slide 32
Final Stage
RF Amplifier Preliminary Design
Amplifier
The 1.5MW Tetrode will be driven by a 100kW solid-state Amp.
For the IPA, the solid-state design is used, and the advanced technology of LDMOS with reflect power protection and adequate redundancy is applied.
For the FPA, the tetrode-based design is used. To guarantee the stability of the FPA output, the ground grid configuration is adopted.
Driven Stage
Solid-state for 100kW driven and 1.5MW Tetrode for the FPA

## Slide 33
LLRF system Preliminary Design
LLRF
A direct RF sampling control is studied for Self-excited Loop
The single gap cavity may suffer from Lorentz Force Detuning. Therefore a self-excited compliable RF control is pursued.
For this purpose, the dedicated control module, as shown on the right side, was developed for this purpose using the FPGA and the SOC (System On Chip) technologies.
Hardware & technology for direct RF sampling is mature enough these years to make it possible.
Direct RF sampling digital control
Voltage Stability: 1X10-4
Phase Stability: ±0.1°
Full digital RF control operates in the self-excited loop using FPGA

## Slide 34
35 MHz waveguide-type cavities
1,rectangular
2,omega
3,racetrack
4,boat shape
1:1 Scale Acceleration Cavity Design
Four numerical cavity modules are investigated. 2 of them seem promising. The boat shape has a 20 Mega-ohm shunt impedance and the highest Q value. Various simulations and experiments were carried on to study the boat shape further.
Item | Rectangular | Omega | Racetrack | Boat
Frequency(MHz) | 35 | 35 | 35 | 35
Operating Mode | TM110 | TM110 | TM110 | TM110
Quality Factor | 65880 | 84100 | 96670 | 103700
Shunt Impedance(Max, MΩ) | 5.38 | 10.08 | 19.29 | 20.14
Shunt Impedance(Min, MΩ) | 2.43 | 2.15 | 10.41 | 10.95
Power Dissipation(kW@2MV) | 743 | 397 | 207 | 200
Acceleration Gap Length(m) | 2.8 | 2.8 | 2.8 | 2.85
Acceleration Gap Height(m) | 0.15 | 0.15 | 0.15 | 0.15
Acceleration Gap Width(m) | 0.8 | 0.8 | 0.8 | 0.8
Has it been built before? | Yes, multiple | Yes, PSI ring | Not known | Not known
Mechanical design challenge | Low | High | Medium | High
Tuning Difficulty | Low | Difficult | Medium | Difficult
Highest Energy
Gain per Turn
High Q Value， High Energy Gain per Turn

## Slide 35: World-Class PSI Ring Cyclotron’s RF Cavity
Resonance frequency | Q-value
35.0 MHz | 103700
RF power@ 2MV W/O Beam loading | 
~200kW | 
Preliminary design of
CIAE 2GeV FFA
boat-shaped cavity
1:1 Scale Acceleration Cavity Design
L×W×H=6.91m×2.10m×3.14m
Bigger Cavity, Higher Q Value
The Q Value
almost doubled

## Slide 36
Q~43500、Rmax~10MΩ
1:4 RF Cavity Design and Manufacturing
The RF  Thermal  Structural  RF fully self-consistent closed-loop multi-physics FEM simulation and analysis is done. According to scale law: Frequency is 4 times higher, and Q/Rsh is expected to be half.
1:4 scale Cavity: design phase

## Slide 37
1:4 RF Cavity Design and Manufacturing
Both the outer elliptical-shaped and inner circular-shaped parts are formed by mold pressing. Due to the existence of the spring back phenomena and the difficulty of finding an accurate reference for the wire-electrode cutting, additional Computer Numerical Control (CNC) machining is needed. Finally, all the dimension errors will be compensated by fine finishing the nosecone according to the measurement during the cavity pre-assembling process for frequency checking.
Sophisticated parts are machined;
EBW is applied in joining all parts;
Surface polishing is handcrafted;
Overall strategy for manufacturing

## Slide 38
1:4 RF Cavity Design and Manufacturing
At 1 atmosphere pressure, two small loop probes with very small coupling coefficients were used to obtain the S21 frequency sweeping curve of the quarter scale cavity, then a loaded quality factor almost equal to the unloaded quality factor Qs can be obtained. It can be known that the unloaded Qs is higher than 42314.3, which is ~97.3% and 96.7% of the calculated values of 43500 and 43700.
Q and Rsh are good: reaches 97%; Manufacture is green light; Tuning of the cavity is verified; The vacuum seal is verified; High Power Coupler is verified; High power test is underway.
1:4 scale Cavity： Result is promising
Q=42314.3

## Slide 39
After obtaining the analytical magnetic field and the basic geometry of the magnets, e.g. the spiral angle, then the magnet design is initiated, to match the field distribution between the FEM and the analytical model
Bd=-0.6386*(r-23.5)3+2.9921*(r-23.5)2-9.0592*(r-23.5)-4.6466
Bf=0.4221*(r-23.5)3-1.7247*(r-23.5)2+4.7565*(r-23.5)+14.8348
Magnetic field of the D magnet
Magnetic field of the F magnet
Orbit range
Field distribution between FEM and soft edge model, at r=26.5m in a single cell
High-temperature superconducting magnets

## Slide 40
The weight and dimension of each F / D magnet is equivalent to the main magnet of CYCIAE-100. Considering successful use of elliptical gap in 100 MeV cyclotron to generate radial varying gradient field, the iron magnet of 2GeV FFAG could benefit a lot from the design and construction experience of the room temperature 100 MeV H- cyclotron CYCIAE-100.
 | Length/Diam. (m) | Weight (ton) | Magnetic field (T)
F Bend | ~5.4 | ~386 | 1.5~2.7
D Bend | ~5.4 | ~266 | -1.0~-2.4
CYCIAE-100 | 6.2 | 435 | 0.3~1.36
100MeV: 435 ton
Bf=0.4221*(r-23.5)3-1.7247*(r-23.5)2+4.7565*(r-23.5)+14.8348
Elliptical pole profile of CYCIAE-100 magnet
Bd=-0.6386*(r-23.5)3+2.9921*(r-23.5)2-9.0592*(r-23.5)-4.6466
Magnet key tech: manufacture, mapping & shimming large range pole profile
High-temperature superconducting magnets

## Slide 41
Why High Temperature Superconducting (HTS) coils?
 | Room temperature coil | HTS coil | LTS coil
Radius of FFAG ring | ~34m | ~27 m | ~18m
Radiation resistance | Yes | Yes | No
Power consumption | Very Large | Low, easier to remove heat@30K | Medium, need more cooling power to remove heat@4.2K
Smaller size than room temperature coil magnets, radiation resistant compared to LTS magnets and lower power consumption to get higher energy efficiency of the whole machine.
High-temperature superconducting magnets

## Slide 42
Superferric: high energy efficiency and radiation resistance
HTS coil：high magnetic field yield compact size；iron pole：magnetic field and gradient modulation in large range.
HTS magnet with large gradient
ReBCO HTS tape has high Bc, Tc and Ic, thus is more stable under the thermal impact from beam loss. And compared to LTS, HTS is a better radiation resistant material.
Cryostat
60 K shielding
30 K cold mass
Iron pole HTS coil
Basic idea
HTS magnet R&D

## Slide 43
General issues
HTS magnet safety, design and shimming scheme
Field shimming by using the combination of degrees of freedom with less influence on the working diagram.
Gradient modulation in large range in radial direction is achieved by varying the pole gap of HTS magnet.
Field shimming by change the height of the gap, width of the pole. Change the spiral angle and trim coil to adjust the local tune diagram
Heat load and the quench protection of large HTS magnet
Heigh of the gap
Width and spiral angle of the pole
HTS tape is co-winding with stainless steel, thus the HTS coil can be self-protected during quench by bypassing the current.
Quench detection is based on voltage probes and is interlocked with the power supply.
未见明显增长
HTS magnet R&D

## Slide 44
Manufacturing process flow of high temperature superconducting coil
Influence of support links and tolerance on beam dynamics
Multiphysics simulation considering the thermal, electromagnetic, mechanical coupling effect; position adjustment method of coil.
Installation of upper shielding
Installation of upper OVC
Installation of support links and the upper shielding
Installation of 300K OVC
Installation of magnet
Single pancake coil winding & test
HTS coil installation
HTS magnet R&D
Multiphysics
EM, thermal, quench and mechanical simulation

## Slide 45
Hall probe
Current source
bubble chamber
Terminal voltage measurement
HTS coil
Ramping history
B-I curve
HTS magnet R&D
HTS Coils
Metel-insulation HTS double pancake was wound and tested
Ramping under liquid nitrogen immersion

## Slide 46
Variable gradient field of 1:4 scaled supperferric magnet is measured
HTS magnet R&D
3rd order pole face
1:4 Magnet
HTS coils are assembled with iron yoke
I/A | B/Gs | Voltage/mV |  |  |  |  |  | Temp
 |  | 1# | 2# | 3# | 4# | 5# | 6# | 
0 | 0.0 | 0 | 0 | 0 | 0 | 0 | 0 | 24.3K
10 | 2820 | 0 | 0.1 | 0.2 | 0.1 | 0.1 | 0 | 24.3K
20 | 5764 | 0 | 0 | 0 | 0 | 0 | 0 | 24.3K
30 | 8554 | 0.1 | 0.3 | 0.2 | 0.2 | 0.2 | 0.1 | 24.3K
40 | 10494 | 0 | 0 | 0 | 0 | 0 | 0 | 24.2K
I=243A，field>2T
Voltage<0.3mV

## Slide 47
1
General consideration and overall design
Plan of Talk
2
Beam dynamics and parallel computing
3
RF system & HTS magnet
4
Possible muon applications
5
Summary

## Slide 48
Muon Experimental Terminal
High Power Proton FFA and Heavy Ion LINAC Accelerator Complex

## Slide 49: Muon properties and decay
Intrinsic Muon Properties
  Gyromatic ratio (g-2)
  Mass
  Lifetime
  EDM
Better precisions
Looking for anormalies

## Slide 50: Mu2e/COMET
Proton Beam：8GeV@8kW
Time Structure: 200ns pulse separated by 1695ns
Going to start…

## Slide 51
Mu2e @ 2GeV/6MW
Construct the pulsed structure:
  200ns pulse separated by 2000ns
  2GeV/ 600kW
Use the same target and detector system
Need to investigate the background
Rough estimation：
Increase the sensitivity by 2 orders of magnitude！
Par. | Mu2e@Ferimilab | Mu2e@CIAE
Running time | 3y | 3y
POT/y | 1.2×1020 | 4.4×1022
Muon yield | 0.0019 | ~5×10-4
Capture rate | 0.609 | 0.609
Detector acceptance | 0.08 | 0.08
Sensitivity | 3×10–17 | 3.11×10–19

## Slide 52
Muon g-2
Fermilab:
  Muon Evergy: 3.094 GeV/c
  dp/p < 0.5%
  Muon rate: 10^4 muon/s
  Total >1.8*10^11 to 0.14ppm
J-PAC:
  300 MeV/c, starting from eV energy.
  Moderate surface muons at a rate of 1E8/s
    Expected muon rate 3E5/s, in case a powerful laser can be achieved.
    Total > 2E12 to 0.14 ppm
g-2 @ 2GeV/6MW, 1E9 μ+/s can be expected,
IMPROVE BY 1 ORDER OF MAGNITUDE

## Slide 53
1
General consideration and overall design
Plan of Talk
2
Beam dynamics and parallel computing
3
RF system & HTS magnet
4
Possible muon applications
5
Summary

## Slide 54
A CW FFA is proposed by CIAE to produce a 2GeV/6MW proton beam.
Beam dynamics results show good isochronism towards 2 GeV and have a very large phase space acceptance. The turn separation can be increased to ~3 cm with 5 additional cavities and off-centered injection, which seems to be enough for single turn extraction and for providing pulsed beam.
R&D Activities for key components, including the 1:4 HTS magnet and the high energy efficiency RF system, are finished for the 2 GeV high power CW FFA accelerator complex.
Some potential muon applications are exciting based on 6 MW proton beam. We are looking forward to more users and cooperation.
Summary

## Slide 55
Thanks for your attention!