## Slide 1
Jie PANG
14th Workshop of the FCPPL 2023.11.06
Accurate in-situ density measurement and anomaly detectability for rock petrophysics with cosmic-ray muon radiography
Ran HAN Zhiwei LI
Beijing Institute of Spacecraft Environment Engineering
North China Electric Power University
In collaboration with Imad Laktineh: Institut de Physique des 2 Infinis de Lyon
Notes: Thank for committee give me this chance to report our work, our work is about

## Slide 2
Outline
Introduction
1
Accurate density measurement
2
Anomaly classify
3
Summary
4
Notes: I will introduce our work from this four part

## Slide 3
Traditional density inversion use gravity data.
Gravity inversion suffer non-uniqueness of solution.
Density inversion is a complex calculation.
Cosmic-ray muon can penetrate thick rocks.
Matter density directly connect with number of muon detected in downstream.
Muon radiography can inversion the in-situ density, and with high spatial resolution.
Introduction
This work try to measure accurate in-situ density by muon radiography.
Honglei Li et. al. 2021
Notes: We make a accurate in-situ density measurement based on muon radiography
Traditional density inversion in rock petrophysics use gravity data, but …, and is complex in calculation
Muon radiography is a new technology in petrophysics can

## Slide 4
Model
Need to detect the muon of opensky and the surviving muon which cross the matter.
Notes: Muon radiography need to detect the attenuation of muon after interaction with the matter, therefore
We use muon radiography to inverse density based on the different energy loss for muon when they cross matter
𝐸_𝑚𝑖𝑛 determines the survival muons that can be detected after cross the matter. It is an integral of the muon flux spectrum
So with the survival muon and the muon flux spectrum we can calculate the minimum initial energy and we can calculate the density length the muon through

## Slide 5
Experiment
Fe
(Thickness
90cm)
Fe
(Thickness
90cm)
Rock
(Thickness
88.5cm)
Water
(Thickness
76cm)
30cm
30cm
30cm
30cm
10cm
10cm
10cm
10cm
Top view
Laboratory photo
We try to invert three different type of matters in our experiment.
Each layer is 5050 pixels.
Notes: In our work we place three type of materials to try to measurement their density

## Slide 6
Outline
Introduction
1
Accurate density measurement
2
Anomaly classify
3
Summary
4
Notes: I will introduce my work from this four part, firstly, I will introduce density inversion method and machine learning method we use in this work

## Slide 7
Raw data stability
Without models
With models
Counts over 3 will be discarded
Detector efficiency is approximately 87%
Each phase with 220 hours of data
Discard
Discard
Next step will select the muon events which be used in density inversion.
Notes: Here shows the stability of our raw detected data, than we obtain 87% of useful counts that mean each phase with 220 hours of data

## Slide 8
Events Reconstruction
Events hit in four layers in the same time.
Events hit in each layer fit with a straight line.
Nearly vertical muon events.
Filtering criteria:
2-D events distribution
Each pixels with few events, that will have an influence to the accuracy of inversion density.
Notes: Here is the filtering criteria we select muon events
Events hits in four layers in the same time consider as a potential muon events
Then use the hits in layer 1 and layer 4 to fit a straight line, hits in layer 2 and layer 3 should with a distance in plus or minor 1pixels
And finally we select the nearly vertical muon events which layer 1 and layer 4 with maximum deviation of plus or minor 2 pixels the selected result are show in right

## Slide 9
Box filtering Processing
A kernel is used to merge the events in each pixels.
The error has been reduced by sacrificing spatial resolution.
2-D events distribution after box filtering
Consider the coulomb scattering, only events in black frame are use in inversion.
Notes: We use box filtering to increase the event we use in density inversion

## Slide 10
Effect of Recording Time
Ratio variation over time
Ratio distribution over time
Divide the events of opensky by the events of models placement can obtain the ratio.
With the recording time increases, the error decreases.
Simulation shows more recording time will have a better result.
With the ratio distribution, we can calculate the inversion density.
Notes: Here we show the effect of recording

## Slide 11
Density Inversion
2-D ratio distribution
Correlation between ratio and
2-D distribution
Known thickness
2-D density distribution
Divide the density length distribution by known thickness can obtain the density distribution.
Notes: The correlation between ratio and density length can be calculated.
The path length of muon cross matter can be considered as the thickness of matter since nearly vertical events filtering.
With ratio distribution, correlation between ratio and density length and matter thickness, one can inverse the distribution of density.

## Slide 12
Density Inversion
Muon radiography used in density inversion with a accuracy about 2.5~9%.

## Slide 13
Outline
Introduction
1
Accurate density measurement
2
Anomaly classify
3
Summary
4
Notes: I will introduce my work from this four part, firstly, I will introduce density inversion method and machine learning method we use in this work

## Slide 14
BP network Method
input
Relu(1,32)
Relu(32,16)
Relu(16,8)
Softmax(8,4)
output
Cross
Entropy
BP process
Ratio
(1500h
simulation)
Density
anomalous
Muon radiography needs a long recording time.
Matter with low density length shows a high sensitivity in ratio variation.
Neural network can quickly divide input features into different labels after training with enough data.
We build a backpropagation neural network to classify different density anomalies.
Notes: We also try to use machine learning way to classify different density anomalous. Here is the backpropagation neural network we construct, it has three hidden layers and use relu as the activation function
And loss function is cross entropy, it can classify anomalous to four type based on the input ratio

## Slide 15
 | 20h Experiment |  |  | 220h Experiment |  | 
 | Fe | Water | Rock | Fe | Water | Rock
Features
Classify
result
High density matter can be classified quickly, but low density matter need more recording time.

## Slide 16
Outline
Introduction
1
Accurate density measurement
2
Anomaly classify
3
Summary
4
Notes: I will introduce my work from this four part, firstly, I will introduce density inversion method and machine learning method we use in this work

## Slide 17
Summary
We use radiography for density inversion, after events filtering and data processing, our obtain accurate inversion results.
We study the detectability of three type of anomalous using machine learning method and the results shows that the anomalous can be well classify.
In next step, we try to classify density anomaly with close features.
Notes: 我们首先开展了实验对没有穿透物质和穿透不同物质情况下的缪子事例进行了探测得到了220个小时的有效数据