## Slide 1
Status of Stereo Crystal ECal
Huaqiao Zhang, Xiao Zhao(IHEP, Beijing)
Chengdong Fu, Fangyi Guo (CEPC software)
Yong Liu, Gang Li, Qian Liu, Manqi, Shengsun, Jianbei, Jianchun,Joao et. al…

## Slide 2: Outline
The design of SCEcal
The simulation of SCEcal
  Energy and 3D position resolution
  γ/γ and γ/π separation
  Higgs  γγ mass resolution
  PFA Hdi-jet mass resolution (developing)
Summary

## Slide 3: Requirement of a CEPC PFA calorimeter
CEPC Physics requirements
  Precision measurements with Higgs and Z/W
  Jet energy resolution (dEjet/Ejet- 3~4%)
  Charged particles : 65% (tracker)
  Photons: 25% (ECAL)
  Neutral Hadrons: 10% (HCAL + ECAL)
PFA based Calorimeter (CEPC)
  Good Shower separation
    Small Moliere radius (Dense detector)
    High lateral granularity (~Moliere radius)
  Good Energy resolution
    Critical in some special process
  Sophisticate algorithm
    Multi-million channels(energy and timing)
    Multi-Dimensional information
Overlap removal

## Slide 4: Stereo Crystal Electromagnetic Calorimeter: Basic idea
Crystal not pointing back to IP(Z axis)
  Angle with inner det. radius is 𝛼
  𝛼 = 0; point to IP(Z axis)
  𝛼 <= 90 degrees
Segmentation along R
  Ex: N_l = 10 layers
Uniform along Z
  Ex: 1 cm each seg.
Total crystal volumme
  pi*(r2^2-r1^2) * Z
Use BGO as baseline
  ~20.5 radiation length
Readout and mounting at R2 surface
r1
r2
D
phi
𝛼=0
Crystal module
𝛼
CEPC: Z = 6.7 m
r1 = 1.9 m, r2 = 2.2 m
readout
Cylindrical coordinate system
（Z, R, phi）
Total volume: 26 m3

## Slide 5: Stereo Crystal Electromagnetic Calorimeter: Design
To improve the 3D position resolution
  Pointing angle of even layers alone Z: 𝛼
  Pointing angle of odd layers alone Z： 𝛼’= -𝛼
Left eye
Right eye
Traditional Crystal Ecal
SCEcal
Not proportional to real angle/size

## Slide 6: Analytical optimization of SCECal geometry
3 DoF. determined the full barrel design (For a given R1, R2)
  𝛼: [0,90] : pointing angle
  N_l:[1,2,3….]: samplings along R
    correlate with the crystal size along phi and 𝛼; Typically ~1 cm
  Z: for the moment choose 1 cm segmentation, uniformly
Crystal length D = sqrt(r2^2 – r1^2*sin(𝛼)^2) – r1*cos𝛼
Crystal bar open phi angle phi=acos(r2^2 + r1^2 -D^2)/(2*r1*r2)
Phi segmentation = phi/N_l
Total number of crystal bars per Z segmentation: 2*pi*N_l/phi
Shower depth along r Sn at nth layer:
  Sn = Fn+1 – Fn
  Fn= r1* ( sin𝛼 /sin(𝛼 –n*phi/N_l) – 1 )
Crystal thickness xn:
  xn=Sn*sin(𝛼 –n*phi/N_l)

## Slide 7: Design of Endcap SCECal
Total shape looks like bottle stopper
Option 1:
  Similar idea of pointing angle definition along phi for each layer with same polar angle.
  Adjacent layers(same polar angle) with reversed pointing angle
Option 2:
  The pointing angle defined as angle between beam direction in (ex. Horizontal plane) for crystals in the same horizontal plate
  Adjacent layers(same horizontal plane) with reversed pointing angle
SiPM Readout and mounting at outside plane(same as Barrel)
not in Simulation yet
BGO+SiPM
New

## Slide 8: Introduction of SCECal simulation
Simulation and reconstruction done using CEPCSW
  Geometry implemented by Chengdong FU
  Crystals without wrapper/gap etc. (not reality)
  Simulation readout using carloStep info (no digitization)
  Reconstruction code initially provided by Fangyi Guo
  Development and reconfiguration by Huaqiao Zhang and X. Zhao
Performance of Energy, position resolution of photon:
  Different R segmentations tested: 5/10/14 layers
    10 layers turn out to be the best
  Different recontruction method:
    Under developing
The following study based on 10 layers segmentation on R

## Slide 9: Simplified Reco method for isolated particle
Find a Cluster, energy is the sum of crystals about 30 MeV
Hit (red points): The cross point of two nearby cluster crystal
  Geometric center of hit define its z, phi, R
  Assign hit energy as sum of the two crossed crystals
  Renormalize the total energy to the Energy of cluster
Cluster Phi/Z/R: energy weighted phi/Z/R of all hits
R [mm]

## Slide 10: Performance of Energy and 3D positioning resolution
5GeV gamma, phi: 10~350°(bugfix needed around 0), theta: 90°
  Z resolution ~ 0.84 mm; Phi resolution ~ 1.9 mm
  R resolution ~ 7.6 mm; Energy resolution as function of Threshold
R resolution
Z resolution
E resolution with gaus. fit
Threshold：0.1MeV
Phi resolution
E resolution
E resolution

## Slide 11: Simplified Reco method for 2 particle separation
For each layer (along Z):Find two locations with maximum energy deposition and separate them by the min. value between them
Merge clusters in individual layers use layer matching alg.
  Criteria on delta phi according to its point angle direction
Phi
Z
Two 5GeV γ

## Slide 12: Separation between two 5 GeV photons
Two 5 GeV photons, vary distance in between them
Success reconstruction: 2 neutral particles, 3.3GeV<Eγ<6.6GeV for each photon
Threshold: 2MeV
two γ from IP
SiW/1cm^3 cubes Crys.

## Slide 13: Separation between γ/π
5 GeV γ/10GeV π, vary distance in between them
Success reconstruction: 3.3GeV<Eγ<6.6GeV
Different π/γ separation power: pointing angle / magnetic field
Threshold: 2MeV
π+
γ
π-
γ
γ
π-
γ
π+
SiW/1cm^3 cubes Crys.

## Slide 14: Event display of shower seperation
Two 5 GeV photon, 66 mm distance
Two 5 GeV photon, 165 mm distance
5 GeV photon and 10 GeV pi-, 195mm
5 GeV photon and 10 GeV pi-, 66mm

## Slide 15: Boson mass resolution in H γγ
Sample: ZH->2neutrinos + γγ at 240 GeV
Energy, position reconstruction and separation using simplified reconstruction method described above
Crystal energy threshold: 2 MeV/50MeV
BMR = 0.33%
BMR = 1.3%
Threshold: 2MeV
Threshold: 50MeV

## Slide 16: γ/γ performance using CLUE algorithm
CLUE (CLUstering of Energy):
  Input parameters to determine cluster seeds, outliers and follower hits
  the cut-off distance in the calculation of local energy density (dc);
  the minimum density to promote a hit as a seed or the maximum density to demote a hit as an outlier (ρc);
  the maximum distance for a hit to be linked to a nearest higher point (δo);
  the minimum distance for a local high density hit to be promoted as a seed (δc).
[1] https://cds.cern.ch/record/2802590/files/CR2022_027.pdf
Separate the raw data into odd and even modules
CLUE clustering algorithm
Merge odd/even sub-Clusters
Current CMS HGCal reco. alg.
γ/γ separation
even dc :1 rho: 2 delta_c: 2 delta_o:3
odd dc :1 rho: 0.2 delta_c: 2 delta_o: 2
higgs->
BMR: 0.35%
Consistent with simplified method, further tunning possible
New
science.1242072

## Slide 17: Multiple particle separation (PFA)
Separation of multiple particle within jet is crucial for PFA
Suffering from
  Ghost hits （multiple hit solution)
  Multiple particle shower deposit energy in the same crystal
    Fine tuning of hit definition
    Add timing? Add readout in front of crystal(double-side readout)?
Still (long) way to be mature for PFA
  Checked clustering algorithm: calo only
  Which tracker? Which HCal?
  Which PFA?
  Detail tuning of algorithm

## Slide 18: Thoughts about Ghost hits
Confusion of red hit with yellow ones
  Happens only in small phi/R range
    R-range: 0-30CM
    Phi-range: -4.5 cm - +4.5 cm (10 layer)
Large probability have hits in middle shower depth, small chance to have hits in small or large shower depth
Big energy deposited in middle shower depth hit, small in inner/outer depth
If ghost hits happens
  largest change of phi: ~4.5 cm,
  Largest change of R: ~15cm
R
Phi
Phi range
Not yet estimated, but should be very small chance to have ghost hit have big impact
Ghost hit in Z*phi plane: 1cm * 9cm
Ghost hit in R*phi plane: 30cm * 9cm

## Slide 19: Summary
Stereo Crystal Ecal
  2D readout, 3D position reconstruction of particle shower
  Mounting and readout behind Ecal
    Radiation shielding, minimize material budget
    Uniform along Z, phi, and R: no dead regions
  Calorimeter only can provide:
    Good energy, 3D position resolution of shower
    Good di-photon, photon-pion separation
    Good higgs mass resolution in di-photon
  PFA Higgs--> di-jet mass resolution need further work
    Key: Multi-particle shower separation
Choice of crystal, SiPM et. al can benefit from other studies
Simplified prototype: SiPM + Sci. + NIM equipment just arrived
Searching personal power to work on this

## Slide 20: Backup

## Slide 21: Existing crystal ecal performance
https://indico.ihep.ac.cn/event/15229/session/15/contribution/11/material/slides/0.pdf

## Slide 22: Typical crystals (From Ren-yuan Zhu’s slides)