## Slide 1
CEPC Mechanics system and mockup tunnel in EDR
Haijing Wang, Xiaolong Wang, Yongsheng Ma, Minxian Li, Lei Wu

## Slide 2: Content
CEPC mechanics system plan in EDR
  Magnet supports and mockup tunnel
  MDI mechanics
  Collimators
Mockup tunnel
  Mockup structure
  Things to verify
Cost estimation
Summary

## Slide 3: CEPC mechanics system plan in EDR
Magnet supports and mockup tunnel
  Huge number of supports. It is necessary to verify the stability and flexibility of the structure, the construction and installation method, and alignment efficiency.
Elements in Collider | Unit | Number
Dipole support | set | 13314
Quadrupole support | set | 4128
Sextupole support | set | 1128
Corrector support | set | 3544
Vacuum device support | set | 98979
Beam Instrument Support | set | 4254
RF Support | set | 100
Elements in Booster | Unit | Number
Dipole support | set | 14866
Quadrupole support | set | 3458
Sextupole support | set | 100
Corrector support | set | 1200
Vacuum device support | set | 69164
Beam Instrument support | set | 2412
RF support | set | 12
Elements in Linac | Unit | Number
Bunching system support | set | 1
Magnet support | set | 144
EBTL support | set | 6
Accelerating structure support | set | 604
Vacuum device support | set | 5589
Beam Instrument support | set | 213
Elements in Damping Ring | Unit | Number
Magnet support | set | 184
Vacuum device support | set | 335
Beam Instrument support | set | 41
Elements in Transport lines | Unit | Number
Magnet support | set | 450
Vacuum device support | set | 3732
Beam Instrument support | set | 82

## Slide 4: CEPC mechanics system plan in EDR
Magnet supports and mockup tunnel
  For the TDR design, the natural frequency between different magnets differs much  optimize them to avoid over-design or weak stability.
Order of modes | Dipole & support | Quadrupole & support
1 | 50.2 | 27.3
2 | 51.3 | 31.5
3 | 59.7 | 33.2
No. of dipole supports | Maximum deformation (um) | 1st natural frequency (Hz)
2 | 50.5 | 33.2
3 | 13.0 | 45.7
4 | 6.5 | 50.2
Dipole support in TDR
No. of support points should be discussed with magnet and accelerator physics colleagues.

## Slide 5: CEPC mechanics system plan in EDR
Magnet supports and mockup tunnel
  For the TDR design, the Booster ring is 2.4 meters higher above Collider.  stability can be improved by shorter support.
Change support height
Change support number
Change steel sections

## Slide 6: CEPC mechanics system plan in EDR
Magnet supports and mockup tunnel
  For the TDR design, the Booster ring is 2.4 meters higher above Collider.  stability can be improved by shorter support.
Support height (m) | 1.3 | 1 | 0.7 | 1.3 | 1.3 | 1.3 | 1.3
Support No. | 4 |  |  | 3 | 2 | 4 | 4
Steel section (mm) | 80*80*5 |  |  |  |  | 60*60*3 | 80*80*3
Max. deformation on dipole (um) | 4 | 1 | 1 | 7.4 | 22 | 5.4 | 5.2
1st order of mode /Hz | 25.5 X | 35.9 X | 48.9 X | 22.5 X | 18.7 X | 17.7 X | 21.5 X
2nd order of mode /Hz | 27.8 yaw | 39.0 X+yaw | 56.3 yaw | 24.5 yaw | 19.5 yaw | 19.0 yaw | 23.5 yaw

## Slide 7: CEPC mechanics system plan in EDR
Magnet supports and mockup tunnel plan
  The final magnet support scheme (such as individual girder or common girder).
  The deformation and stability simulation and optimization of typical supports.
  The structure design of more magnet supports.
  The mockup tunnel and the verification of support structure, stability, installation and alignment.
Aim
  Be simple and fulfill the physics requirements, large adjustment ranges and high resolution.
Direction | Range of adjustment | Direction | Resolution
X | ≥±20 mm | X | ≤10μm
Y | ≥±30 mm | Y | ≤10μm
Z | ≥±20 mm | Z | ≤10μm

## Slide 8: CEPC mechanics system plan in EDR
MDI mechanics
  In TDR, we have optimized the MDI layout, all the accelerator devices within the detective angle acos0.99.
  Preliminary design and analyses of cryostat support and RVC.

## Slide 9: CEPC mechanics system plan in EDR
MDI mechanics plan
  Further assessment and mechanical design of the RVC, and a prototype if possible.
  The basically determined structure design of the support for cryostat at MDI, the detailed FEA of structure and stability, including the rough assessment of Lorenz force, quench cases and temperature change. Begin the necessary technique study if possible (eg. Vibration, movement and alignment related techniques).
  Refine the mechanics layout of all the accelerator components on base of TDR design.
Aim:
  RVC leak rate: 2.7 10–11 Pa·m3/s
  Support resolution: 5 um. Support can work theoretically.

## Slide 10: CEPC mechanics system plan in EDR
Collimators
  In TDR, we made a preliminary design of horizontal movable collimator for background decreasing.
  Jaw and vacuum vessel material: Glidcop Al-15, can endure the SR and HOM power in normal operation.

## Slide 11: CEPC mechanics system plan in EDR
Collimators
  For MPS collimators: beam incidence into the jaw, causing intense thermal shock.
  We are focusing on the new material similar to MoGr developed by LHC.
Facilities | Material
LHC | CFCMoGr
SKEKB | TaCFCCFC+Ta
HEPS | Graphite
APSU | Al or MoGr
Fcc-ee | MoGr
Materials of jaw tips
Samples developed recently, Gr 50%，Mo 25%，Ti 25%.
By vacuum hot pressing sintering method. Needs to be tested.

## Slide 12: CEPC mechanics system plan in EDR
Collimator plan
  The structure design and detailed FEA of the collimator for background decreasing and MPS, cooperate with accelerator physics, beam-material interaction and impedance colleagues.
  Begin the necessary technique study if possible (eg. Tip material and connecting technique with jaw body. )
Aim:
  Collimators can work theoretically.
  Thermal conductivity of new material ≥600 W/(m.K）
  Connection strength higher than 90% strength of base material.

## Slide 13: Mockup tunnel
CEPC is a 100 km facility with huge numbers of devices. There are many techniques and construction method to be verified in the mockup.
  The support stability and flexibility.
  The alignment method and alignment efficiency improvement.
  The installation method and operation space verification like HEPS before tunnel installation.
The tunnel mockup is a good way for CEPC exhibition, with some typical devices like magnet and support, vacuum devices and cryomodules.

## Slide 14: Tunnel mockup
A 60 m long tunnel mockup, including parts of arc section and part of RF section.

## Slide 15: Tunnel mockup
Mockup structure

## Slide 16: Tunnel mockup
Mockup structure
  RF section: 28 m.
  1 Collider cryomodule, 1 Booster cryomodule, wave guides, 2 single-aperture quadrupoles and supports.
  1:1 fake models made of plastic or steel sheets.

## Slide 17: Tunnel mockup
Mockup structure
  Arc section: 32 m.
  Collider: 1 quadrupole, 3 sextupole, 1 dipole (4 cores), 2 correctors and 2 BPMs, supports, vacuum devices.
  Booster: 1 quadrupole, 1 sextupole, 5 dipoles, supports, vacuum devices.

## Slide 18: Tunnel mockup
Mockup structure
  Arc section: 32 m.
  Collider: 1 quadrupole, 3 sextupole, 1 dipole (4 cores), 2 correctors and 2 BPMs, supports, vacuum devices.
  Booster: 1 quadrupole, 1 sextupole, 5 dipoles, supports, vacuum devices.
Collider arc section devices
Booster arc section devices

## Slide 19: Tunnel mockup
Mockup structure
  Arc section 32 m.
    All the magnets are fake steel model with real weight, can be replaced by magnet prototype.
    All the supports are prototypes, and installed as real project (eg. grouting).
    The vacuum tubes and bellows are prototypes.
    Valves, pumps and BPMs are fake ones.

## Slide 20: Tunnel mockup
  Stability for dipole will be compared with 3 or 4 supports
Quadrupole & support
Dipole & support
Valve
Vacuum tubes
Bellows
Sextupole & support
Things to verify
  Collider: Installation experiment of all devices, operating space
  Coil installation and connection on site
  Magnet & support stability

## Slide 21: Tunnel mockup
Things to verify
  Booster: Installation experiment of all devices, operating space
  Difficulties: installation to the ceiling, tight space between dipoles
  Magnet & support stability
Quadrupole & support
Sextupole & support
Dipole & support
Vacuum devices

## Slide 22: Tunnel mockup
Things to verify
  Semi-automatic adjustment and high-precision alignment field
  Aim: save alignment manpower and cost.
  Add some movable drivers and interface on the adjusting mechanism.
  Validating the technical solution in PAPS, and conducting tunnel alignment simulations in mockup.
For dipole supports
For sextupole girders, similar to girder of EBS

## Slide 23: Tunnel mockup
Things to verify
  Pre-alignment and tunnel alignment are the most time-consuming and labor-intensive task in the alignment process.
  The alignment method right now:
    Laser tracker
    Single-point monitoring, single-point adjustment, manual operation, repeated iterations, inefficiency.
  High-precision alignment field
    Multi-camera photogrammetry system
    Multi-point synchronous monitoring
    50% lower cost, significantly larger number of synchronous monitoring points.

## Slide 24: Tunnel mockup
Things to verify
  功能
    根据被测对象类型，自动调整测量视野；
    自动标定相机内外参数和畸变系数。
    通过空间坐标提取，采集标定工装图像，自动建立多目相机空间位姿数学模型；
    高带宽图像传输，实时获取测量场内监测点实测坐标，显示\输出实测坐标与理论坐标的差值。
  系统预期指标
    标定场范围0.5m~20m
    采集频率：≥15 Hz
    空间单点测量误差：≤ 4μm+4μm/m

## Slide 25: Tunnel mockup
Things to verify
  Magnet transport vehicles
  Aim: efficiency of the transportation and installation of the magnets.
  The resolution of the lifting fork is designed as better than 0.5 mm for the coarse positioning.

## Slide 26: Cost
模拟隧道
  共798万
  实验验证件~439万，含隧道内设备124万，三自由度安装运输车35万及准直高精度测量场280万。
子设备名称 | 单位 | 数量 | 价格 | 备注
Collider二极铁支撑 | 套 | 1 | 16 | 
Collider四极铁支撑 | 套 | 1 | 4 | 
Collider六极铁支撑 | 套 | 1 | 12 | 
Collider校正铁支撑 | 套 | 1 | 2 | 
Collider二极铁配重 | 套 | 1 | 17 | 2.7ton/每铁芯*4
Collider四极铁配重 | 套 | 1 | 10.5 | 7ton/每铁芯
Collider六极铁配重 | 套 | 1 | 4 | 0.9ton/每铁芯*3
Booster二极铁支撑 | 套 | 1 | 4 | 
Booster四极铁支撑 | 套 | 1 | 3 | 
Booster六极铁支撑 | 套 | 1 | 2 | 
Booster二极铁配重 | 套 | 1 | 2 | 1.2ton/每铁芯
Booster四极铁配重 | 套 | 1 | 3 | 2ton/每铁芯
Booster六极铁配重 | 套 | 1 | 0 | 0.25ton/每铁芯
真空设备 | 套 | 1 | 41.4 | 真空盒+波纹管
真空设备支架 | 套 | 1 | 4 | 12 in Collider +3 in Booster
三自由度安装运输车 | 辆 | 1 | 35 | 
准直高精度测量场 | 套 | 1 | 280 | 
部件名称 | 组件名称 | 数目 | 单位
多目摄影测量系统 | 测量相机 | 4 | 套
 | 同步控制器 | 1 | 套
 | 工控机 | 1 | 台
 | 测量软件 | 1 | 套
 | 基准尺 | 1 | 套
 | 相机姿态调整机构 | 1 | 套
辅助工装 | 相机标定工装 | 1 | 套
 | 基准测量工装 | 1 | 组
*准直预算 王小龙； 真空设备预算 马永胜。

## Slide 27: Cost
模拟隧道
  共795万
  隧道~332万（粗估，按1000m3及2.5%钢筋计算)。最短可30米，只含Booster RF模组及Booster 四极铁、六极铁及2块二极铁。
  展示件~24w
子设备名称 | 单位 | 数量 | 价格
模拟隧道 | 米 | 60 | 332
Collider 高频腔支撑 | 套 | 1 | 1
Booster高频腔支撑 | 套 | 1 | 2
Collider 高频腔模拟件 | 套 | 1 | 8
Booster高频腔模拟件 | 套 | 1 | 8
通用管线模拟件 | 套 | 1 | 5
真空束测模拟件 | 套 | 1 | 3

## Slide 28: Cost
MDI 关键工艺验证
  RVC样机：27万
  MDI超导铁支架调节及准直验证样机：56万
准直器关键工艺验证
  耐热冲击材料试验：59万
  材料连接及性能测试：30万
其他 60万
  Autodesk PDMC： 20万，共4人
  Ansys：10w/年，共30万
  差旅费:10万
设备名称 | 子设备名称 | 单位 | 数量 | 价格
RVC样机 |  | 套 | 1 | 27
 | 充气波纹管组件 | 套 | 1 | 9
 | 管路 | 套 | 1 | 1
 | 固定法兰及真空盒 | 套 | 1 | 3
 | 两个真空腔体及支撑 | 套 | 1 | 2
 | 铜密封圈 | 件 | 10 | 3
 | 改制及测试费 | 套 | 1 | 9
MDI超导铁支架调节及准直验证样机 |  | 套 | 1 | 56
 | 上层支架 | 套 | 1 | 18
 | 支架调节机构 | 套 | 7 | 14
 | 悬臂托架 | 套 | 1 | 11
 | 辅助支撑 | 套 | 1 | 3
 | 恒温器模拟件 | 套 | 1 | 5
 | 位移传感器及限位开关 | 套 | 6 | 4
 | 控制系统 | 套 | 1 | 2

## Slide 29: Summary
A tunnel mockup has been preliminary designed according to TDR design. Based on which the stability of magnet & support assembly, the high-precision alignment field, and the installation experiment can be verified.
The mechanics system also wants to make some progress on the magnet support design, the MDI mechanics and the collimators.