## Slide 1
Vertex detector toward TDR
Zhijun Liang (IHEP)
梁志均 （中国科学院高能物理研究所）

## Slide 2: Plan toward TDR
Major change from CDR to TDR
  Beam pipe diameter: 28mm (CDR)  20mm (TDR) (reduce 30%)
  Instant Luminosity per IP:
    Z pole: 32×1034 cm-2s-1 (CDR)  192 ×1034 cm-2s-1 (TDR, 50MW) (6 times increase)
    ZH: 5.6×1034 cm-2s-1 (CDR)  8.3 ×1034 cm-2s-1 (TDR) (~1.5 times increase)
Action item
  Optimize the geometry
    Whether we can reduce the radius of the first vertex layer , put it close to beam pipe
      First vertex layer: Radius=12mm (TDR candidate) or Radius =16mm (CDR design) ?
  Estimate the hit rate from background
  Fluence and total ionization dose estimation

## Slide 3: Vertex detector optimization for TDR
1st priority: Small inner radius, close to beam pipe (new baseline beam pipe radius=10um )
2nd priority: Low material budget <0.15% X0 per layer
3rd priority: High resolution pixel sensor： 3~5 μm
Global Timing resolution of CEPC tracker: ~25ns (40MHz collision @ Z pole)
C-tagging performance

## Slide 4: Hit rate and radiation from background (input for vertex)
Waiting for the update on background estimation (Haoyu)
First guess of background based on input (Haoyu)
  Instant Luminosity increase  radiation hardness requirement increased, tiny impact on hit density
  Beam pipe diameter: 28mm  20mm : Expect 3-5 times larger hit density and radiation
Hit density per crossing (CDR)
Total ionization dose (CDR)
Fluence (CDR)

## Slide 5: Hit rate and radiation from background (input for vertex)
Waiting for the update on background estimation (Haoyu)
First guess of background based on input (Haoyu)
  Instant Luminosity increase  radiation hardness requirement increased, tiny impact on hit density
  Beam pipe diameter: 28mm  20mm : Expect 3-5 times larger hit density and radiation
Hit rate and radiation from Background (CDR study, from Haoyu)

## Slide 6: Radiation hardness (Total ionization dose)
First guess on Radiation requirement (need final input from Haoyu):
Taichupix2 was irradiated in-situ tested up to 30 Mrad
Based on LHC experience, chip have potential to survive serval hundred Mrad
Taichupix3 irradiation test
Pixel threshold vs. TID
Taichupix2 irradiation test
Initial input on TID | First layer radius=16mm (CDR vertex design) | First layer radius=12mm (TDR design candidate)
ZH (240GeV) | ~1 Mrad/year | 3-5 Mrad/year
Z pole (91GeV) | ~60 Mrad/year | 200-300 Mrad/year

## Slide 7: Radiation hardness (neutron Fluence)
First guess on Radiation requirement (need final input from Haoyu):
CDR requirement: ~2*𝟏𝟎𝟏3𝒏𝒆𝒒⋅ 𝒄𝒎-𝟐 ⋅ 𝒚𝒓
TDR requirement: 1-6 *𝟏𝟎𝟏4𝒏𝒆𝒒⋅ 𝒄𝒎-𝟐 ⋅ 𝒚𝒓 (depending on radius)
  Whether CEPC MAPS sensor can survive 𝟏𝟎𝟏4𝒏𝒆𝒒⋅ 𝒄𝒎-𝟐 ?
neutron fluence 𝒏𝒆𝒒 𝟏𝟎𝟏𝟐 ⋅ 𝒄𝒎-𝟐 ⋅ 𝒚𝒓 | First layer radius=16mm (CDR vertex design) | First layer radius=12mm (TDR design candidate)
ZH (240GeV) | 3 | 9-15
Z pole (91GeV) | 120 | 360-600

## Slide 8: Radiation hardness (neutron Fluence)
Beam test for irradiated TaichuPix @BSRF (Nov 2023)
  Radiation of Taichu @ CSNS ( up to 1.5*𝟏𝟎𝟏4𝒏𝒆𝒒 )
  DUT is irradiated TaichuPix with modified process
  Preliminary result (by Yiming)
    Efficiency >99% @ 𝟏𝟎𝟏3𝒏𝒆𝒒
    Efficiency >95% @ 1.5* 𝟏𝟎𝟏4𝒏𝒆𝒒

## Slide 9: Hit density
First guess on Radiation requirement (need final input from Haoyu):
CDR : ~2 hits cm-2 BX -1
TDR requirement: 2~10 hits cm-2 BX -1(depending on radius)
Hit density Hits cm-2 BX -1 | First layer radius=16mm (CDR vertex design) | First layer radius=12mm (TDR design candidate)
ZH (240GeV) | ~2 | 6-10
Z pole (91GeV) | 0.6 | 1.8-3
Data rate per chip (triggerless) | First layer radius=16mm (CDR vertex design) From Weiwei | First layer radius=12mm (TDR design candidate)
ZH (240GeV) | 1.3 Gbps | 4-6.5 Gbps
Z pole (91GeV) | 2.6 GBps | 8-13 Gbps

## Slide 10: Summary： Action item
Based on initial input of background, compare advantage and disadvantage of different layout
  First layer radius 12mm Vs 16mm
  Still waiting for final input of background from MDI group (Haoyu)
Revisit vertex time resolution and occupancy, spatial resolution requirement
  Roadmap for R & D (Taichu –like/ Jadepix –like architecture)
  Finalize the readout architecture design ( need to consider trigger design)
Integration vertex design with beam pipe in MDI region
  For Cooling design and support structure, Cabling, and frontend boards location

## Slide 11: Air cooling for CEPC vertex detector
Air cooling is baseline design for CEPC vertex detector
Sensor Power dissipation:
  Taichupix design : ≤ 100 mW/cm2. (trigger mode), ≤ 150 mW/cm2 (triggerless mode),
  Taichupix measured result: ~60 mW/cm2(triggerless mode, 17.5MHz )
  CEPC final goal : ≤ 50 mW/cm2
Cooling simulations of a single complete ladder with detailed FPC were done.
  Need 2 m/s air flow to cool down the ladder