## Slide 1
Studies on Time Resolution of BGO Long Crystal Bar
Zhiyu Zhao, Baohua Qi, Yong Liu
2024.01.03

## Slide 2
Workflow for Time Resolution Simulation
G4 optical simulation for crystal unit
SiPM laser test
Toy MC of SiPM
Photon hit time
Single photon waveform
Waveform simulation
(digitization)
Pixels’ fired time
Time resolution
Waveform
5GeV e-
detected time of scintillation photon
Waveform fitting to get the time constant of leading and falling edge
Fired time of all the pixels
Pixel waveform
Total waveform(digitized)

## Slide 3
Optical Simulation for Crystal Unit
Get the time distribution of scintillation photon hitting on SiPM
  BGO crystal bar
  SiPM(S14160-3015PS)
5GeV e-

## Slide 4
SiPM Laser Test And Waveform Fitting
Get a function to describe the single photon waveform of SiPM
Fitting with a function to get the two time constants and , which determine the width of leading edge and falling edge
  First fitting the entire waveform
  Then fitting the leading edge and falling edge to get and , respectively
    : discharging time constant
    : charging time constant
    : amplitude and position
Waveform output by SiPM

## Slide 5
Toy Monte Carlo of SiPM
Get fired time of SiPM pixel, which would be used in waveform simulation
  Incident time of photon comes from Geant4 optical simulation
  Uniform light spot on SiPM
  BGO emission spectrum
  SiPM pixel density, PDE spectrum, crosstalk, pixel recovery effect
Fired time of all the pixels

## Slide 6
Waveform Simulation
Waveform simulation of SiPM with full digitization
  Integrate pixel waveform to get the entire waveform
    Recovery effect exists when photons hit on the same pixel
    Pixel waveform function from laser test and fitting
  Sampling rate: 2.5GHz
  ADC bit : 8
  Gaussian white noise: 0.2/0.38mV for 40/60cm BGO(from testbeam data)
  Amplification and QDC correction
……×40000
Waveform from simulation
Waveform from data

## Slide 7
Time Resolution
Timing method: 10% CFD
~30% difference between simu and data, but the gap between 40/60cm BGO is almost the same(~0.5ns)
  Fluctuations of number of p.e., single p.e. waveform and crystal uniformity need to be considered
DESY 5GeV Beam data
Simulation
Time
n%×Max1
n%×Max2
60cmBGO, ~2100p.e.
40cmBGO, ~1700p.e.

## Slide 8
Time Resolution with Pre-Shower Crystals
SiPM: S13360-6025PE
Preshower BGO thickness: 1, 3, 5, 6, 7cm
Time resolution of extremely large signal is about 0.5ns/1ns for 40cm/60cm BGO
  Entries>100 & fitting
Seff Amp:
Seff Amp:
better
  Fitting function:
    https://doi.org/10.1016/j.nima.2017.03.065

## Slide 9
Next
Simulate the time resolution as a function of energy deposit.
  Light yield calibration for G4 optical simulation
  Simulate with preshower
  Measure the devices in lab to get the intrinsic resolution of BGO.