## Slide 1
Source of instability in the RCS of CSNS
Liangsheng HUANG
huangls@ihep.ac.cn@CSNS·IHEP
6th ICFA Mini-Workshop on Space Charge 2024
DONGGUAN 2024.9.11-13

## Slide 2: Outline
Introduction
Beam instability in the RCS of CSNS
  Characteristic of instability
  Mitigation methods
Source investigation
  Source study overview
  Impedance measurement of ceramic chamber
  Impedance simulation of RF shield ceramic chamber
Summary

## Slide 3
Introduction
CSNS & RCS
  Lianc + RCS + target
  RCS
    Because of fast varied field, ceramic chamber is chosen to reduce the eddy currents
    76 ceramic chambers with length ~ 130 m
  Beam power
    CSNS: 100 kW, 1.56×1013 per pulse
    CSNS-II: 500 kW, 7.8×1013 per pulse
  Increase injection energy (from 80 MeV to 300 MeV) to mitigate SC effects
  Dual harmonic cavity in the RCS
Circumference/m | 227.92
Beam energy (Inj./Ext.)/GeV | 0.08(0.3)a/1.6
Repetition rate/Hz | 25
Nominal tune (H/V) | 4.86/4.78
Natural chromaticity (H/V) | -4.0/-9.2
Beam intensity/ 1×1013 | 1.56 (7.8)
a means CSNS (CSNS-II)

## Slide 4
Introduction
CSNS & RCS
  An oscillation observed at the beam power of 50 kW
  Optimizations of the tune curve and chromaticity to suppress the instability
  With some upgrades, the beam power reaches 160 kW
100kW
125kW
160kW
140kW
AC sextupole
QT
1st harmonic CAV
2nd harmonic CAV
MC and octupole
2020/2/28
2022/2/21
2022/10/07
2024/03/04

## Slide 5: Beam instability in the RCS of CSNS
Characteristic of instability
  Scan intensity: double-bunch for normal tune with natural chromaticity
    The intensity of the Linac is adjusted to adjust the intensity in the RCS
    The oscillate around 8 ms is firstly observed and it is worse as the intensity goes higher
    The growth time is less than 1 ms
    Only coupled bunch mode of 1 has been observed
    The beam behavior of single bunch is similar that of double bunches with same beam intensity
  The instability was also observed in the vertical plane when the power was further increased
  The oscillation before 5 ms appears soon after the injection, but it disappears for 100 kW

## Slide 6: Beam instability in the RCS of CSNS
Characteristic of instability
  Head-tail (HT) mode can be analyzed from the difference of BPM signals.
  Before 5 ms, HT mode of 75 kW is different from that of 100 kW
  The measured tune is shifted with beam intensity
  Space charge?

## Slide 7: Beam instability in the RCS of CSNS
Characteristic of instability
  Scan horizontal tune with Np = , corresponding to a beam power of 100 kW.
  is changed from 4.3 to 4.9 while
  The instability is not observed =4.3
  The instability becomes clear as the tune moves toward 5.0 from below
  The instability shows up later
  is closed to 0.12 MHz
  A potential resonance may exist in the RCS
  It provides valuable guidance for adjusting the transverse tunes to mitigate the instability

## Slide 8: Beam instability in the RCS of CSNS
Characteristic of instability
  its sensitivity to chromaticity ξ
  encourages us introduce sextupole magnets to mitigate this issue
  Test with AC sextupole, so the ξ is constant
  The test was done with beam power of 60 kW at tune of (4.86, 4.78)
  The beam position is tamed with ξ decreasing
  The HT mode is clearly changed with ξ
TbT measured beam position and the beam survivals curve for different consistant chromaticity in the acceleration cycle.
The head-tail mode with different chromaticity
https://doi.org/10.1007/s41605-023-00428-7

## Slide 9: Beam instability in the RCS of CSNS
Mitigation method
  Optimization of the tune and chromaticity
  The tune below 0.5 can avoid instability, but with low transmission. The tune above 0.5 is selected
  A tune tracking pattern has been optimized for the operation mode, in which the initial tune is set high to reduce beam loss due to space charge, and then it is gradually decreased to avoid instability.
  Chromaticity optimization using DC sextupole is employed
  With two mitigation methods, the beam power arrived at 100 kW successfully
ξ with DC sextupole
Tune pattern

## Slide 10: Beam instability in the RCS of CSNS
Mitigation method: AC sextupole played a crucial role with 100 kW+
  AC sextupole was installed in 2021
  The chromaticity can reach (-10,-10) with AC sextupole for all energies
  With help of AC sextupole in the operation mode, the transmission has been improved by ~ 2 %
  It is very vital to suppress the instability from 100 kW to 160 kW
RCS transmission (left) and TbT beam position (right) and with the DC and AC sextupole field in the operation mode

## Slide 11: Beam instability in the RCS of CSNS
Mitigation method
  A pulsed octupole magnet was developed
  The instability can be suppressed by using the pulsed octupole
  At the high energy stage, meeting the requirements for operation
  At the low energy stage, the transmission remains low for operation.
  This may be attributed to the reduction in dynamic aperture

## Slide 12: Source investigation
Overview impedance
  Generally components are used, including ceramic and SS chambers, kickers, etc
  The impedance of all components has been estimated. It is small except ceramic chamber
  Mismatch between the Pulse Form Network and cable induces reflections and affects the beam
  Impedance measurements about 10 years ago showed the RCS kicker was perfectly matched, so the impedance can be ignored.
  During beam commissioning, we confirmed it by the beam at 50 kW beam power

## Slide 13: Source investigation
Overview impedance
  A very complicated structure of the ceramic chamber: 100 nm TiN + ceramic + RF shield
    Ceramic chamber is used in magnet to decrease eddy current effects
    100 nm TiN to reduce SEY
    RF shield/screen to prevent from field leakage and noise in the tunnel into chamber, reducing impedance
    A capacitor is employed in each copper strip to create a high-frequency pass filter
  The imaginary part of the impedance for the ceramic chamber is expected to be large
  Simplified structure in theoretical calculations: (1) Cu strip  good conductor. (2) capacitors are ignored


## Slide 14: Source investigation
Impedance measurement of ceramic chamber
  Impedance measurements based on a spare chamber in injection area (INB1)
  A coil is used as a probe to measure impedance
  Measure S11
  A narrow impedance was observed with BIG shut impedance. The center freq. is 0.123 MHz with Q ≈ 150
  The source is identified by remove the RF shield
With RF shield/screen
Without RF shield/screen

## Slide 15: Source investigation
Impedance measurement of ceramic chamber
  Confirmed the resonance using the spare chamber in the quadrupole QA
  A narrow impedance was also observed with center freq. of 0.139 MHz
  Based on two measurements, the resonance should exist for all ceramic chambers
  The impedance is too much BIG, so the instability can be observed at a such low beam power

## Slide 16: Source investigation
Impedance measurement of ceramic chamber
  TCBI calculation
  Betrtron line is coupled with impedance when
  The instability can be repeated in the simulation
K. Y. Ng, Physics of Intensity Dependent Beam Instabilities (World Scientific, Singapore, 2006)，p393

## Slide 17: Source investigation
Impedance simulation of ceramic chamber （CST simulation code）
  Particle Studio (PS) is generally used to simulate wake produced by the beam and the hexahedral mesh is employed in TD. No impedance has been found
  Microwave Studio (MS) is used recently and the resonance agrees well with that of measurement. The tetrahedral meshi is employed in FD
  Hexahedral mesh method is suitable for the regular geometry. Tetrahedral mesh can adapt more complicate structure, i. e, RF shield
  A simplified mode is used in the simulation: ignored the TiN
  Dipole source is produced by the coil, formed by two parallel wires with short end. S11 is obtained at Discrete port

## Slide 18: Source investigation
Impedance simulation of ceramic chamber
  Confirmed the measurement: simulated impedances are consistent with measurement for INB1 and QA
INB1
QA

## Slide 19: Source investigation
Impedance simulation of ceramic chamber
  7 types ceramic chambers ( total number of 76) in the RCS
  The resonance exists for all chambers
  Horizontal impedance is closed to vertical impedance

## Slide 20: Source investigation
Impedance simulation of ceramic chamber
  The resonance is affected by the yoke
  10 mm thickness PEC is added to replace the real yoke outside
  The impedance of every type is too much BIG
    The instability can be observed with a 1Mohm/m.
    impedance of every type mostly exceeds this value
 | Number | Fr w/o [KHz] | Fr w [KHz] | Q
MB, Elliptic/hor | 24 | 71 | 85 | 150
MB, Elliptic/ver | 24 | 79 | 114 | 40
QB, Circular #1 | 16 | 88 | 98 | 35
QD, Circular #2 | 8 | 102.2 | 109 | 70
QC, Circular #3 | 8 | 87 | 100 | 25
QA, Circular #4 | 16 | 135.7 | 141 | 120
INB/hor, Circular #5 | 4 | 123 | 126 | 150
INB/ver, Circular #5 | 4 | 123 | 134 | 150

## Slide 21: Source investigation
Impedance simulation of ceramic chamber
  Some parameter scan to understand the physics behind the impedance and try decreasing the impedance
    Cu strip number, Cu strip width, Cu strip thickness, Capacitance of capacitors, Chamber length, Chamber radius, etc.
  Dependance on ceramic length: fr shifts downward as the length increases
  Dependance on capacitance of capacitors
    With an increase in capacitance, the resonant frequency shifts downward
    With an increase in capacitance, the impedance also decreases
    The inductance L0 is given by the simulation of one capacitance, and theoretical frequency with others is calculated

## Slide 22: Source investigation
Impedance simulation of ceramic chamber
  Simplified structure
    Round chamber is instead of rectangle chamber
    Further simplify to decrease Cu strip and capacitance
  Two strips and capacitors can be reproduced the resonance

## Slide 23: Source investigation
Impedance simulation of ceramic chamber
  Simplified structure
    Scan length: 1-10 m
    Small coil with gap of 10 mm
    The inductance can be calculated as
    As the chamber length decreases, the end effects become clearer

## Slide 24: Source investigation
Why is it a transverse impedance?
  Simplified structure： E&B field, and surface current are clear
E field
B field
surface current

## Slide 25: Source investigation
Why is it a transverse impedance?
  For the monopole, equal voltage at capacitors
  For dipole, voltage is not equal, so the current circuit is formed
  It should be further confirmed

## Slide 26: Summary
An instability in transverse plane has been observed during the RCS commissioning, It is the main bottleneck of the beam power.
A systematic measurement suggests that it is TCBI
Optimizations of the tune and chromaticity were implemented to suppress the instability, successfully achieving beam power of 100 kW
The beam power is enhanced to 160 kW with the main help of sextupole magnets.
According the beam behavior, the beam power is achieved the RCS threshold
Measurements have confirmed that the RF shield on ceramic chambers is responsible for the instability
  The beam behavior is perfectly consistent with the impedance
The impedance of all chambers in the RCS has been offered, showing that the impedance is much BIG

## Slide 27: Summary
The point is CSNS-II: reduce impedance by shift down the frequency or reducing the impedance
  Optimized the impedance is the first and best method.
  Move tune to between 0 and 0.5: low transmission
  Low transmission with octupole at low energy stage due to the loss of dynamic aperture
  BxB feedback is planning
Numerous simulations have been performed to understand the physics behind the impedance
Optimizing capacitance of capacitor is a promising method for reducing impedance
  it should be confirmed. Because of the broken of capacitor, the instability at injection can be observed in JPARC
Many impedance reducing techniques are being explored
Both theoretical and experimental work are in the early stages
Any suggestions and comments are greatly appreciated
H. Hotchi, 10.1103/PhysRevAccelBeams.20.060402

## Slide 28
Thanks a lot！
Acknowledgements
Many thanks to D. Posthuma De Boer from ISIS, Xiao LI, Bin WU, Weidong CHEN, Yongchuan XIAO, Haibo Li, Shenghua LIU, Shengyi CHEN for helps in the simulation and measurement

## Slide 29: Dangerous tunes with current impedance
CSNS
CSNS-II

## Slide 30: Dangerous tunes with optimized resonance

## Slide 31: ISIS measurement

## Slide 32: JPARC instability at tune of 5.86

## Slide 33
Impedance measurement of ceramic chamber
  The twin-wire method is widely used to measure the transverse impedance
  Because of noise at low frequency, the standard twin-wire method is not suitable
10.1088/1674-1137/40/4/047002