## Slide 1
Pranab K. Saha
J-PARC, Japan
6th ICFA mini-workshop on Space charge
Dongguan, China, Sep. 11-13, 2024
Space charge effect in the J-PARC RCS

## Slide 2
3 GeV Rapid Cycling Synchrotron (RCS)
400 MeV H- Linac
Hadron Expt. Hall (HD)
Neutrino Beam Line to Kamiokande (NU)
Material and Life Science Experimental Facility (MLF)
J-PARC
(KEK & JAEA)
Foil
J-PARC facility
Accelerators at J-PARC:
■ 400 MeV H- Linear Accelerator (LINAC)
■ 3-GeV Rapid Cycling Synchrotron (RCS)
■ 30 GeV Main Ring (MR)
J-PARC provides high intensity proton beams
for multi-dimensional experimental research,
such as
◆ Material and Life Science
◆ Particle Physis
◆ Nuclear Physics
…….
Overview of J-PARC
30 GeV Main Ring Synchrotron (MR)

## Slide 3
Outline:
Overview of 3-GeV J-PARC RCS
Scenario of space charge (SC) effect in the RCS
Numerical simulation for identifying the SC effect
Results of beam loss mitigation at 1 MW until 2020
Recent further mitigation of the SC effect for beam loss minimization
Operational performance and suppression of machine activation
Summary and outlook

## Slide 4
Key parameters:
Circumference : 348.333 m
Superperiodicity : 3
Harmonic number : 2
Number of bunches : 2
Injection : H- multi-turn
charge-exchange injection
Injection energy : 400 MeV
Injection period : 0.5 ms
Injection peak current : 50 mA
Extraction energy : 3 GeV
Repetition rate : 25 Hz
Particles per pulse : 8.33 x 1013
Beam power : 1 MW
Overview of the J-PARC RCS
Beam sharing ratio between MLF and MR:
88:12 for MR-FX, 96:4 for MR-SX
Operational strategy:
Beam loss mitigation for beam operation to the MLF
Ensure a smaller beam emittance for the MR
RCS is a highly space charge (SC) dominated machine at a beam power of 1 MW.
Moreover, RCS is a multi-user machine for
Proton driver for producing pulsed muons
and neutrons at the MLF.
Injector to the MR
The SC effect poses serious challenges to fulfil multiple
demands simultaneously.

## Slide 5
RCS beam power history to the MLF to date
We have started 1 MW routine operation to the MLF since April 2024.
Net beam power to the MLF: 0.95 MW
(when MR takes 5% of the RCS beam for SX operation)
1 MW trial operation
in 2020 (1.5 days)

## Slide 6
Parameter | For MLF | For MR
Beam power | ~1 MW | 800 kW-eq. (FX), ~200 kW-eq.(SX)
Tune at inj. & ext. | (6.46, 6.36) & (6.38, 6.35) | (6.417, 6.447) & (6.38, 6.35) by Trim Quads
Trans. painting (TP) & type | 200p mm mrad anti-correlated | 50p mm mrad correlated
Longitudinal Painting (TP) | Inj. Dp/p offset: -0.15% 2nd harmonic duration: 6ms RF freq. offset at inj. | Inj. Dp/p offset: -0.15% 2nd harmonic duration: 7 ms RF freq. offset: None
Sextupoles | nx-2ny = -6 Resonance correction | x manipulation by bipolar Sextupole Partial x cor. at lower energy but extra x at higher energy. Reduce SC effect at lower energy and mitigate beam instability at higher energy
Beam loss minimum
Beam emit. minimum
The SC and resonance effects are complicated at high-intensity for simultaneous beam optimizations.
Systematic beam studies and numerical simulations are conducted for optimization of many parameters and their switching pulse-by-pulse for beam loss and beam emittance minimization to the MLF and MR
Beam loss and beam emittance minimization strategy
Tune at injection for the MR is changed
by 6 trim quadrupoles (QDT).
3nx=19
nx–2ny=-6
nx+2ny=19
2nx–2ny=0
MR
MLF

## Slide 7
Space charge (SC) effects in the J-PARC RCS
3nx=19
nx–2ny=-6
nx+2ny=19
2nx–2ny=0
MR
MLF
For | Tune at inj. | Painting emittance (p mm mrad) | Dn
MLF | (6.46, 6.36) | ~200 | -0.2
MR | (6.42, 6.45) | ~50 | -0.5
Major resonances driven by the SC effect at injection energy:
① nx – 2ny = -6 ; Structure resonance
Excited by sextupole field component intrinsic in the BMs.
K2 = 0.1006 m-2 (1/4 strength of full x correction)
Affects at lower beam energy due to large Dn. Larger emittance growth in the vert. plane.
Corrected for the MLF beam by Sextupoles as x correction is not done.
② 3nx = 19 ; 3rd order random resonance
Excited by not cancelled Sextupole field component (K2 = 0.0012 m-2) in the injection
chicane magnets (SB). Hori. emittance growth when SBs are ON during beam injection.
Partially mitigated by reducing magnetic fields of the SB by 20%.
➂ nx + 2ny = 19 ; 3rd order random resonance
Arises by sextupole fields in the BMs and x correction sextupole magnets.
Additionally, excited due to a distortion of the lattice superperiodicity caused by beta
beating of the SB during injection. Twice larger emittance growth in the vertical plane.
Currently, Db/b ~ 10% as ny is set far from the ny = 6.5, which is further
reduced by reducing SB fields.
➃ 2nx-2ny = 0. ; 4th order systematic resonance (Montague resonance)
Excited by skew-quadrupole errors, 2nd-order effect of Sext. field and also octupole
component in the SC field. Critical when nx and ny are closer.
Emittance exchange occurs. Careful choice of injection painting is essential.
Anti-correlated painting is favorable for a larger transverse painting
(H. Hotchi, PRAB23 2020)

## Slide 8
Numerical simulation
Time independent imperfections
-- Multipole field components for all the main magnets obtained
from field measurements
-- Measured field and alignment errors
Time dependent imperfections
-- Static leakage fields from the extraction beam line:
K0,1 and SK0,1 estimated from measured COD and optical functions
-- Edge focus of the injection chicane magnets (SB):
K1 estimated from measured optical functions
-- Multipole field components of the SB:
K2 . . . estimated from field measurements
-- BM-QM field tracking errors
estimated from measured tune variation over acceleration
-- 1-kHz BM ripple
estimated from measured orbit variation.
Almost corrected by COD correctors.
-- 100-kHz ripple induced by injection bump magnets
estimated from turn-by-turn BPM data . . . etc.
Now PS has almost no such ripples.
Foil scattering
-- Coulomb & nuclear scatterings
The 3-D space charge code simpsons (developed by Shinji Machida) is mainly used since RCS design stage, and continuing the improvement of the calculation model step by step --- Hotchi Hideaki
Since 2012, we also started using ORBIT code (developed at the SNS) for 3-D SC with impedances.
Both codes enable us to simulate,
3-D motion of beam particles including the SC modeled
by the PIC algorism.
Applied all beam handlings, such as injection paintings,
dynamic tune manipulations, etc.
To realize realistic and precise numerical simulations, we
have incorporated all lattice imperfections identified so far.
H. Hotchi: Previous SC workshop talks
H. Hotchi et al.: PRAB19, 010401 (2016), PRAB 20, 060402 (2017)
PRAB 23, 050401 (2020)
P.K. Saha et al.: PRAB 21, 024203 (2018), PRAB 16, 120102 (2013)

## Slide 9
x
s
y
BM
= 0.47 + 0.11j
Driving term of nx 2ny = 6 ;
Compensated by two families of sextupole
magnets with following modest strength;
SDA, SDB K2 = 0.066 m-2
K0= 2.618E-1
K1=-2.023E-2 (m-1)
K2=-1.006E-1 (m-2)
・・1/4 of the field Strength needed for the
full x correction
x (m)
ByL (Tm)
However, residual effect of the
nx -2ny = -6 resonance remains for
“OFF-momentum particles”
Identification of the effects of resonances
① nx – 2ny = -6 resonance
Beam loss is considerably reduced by
correcting nx – 2ny = -6 resonance
Turn by turn single particle motion leading to the vertical beam halo
Measurement
Simulation
H. Hotchi

## Slide 10
Concerning nx + 2ny = 19 and 2nx – 2ny = 0 resonances
2D plot of turn-by-turn
betatron actions
nx+2ny=19
nx−ny/2nx−2ny=0
The incoherent tunes are located
on the nx+2ny=19 resonance as well as
near the nx−ny / 2nx−2ny=0 resonances.
Turn by turn incoherent tune
Characteristic emittance blow-up that implies the combined effect of the two resonances,
nx+2ny=19 and nx−ny /2nx−2ny=0;
The horizontal and vertical actions gradually
grow up along the line of 2Jx−Jy=const.,
while oscillating in a direction parallel to
the line of Jx+Jy=const..
Transverse painting (TP) area limited to
150p mm mrad.
Recover super-periodicity by trim quads (QDT) to
correct the nx + 2ny = 19 resonance.
Anti-Correlated painting to mitigate the effect of
nx−ny /2nx−2ny=0 resonance.
TP area enlarged to 200p mm mrad.
Tune changed (6.45, 6.42)  (6.45, 6.38)
No chromaticity correction (Sextupoles OFF)
Beam loss at 1 MW : 0.2%
Operating point (6.45, 6.42)
H. Hotchi et al., PRAB 20, 060402 (2017)

## Slide 11
Space charge and impedance: ORBIT simulation for
beam instability and cures
Transverse impedance of the extraction kickers is extremely serious.
The SC effect should be perfectly taken done for realistic beam instability simulation.
We have implemented time dependent impedances in the ORBIT code.
ORBIT takes indirect SC into account, important to study beam instability with SC.
Tested in the presence of strong SC & x corrected
Beam instability occurs when the SC effect is reduced.
Beam is stable in a strong SC condition.
The Landau damping effect of the non-linear SC force
is more effective to stabilize the beam.
ORBIT guideline to accomplish 1 MW
For MR: Dynamic variation of x. 1/2 correction by DC Sext. up to 6 ms, then
reverse Sext. field for 15% extra x than natural one. Beam is stable.
P.K. Saha et al., PRAB21, 024203 (2018)
Simulation
Meas.
­­­- Single RF
- Dual RF

## Slide 12
Beam loss scenario in 2020
No beam intensity loss can be seen.
Temporal structure of the beam loss at the collimator
Estimated beam loss at 1 MW: ~0.2% (Collimator limit: 4%)
However, machine activations measured after 1.5 days operation at 1 MW were not negligible,
especially at the injection, collimator and 1st arc sections.
Further beam loss mitigation is challenging, but interesting for beam dynamics point of view.
We first reduced foil scattering beam loss by reducing sizes of the stripper foil and injection beam.
Next, we studied for further mitigation of the SC and the corresponding resonance effects at 1 MW.
The beam loss occurs lower energy.
But there exists some additional
beam losses after the injection
Measured beam loss throughout the RCS
From the
dump

## Slide 13
Further beam loss mitigation at 1 MW
The following four measures were taken into account recently for further reducing
the SC effect to minimize the beam loss and beam emittance at 1 MW.
Partial suppression of the 3nx = 19 resonance
Optimization of the Longitudinal painting (LP)
Modification of the Transverse painting (TP)
Optimization of tune at injection

## Slide 14
Effect of 3nx = 19 resonance
The 3nx = 19 resonance is driven by sextupole fields intrinsic in the
Injection chicane magnets (SB).
ーDipole fields of SBs are compensated through integration over SBs.
ー But for higher order field components, such a compensation is
incomplete due to magnetic interferences in reality.
Remains K2 = 0.012 m-2 and excites 3nx=19
Chicane magnets (SB1~4)
Most of the halo particles move around the center of the rf bucket
Tunes of such particles do not widely change turn by turn because
Turn by turn chromatic tune shift is restrictive as Dp/p of such
particles do not widely change.
Turn by turn SC tune shift is also restrictive due to almost constant
effect of the SC because of flat bunch distribution.
A part of such particles stay near the 3nx = 19 for a relatively
longer time and suffer the resonance effect continously.
Horizontal beam emittance growth, making a part of the
residual beam loss.
Unfortunately, no additional sextupoles exist for correction.
We considered a partial correction by reducing
20% magnetic fields of the SB.
H. Hotchi

## Slide 15
For partial suppression of the 3nx = 19 resonance, we tested reducing
SB magnetic field itself by 20%.
(Further reduction difficult due to injection difficulties)
Reduction of the SB magnetic field has two more advantages:
A less SB magnetic field helps reducing decay rates (~5%)
of the excited H0 before arriving to the 2nd foil.
The vertical beta function beating caused by the edge focusing
effect of the SB can also be 40% reduced.
SB with0.8 magnetic fields has already
been implemented to the RCS operation.
Partial suppression of 3nx = 19 resonance
The SB with 0.8 gives ~20% beam loss mitigation
at the collimator and 1st arc sections.
The horizontal rms emittance of the extracted
beam is also 10% reduced.

## Slide 16
Optimization of the LP gives further 30% beam loss mitigation.
But beam emittances remain unchanged,
Therefore, the longitudinal beam motion is improved reducing
longitudinal beam halos lost by the chromaticity effects.
Simulation results confirm a reduction of the longitudinal beam halos
for an optimized LP.
Optimization of the LP
Simulation results of longitudinal distribution
of the lost particles

## Slide 17
Optimization of the TP
y
ACAB
Emittance exchange
The unpainted area is filled by the SC effect
and emittance exchange.
Reduce number of particles exceeds the
painting emittance.
Slow variation of painting
Reduce spatial charge concentration and produce uniform beam distribution.
Maintain a balance distribution of horizontal and vertical painting emittances
crucial for controlling beam emittance growth and emittance exchange.
Obtain a symmetric tune distribution reduceing numerous particles
trapping on the nx-2ny = -6 resonance.
Additional beam losses continue after the injection are almost mitigated.
Temporal structure of
the beam loss
Simulation results:

## Slide 18
Optimization of the TP
Measurement results:
The beam loss at 1 MW is another ~35% mitigated by applying a modified TP.
The rms emittance of the extracted beam, especially the horizontal one is ~20% reduced.
The beam loss occurs only around injection energy reducing additional beam losses.
Temporal structure of
the beam loss at the collimator

## Slide 19
Optimization of the tune at injection
Tune scan around (6.45, 6.36)
A little (0.01) increase of the horizontal tune keeping vertical tune
unchanged gives the minimum beam loss .
Gives a better separation from the coupling resonance.
The best tune at injection is set at (6.46, 6.36).
Further increase of the horizontal tune to 6.47 results in considerable
beam loss owing the effect of half-integer resonance (2nx = 13).
Due to chromatic tune shift (~ 0.1) of large emittance beam near the bare tune.
Correction of the half-integer resonance by using trim quadrupoles are under study.
Chromatic
tune shift
~20% reduced.

## Slide 20
Summary of beam loss mitigation 1 MW beyond 2020
Extracted beam emittance (rms)
Time structure of the beam loss
Beam loss:
80% mitigated
Simulations:
The SC effect at 1 MW is well mitigated reducing 80%
beam loss compared to that of a trail operation in 2020.
Beam loss occurs only at the injection energy.
The residual beam loss is << 0.1%, ~1/2 is attributed to
the foil scattering of the circulating beam.
The transverse rms emittance is 40% reduced at maximum.
The simulation results are consistent with measurements.
Measurements:
The beam loss power in the collimator is ~ 0.1 kW,
where collimator capacity is 4 kW.

## Slide 21
Confirmation of beam emittance and beam halos reduction at the beam transport.
NanoDot Monitor Unit: mSv | June 16~22 (1021 p) | Dec. 1~7 (1021 p)
3*H | 9674 | 3479
3*V | 12315 | 4787
BLM integral:
(1) 8.5  6.4
Courtesy: Y. Yamaguchi, S. Meigo
2022 run
Not only the rms emittance but also the beam quality is significantly improved
reducing the beam halos for the users.
Useful for beam broadening (flat beam) by octupole magnets at the 3-NBT.
3-GeV to Neutron Beam Transport (3-NBT)
Near the neutron target
RCS

## Slide 22
Suppression of machine activation improving operational performance of the RCS
RCS machine activation at present with ~1MW routine operation is significantly
reduced as compared to 1 MW trail operation and even 0.6 MW operation in 2020.
We have achieved sustainable operation with more than 98% availability.
The downtime mainly caused by the Kicker and RF failures and their recovery.
Measurement location:
#1 Collimator max
#2 Collimator exit
#3~6 Dispersion peaks
Recent availability chart

## Slide 23
Summary and outlook
The 3-GeV RCS of J-PARC is SC dominated machine at the designed beam power of 1 MW.
The SC effect at injection energy excite many resonances resulting beam emittance and beam losses.
We have incorporated all beam handling, machine properties and errors in the simulation, which gives
precise results to identify each individual resonance effect and the corresponding measures.
Recently, the SC effect at 1 MW is sufficiently mitigated taking into account several appropriate measures.
The beam loss and the beam emittance have been minimized.
The residual beam loss 1 MW is <<0.1% occurs almost during injection period and ~1/2 is attributed
to the foil scattering beam losses.
The beam loss power in the collimator is ~0.1 kW (collimator capacity : 4 kW).
The simulations results are well consistent with measurement ones.
RCS beam quality improvement has also been well recognized at the downstream facilities.
The machine activation is well suppressed achieving sustainable operation with more than 98% availability
We are continuing our efforts for further beam loss mitigation at 1 MW operation as following;
1) Further momentum spread of the injection beam, 2) manipulation of the RF freq. during injection,
3) correcting half-integer resonance, introducing 3rd order RF harmonic and so on.
We would also like to achieve further beyond 1 MW with minimum beam loss.