## Slide 1: Longitudinal quadrupole frequency shifts in the PSB due to space charge and Finemet cavity impedance
12/09/2024
Mariangela Marchi, Simon Albright
Acknowledgements: OP-PSB and all those involved in PSB and Linac4 operation.
ICFA Mini-Workshop on Space Charge 2024 - M. Marchi

## Slide 2: Outline
Introduction
  PSB overview
  Space charge and Finemet interplay in the PSB
Quadrupole synchrotron frequency shifts
  Aim
  Measurements setup and analysis
  Comparison with simulations
Conclusions and next steps
mariangela.marchi@cern.ch

## Slide 3
mariangela.marchi@cern.ch
INTRODUCTION

## Slide 4: CERN Proton Synchrotron Booster
mariangela.marchi@cern.ch
  First proton synchrotron in the LHC injectors chain
  Composed of four identical super-posed rings
  Variety of proton beams production
  High-intensity beams for fixed-target experiment facility (e.g. ISOLDE)
  Ekininj = 160 MeV ; Ekinextr = 1.4 , 2 GeV
  Large revolution frequency sweep
  Below transition energy operation
4 rings

## Slide 5: PSB Longitudinal Space Charge
mariangela.marchi@cern.ch
PSB is space charge dominated
Longitudinal space charge modeled through purely imaginary impedance
|ZSC| directly proportional to frequency
Scaling with energy
Reduction of a factor of 8
Formula takes into account direct and indirect space charge
Self-fields modify RF waveform
Below transition energy: decrease of the effective RF voltage ⇒ defocusing effect
Coupling coefficient
dependent on geometry
623 Ω

## Slide 6: PSB High-Level RF
mariangela.marchi@cern.ch
Finemet-based High-Level RF system
Modular and multi-harmonic operation
1-18 MHz
3 sectors per each ring, 12 cells per each sector
Large broad-band cavity longitudinal impedance
Latest measurements of the model (0 to 100 MHz)
Independent on beam energy
Fast RF feedback compensation (-10 dB)
Mainly resistive in the beam revolution frequency range

## Slide 7: PSB Finemet LLRF
mariangela.marchi@cern.ch
D. Barrientos et al., “A New Beam Loading Compensation and Blowup Control System Using Multi-Harmonic Digital Feedback Loops in the CERN PS Booster “ IPAC’22, Bangkok, Thailand, June 2022.
PSB LLRF architecture
Space charge compensation action reduced
16 harmonic LLRF feedback loops
Notch-filter action on the induced voltage
Current model applied on the coupling impedance

## Slide 8: PSB Longitudinal Impedance
mariangela.marchi@cern.ch
Longitudinal Space Charge
Longitudinal Finemet cavity impedance
+
=
  Main contributors to the longitudinal impedance in the PSB
Combined coupling impedance of Finemet and space charge and spectrum of a bunch with parabolic distribution.
Vast majority of beam power is at low frequency.

## Slide 9: PSB Longitudinal Impedance
mariangela.marchi@cern.ch
+
+
Longitudinal Space Charge
Longitudinal Finemet cavity impedance
+
=
  Main contributors to the longitudinal impedance in the PSB
=
  Focus: Reactive impedance probing through induced quadrupole oscillations
CHANGE TO PLOTS WITH SAME LIMITS IN THE AXIS AND LESS NOISE: LARGER INTENSITY OR # MACROP

## Slide 10: Quadrupole oscillations and synchrotron frequency shifts
mariangela.marchi@cern.ch
ΔE
𝝉
Matched bunch
Mismatched bunch
×

## Slide 11
mariangela.marchi@cern.ch
QUADRUPOLE SYNCHROTRON FREQUENCY SHIFTS

## Slide 12: From simulations
mariangela.marchi@cern.ch
Macro-particle simulations with BLonD tracking code help in the study of the quadrupole frequency shift dependence on the PSB impedance.
Incoherent shift decreases when Finemet impedance is included
⇒ Space Charge partially compensated
BLonD GitLab

## Slide 13: From simulations
mariangela.marchi@cern.ch
Pure Space Charge
Space Charge and Finemet
Pure Space Charge
Space Charge and Finemet
Longer bunch length:
Expected behaviour
Shorter bunch length:
Intermediate intensity with Finemet shows growing oscillations

## Slide 14: Measurements at flat bottom energy
mariangela.marchi@cern.ch
Setup:
Flat Bottom energy : 160 MeV
Voltage at first harmonic: 3 kV, 8 kV
Small-amplitude synchrotron frequency: 1.030 kHz ,
1.678 kHz
Reference quadrupole synchrotron frequency: 2.060 kHz,
3.357 kHz
Procedure:
Generation of energy plateau of desired time length
Induction of quadrupole oscillations through non- adiabatic kick in the voltage: mismatch
Acquisition of bunch profiles at different intensities and bunch lengths

## Slide 15: Measurements: two striking examples on cavity loops action
mariangela.marchi@cern.ch
Bunch length evolution during acquisition time (3 kV)
Finemet with LLRF servo-loops inactive : fast damping of the oscillations due to large incoherent effect
Finemet with LLRF servo-loops active: at higher intensity space charge effect visible

## Slide 16: Measurements: two striking examples on cavity loops action
mariangela.marchi@cern.ch
Bunch length evolution during acquisition time (8 kV)
Finemet with LLRF servo-loops inactive : fast damping of the oscillations due to compensation
Finemet with LLRF servo-loops active: different effect due to loops action

## Slide 17: Quadrupole synchrotron frequency shifts
mariangela.marchi@cern.ch
Linear fit:
no intensity effects
intensity effects
500 ns:
a = 3152.82 Hz
b = -0,51 Hz/1010
350 ns:
a = 3279.56 Hz
b = -0,70 Hz/1010
200 ns:
a = 3337.23 Hz
b = -1,11 Hz/1010
500 ns:
a = 3169.73 Hz
b = -0,60 Hz/1010
350 ns:
a = 3231.16 Hz
b = -0,66 Hz/1010
200 ns:
a = 3324.87 Hz
b = -2,44 Hz/1010
Measurement
Simulation
Full comparison not possible for different
implementation of initial conditions !
comparable
different

## Slide 18
mariangela.marchi@cern.ch
CONCLUSIONS AND NEXT STEPS
Reactive longitudinal impedance can be probed through quadrupole oscillations
Interesting in the PSB to study the expected compensation of space charge with Finemet impedance
Quadrupole synchrotron frequency shifts comparison between measurements and simulations at flat-bottom
  Space Charge + Finemet :
    Longer bunches behave coherently
    Effect at high frequency seen not visible in simulations for short bunch
  Pure Space Charge:
    Comparable to the closed loops condition in measurements: effect of the loops to be further investigated,
especially with the higher voltage case
Next steps:
  Refinement of the initial conditions for comparison between measurements and simulations
  Other energies to be included in the study
  Cavity loops modeling based on the observations
Thank you!