## Slide 1: The equilibrium longitudinal emittance of cold ion bunches in storage rings
Lijun MAO
Institute of Modern Physics, CAS
CSNS, 2024.09.13

## Slide 2: Contents
Equilibrium between beam cooling and heating
HIRFL and experimental results
Simulation with multi-model particles
Conclusion

## Slide 3: Beam cooling in heavy ion storage ring
Low energy heavy ion storage rings, beam with large emittance is obtained after injection
Horizontal multi-turn
Combined longitudinal & transverse multi-turn
---Used at CERN LEIR
Beam cooling is used for a reduction of beam temperature
Temperature is equivalent to terms as phase space volume, emittance and momentum spread
Beam cooling techniques are non-Liouvillean processes which violate the assumption of a conservative force, as interaction of the particles with other particles (electrons, photons)
---M.Steck, GSI

## Slide 4: Beam cooling in heavy ion storage ring
Electron cooling, stochastic cooling and laser cooling are used for different purpose in heavy ion storage rings
Heavy ion research facility at Lanzhou, HIRFL
Main parameters
 | CSRm | CSRe
Ions | H2+~U | C~U
Circumference [m] | 161 | 128
Magnetic rigidity [Tm] | 12 | 9.4
E-cooling [keV] | 35 | 300
Stochastic cooling [GHz] | / | 0.1~1.2
Laser cooling [nm] | / | =257

## Slide 5: Beam cooling in heavy ion storage ring
Electron coolers developed by BINP
Variable transverse electron beam profile to avoid “heating”
Electrostatic bending to reduce the leakage current
Homogeneity of magnetic field to improve the cooling force
Stochastic cooling and laser cooling system at CSRe
electrodes inside the dipole
stochastic cooling control
laser device

## Slide 6: Beam cooling in heavy ion storage ring
Electron cooling, stochastic cooling and laser cooling are used for different purpose in heavy ion storage rings
Fe26+ @ 25MeV/u in CSRe
Electron cooling
O5+ @275.68 MeV/u in CSRe
Laser cooling
C5+ @380 MeV/u in CSRe
Stochastic cooling

## Slide 7: Equilibrium of cooling and heating
Phase space volume increases with coasting ion beam intensity and ion charges
Electron cooled beams equilibrium with Intra-beam Scattering (IBS)
---M.Steck, Seminar at IMP
What about longitudinal emittance (bunch length) in equilibrium?
exp. @ GSI
exp. @ IMP

## Slide 8: HIRFL and experimental results
First measurement of cold ion beam bunch length at CSRe in 2009
200MeV/u C6+ ions cooled by 0.5A electron beam
URF3kV with a fixed frequency
Bunch length increased faster for higher beam intensity, maybe it’s driven by different beam dynamics
lower intensity
higher intensity
Bunch length measured

## Slide 9: Beam cooling in heavy ion storage ring
uncooled
cooled
BPM are used for the bunch length measurement
The timing sequence is triggered by events generator
CSRm injection energy
6.9 MeV/u 12C6+ & 3.7 MeV/u 112Sn36+
Bunched ion beam vs. DC e-beam
RF-Cooler-BPM-Schottky
Experiment at CSRm

## Slide 10: HIRFL and experimental results
How to get the bunch length?
Spectrum transform method: get the ion beam shape
Fokker-Plank equation: the beam distribution in longitudinal

## Slide 11: HIRFL and experimental results
Longitudinal cooling time measurement
The bunch length is compressed during cooling
What we are interested is the final bunch length at the equilibrium state
6.9 MeV/u C6+ @CSRm, RF=1.5 kV, Ie=17 mA, Iion=30 uA

## Slide 12: HIRFL and experimental results
Final bunch length vs. particle numbers, also influenced by the RF voltage
The final bunch length increases proportional to stored particle number
The equilibrium state is determined by cooling, IBS and space charge effect

## Slide 13: HIRFL and experimental results
Estimation with IBS theory and space charge field
Intra-Beam Scattering
Small Amplitude Oscillation:
Equilibrium state between cooling and IBS heating:
Gas relaxation IBS model:
Finally, the bunch length σb:
The space charge potential is:
The synchrotron tune considered SC is:
Considering σbΩs= σb0Ωs0, the σb satisfies:
Finally, the bunch length σb:
Space Charge Effect

## Slide 14: HIRFL and experimental results
First measurement of cold ion beam bunch length at CSRe in 2009
If we believe the bunch length is determined by the IBS effect only:
Bucket height is too small
Space charge effect
Space charge effect can not be ignore!

## Slide 15: Simulation with multi-model particles
Model particle tracking code
CERN
https://e-beam.web.cern.ch/
H. Zhao, PRAB, 26, 030101 (2023)
H. Zhao, PRAB 24, 083502 (2021)
H. Zhao, PRAB 24, 043501 (2021)
H. Zhao, PRAB 23, 074201 (2020)
H. Zhao, NIM A 902, 219 (2018)
Generation of particles
Betatron motion
Synchrotron motion
Parkhomchuk Force Formula
Ion beam space charge effect used as RF voltage

## Slide 16: Simulation with multi-model particles
Cooling process similation
Ion | C6+
Energy | 6.9 MeV/u
Particle number | 1.0 x 108
Emittance (RMS) | 2/1 pi mm.mrad
dp/p (RMS) | 5.0 x 10-4
Tune (h/v) | 3.63/2.61
Beta function | 10/10 m
γtr | 5.42
RF voltage | 1.0 kV
h | 2
E-bean density | 3.8x106 cm-3
E-beam diameter | 50 mm
E-beam temp. | 0.2/10-4 eV
Magnetic field | 365 Gs
Parameters
RF bucket
Space charge field

## Slide 17: Simulation with multi-model particles
Simulation of cold ion bunch length equilibrium
The simulation results show a good agreement with the measurement
The emittance increases with increasing of RF voltage, which is different to longitudinal phase space
The beam intensity is quite low in the experiment and simulation
emittance
Bunch length

## Slide 18: Application on machine operation
RF capture with different harmonic numbers
Kr26+@CSRm with 6MeV/u, capture with 2nd harmonic numbers after cooling, beam loss with high intensity,
3rd harmonic numbers
2nd harmonic numbers
A higher RF harmonic number, lower line density, smaller bunch length

## Slide 19: Conclusion
The experimental results belong to the IBS dominated region, which is coincidence with the theoretical analysis
The bunch length is quite short
The limitation of the bunch length can be estimated
The influence of IBS and space charge effect on the bunch length can be estimated
Exp. & Simulation

## Slide 20: Thanks for your attention!