## Slide 1: Vertex readout electronics
Jun Hu
2024.2.22

## Slide 2
前端电子学
后端电子学
时钟与触发
电子学工艺及散热

## Slide 3: 已知需求
通道数：64 double-side ladders
~1280 chips
数据率：160Mbps/chip @trigger
3.2Gbps / ladder

## Slide 4
Interposer board
  DC-DC：low power supply provider for front-end
  Data aggregation to high speed link/optical link（lpGBT, VTRX+）
  Chip configuration transmission
  Clock and trigger distribution
FELIX
  Route data between optical link of front-end and the highspeed network of DAQ system
  Connect with TTC and get synced clock, global trigger decision, reset and so on.
  Fanout low speed clock, trigger and reset to front-end
Power supply
  Provide higher voltage to front-end
Clock, trigger, fast control
  Fanout the common information to FELIX
  Sync with FELIX and provide clean clock，
X64@10Gb/s
Front-end module
Back-end
(off detector)

## Slide 5: Front-end module
Flex
  PCB : 1300/Pcs
  Component (connectors) : 200/Pcs
  Assembly (bonding, glue) : 100/pcs
  In total ：1600/Pcs X 64 X 2 = 205k
  测试及老化？
Interposer board
  ASIC：?

## Slide 6: FELIX

## Slide 7: FPGA选型考虑
主要综合考虑可用IO资源，成本及可获取性考虑
 | KC705 (XC7K325T-2FFG900C) | KCU105 (XCKU040-2FFVA1156E) | VC709 (XC7VX690T-2FFG1761C) | VCU108 (XCVU095-2FFVA2104E) | XCKU115
Logic Cells(k) | 326 | 530 | 693 | 1,176 | 1451
DSP Slices | 840 | 1920 | 3,600 | 768 | 5520
Memory(Kbits) | 16,020 | 21,100 | 52,920 | 60,800 | 75,900
Transceivers | 16(12.5Gb/s) | 20(16.3Gb/s) | 80(13.1Gb/s) | 32(16.3Gb/s) and 32(30.5Gb/s) | 64(16.3Gb/s)
I/O Pins | 500 | 520 | 1,000 | 832 | 832
Cost | 2748 (650) | 3882(1500) | 8094 | 7770 | 

## Slide 8
PCB : 4000
Component: 22000
  FPGA : 8000
  Jitter clean: 400
  CDR: 350
  DCDC/LDO: 1000
  DDR: 250 / 16GB
  Opti-connector: 1500
  Others：500
  WR endpoint : 10000
Assembly : 2000
Test and aging：2000
In total： 30000
XC7VX690T-2FFG1158C
支持1路 X16 PCIE + 32 ch GXH

## Slide 9: 时钟系统（WR）
  WR Switch : 40000
  WR endpoint : 10000

## Slide 10: 电源
前端功耗
  芯片功耗约为0.4W，按80%效率计算，输出功率0.5W，
  每个ladder 功耗 （0.5W + 0.5W) X 20 = 20W
  20W/channel带冗余，每通道500元，64通道总计32000元
后端功耗
  单板约为64W，每通道1000元，2块总计2000元

## Slide 11: 线缆
电源线：直径大约2mm，线上电阻<1欧@100m, 单价2元/米
同轴电缆：单价5元/米，每通道2根，
光纤：2元/米
长度按50m计算，每米单价14元

## Slide 12
 | Cost | Number | In total
FELIX | 30000 | 2 | 60000
TTC | 40000 | 1 | 40000
Power supply |  |  | 34000
cable | 14 | 50mX64 | 44800
不包含预研费用