## Slide 1: LGAD based time of flight and outer tracker
Yunyun Fan, Mei Zhao, Mengzhao Li, Zhijun Liang
On behalf of the ToF group
Mar. 1, 2024

## Slide 2
CEPC 4D outer tracker
mzli@ihep.ac.cn
CEPC 4D outer tracker concept design：
Strip AC-LGAD + ASIC ：
TOT->amplitude->charge sharing->position
TOA+TOT->timing (time–amplitude correction)
  Should be part of SET (silicon wrapper layer outside TPC or drift chamber)
  Serve as Timing detector and part of the tracker
  Barrel : 50 m2 , Endcap 20 m2 , ~ 106 channels
  Strip AC-LGAD ( each strip: 4 or 10 cm × 0.05cm)
    Timing resolution: 30-50 ps
    Position resolution: ~ 10 μm @ R-phi direction
    ~ 1mm @ z direction
Y
Z

## Slide 3: Arrangement of the ToF with strip LGAD
One layer:
90 ladders，45 ladders each side,
36 modules/ladder，14 strip/module
Total modules needed：
45 *2*36 = 3240 modules
One layer ToF
R= 1800 mm
H～5000mm
Module
140mm x 160mm
Ladder

## Slide 4: Backup

## Slide 6: Strip direction resolution from double side readout

## Slide 7: Timing resolution (different dimension of strip )

## Slide 8
other applications
Beam Telescope for Beam Test Platform
LiDAR: Positioning and Navigation
Track and time detectors in other particle physics and nuclear physics experiments
…
Application of AC-LGAD
Nuclear Medicine Instruments：
Such as proton therapy and proton CT
X-ray detectors @ advanced light sources
mzli@ihep.ac.cn
Electron-Ion Collider (EIC)：Timing-tracker
10.9 m2
2.22 m2
6 KeV X-Ray
HEPS @ Beijing

## Slide 9
Picosecond laser scanning system
Displacement accuracy 1 μm
Automated scanning
Picosecond laser 1064nm
Spot size 2~5 μm
Picosecond laser 1064nm
Sensor & Board
3D platform
Picosecond laser scanning system
focuser
mzli@ihep.ac.cn
4.1 AC-LGAD sensor test ： Picosecond laser test

## Slide 10: Plan and funding needed
AC-LGAD sensor
  Small MPW chips developed, but there is no full-size sensor
  Still need 2~3 round of engineering run (2M RMB)
ASIC:
  Expect to develop based on ASIC chip developed TOF-PET (1.5M RMB)
  Still need at least one engineering run to modify this ASIC chip for AC-LGAD
    Sensor capacitance and raising time is difference
    Clock structure and logic is different
 | CEPC TOF
AC-LGAD runs | 2 M RMB
ASIC engineering run | 1.5 M RMB
Total | 3.5 M RMB

## Slide 11
HGTD Module assembly
225 front-end channels (15 ×15) in each module
  Fast ASIC and LGAD connected by bump bonding
  Dead area between pixels is about 50 μm
Jigs tools
15 ×15 pixels efficiency map
In module beam test