## Slide 1: Track Finding for CEE TPC
Hao Qiu, Dhananjaya ﻿Thakur, Aiqiang Guo
Institute of modern physics (IMP)
实验粒子物理径迹重建研讨会– 郑州大学 – 2024-05

## Slide 2: Introduction of CEE
The Cooler-Storage-Ring External-target Experiment (CEE) is a spectrometer to study the properties of nuclear matter at high baryon density region.
The first large-scale nuclear physics experimental apparatus in China
Main scientific objectives:
  Searching for the QCD critical point
  Studying the equation of state of asymmetric nuclear matter at high density and low temperature.

## Slide 3: TPC of CEE
﻿A charged particle ionizes the gas along its flight path, and the ionized electrons drift towards the readout plane, where they are collected. The readout signals provide the 3D position and arrival time.
The particle's momentum is determined by its deflected trajectory in the magnetic field.
Sensitive area: 500900800(2) mm

## Slide 4: TPC of CEE
• Number of readout channels not less than 10,000
• Momentum resolution reaching 5%
• Track reconstruction residual better than 300 µm
• Dual-track discrimination capability less than 3 cm
• Track reconstruction efficiency better than 90%
34 row
56 row
TPC

## Slide 5: Concept of Graph theory
Just look at an example
Three key elements in Graph theory
Node(cell)-doublet
Edge
Direction
Cell
Edge
Direction
A
B
B is the neighbor of A,
A is not the neighbor of B

## Slide 6: How does graph work?
Goal: find the longest path from a root cell longest Path problem
Each cell has an initial state value
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 7: How does graph work?
Goal: find the longest path from a root cell longest Path problem
Each cell has an initial state value
Evolution: loop all the cell, update the state according to rule:
If Si = Sineighbor
Then Si = Sineighbor +1
0
1
0
1
1
0
0
1
1
0
1
1
1
0

## Slide 8: How does graph work?
Goal: find the longest path from a root cell longest Path problem
Each cell has an initial state value
Evolution: loop all the cell, update the state according to rule:
If Si = Sineighbor
Then Si = Sineighbor +1
Repeat the evolution to N generation according to graph
0
1
0
1
2
0
0
1
1
0
2
1
1
0

## Slide 9: How does graph work?
Goal: find the longest path from a root cell longest Path problem
Each cell has an initial state value
Evolution: loop all the cell, update the state according to rule:
If Si = Sineighbor
Then Si = Sineighbor +1
Repeat the evolution to N generation according to graph
0
1
0
1
2
0
0
1
1
0
2
1
1
0
The state of cell only depend on its neighbors
Multiple tracks can be found simultaneously !! Sort of parallel computing

## Slide 10: The workflow of CA
Create Graph
Create doublet and cell
Connect cell
Evolution
Find Ntuplet

## Slide 11: Graph creation
IP
Graph 1
Graph 2
Graph 3
Graph 4

## Slide 12: Cell creation
The doublet creation
Only the 2 hits on the layer-pair passing the dphi and dz (or dx, dy) selection are chosen
Reduce the combination in the cell creation
IP

## Slide 13: Cell connection
The cell connection
The condition in RZ plane
  is determined by the minimum Pt and material budget
The condition in XY plane
  is determined by the minimum Pt and material budget and B field
R
Z
X
Y
B
B

## Slide 14: The track candidates
A RootCell is defined as the first cell of the path and length of the path should be longer than minimum hit requirement (5 in our case)
Each RootCell can create multiple track candidates with the same length
Multiple track candidates can be cleaned by the chisq of the fit in following step

## Slide 15: Event display
Generated Hit
Found Cells by CA

## Slide 16: Event display
Generated Hit
Found Cells by CA

## Slide 17: Event display
Generated Hit
Found Cells by CA

## Slide 18: Performance

## Slide 19: Track merging
Select the longest track segment as seed of the track

## Slide 20: Track merging
Select the longest track segment as seed of the track
Extend to the next layer, pick an addition hit if it pass the selection criteria

## Slide 21: Track merging
Select the longest track segment as seed of the track
Extend to the next layer, pick an addition hit if it pass the selection criteria
Extend to the 1st layer
Repeat the procedure in the inversed direction

## Slide 22: Track merging

## Slide 23: Workflow of CEE TPC TF algorithm
Event Simulation
Track finding by CA
Track fitting by KF
Track merging by CKF

## Slide 24: Hit efficiency and purity
Hit efficiency
Hit purity

## Slide 25: Efficiency and Purity : Efficiency

## Slide 26: Efficiency and Purity : Purity

## Slide 27: Momentum and DCA resolution
The momentum resolution is less than 5%
The DCA resolution is less than 0.3 cm [P > 0.1 GeV]

## Slide 28: Results from Beam Test
x
z
TPC
2 adjacent pad rows
16 rows in total

## Slide 29: Results from Beam Test
x
z
TPC
2 adjacent pad rows
16 rows in total

## Slide 30: Results from Beam Test
x
z
TPC
2 adjacent pad rows
16 rows in total

## Slide 31: Summary
Track finding algorithem based on CA is developed for CEE TPC
The algorithm is proven to have good speed
The parameters of geometrical requirement need to be optimized to get higher efficiency
The momentum and DCA resolution meet the CEE experiment requirement
Thank You !!

## Slide 32: Backup

## Slide 33: The coordinate
x
y
z
2 changes:
The origin is at IP
The Z axis is the same as the direction of B field
OLD
NEW