## Slide 1: CEPC vertex detector towards TDR
Zhijun Liang,
On behalf of CEPC vertex working group

## Slide 2: Plan: MDI background input
Got 1st offical background input from MDI group last week
  Request MDI group to provide the background distribution and raw data
  Get background hit density distribution in vertex detector in software

## Slide 3: Readout architecture
End of March: Plan to work with electronics group to finalize the design
  Readout architecture is the key for next step
  Readout speed and buffer size are the major concern
Question
  Physics requirement to Vertex detector Time stamp uncertainty
    Manqi suggested to ask event building experts
  What is the trigger latency? 3us or 10us ?
    Impact to Jadepix-like readout (Analog buffer )
    Impact to Taichu-like readout (FIFO depth)
 | Jadepix4-like readout | Taichu-like readout
Time stamp uncertainty (Higgs/WW/Z runs ) | 5/12/120 bins | 1/1/1 bins
Data rate@trigger (Z run ) | ~1200 Mbps | ~120 Mbps
Data rate@triggerless(Gbps) (Higgs/WW/Z runs ) | 0.3/?/3.8 Gbps | 0.4/1/6 Gbps

## Slide 4: Plan : geometry and layout optimzation
End of March: finalize the detector geometry and mechnical design
  Physics Layout optimization
    How to deal with Endcap ?
  Feasibility study of 2 layout ( mechanics support, cooling, cable ….)
Vertex detector MOST2 prototype layout has been implement in CEPCSW
  Try to perform further optimization with full simulation
Short barrel With endcap
Long barrel

## Slide 5: backup

## Slide 6: Weekly meeting
Group Meeting every Thursday afternoon (2nd meeting last Thursday)
  https://indico.ihep.ac.cn/event/21543/
From last meeting, Discussion about the choice of technology
  Discussion with L3 Stitching (Mingyi) and SOI (Yunpeng)
  Agree to focus CMOS pixel for reference TDR baseline

## Slide 7: Key parameters
  Single-point spatial resolution (now and in the next 5 years)
  Time stamp precision requirement (to be discussed with Shengsun Sun)
  Material budget
  Cost estimation
  Occupancy
  Max data rate that can be handled by this technology (now, and in the next 5 years)
  Radiation hardness (now, and in the next 5 years)
  Power dissipation (now, and in the next 5 years)
  Expected Technology availability in the future
  Technology Readiness