## Slide 1: Tracker for CEPC reference detector TDR
WANG Meng 王萌
2024.3.25

## Slide 2: CEPC tracking system, draft
Three tracking regions
barrel: full Main + Si trackers
endcap: partial Main tracker
forward: Si tracker only

## Slide 3: TPC vs DC
a mini-review will be held at IHEP on April 2nd. https://indico.ihep.ac.cn/event/22016/
 | unit | TPC, Higgs | TPC, Z | DC, Higgs | DC, Z
B-field | T | 3 | 2 | 3 | 2
Performance |  |  |  |  | 
material budget barrel | X0 | 1.20% |  | 1.14% | 
material budget endcap | X0 | 17% |  | 28% (plate) + 1.8% (cable) | 
Npoint of measurement/full-trk |  | 2300 | 2300 | 66 | 66
point resolution in rφ, max | μm | 120 | 400 | 100 | 100
point resolution in rz | μm | 100 -- 400 | 200 -- 800 | 2000 | 2000
momentum resolution: σ(pT)/pT = a·pT ⨁ b |  |  |  |  | 
a | 1/GeV | 1.2E-05 | 2.7E-05 | 2.1E-05 | 3.2E-05
b |  | 5.9E-04 | 9.0E-04 | 7.7E-04 | 1.2E-03
K/π separation power @ 20GeV |  | 3σ | 3σ | 3.1 σ | 3.1 σ
dE/dx or dN/dx resolution |  | 3.2% | 3.2% |  | 2.5--2.6%
hit rate, max |  |  |  |  | 70 kHz/cell
occupancy, max |  |  |  |  | 11%
note |  | pad 0.5x0.5 mm2, ch 2x3e7 |  | cell size 18x18mm2, 27.6 kCells | 

## Slide 4: Easy-to-install modular design of TPC for TDR
Optimization of Geometry of TPC detector and the Endplate
  High granularity readout TPC can operate at Higgs run in 3.0T and Tera-Z run in 2.0T
  Easy-to-install modular design: optimized modules in the endcap
    Coverage of the sensitivity readout area increased to 96%
  Cost estimation: ~170 Million RMB (Detector 80 Million + Electronic/DAQ 90Million)
4

## Slide 5: Status of the simulation of pixelated TPC for TDR
Simulation of TPC detector under 3T/2T and T2K mixture gas
  Full simulation framework of pixelated TPC developed using Garfied++ and Geant4 at IHEP
  Investigating the π/κ discrimination capability using reconstructed clusters, a 3σ separation at 20GeV with 50cm drift length can be achieved
  dN/dx has significant potential for improving PID resolution
5

## Slide 6: Status of the prototype of pixelated TPC for TDR
6
R&D on Pixelated TPC readout for CEPC TDR
  Macro-Pixel TPC ASIC chip was started to developed and 2nd prototype wafer has done and tested
  The TOA and TOT can be selected as the initiation function in the ASIC chip
    500μm×500μm pixel readout designed
    Time resolution: 14bit (5ns bin)
    Power consumption: <1mW/pixel (2nd prototype)
        ~100mW/cm2
    Technology: 180nm CMOS -> 60nm CMOS
    High metal coverage: 4-side bootable
Prototyping pixelated TPC detector using the chips
  Principle of the prototype is no problem for testing
  The validation of prototype in April and May
Prototyping pixelated TPC detector using the chips
Photo and layout of ASIC Chip R&D for TPC

## Slide 7: drift chamber

## Slide 8: Updated parameters
R extension | 600-1800mm
Length of outermost wires（cosθ=0.85） | 5800mm
Thickness of inner CF cylinder： (for gas tightness, no load) | 200μm (0.08% X0)
Thickness of outer CF cylinder： (for gas tightness, no load) | 300μm (0.13% X0)
Outer CF frame structure： | Equivalent CF thickness: 1.8 mm (0.77% X0)
Thickness of end Al plate: | 25mm (28% X0)
Cell size: | ~ 18 mm × 18 mm
Cell number | 27623
Diameter of field wire (Al coated with Au) | 60μm
Diameter of sense wire (W coated with Au) | 20μm
Ratio of field wires to sense wires | 3:1
Gas mixture | He/iC4H10=90:10
Gas + wire material | 0.16% X0

## Slide 9: Cost
1.1 |  | Chamber |  | unit | 2880.00
 | 1.1.1 | End plate | 405 | 2 | 810.00
 | 1.1.2 | Outer frame structure | 500.00 | 1 | 500.00
 | 1.1.3 | Inner and outer cylinders | 150.00 | 1 | 150.00
 | 1.1.4 | Wire | 460.00 | 含30%余量 | 460.00
 | 1.1.5 | Feedthrough | 530.00 | 含20%余量 | 530.00
 | 1.1.6 | Wire test system | 50 | 1 | 80
 | 1.1.7 | Wiring tooling | 300 | 1 | 350
1.2 |  | Electronics |  |  | 5170.00
 | 1.2.1 | Readout Channel | 0.17 | 27623*1.1(10%备件) | 5170.00
1.3 |  | HV and Gas system |  |  | 340.00
 | 1.3.1 | High Voltage system | 220.00 | 6机箱，50插件 | 220.00
 | 1.3.2 | Gas system | 120.00 | 1 | 120.00
total |  |  |  |  | 8390

## Slide 10
Overall Design
CF Frame structure：8 longitudinal hollow beams + 8 annular hollow beams + inner CF cylinder and outer CF cylinder
Length : 5800mm
Outer radius: 1800mm，Inner radius: 600mm；
Thickness of each end plate: 25mm，weight :1100kg

## Slide 11
Vertical self weight
Buckling coefficient : ~12
Horizontal self weight
Buckling coefficient : ~14
Loads: Wire tension+ Axial self weight ：
The structure is stable

## Slide 12: Beam test with detector prototype (IHEP)
Two drift tubes + preamps + ADC (1GHz)
The system was tested with electron beam at IHEP
Signal waveform (rad)
Trigger signals (blue and green)
Beam

## Slide 13: Preliminary analysis
Low noise and high bandwidth preamplifiers
Rise time : ~ ns
Clear peaks
Reconstruction

## Slide 14: CMOS pixel tracker
Design goal for future fulls-size chip
  Spatial resolution <10 µm
  Time resolution <10ns (ideally 3-5ns, to achieve bunch tagging) <- most challenging
  Power consumption: as low as possible, ~100mW/cm2 level
sensor cost estimated
data rate estimated  electronics
truss structure mechanical design is in progress
layout optimisation is in progress

## Slide 15: HVCMOS cost
Sensor cost scales with area
  NTO overhead is a small fraction
Quotes for SMIC 55nm process
  12-inch wafer with 1k Ohmcm resistance
56k USD/m2 <~ 400k CNY/m2
Unit cost drops when area increases
SET 66 m2  26 MCNY
SIT only
SIT + SET
万元/平米

## Slide 16: Data rate estimation
Layer | Hit density [kHz/cm2] | Data rate /chip [Mbps] | Data rate / module [Mbps] | Data rate / layer [Gbps]
Barrel SIT 1 | 5.2 | 1.0 | 8.0 | 1.5
SIT 2 | 2.2 | 0.43 | 3.5 | 1.5
SIT 3 | 0.79 | 0.15 | 1.2 | 1.4
SET | 0.08 | 0.02 | 0.13 | 1.4
Endcap SIT 1 | 1.3 | 0.24 | 2.0 | 0.17
SIT 2 | 0.57 | 0.11 | 0.87 | 0.17
SIT 3 | 0.26 | 0.05 | 0.41 | 0.22
SET | 0.03 | 0.006 | 0.05 | 0.24
Total data rate: 6.6 Gbps for SIT+SET, or 5.0 Gbps for SIT only
Key assumptions: Event rate 112kHz, track multiplicity 100, cluster size 3, bits per hit 48; Beam bkg to be added
=> Data rate is generally low for SIT (to confirm for the innermost layer); similar readout scheme can be adopted as SET

## Slide 17: Mechanical design
Dedicated discussions with mechanical group to understand boundary conditions
  Outer radius: < 600mm
  Inner radius: > 150mm (if vertex using endcaps) or > 75mm (if vertex adopts long barrel option)
Truss structure to support barrel ladders for minimum material budget
  Design and simulation in place for 2nd SIT layer in CDR by INFN Pisa (1.3m in length)
  Truss-based design for the whole SIT ongoing
  Space for truss to be considered in layout optimization
SIT and beampipe should be considered together in the mechanical design
Quan Ji, Jinyu Fu, Junsong Zhang
Filippo Bosi, Fabrizio Palla

## Slide 18: Layout optimisation
Initial layout available for mechanical/ software/electronics design
Optimisation campaign based on fastMC to converge on:
  Radii of the 3 layers (really the middle layer as the 1st and 3rd are defined by boundaries)
  Position of the endcap disks
  Inclination angles of endcaps
An extra layer of endcap added to ensure enough hits in forward region (position to be optimized)
An extra layer of endcap may be needed to ensure enough hits in forward region (position to be optimized)
Gang Li, Meng Wang, Qinglin Geng, Xiaojie Jiang, Yiming Li

## Slide 19: silicon microstrip tracker

## Slide 20: SET Module
Strip length 20cm
  Two 10 cm X 10 cm stitching
Strip pitch 75um
  Practical for wire-bonding
1280 channels per module
  Compatible with ASIC design
Single Module | 
Area | 20cm x 10cm
Strip pitch | 75um
# channels | 1280
Zhan Li

## Slide 21: Preliminary Readout Strategy for Si Strip
Readout scheme with two levels of data concentration
  Module Level
  Stave Level
Common design with TOF
Xiongbo Yan

## Slide 22: Cost estimation Sensor + ASICs
Items | Unit Cost (RMB) | Quality | Total (10k RMB)
Sensors | 5500 | 6612 | 3637
Electronics |  |  | 1825
Total |  |  | 5462

## Slide 23: LGAD

## Slide 24: CEPC 4D outer tracker
mzli@ihep.ac.cn
CEPC 4D outer tracker concept design：
Strip AC-LGAD + ASIC ：
TOT->amplitude->charge sharing->position
TOA+TOT->timing (time–amplitude correction)
  Should be part of SET (silicon wrapper layer outside TPC or drift chamber)
  Serve as Timing detector and part of the tracker
  Barrel : 50 m2 , Endcap 20 m2 , ~ 106 channels
  Strip AC-LGAD ( each strip: 4 or 10 cm × 0.05cm)
    Timing resolution: 30-50 ps
    Position resolution: ~ 10 μm @ R-phi direction
    ~ 1mm @ z direction
Y
Z

## Slide 25: Arrangement of the ToF with strip LGAD
One layer: 3780 modules
  90 ladders，45 ladders each side,
  42 modules/ladder，
  22 ASIC/module，128 Channel/ASIC
One layer ToF
R= 1800 mm
H～5800mm
Module
140mm x 160mm

## Slide 26: Electronic System Cost of LGAD ToF and OTracker

## Slide 27: backup

## Slide 28: CDR layout for acronyms