## Slide 1: CEPC vertex detector towards TDR
Zhijun Liang

## Slide 2: Towards TDR
Aim to have a draft of TDR by the end of 2024.
  System level design, choose baseline technology
  Electronics, service and mechanics needs to be included
Major change from CDR to TDR
  Beam pipe diameter: 28mm (CDR)  20mm (TDR) (reduce 30%)
  Instant Luminosity per IP:
    Z pole: 32×1034 cm-2s-1 (CDR)  192 ×1034 cm-2s-1 (TDR, 50MW) (6 times increase)
    ZH: 5.6×1034 cm-2s-1 (CDR)  8.3 ×1034 cm-2s-1 (TDR) (~1.5 times increase)

## Slide 3: Plan: MDI background input
Got 1st offical background input from MDI group last week
  Request MDI group to provide the background distribution and raw data
  Get background hit density distribution in vertex detector in software
     Haoyu, Tianyuan

## Slide 4: Priority of key parameters
1st priority: Small inner radius, close to beam pipe (new baseline beam pipe radius=10um )
2nd priority: Low material budget <0.15% X0 per layer
3rd priority: High resolution pixel sensor： 3~5 μm
  Question : d0 and Z0 requirement ?

## Slide 5: CMOS pixel chip key parameters
Key parameters need to specify in TDR for the CMOS pixel chip
 | What we achieved now | what we expect to achieve in next 5 years
Spatial resolution | 3~5 um | ~3um
Power dissipation (Air cooling ) | ~100 mW /cm2 ? | <50 mW /cm2 ?
Max data rate that can be handled by this technology |  | 
Radiation hardness | 3Mrad ? | 
Time stamp precision |  | 

## Slide 6: Readout architecture
End of March: Plan to work with electronics group to finalize the design
  Readout architecture is the key for next step
  Readout speed and buffer size are the major concern
Question
  Physics requirement to Vertex detector Time stamp uncertainty
    Manqi suggested to ask event building experts
  What is the trigger latency? 3us or 10us ? Or triggerless
    Impact to readout architecture design

## Slide 7: Plan : geometry and layout optimzation
End of March: finalize the detector geometry and mechnical design
  Physics Layout optimization
    How to deal with Endcap ?
  Feasibility study of 2 layout ( mechanics support, cooling, cable ….)
Vertex detector MOST2 prototype layout has been implement in CEPCSW
  Try to perform further optimization with full simulation
Short barrel With endcap
Long barrel

## Slide 8: backup

## Slide 9: Weekly meeting
Group Meeting every Thursday afternoon (2nd meeting last Thursday)
  https://indico.ihep.ac.cn/event/21543/
From last meeting, Discussion about the choice of technology
  Discussion with L3 Stitching (Mingyi) and SOI (Yunpeng)
  Agree to focus CMOS pixel for reference TDR baseline

## Slide 10: Key parameters
  Single-point spatial resolution (now and in the next 5 years)
  Time stamp precision requirement (to be discussed with Shengsun Sun)
  Material budget
  Cost estimation
  Occupancy
  Max data rate that can be handled by this technology (now, and in the next 5 years)
  Radiation hardness (now, and in the next 5 years)
  Power dissipation (now, and in the next 5 years)
  Expected Technology availability in the future
  Technology Readiness