## Slide 1: LGAD based time of flight and outer tracker
Yunyun Fan

## Slide 2: Physics requirement
3 sigma K/pi seperation below 2GeV
  50 ps precision is the target

## Slide 3
CEPC 4D outer tracker
mzli@ihep.ac.cn
CEPC 4D outer tracker concept design：
Strip AC-LGAD + ASIC ：
TOT->amplitude->charge sharing->position
TOA+TOT->timing (time–amplitude correction)
  Should be part of SET (silicon wrapper layer outside TPC or drift chamber)
  Serve as Timing detector and part of the tracker
  Barrel : 50 m2 , Endcap 20 m2 , ~ 106 channels
  Strip AC-LGAD ( each strip: 4 or 10 cm × 0.05cm)
    Timing resolution: 30-50 ps
    Position resolution: ~ 10 μm @ R-phi direction
    ~ 1mm @ z direction
Y
Z

## Slide 4: Arrangement of the ToF with strip LGAD
One layer:
90 ladders，45 ladders each side,
42 modules/ladder，28 ASIC/module
Total modules needed：
45 *2*42 = 3780 modules
One layer ToF
R= 1800 mm
H～5800mm
Module
140mm x 160mm
Ladder

## Slide 5: ATLAS HGTD VS CEPC TOF detector
 | ATLAS HGTD | CEPC TOF barrel
Area (m2) | 6.4 | ~ 70
Granularity | 1.3 mm ×1.3mm | 70mm × 0.1mm
Capacitance | 4pF | ~10 pF
Charge | >4fC | >15fC
Channel number | ~ 3.6 × 106 | ~ 1×107
Module assembly | Bump bonding | Wire bonding at strip
MIP Time resolution | 30-50 ps | ~50 ps
Spatial resolution | ~ 300 μm | ~ 10 μm
Number of Module | 8032 | 3780 (14cm*14cm)
Number of channels per module | 255 | 2800
Data size | 16 bit (9 TOT, 7 TOA) | 16 bit (9 TOT, 7 TOA)
Data rate |  | 
 | ATLAS HGTD | CEPC TOF barrel
Area (m2) | 6.4 | ~ 70
Granularity | 1.3 mm ×1.3mm | 70mm × 0.1mm
Capacitance | 4pF | ~10 pF
Charge | >4fC | >15fC
Channel number | ~ 3.6 × 106 | ~ 1×107
Module assembly | Bump bonding | Wire bonding at strip
MIP Time resolution | 30-50 ps | ~50 ps
Spatial resolution | ~ 300 μm | ~ 10 μm
Number of Module | 8032 | 3780 (14cm*14cm)
Number of channels per module | 255 | 2800
Data size | 16 bit (9 TOT, 7 TOA) | 16 bit (9 TOT, 7 TOA)
Data rate |  | 

## Slide 6: Endcap design
ITK strip dendcap

## Slide 7: Backup

## Slide 9: Timing resolution (different dimension of strip )

## Slide 10
other applications
Beam Telescope for Beam Test Platform
LiDAR: Positioning and Navigation
Track and time detectors in other particle physics and nuclear physics experiments
…
Application of AC-LGAD
Nuclear Medicine Instruments：
Such as proton therapy and proton CT
X-ray detectors @ advanced light sources
mzli@ihep.ac.cn
Electron-Ion Collider (EIC)：Timing-tracker
10.9 m2
2.22 m2
6 KeV X-Ray
HEPS @ Beijing

## Slide 11
Picosecond laser scanning system
Displacement accuracy 1 μm
Automated scanning
Picosecond laser 1064nm
Spot size 2~5 μm
Picosecond laser 1064nm
Sensor & Board
3D platform
Picosecond laser scanning system
focuser
mzli@ihep.ac.cn
4.1 AC-LGAD sensor test ： Picosecond laser test