## Slide 1
CEPC Detector Magnet Ref TDR
Physical Design Magnet_RT V1
Feipeng NING
2024.03
中国科学院高能物理研究所
Institute of High Energy Physics, CAS

## Slide 2: Outline
Magnetic parameters
Physical design of the detector magnet
Yoke and stray field
Ongoing work

## Slide 3: 1. Magnet parameters
Magnet Interface：
Item | Value (mm)
Inner diameter | 7200
Out diameter | 8800
Length | 9400
Thickness | 800

## Slide 4: 1. Magnet parameters
Coil parameters:
Coil parameters | Value
Inner radius (mm) | 3720
Length (mm) | 7690
Current (A) | 17940
Stored energy (GJ) | 1.6
Inductance (H) | 10
Layers | 4

## Slide 5: 2. Physical design of the detector magnet
Magnetic field distribution:
Two options of CEPC aluminum stabilized LTS conductor are on R&D.
Dummy cable 22*56mm2
Option A
Option B

## Slide 6: 2. Physical design of the detector magnet
Magnetic field distribution of the Track Volume:
The non uniformity of Tracking Volume (diameter 3.62m,length 4.7m) is 14.6%
Bmax= 3.09618242
Bmin = 2.65912069
Bmax-Bmin= 0.4370617310
Peak-Peak non-uniformity:
= 14.6%
 | Peak-peak non uniformity
Ref TDR | 14.6%
4th Design | 16.7%
CDR | 9.2%

## Slide 7: Yoke parameters:
 | Ref TDR | CDR(CEPC) | CEPC 4th detector
Central field (T) | 3 | 3 | 3
Length of Yoke (m) | 12 | 14 | 11.1
Outer diameter(m) | 11 | 14.5 | 8.5
Inner diameter(m) | 8.9 | 8.8 | 7.3
Total yoke mass [kt] | 3 | 12.573 | 1.143
3. Yoke and stray field
 | Mass (ton)
Barrel yoke | 1812
Each End yoke | 570
Total | 3000

## Slide 8: stray field:
Stray field |  | Ref TDR | CEPC CDR | 4th design
50 Gs | R direction | 25.6 m | 13.6 m | 16.3m
 | Z direction | 32 m | 15.8 m | 19.9m
100 Gs | R direction | 20.4 m | 10 m | 12.6m
 | Z direction | 25.3 m | 11.6 m | 15.7m
3. Yoke and stray field
50 Gauss and 100 Gauss distribution

## Slide 9: stray field:
3. Yoke and stray field
The magnetic field on the yoke iron is saturated.
Stray field away from yoke (unit, Gauss):
The magnetic field distribution from 0 to 20 m in axial direction:
 | 5m | 10m | 15m
Radial | 664 | 235 | 100
Axial | 1080 | 385 | 174

## Slide 10: Magnetic field at the booster ring
The detector stray field can reach the booster and influences the beam dynamics of booster. The current study shows that the correction to the detector stray field seems possible at low field (less than 50 gauss) level by orbit correction.
Add correctors
Dou Wang, Yuan Zhang, Daheng Ji, Feipeng Ning, Impacts of Detector Stray Field on Booster, AP NOTE, ACC-AP-NOTE-2020-001, Receive Date (October 15, 2020)
25m
From 54Gs to 36Gs
The impact of the stray field on the beam is being evaluated.
  Anti-solenoid or Yoke?
Are there any other requirements for stray magnetic fields?
A little higher than 50 Gs at the booster location.

## Slide 11
1, magnetic field uniformity of Tracking volume?
2, stray field on detectors, electronics, power source, Vacuum pumps?
3, stray field on beam?
4, stray field on booster?
Any requirements?

## Slide 12
1, Optimization design of LTS cable;
2, Cryogenic system research;
3, Mechanical structure research;
4, Quench detection and protection system;
5, Yoke and stray field;
6, HTS options study.
Work towards TDR