## Slide 1: Timing-trigger-control distribution

## Slide 2: General structure
Backend Interface Unit
  Recovered Clock for FPGA fabric.
  Lower jitter clock from jitter cleaner for GTH transceivers reference clock.
  TTC Interleaved data stream
    CHA ： Trigger accept
    CHB ： Control command，like bunch counter reset

## Slide 3: FIU Option 1： lpGBT-like
Data transceiver with fixed and “deterministic” latency for both up and down links
  Provide 40/80/160…/1280MHz synchronization clock
E-ports Groups
  Bandwidth @ links
    Up-link: 320Mb/s @ 24 links
    1280Mb/s @ 6 links
    Down-link: 80Mb/s @ 16 links
    320Mb/s @4 links
ASIC control: 80Mb/s
Slow control: 80Mb/s

## Slide 4: FIU Option 2： Dedicated clock cable
Use near-detector clock fanout board (No or small radiation doses)
Reduce the difficulty in handing clocks in lpGBT-like.

## Slide 5: FIU Option 3： lpGBT-FPGA
FPGA used in small radiation doses region
To much cables into detector

## Slide 6
Clock performance requirement: jitter 10ps rms for all?
Simplify types of elinks?

## Slide 7
https://espace.cern.ch/GBT-Project/Talks/lpGBTtutorialTwepp20180927.pptx?Web=1