## Slide 1
Plastic scintillator ECAL and HCAL
Yunlong Zhang
University of Science and Technology of China

## Slide 2
Requirements of CEPC Calorimeter
ILD-like detector with additional considerations.
The Particle Flow Algorithm (PFA) calorimeter concept was proposed
  High granularity
  Good track finding
  Good energy resolution

## Slide 3
Calo | Sampling No. | Sensitive detector | Absorber | Granularity | Electronics | Absorb length | Energy Resolution | weight
Sci-W ECAL | 32 | PSD+SiPM | W-Cu | 5mm×5mm | SP-2E | 22 X0 | 16%@ 1 GeV | 0.3 T
AHCAL | 40 | PSD+SiPM | Fe | 40mm×40mm | SP-2E | 4.6 NIL | 60%@ 1 GeV | 5.0 T
Sampling Calorimeter
AHCAL
hadron
Sci-W ECAL
PFA Calorimeter

## Slide 4
Sci-W ECAL
Sci-W ECAL
  32 layers，16 super-layes
  210 channels of each layer，total channels:6720
  Sensitive area：22cm×22cm

## Slide 5
ECAL
BMR
能量分辨率16%@1GeV
BMR：1.97% （H->γγ）

## Slide 6
AHCAL
The AHCAL was assembled this summer
  40 sensitive layers, and sensitive area is ~ 72 cm x 72 cm
    Each layer has 324 sensitive cells
    Total number is 12960

## Slide 7
AHCAL
能量线性优于1%
能量分辨率~48%@1 GeV
BMR ~3.7% （H->gg）

## Slide 8
ECAL & AHCAL Beam Test
ECAL
AHCAL

## Slide 9
ECAL & AHCAL Beam Test
Energy linearity better than 2%
Energy resolution is
10 – 80 GeV

## Slide 10
计算依据
HCAL Barrel Inner radius R1=2.25 m, Outer radius R2=3.69m, length L= 6.7m, Nlayers=48, Area of Barrel = 2*PI*[(R1+R2)/2]*L * NLayer = 6001.4 m2
HCAL Endcap Inner radius r1 = 0.4m, Outer radius r2 =3.69m, Nlayers=48, Area of Endcap = 2*PI*(r2*r2 – r1*r1) * NLayer = 4058.3 m2
ECAL Barrel Inner radius R1 = 1.90m, Outer radius R2 = 2.14m, length L= 6.0m, Nlayers=30 Area of Barrel = 2*PI*[(R1+R2)/2]*L * NLayer = 2284.6 m2 ECAL Endcap Inner radius r1 = 0.35m, Outer radius r2 =2.14m, Nlayers=30 Area of Endcap = 2*PI*(r2*r2 – r1*r1) * NLayer = 840.2 m2

## Slide 11
Performance Summary
Items | Priority | Results / Status |  | Remarks
Boson Mass Resolution | A | 1.97% （H->γγ） 3.73% （ννH->ννgg） |  | BMR < 4%
Intrinsic EM/hadronic energy resolution | A | 0.9% ; |  | 
Separation power |  |  |  | gamma/gamma, gamma/hadron, hadron/hadron
Lepton ID in jets |  |  |  | 
Timing capability |  |  |  | 
reconstruction |  |  |  | 
Pile-up at Z-pole |  |  |  | 
Items | Priority | Results / Status |  | Remarks
Boson Mass Resolution | A | 1.97% （H->γγ） 3.73% （ννH->ννgg） |  | BMR < 4%
Intrinsic EM/hadronic energy resolution | A |  |  | 
Separation power |  |  |  | gamma/gamma, gamma/hadron, hadron/hadron
Lepton ID in jets |  |  |  | 
Timing capability |  |  |  | 
Pile-up at Z-pole |  |  |  | 
Priority/importance for performance requirements: (A) must-have; (B) plus; (C) not essential

## Slide 12
ECAL Cost Summary
Parameter Name | Barrel | Endcaps (x2) | Sum
Inner Radius for ECAL | 1900 mm | 350 mm | NA
Length for barrel; Outer radius for endcap | 6000 mm | 2200mm （1900 mm + ）; Sc-ECAL：2146 mm | NA
Longitudinal Depth | （edge217.1） |  | NA
Modularity | #modules in phi, #rings along Z | Assuming ideal geometry if no design? | NA
Material Volume (m³) | 6.5 | 2.4 | 8.9m3 152 M
Readout channels | 21.3M | 8.1M | 29.4M
Power dissipation (kW) | 150.5 | 55.3 | 205.8
Cost: sensitive materials (Yuan) | 245.1 M | 90.1 M | 335.2M
Cost: electronics | 319.2 M | 121.1 M | 440.3 M
Total Cost |  |  | 0.93 B
Parameter Name | Barrel | Endcaps (x2) | Sum
Inner Radius for ECAL | 1900 mm | 350 mm | NA
Length for barrel; Outer radius for endcap | 6000 mm |  | NA
Longitudinal Depth |  |  | NA
Modularity | #modules in phi, #rings along Z | Assuming ideal geometry if no design? | NA
Material Volume (m³) | 6.5 | 2.4 | 8.9m3 152 M
Readout channels | 21.3M | 8.1M | 29.4M
Power dissipation (kW) | 150.5 | 55.3 | 205.8
Cost: sensitive materials (Yuan) | 245.1 M | 90.1 M | 335.2M
Cost: electronics | 319.2 M | 121.1 M | 440.3 M
Total Cost |  |  | 0.93 B
Please also consider to indicate in extra or supporting materials
Unit cost for key components and materials
References for unit cost or estimates
Uncertainty or risks if applicable
闪烁体：3.5元/channel
SiPM: 10 元/片
电子学：15 元/channel
W：123$, 886 元/kg

## Slide 13
AHCAL Cost Summary
Parameter Name | Barrel | Endcaps (x2) | Sum
Inner Radius for HCAL | 2250 mm | 350 mm | NA
Length for barrel; Outer radius for endcap* | 6600 mm | 3690mm | NA
Longitudinal Depth | , 1440 mm, edge 3762.3 mm |  | NA
Modularity | #modules in phi, #rings along Z | Assuming any ideal geometry if no design? | NA
Material Volume (m³) | 119.8 | 81.4 | 201.2m3 （1567吨） 124.0 M
Readout channels | 3.68 M，3.67（考虑gap） | 2.51 M | 6.19 M ，6.17（考虑gap）
Power dissipation (kW) | 24.6 | 17.7 | 42.3
Cost: sensitive materials(Yuan) | 64.5 M | 43.7 M | 108.3 M
Cost: electronics | 55.3 M | 37.5 M | 92.8 M
Total Cost |  |  | 325.1 M -> 0.3B
Parameter Name | Barrel | Endcaps (x2) | Sum
Inner Radius for HCAL | 2250 mm | 350 mm | NA
Length for barrel; Outer radius for endcap* | 6600 mm | 3690mm | NA
Longitudinal Depth |  |  | NA
Modularity | #modules in phi, #rings along Z | Assuming any ideal geometry if no design? | NA
Material Volume (m³) | 119.8 | 81.4 | 201.2m3 （1567吨） 124.0 M
Readout channels | 3.68 M，3.67（考虑gap） | 2.51 M | 6.19 M ，6.17（考虑gap）
Power dissipation (kW) | 24.6 | 17.7 | 42.3
Cost: sensitive materials(Yuan) | 64.5 M | 43.7 M | 108.3 M
Cost: electronics | 55.3 M | 37.5 M | 92.8 M
Total Cost |  |  | 325.1 M -> 0.3B
Please also consider to indicate in extra or supporting materials
Unit cost for key components and materials
References for unit cost or estimates
Uncertainty or risks if applicable
* Endcaps encompass barrel
闪烁体：7.5元/channel
SiPM: 10元/片
Ele：15元/channel
Fe：7.9万元/吨

## Slide 14
Technical readiness level
Category | Status | Design 1 | Other Alternative Design (if any)
Technical Readiness Level | Full Simulation (system level) |  | 
 | Full Simulation (module level) |  | 
 | Prototyping R&D (common) |  | 
 | Prototyping R&D (modules, units) |  | 
Status and plans of simulation studies and R&D (a table template)
Person power

## Slide 15
ECAL and AHCAL
ECAL (Scintillator + SiPM, Barrel 2323 + Endcap 840 = 3163 m2)
P(inside layer) ~ 3.163^7 (channels) * 7mW/ch(SPIROC) = 221.4 kW (full load)
P(interface) ~ 9W /DIF/m2 * 3163m2 = 28.5 kW
P(total) ~ 250 kW
AHCAL (Scintillator + SiPM, Barrel 5609.2 + Endcap 4045.3 = 9654.5m2)
P(inside layer) ~ 6.0341e6 (channels) * 7mW/ch (SPIROC) = 42.24 kW
P(interface) ~ 9W /DIF/m2 * 9654.5m2 = 86.9 kW
P(total) ~ 129.14 kW