## Slide 1
CEPC MDI Cryomodule design status
Xiangzhen Zhang, Xiaochen Yang
On behalf of cryogenics system
2024.10.24
The 2024 CEPC Workshop, Hangzhou, Zhejiang

## Slide 2: Content
Introduction
Cryogenic scheme of the cryostat
Structural design of the cryostat
Calculation and simulation
Current leads design
Summary and plan

## Slide 3
  Introduction
In CEPC, there are two combined-function Superconducting magnets in each MDI.
Each combined-function magnet includes three high gradient quadrupoles (Q1a, Q1b, Q2) and one anti-solenoid.
The cryostat is used to provide the cryogenic environment for SC magnets , which is lower than 5.0 K.
From Yingshun Zhu
ITEM | Q1a | Q1b | Q2 | Anti-solenoid
Central field gradient (T/m) | 142.3 | 85.4 | 96.7 | 
Cooling type | LHe | LHe | LHe | LHe
Operating current (A) | 780 | 650 | 770 | 1300
Magnetic storage energy (KJ) | 11.5 | 11 | 33.2 | 630
Cross section parameter (mm) | Φ40~61 | Φ52~78 | Φ62~88 | 100 sections
Magnet length (m) | 1.21 | 1.21 | 1.53 | 5.1
Net weight (Kg) | 25 | 32 | 43 | 302
Total weight of magnets (Kg) |  |  |  | 402

## Slide 4
  Introduction
Scheme and structure of the cryostat.
Scheme of the cryogenic system.
Heat and mass transfer in the cryostat.
Scheme of the current leads.
From Yingshun Zhu
Works to be done in cryogenic engineering.

## Slide 5
  Introduction
KEK and FCC
The length is approximately 3.3 m, and diameter is 1.1 m.
The weight of the magnet cryostat is 1570kg.
It is cooled by subcooled liquid helium at the pressure of 1.6 bara.
The length is approximately 3.36 m initially, and 6.24 m for second option.
It is cooled by superfluid helium He∥. (2.0 K)

## Slide 6
Superconducting magnets are immersed in the helium tank for the low temperature.
One thermal shield is set for the heat interruption from the ambient temperature.
The shield is extended between the helium tank and the beam chamber.
The 4 K cold mass is cooled by supercritical or subcooled liquid helium, and the shield is by liquid nitrogen.
Cryogenic scheme of the cryostat
Cryostat scheme

## Slide 7
Conventional helium cooling scheme: Subcooled liquid helium or supercritical helium is directly provided by helium refrigerator. The flow rate is limited.
Helium circulation (Potential): A closed helium circulation can be established depending on a pump to increase the flow rate. The scheme will be introduced later.
Superfluid helium(HeⅡ, Potential): Perfect cooling uniformity; Stable pressure; Higher magnet current.
Cryogenic scheme of the cryostat
Cooling system

## Slide 8
1985mm
1915mm
2885mm
Q1a
Q1b
Q2
Anti-solenoid
Structural design of the cryostat
Support of SC magnet
The superconducting magnets Q1a,Q1b and Q2 are supported on the inner wall of the solenoid.
The anti-solenoid is supported by a ring on the inner wall of the helium tank.
Vacuum
Thermal shield
LHe tank
Support
Anti-solenoid
Q1a
Beam chamber
Notes: 标注尺寸

## Slide 9
Outer cylinder of helium tank
Fluid domain
inlet
outlet
Cooling flow: One-way in and out
Heat conduction of support is 13.68 W; Heat flux of thermal radiation is 0.1 W/m2;
Helium inlet flow is at 4.2 K.
Chart: Coil number of anti-solenoid
| 1 | 2 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
4.0 g/s | 4.39 | 4.71 | 16.6 | 11.95 | 10.07 | 13.438 | 12.49 | 10.25 | 9.04 | 8.59 | 6.8 | 5.34 | 4.86 | 4.74 | 4.52 | 4.56 | 4.69 | 4.84 | 4.78
6.0 g/s | 4.295 | 4.297 | 12.81 | 9.592 | 8.624 | 9.58 | 9.492 | 8.457 | 7.56 | 7.25 | 6.37 | 5.49 | 4.65 | 4.61 | 4.39 | 4.36 | 4.37 | 4.46 | 4.54
8.0 g/s | 4.29 | 4.29 | 7.26 | 8.39 | 8.02 | 11.46 | 11.12 | 9.14 | 7.63 | 6.45 | 5.53 | 4.82 | 4.47 | 4.38 | 4.32 | 4.3 | 4.31 | 4.32 | 4.38
12.0 g/s | 4.262 | 4.262 | 8.301 | 6.94 | 6.31 | 5.96 | 6.18 | 5.83 | 5.5 | 5.26 | 4.78 | 4.42 | 4.4 | 4.42 | 4.35 | 4.34 | 4.33 | 4.32 | 4.43
Calculation and simulation
Cooling of anti solenoid
Not feasible！

## Slide 10
Cooling flow: Outer single-layer flow channel
Chart: Coil number of anti-solenoid
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
2g/s | 4.9018 | 4.9282 | 4.9373 | 4.9266 | 4.926 | 4.9229 | 4.9462 | 4.9511 | 4.9833 | 4.9767 | 5.0021 | 4.9386 | 4.9673 | 4.9463 | 4.9375 | 4.9436 | 4.9458 | 4.9556 | 4.972 | 5.0009
4g/s | 4.6213 | 4.6405 | 4.6486 | 4.6389 | 4.6412 | 4.6358 | 4.6493 | 4.6539 | 4.6883 | 4.6817 | 4.7157 | 4.6507 | 4.7019 | 4.6544 | 4.649 | 4.6522 | 4.6551 | 4.6621 | 4.6685 | 4.6788
6g/s | 4.5924 | 4.6094 | 4.6143 | 4.6077 | 4.6109 | 4.603 | 4.6196 | 4.6153 | 4.6559 | 4.6486 | 4.7045 | 4.6507 | 4.6786 | 4.6373 | 4.6307 | 4.6476 | 4.645 | 4.6522 | 4.6507 | 4.6525
10g/s | 4.4571 | 4.471 | 4.4757 | 4.4682 | 4.47 | 4.4629 | 4.4767 | 4.4715 | 4.5003 | 4.4955 | 4.5597 | 4.5019 | 4.547 | 4.4848 | 4.4695 | 4.4848 | 4.4896 | 4.4946 | 4.4868 | 4.4709
Chart: Coil number of anti-solenoid
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
2g/s | 4.6856 | 4.6678 | 4.6984 | 4.7036 | 4.7072 | 4.711 | 4.714 | 4.7202 | 4.734 | 4.7332 | 4.758 | 4.7424 | 4.7473 | 4.7652 | 4.7707 | 4.7721 | 4.7678 | 4.7749 | 4.7837 | 4.7986
4g/s | 4.4286 | 4.4316 | 4.4506 | 4.4592 | 4.4631 | 4.4701 | 4.4665 | 4.4708 | 4.4883 | 4.4882 | 4.5134 | 4.4833 | 4.504 | 4.5127 | 4.5204 | 4.5222 | 4.5155 | 4.5194 | 4.5257 | 4.5321
6g/s | 4.4004 | 4.4041 | 4.4091 | 4.41 | 4.4199 | 4.4211 | 4.4254 | 4.4275 | 4.4478 | 4.4484 | 4.4884 | 4.4452 | 4.4681 | 4.4731 | 4.4827 | 4.4916 | 4.4834 | 4.4857 | 4.4869 | 4.4931
10g/s | 4.3302 | 4.3328 | 4.3358 | 4.3342 | 4.3412 | 4.338 | 4.3468 | 4.3456 | 4.3607 | 4.3566 | 4.3936 | 4.3545 | 4.3801 | 4.3734 | 4.375 | 4.385 | 4.3844 | 4.386 | 4.3807 | 4.3802
Chart: Helium flow channel（single-layer）
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 20
进出口压差Pa | 0.8413 | 3.3359 | 7.4465 | 13.2656 | 20.9472 | 29.6841 | 40.5507 | 53.136 | 82.7403
Temperature distribution of the outer cylinder of the helium tank: 4.2K 10g/s
Calculation and simulation
inlet
outlet
Cooling of anti solenoid

## Slide 11
Optimized helium channel
Inner and outer double flow channel design：
Minimum gap is 4mm
inlet
outlet
Calculation and simulation
Comparison of single-layer and double-layers cooling channels ：
Chart: Coil number of anti-solenoid
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
2g/s Single flow channel design Anti-solenoid Peak temperature | 4.9018 | 4.9282 | 4.9373 | 4.9266 | 4.926 | 4.9229 | 4.9462 | 4.9511 | 4.9833 | 4.9767 | 5.0021 | 4.9386 | 4.9673 | 4.9463 | 4.9375 | 4.9436 | 4.9458 | 4.9556 | 4.972 | 5.0009
10g/s Single flow channel design Anti-solenoid Peak temperature | 4.4571 | 4.471 | 4.4757 | 4.4682 | 4.47 | 4.4629 | 4.4767 | 4.4715 | 4.5003 | 4.4955 | 4.5597 | 4.5019 | 4.547 | 4.4848 | 4.4695 | 4.4848 | 4.4896 | 4.4946 | 4.4868 | 4.4709
2g/s Double flow channel design Anti-solenoid Peak temperature | 4.6173 | 4.6526 | 4.6609 | 4.6415 | 4.6379 | 4.6348 | 4.663 | 4.6674 | 4.7316 | 4.7112 | 4.7102 | 4.6389 | 4.6693 | 4.6463 | 4.6367 | 4.6397 | 4.6417 | 4.6514 | 4.6704 | 4.7153
10g/s Double flow channel design Anti-solenoid Peak temperature | 4.441 | 4.4609 | 4.4646 | 4.4531 | 4.4536 | 4.4477 | 4.4703 | 4.4697 | 4.5207 | 4.5111 | 4.5565 | 4.497 | 4.5315 | 4.4571 | 4.4533 | 4.467 | 4.4697 | 4.4763 | 4.4689 | 4.4536
The double-layers flow channel is more effective compared to a single-layer flow channel, especially when the helium flow rate is low ；
Some other advantages with double heat exchange surface, including the heat management, quench recovery or magnet cooling time.

## Slide 12
Calculation and simulation
Cooling of quadrupole coils
Helium flows into the inner channel and out from the outer channel.
Q1-A
Q1-B
Q2
Thermal radiation 0.2 W/m2
Thermal radiation 0.2 W/m2
Surface emissivity:
Thermal radiation 17.055 W/m2
Fluid pressure difference diagram (Inlet flow rate 10g/s)
Chart: Mass flow rate of helium at the inlet （g/s）
| 4 | 6 | 8 | 10 | 12 | 14 | 16
压差Pa | 8.2361 | 16.772 | 28.1237 | 41.8732 | 58.0346 | 76.5527 | 97.2631

## Slide 13
Calculation and simulation
X
Temperature distribution of helium fluid
Inlet flow rate 10g/s
x=3.500 m
x=1.400 m
x=0.060 m
x=1.250 m
x=2.500 m
Helium fluid is heated in the inner channel.
The temperature of the fluid in the inner channel varies greatly near Q1-A.
Cooling of quadrupole coils

## Slide 14
Calculation and simulation
X
Temperature distribution inside the inner channel
Temperature distribution outside the inner channel
After passing through Q2 and Q1-B, the helium temperature increases by approximately 0.04K.
When subcooled helium flows through Q1-A, its temperature rises rapidly, with a gradually increasing temperature difference at the same X position.
Cooling of quadrupole coils

## Slide 15
Calculation and simulation
Chart: Mass flow rate （g/s）
| 4 | 6 | 8 | 10 | 12 | 14 | 16
Maximum temperature: inside the inner channel | 4.9649 | 4.8373 | 4.7427 | 4.6902 | 4.6637 | 4.6387 | 4.6216
Maximum temperature: Outer side of inner channel | 4.8161 | 4.7071 | 4.6345 | 4.5947 | 4.5741 | 4.5615 | 4.5527
Maximum temperature: inside the outer flow channel | 4.7557 | 4.6667 | 4.632 | 4.602 | 4.5826 | 4.5696 | 4.5602
The static thermal radiation of a quadrupole focusing magnet is constant.
The higher the flow rate is, the lower the temperature of the Q1-A magnet will be.
The flow rate of subcooled helium is determined based on the temperature of the magnet.
Cooling of quadrupole coils

## Slide 16
Subcooled LHe Circulation
A tank is used to control the pressure.
The flow rate can be improved largely.
Temperature distribution can be more uniform.
The system is complicated.
Calculation and simulation

## Slide 17
Current leads design
MDI superconducting anti-solenoid magnet need to develop 1.3 kA level current leads;
The traditional pure copper leads are not easy to meet the requirements, and binary current leads are used based on high-temperature superconductivity;
The superconducting wire welding resistance optimization, safe protection and low-temperature insulation and other issues are considered;
Current lead in BEPC2

## Slide 18
Current leads design
HTS current lead
Current leads cooled by liquid nitrogen or helium are designed based on Bi-2223 high-temperature superconductor and high-purity copper;
With the help of numerical simulation, for the cooling of the copper section is designed; An enhanced heat transfer scheme is proposed；
1.3 KA HTS current lead cooled by helium gas
New heat exchange method
Oxygen free copper
HTS
LTS
 | 1300A current lead |  | 800A current lead | 
Sections | HTS | Copper part | HTS | Copper part
Cooling | 5K helium gas | 5K helium gas | 5K helium gas | 5K helium gas
Structure | Bi-2223 | RRR40 copper | Bi-2223 | RRR40 copper
Temperature | ＜60K | ＜60K-300K | ＜60K | ＜60K-300K
Current | 1500 A+ | / | 900 A+ | /
Heat load | ＜0.15 | / | ＜0.1 | /
Flow rate | / | ＜0.1g/s | / | ＜0.05g/s

## Slide 19
Current leads design
For the 1300A current lead, the temperature of the cold end can be controlled to be lower than 60 K with a flow rate of 0.06 g/s.
Meanwhile, the heat load on the liquid helium temperature is 0.12 W.

## Slide 20: Summary
Design status of cryomodule:
The cryostat is designed now and will be updated as the optimization of the SC magnets in future.
Supercritical/ Subcooled liquid helium is used as the cold source and the calculation is performed.
A subcooled LHe circulation is designed, which can increase the flow rate largely.
Current leads for the magnets are designed;
Works to be done next:
Optimization of the cryostat;
Thermal and mechanical analysis; (quench protection, energy storage , supports )
Measurement requirements; (temperature/pressure/BPM)
Consideration of processing and manufacturing technology;

## Slide 21
Thanks for your attention!