## Slide 1
CEPC collider ring beam dynamics
EDR plan and status
Yiwei Wang
23-26. Oct. 2024, Hangzhou, CEPC Workshop 2024
Thanks to Y. Zhang, N. Wang, Zhe Duan, B. Wang, S. Bai, D. Wang for their contribution the slides!

## Slide 2: Content
Introduction
EDR goal, scope and plan
EDR progress and Key milestones from 2024-2027
EDR system team human resource status
Conclusion
Acknowledgement

## Slide 3
Introduction
This talk is about CEPC collider ring beam dynamics EDR plan and status
  lattice, error correction, beam-beam effects
  impedance and collective instabilities
  polarization of the collider rings
  Beam dynamics code development

## Slide 4: Overall design requirement of the CEPC collider ring
SR power per beam 30 MW (50 MW upgradable), 100 km, 2 interaction points
Compatible modes for H/Z/W/runnig: provide high quality beam energy from 45.5 to 180 GeV
Compatible with SPPC: 100km, section length, two machines share the most tunnels
Tunnel in the arc regions
CEPC detectors
CEPC+SPPC complex

## Slide 5: Lattice design requirement of the CEPC collider ring
Ref: CEPC TDR; Radiation Detection Technology and Methods (2024) 8:1–1105, https://doi.org/10.1007/s41605-024-00463-y
Basically 2 folded symmetry
2 interaction regions @ IP1 and IP3
  crab waist collision
  local chromaticity correction for the interaction region
  asymmetric interaction region
2 RF acceleration regions @ IP2 and IP4
  shared cavities for two beam @ ttbar, Higgs
  flexible switching between compatible modes
8 arc sections
  dual aperture dipole and quadrupole magnets
4 short straight section
  on/off axis injection regions for different modes
  beam dumping
SS4
SS1
SS2
SS3
SS: short straight section

## Slide 6
CEPC Design Parameters
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch Spacing (ns) | 576.9 | 23.1 | 253.8 | 4523.1
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 317/317 | 317/317 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.0/1.7 | 1.05/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (min) | 18 | 77 | 22 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5
 | Higgs | Z | W | 
Number of IPs | 2 |  |  | 
Circumference (km) | 100.0 |  |  | 
SR power per beam (MW) | 30 |  |  | 
Half crossing angle at IP (mrad) | 16.5 |  |  | 
Bending radius (km) | 10.7 |  |  | 
Energy (GeV) | 120 | 45.5 | 80 | 180
Energy loss per turn (GeV) | 1.8 | 0.037 | 0.357 | 9.1
Damping time x/y/z (ms) | 44.6/44.6/22.3 | 816/816/408 | 150/150/75 | 13.2/13.2/6.6
Piwinski angle | 4.88 | 24.23 | 5.98 | 1.23
Bunch number | 268 | 11934 | 1297 | 35
Bunch Spacing (ns) | 576.9 | 23.1 | 253.8 | 4523.1
Bunch population (1011) | 1.3 | 1.4 | 1.35 | 2.0
Beam current (mA) | 16.7 | 803.5 | 84.1 | 3.3
Phase advance of arc FODO () | 90 | 60 | 60 | 90
Momentum compaction (10-5) | 0.71 | 1.43 | 1.43 | 0.71
Beta functions at IP  x*/ y* (m/mm) | 0.3/1 | 0.13/0.9 | 0.21/1 | 1.04/2.7
Emittance x/y (nm/pm) | 0.64/1.3 | 0.27/1.4 | 0.87/1.7 | 1.4/4.7
Betatron tune nx/ny | 445/445 | 317/317 | 317/317 | 445/445
Beam size at IP sx /sy (um/nm) | 14/36 | 6/35 | 13/42 | 39/113
Bunch length (natural/total) (mm) | 2.3/4.1 | 2.5/8.7 | 2.5/4.9 | 2.2/2.9
Energy spread (natural/total) (%) | 0.10/0.17 | 0.04/0.13 | 0.07/0.14 | 0.15/0.20
Energy acceptance (DA/RF) (%) | 1.6/2.2 | 1.0/1.7 | 1.05/2.5 | 2.0/2.6
Beam-beam parameters xx /xy | 0.015/0.11 | 0.004/0.127 | 0.012/0.113 | 0.071/0.1
RF voltage (GV) | 2.2 | 0.12 | 0.7 | 10
RF frequency (MHz) | 650 |  |  | 
Longitudinal tune ns | 0.049 | 0.035 | 0.062 | 0.078
Beam lifetime (min) | 18 | 77 | 22 | 18
Hourglass Factor | 0.9 | 0.97 | 0.9 | 0.89
Luminosity per IP (1034 cm–2 s–1) | 5.0 | 115 | 16 | 0.5
𝛽y∗ and emittance chosen for luminosity
adequate bunch population Ne for the luminosity and the achievable energy acceptance for lattice design
Number of bunches Nb is adjusted to keep the beam current
Updated bunch spacing for the requirement from detector (D. Wang, Aug 2024, CEPC day)
Ref: CEPC TDR; Radiation Detection Technology and Methods (2024) 8:1–1105, https://doi.org/10.1007/s41605-024-00463-y;

## Slide 7: Lattice design of the CEPC half ring
ttbar: εx=1.4nm, β=1.04m/2.7mm
Higgs: εx=0.64nm, β=0.30m/1mm
W: εx=0.87nm, β=0.21m/1mm
Z: εx=0.27nm, β=0.13m/0.9mm
Notes: 11?𝜎_𝑥×15𝜎_𝑦×1.7%(booster 3.6nm)

## Slide 8: Key issues of lattice, error corrections and beam-beam in the EDR phase
Trade off the accelerator physics requirements and the engineering constraints.
Lattice with the more insertion sections and more realistic model; Exploring more robust lattice w/o changing the geometry significantly
Further improve the beam lifetime including lattice, beambeam and beamstrahlung.
More static errors and improve the global corrections; Dynamic error effects (inclu. ground motion) and possible feedback; IP tuning
Perform tracking simulations with a realistic lattice and strong-strong beam-beam interaction, to study the effects of machine errors on the beam-beam performance and the interplay with the luminosity-tuning knobs.
Establish the detailed procedures for the tuning, operation, different modes switching et al.
Establish the tools and soft wares for tuning and operation.
Compatibility with the future SPPC

## Slide 9: Super conducting final quadrupoles for all modes
Dipole field aberration due to cross talk of the two aperture
  Three types of SCQ design are undergoing.
  Beam dynamics: integrated dipole field should be corrected
  Radiation and particle loss: maximum 450/300/200/100 gs in the good field region along the SCQs for ttbar/Higgs/W/Z modes (the requirement will be updated with simulation of an integrated model of the quadrupoles, dipole error and solenoid)
    This is also the max field allowed for the correctors in SCQ
  The normal conducting quadrupole of Q3 for ttar running was moved outward (outer end from 7.2m to 7.55m) due to conflict between the cryomodule and the Q3
Layout of the dual aperture SCQ final quadrupoles
Parameters of the twin-aperture SCQs between the IP
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -142 | -142 | -95 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -57 | +65
Q2IRU | 1.5 | 4.7 | -51 | +97 | +65 | 0
Q3IRU | 3 | 7.2 (7.55) | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -59 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -51 | +97 | +65 | 0
Q3IRD | 3 | -7.2 (7.55) | +40 | 0 | 0 | +2
Quadrupole | L [m] | Distance from IP [m] | Strength [T/m] |  |  | 
 |  |  |  | Higgs | W | Z
Q1AIRU | 1.21 | 1.9 | -142 | -142 | -95 | -110
Q1BIRU | 1.21 | 3.19 | -59 | -85 | -57 | +65
Q2IRU | 1.5 | 4.7 | -51 | +97 | +65 | 0
Q3IRU | 3 | 7.2 (7.55) | +40 | 0 | 0 | +2
Q1AIRD | 1.21 | -1.9 | -142 | -142 | -95 | -110
Q1BIRD | 1.21 | -3.19 | -59 | -85 | -57 | +65
Q2IRD | 1.5 | -4.7 | -51 | +97 | +65 | 0
Q3IRD | 3 | -7.2 (7.55) | +40 | 0 | 0 | +2

## Slide 10
  Vertical emittance generated by solenoid field
The detector solenoid are compensated locally with anti-solenoids
From IP to the entrance of Q1A (0 to 1.9m):
  ∫Bzdz cancled between the IP and the entrance of final quadrupole with strong anti-solenoid field in 1.1m to 1.9m.
  Field configuration optimized to get emittance minimum and iterate with anti-solenoid technical constraints
Compensated solenoid field from IP to the entrance of Q1A (same with TDR for combined field)
Emittance contribution from the from IP to the entrance of Q1A
by Ande MA, Yiwei Wang, Yingshun Zhu
Version | ttbar | Higgs | W | Z
(pm) | 4.7 | 1.3 | 1.7 | 1.4
op. design (pm) | 0.03 | 0.26 | 0.85 | 0.67
tech. design v6 (pm) | 0.04 | 0.41 | 1.35 | 1.07
tech. design V7 (pm) | 0.04 | 0.36 | 1.20 | 0.95
Version | ttbar | Higgs | W | Z
 | 4.7 | 1.3 | 1.7 | 1.4
 | 0.03 | 0.26 | 0.85 | 0.67
 | 0.04 | 0.41 | 1.35 | 1.07
 | 0.04 | 0.36 | 1.20 | 0.95
Updated detector solenoid field @ W/Higgs/ttbar
(Scaled to 2T at IP @ Z)
Chart: Z(m)
Data from Feipeng Ning
tentative, to be optimized with the evolution of the detector design
Z(m)

## Slide 11
  Vertical emittance generated by solenoid field
From the entrance of Q1A to Q3(1.9m to 10.55m)
  Bz keep fully cancellation along this region
  Torlerance of the cancellation: amplitude ≤±200 Gs in a region L≥2 cm to limit the emittance growth less than 1% nominal value
From the Q3 to the last bend (farer than 10.55m)
  ∫Bzdz from detector only < 0.5 T*m.
  Along beam line (not z), fully cancelation in Q3 and pre-cancelation in some extension region (with length of 1m) for the long tail of the detector solenoid field
Updated detector solenoid field @ W/Higgs/ttbar
(Scaled to 2T at IP @ Z)
Chart: Z(m)
tentative, to be optimized with the evolution of the detector design
Z(m)
Data from Feipeng Ning

## Slide 12
  Update of the ARC lattice
FODO cells in the arc to provide a large filling factor of dipole
  Dual-aperture dipoles and quadrupoles in the arc to save magnet power
  Single-aperture sextupoles for independent nonlinearity optimization of e+ e- rings
  Two kind of dipole length to use the space where no sextupoles
Single aperture magnets in the RF, injection and interaction regions
Correction of the energy sawtooth effects require adjusting range of magnets strength 2.5% with the trim coils
Running at energy up to 180 GeV
The layout of the lattice in the arc area were updated based on the space required for vacuum, BPM, magnets, and mechanical equipment.
Qaud BPM Sext VCconection Dipole
Dipole VCconection Dipole
BPM
Dipole VCconection Quad Corr VCconection Dipole

## Slide 13: Beam lifetime of lattice + beam beam(s-s) + beamstrahlung
Using an integrated simulation code in APES-T (IHEP homemade, in progress) which can implement element-by-element tracking with strong-strong beam-beam interaction and lattice
 | Equilibrium bunch (e-) | Injected bunch (e+)
(nm) | 0.66 | 1.26
(pm) | 1.35 | 13
Bunch length (mm) | 4.1 | 1.85
Energy spread (%) | 0.17 | 0.099
 | Equilibrium bunch (e-) | Injected bunch (e+)
 | 0.66 | 1.26
 | 1.35 | 13
Bunch length (mm) | 4.1 | 1.85
Energy spread (%) | 0.17 | 0.099
The injection pattern reaches a stable state equivalent to the equilibrium collision after 2000 turns, with a lifetime of approximately 40-60 minutes (33 min required). The particle loss before stability is about 0.06%.
Zhiyuan Li etal., NIMA 1064 (2024) 169386
In collaboration with KEK team

## Slide 14: Luminosity of lattice + beam beam(s-s) + beamstrahlung
The vertical size blowup of beam is the result of Carb-waist transformation and IP chromaticity
  Good agreement between theoretical prediction and simulation results
  The residual IP chromaticity should be better controlled during the beam lifetime optimization.
CW 80%, linear tracking
  w/o chromaticity：1.06
  w/ chromaticity：1.10
Zhiyuan Li etal., NIMA 1064 (2024) 169386
In collaboration with KEK team

## Slide 15: Luminosity with local coupling error at IP
Sensitivity study of the luminosity with local coupling error only in one beam (ring); for Higgs energy
The scaled coupling parameters R1/R2/R3/R4 have similar effects, where the scaled parameters should < ~1 to keep luminosity loss < 10%
Next step: IP tuning and get the corrector requirement to fulfill scaled parameters < ~1
by Yuan ZHANG et al.
R1, R2, R3 and R4 are the components of the x-y coupling matrix

## Slide 16: Beam-based alignment target for the sextupole
Component | x (mm) | y (mm) | z (mrad) | Field error
Dipole | 0.10 | 0.10 | 0.10 | 0.01%
Arc Quadrupole | 0.10 | 0.10 | 0.10 | 0.02%
IR Quadrupole | 0.10 | 0.10 | 0.10 | 0.02%
Sextupole | 0.10* | 0.10* | 0.10 | 0.02%
The DA with error correction of Higgs lattice decreases as the sextupole offsets target increase, the success rates, DA satisfies with the injection requirement, are 90% (10 um), 86% (20 um), 60% (30 um), and 3% (30 um).
Requirement of the alignment accuracy of the adjacent equipment is basically 100um based on the current error correction simulation.
by Bin WANG et al.
Beam-based alignment (BBA) techniques will be implement, for esp. sextupole, to reach a much smaller offsets with respect to the beam
  With a large IP beta lattice; with quadrupole coils in the sextupoles; 10 um is possible as O(BPM resolution)=1um. (TBD)
  Scan the target from 10 um to 50 um to find a relaxed target for the sextupole BBA
arrow indicate the DA requirement 8𝜎𝑥 ×20𝜎𝑦 ×1.6%
More details in talk of
B. Wang, CEPC first tune operation required machine tuning. 3:00-3:20 PM, 23 Oct.

## Slide 17: Work under going for the error corrections
Error simulation with the long range alignment data and first turn tuning is ongoing.
  A large beta* lattice (3mm, 45GeV) and long range alignment data (rms ~7mm) were prepared.
  The existing first turn commission program has been developed for HEPS, part of the program has already been modified according to the CEPC lattice.
Preliminary result show the integrated RMS offset of the ground motion around the IP should less than some nanometers for the frequency of 1-100Hz
  Magnify factor for ground to magnet 1, magnify factor for magnet to beam 3
  (∆𝑦_𝐼𝑃/𝜎𝑦_IP)𝑟𝑚𝑠 <0.2 , if limit the luminosity decrease < 1%

## Slide 18: Key milestones from 2024-2027 for lattice, error corrections and beam-beam
2025
  An optimized collider accelerator physics design including the evolution corresponding to the CEPC EDR hardware design will be provided for the CEPC Project Proposal.
2026-2027
  Establish the detailed procedures for the tuning, operation, different modes switching et al.
  Establish the tools and soft wares for tuning and operation.

## Slide 19: Key issues of the impedance and collective instabilities in the EDR phase
Develop the impedance model with more realistic hardware designs, along with possible impedance mitigations
Contributions from the missing elements  increase the impedance budget  Limitations to the Luminosity
  Inj./ext. elements, feedback kickers, absorbers, masks and collimators outside the IR region are not included.
Influence of the High Order Modes (HOMs) should be further identified
  IR Chambers, Electro-separators, Collimators…
Influence of updated impedance on beam instabilities, along with mitigations
  Bunch current threshold
  Luminosity
by Na Wang et al.

## Slide 20: Impedance update
Collimators
Resistive wall
Masks
Electro separators
Feedback kickers
slotted-pipe kicker
Collimator
Masks
Electro separators
Trans. feedback kicker
Long. feedback kicker
by Na Wang et al.

## Slide 21: Impedance evolution
Evaluate with rms bunch length of 3mm
2018
2021
2023_V1
Elliptical cross section (CDR)
Circular cross section
More contributors included (TDR)
More detailed chamber material, collimator updated, weighing
The transverse impedance budget increased dramatically  mainly contributed by the collimators for the machine protection
  Influences: single bunch current threshold, beam-beam interaction/luminosity reach
  Careful machine protection & collimator design with low impedance + instability mitigations
2023_V2
Collimators for machine protection, masks and feedback kickers included
2024
More detailed collimator design, resistive wall and Eseparator updated
Chart: Normalized by V2018
| Z/n | kloss | ky
2018 | 1 | 1 | 1
2021 | 1.3421 | 0.8452 | 1.099
2023_V1 | 1.3947 | 0.9423 | 1.6733
2023_V2 | 1.4354 | 1.0296 | 2.8989
2024 | 1.4491 | 1.0419 | 3.1782
longitudinal effective impedance loss factor vertical kick factor
More details in talk of
N. Wang, CEPC impedance budget update in EDR. 4:40-5:00 PM, 23 Oct.
by Na Wang et al.

## Slide 22: Combined impedance and beam-beam effect at Z energy
With longitudinal impedance
With vertical impedance
Combined effect of beam-beam + transverse impedance results in strong TMCI, induce collision unstable
beam-beam can be stable at design parameter of Z with strong feedback and high chromaticity
  Stable with damp rate ~ 0.05, Qy’~10 (half ring)
by Yuan Zhang
w/o FB, Qy’=10
w/o FB, Qy’=10
w/ FB, Qy’=10
Notes: Qy’~10: lattice; nonlinear kicker to lower impedance;
damping rate 0.05, 10 turns

## Slide 23: Key issues of the polarization R&D in the EDR phase
Key aspects | Figure of merit | R&D goal
Design study | > 50% polarization for both beams | improve pol e- design, study pol e+ scheme
Polarized electron source | polarization > 85% | polarized DC gun @ PAPS, polarization > 85%
Compton polarimeter | 3D measurements ~ 0.1% | vertical measurement @ BEPCII, ~1%
Resonant depolarization technique | ~1e-6 accuracy @ Z & W | demonstration @ BEPCII
Solenoid spin rotator for longitudinal polarization @ Z-pole | Solenoid integral field ~ 1000 T.m per IP | YBCO SC solenoid, B ~ 12 T, BL > 10 T.m
polarimeter
IP/detector
IP/detector
Spin rotators near IR @ CEPC
by Zhe DUAN et al.
More details in talk of
Z. Duan, CEPC polarization. 9:00-9:20AM, 25 Oct.

## Slide 24: Beam dynamics code development: APES
Motivation: meeting the challenge of CEPC
  High luminosity, high energy, strong SR(energy sawtooth), crab-wasit collision, beamstrahlung, small (strong lattice non-linearity), new instability, combined effects
Objective:
  accurate modeling and simulation
  Self-consistent
  High performance (GPU+MPI)
Yuan Zhang et al, Supported by Innovative Study of IHEP
More details in talk of
Y. Zhang, Z. Liu, The status of accelerator design program kit: APES. 3:20PM, 23 Oct.
Notes: Accelerator Physics Emulation System

## Slide 25: Beam dynamics code development: APES
Lattice modeling and optics calculation
Sawtooth orbit deviates from energy loss due to synchrotron radiation
Orbit deviates after rad-taper
Beam-beam simulations
Some results for CEPC Higgs lattice
Collimators in the ring
FMA
Benchmark with SAD

## Slide 26: Human resource
Lattice design: Yiwei Wang, Yuan Zhang, Sha Bai, Ande Ma (PhD)
Global error correction: Bin Wang, Daheng Ji, Yuanyuan Wei
Ground motion: Fang Yan, graduate students
IP tuning：Yuanyuan Wei, Sha Bai, Yiwei Wang, Dou Wang
Beam-beam simulation: Yuan Zhang, Zhi Yuan Li (Post doc), Yixian Dai (PhD), international collaboration
Impedance and collective instability: Na Wang, Yudong Liu, graduate students
Polarization: Zhe Duan et al, international collaboration
Staff >11, several PhD students and Post doc

## Slide 27: Conclusions
Progress of the collider ring beam dynamics toward EDR are presented.
    The lattice were updated due to the trade off with the engineering constraints
    The DA with error correction for Higgs were studied versus different BBA target.
    Strong beambeam + lattice+ beamstrahlung for Higgs were simulated for beam lifetime and luminosity.
    Impedance updated for several equipment with more realistic hardware designs.
    R&D of polarization has been studied.
EDR plans for the collider ring beam dynamics from 2024 to 2027 have been established aiming at the construction in the 15th five year plan.
  In 2025, an optimized collider accelerator physics design including the evolution corresponding to the CEPC EDR hardware design will be provided for the CEPC Project Proposal.

## Slide 28: Backup

## Slide 29: Collider Ring RF Staging
stage 1: 2-cell H cavities are shared by two rings for the Higgs and W running; Half the number of H cavities are bypassed for W and Z running.
stage 2: 1-cell Z cavities will be installed, and the low current H cavities are bypassed with the transfer line (shown in green) when running in Z mode; For Higgs and W running, the beams go through both the 2-cell and 1-cell cavities.
stage 3: 5-cell t𝑡𝑡̅ cavities will be installed in the center for t𝑡𝑡̅ running; For W/Z running, the beams go through the same beamline as in stage 2 and is possible to switch to Higgs running by bypassing the t𝑡̅ cavities with a transfer line (in black colour).
Higgs priority
- timeline and performance priority
Upgradable
- power (luminosity) and energy upgrade
Low cost (especially first stage)
- staged cost and in-kind contribution
Max luminosity for each mode
- up to 50 MW SR power per beam
Seamless mode switch
- switch among H/W/Z/(ttbar)
Ref: CEPC TDR, arXiv 2312.14363; Jiyuan Zhai, CEPC workshop-EU 2024

## Slide 30: Summary on the impedance budget update
Longitudinal impedance：
  dominated by the RW, flanges, bellows and RF cavities
Transverse impedance：
  dominated by the RW, flanges, bellows and collimators
  Prominent impedance increase due to the collimators
Shows limitations for Z luminosity reach
Possible mitigations
  Combination of Feedback and chromaticity
  Optimization on the machine protection & collimation design
  Nonlinear collimator as adopted in SuperKEKB
by Na Wang et al.

## Slide 31
Beam lifetime of lattice + beam beam(w-s) + Beamstrahlung
The beam lifetime including both beam-beam and lattice are optimized with large number of nonlinear knobs with algorithm of multi-objective differential evolution (MODE)#
  Beam lifetime with bare lattice + beam beam (weak-strong) + beamstrahlung fulfill the requirements of the H/ /W modes.
  More realistic requirement of the Z mode beam lifetime should be carried out.
#J. Wu, Y. Zhang, Q. Qin, Y. Wang, C. Yu, D. Zhou, NIMA 959 (2020) 163517.
J. Wu, Y. Zhang, Q. Qin, doi:10.18429/JACoW-IPAC2019-MOPGW051, IPAC19.
Y. Zhang et al, doi:10.18429/JACoW-eeFACT2018-TUYBA04, eeFACT2018.
K. Oide, FCCIS 2022 workshop, Dec. 06, 2022.
Y. Zhang, Y. Wang, D. Wang, H. Geng, Z. Duan
 | Higgs | ttbar | W
Beam lifetime requirement for top-up injection [min] | 18 | 18 | 22
Bhabha lifetime [min] | 40 | 80 | 60
Required lattice + beambeam + beamstrahlung beam lifetime [min] | 33 | 24 | 35
Simulated lattice + beambeam + beamstrahlung beam lifetime [min] | 139 | 278 | 139
Crab sextupole strength [%] | 80 | 49 | 80
Notes: 详细描述优化过程