## Slide 1
The IDEA drift chamber
Paolo Giacomelli
INFN Bologna
These projects have received funding from the European Union’s Horizon Europe Research and Innovation programme under Grant Agreements No. 101004761 (AIDAinnova), 101057511 (EURO-LABS).
CEPC workshop
Hangzhou, 25/10/2024

## Slide 2: The IDEA detector concept
New, innovative, possibly more cost-effective concept
  Silicon vertex detector
  Short-drift, ultra-light wire chamber
  Dual-readout calorimeter
  Thin and light solenoid coil inside calorimeter system
    Small magnet ⇒ small yoke
  Muon system made of 3 layers of m-RWELL detectors in the return yoke
https://pos.sissa.it/390/
IDEA concept (proposed also in CEPC CDR)
Innovative Detector for e+e- Accelerator
Acknowledgments
I need to thank many colleagues, in particular:
N. de Filippis

## Slide 3: IDEA detector layout
Beam pipe: R∼1.0 cm
Vertex:
5 MAPS layers
R = 1.37-31.5 cm
Drift Chamber: 112 layers
4 m long, R = 35-200 cm
Outer Silicon wrapper:
Si strips
Superconducting solenoid coil:
2 T, R ∼ 2.1-2.4 m
0.74 X0, 0.16 l @ 90°
Preshower: ∼1 X0
Dual-Readout Calorimeter:
2m / 7 lint
Yoke + Muon chambers

## Slide 4: Momentum measurement
ZH (Hmm)
Muon pt
ZH (Hmm)
Muon pt
90 degree
MS only
ZH (Zmm)
Muon pt
Z or H decay muons in ZH events have rather low pt
  Transparency more important than asymptotic resolution

## Slide 5: Drift chamber
IDEA DC
IDEA: Extremely transparent Drift Chamber
  Gas: 90% He – 10% iC4H10
  Radius 0.35 – 2.00 m
  Total thickness: 1.6% of X0 at 90o
  All stereo wires (56448 cells, 343968 wires)
    Tungsten wires dominant contribution
  112 layers for each 15o azimuthal sector
  max drift time: 350 ns
L = 4m

## Slide 6: Drift chamber
dN/dx from Garfield++
In general, tracks have rather low momenta (pT ≲ 50 GeV)
  Transparency more relevant than asymptotic resolution
Drift chamber (gaseous tracker) advantages
  Extremely transparent: minimal multiple scattering and secondary interactions
  Continuous tracking: reconstruction of far-detached vertices (K0S , L, BSM, LLPs)
  Outstanding Particle separation via dE/dx or cluster counting (dN/dx)
    >3s K/p separation up to ~35 GeV

## Slide 7: Challenges for large-volume chambers

## Slide 8: Drift chamber - mechanical structure

## Slide 9: Mechanical structure: a complete model

## Slide 10: Full length prototype - goals

## Slide 11: Full length prototype - wiring

## Slide 12: Full length prototype - coverage

## Slide 13: Cluster counting

## Slide 14: Beam tests in 2021, 2022 and 2023

## Slide 15: Beam tests in 2021, 2022 and 2023

## Slide 16: Beam tests: resolutions

## Slide 17: Conclusions
Good progress on:
    Mechanical structure design
    Ongoing effort to build a full-length prototype in 2025
    Testbeam data analysis → NEW and quite conclusive results
Plenty of areas for collaboration
  detector design, construction, beam test, performance
  local and global reconstruction, full simulation
  physics performance and impact
  much more...
Efforts to build an international collaboration enforced
  Well established with IHEP for NN-based cluster counting algorithms

## Slide 18: Backup

## Slide 19: Drift chamber
Gas envelope
Wire Cage
Based on MEG2 experience
Based on MEG2 experience
90% He - 10% C4H10 – All stereo – s ~ 100 mm
Small cells, max drift time ~ 350 ns

## Slide 20: Drift chamber future plans
Complete mapping of dN/dx data in all relevant bg regions (few years)
  Understand details of cluster counting performance
Build large mechanical prototype (few years)
Build full length functioning prototype with few cells (few years)
Develop on-detector cluster counting electronics (few years)
Towards a drift chamber TDR

## Slide 21: Cluster counting
Test beam data 2022
Cluster counting 2x better than dE/dx
  Poisson vs . Landau  no large tails
Sample signal few GHz  on detector electronics R&D
For dN/dx method:
  RTA algorithm has been used for peak finding.
  dN/dx resolution dependence on the track length L-0.5
~ 2 times improvement in the resolution using dN/dx method as expected from the analytical calculation.
Test beam 2024