## Slide 1: CEPC vertex detector towards TDR
Zhijun Liang,
On behalf of CEPC vertex working group

## Slide 2: Plan : geometry and layout optimzation
Aim to have 1st draft of the detector geometry and mechnical design
  Physics Layout optimization (mainly focus on layout for endcap )
  Feasibility study of 2 layout ( mechanics support, cooling, cable ….)
Vertex detector MOST2 prototype layout has been implement in CEPCSW
  Try to perform further optimization with full simulation
Short barrel + endcap
Long barrel

## Slide 3: Long barrel cabling
Optoelectronics module is proposed.
  Radiation hardness of Optoelectronics module
  Optical fiber and power cable goes out from cabling space below
  Space for Optoelectronics module and cabling enough ?
    Optoelectronics : 5mm height, Power module: 5mm height
  Next step: need dimension of Optoelectronics module and fit them into engineering design
Example from CERN vtrX

## Slide 4: Beam background (from MDI group)
2D pair production background from Haoyu at the end of last week
  Will re-visit the data rate and readout scheme for vertex in next two weeks
  Pairs: /cefs/higgs/shihy/work/cepc_bkg/Results/Ref-TDR/20240312/Higgs/Pairs.root
  BeamLoss: /cefs/higgs/shihy/work/cepc_bkg/Results/Ref-TDR/20240312/Higgs/BeamLoss.root
ZH runs beam backgroun ( from Haoyu)

## Slide 5: Summary
Feedback from CEPC day by Yifang
  Mechanical design (connection to beam pipe)
  Material budget, vibration
  Power consumption, air cooling simulation
Space for cabling and service need to be refined urgently
  Feedback to Quan Ji about the space in 1~2 weeks
Revisit the data rate and readout scheme using the latest MDI background
  In next 1~2 weeks
Vertex detector layout optimization is in progress using CEPCSW
  Plan to converge in about 1~2 months

## Slide 6: Beam pipe Cooling discussion
Discussion with Quan and experts from Hunan University about beam pipe cooling
  Water cooling vs paraffin cooling
  Converging on water cooling solution
    Advantage Better cooling power , Less material budget (a factor of 2 lower)
    Disadvantage: Beam pipe corrosion by water during Radiation hardness (need more study)
      Beam pipe coating as one of possible solution to be studied

## Slide 7: Layout optimization: CEPCSW full simulation
MOST2 prototype layout has been implemented in CEPCSW
Layout Optimization for reference-TDR is based on CEPCSW
  Long barrel and short barrel layout are optimized in parallel

## Slide 8: Backup

## Slide 9: backup: CEPCSW full simulation
50um Si
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
12um G4_Al
25um Kapton
12um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
250um CFPR
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
12um G4_Al
25um Kapton
12um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
50um Si
layer1
layer2、3 (for each ladder with more than 10 sensors)
50um Si
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
12um G4_Al
25um Kapton
12um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
250um CFPR
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
12um G4_Al
25um Kapton
12um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
50um Si

## Slide 10: backup: CEPCSW full simulation Vs tklayout (fastsim)
相同结构，在0.1~0.6GeV/c和8~100GeV/c,CEPCSW有较好的d0分辨率
0.6~8GeV/c，tklayout有较好的分辨率。

## Slide 11: Toward geometry update for CEPCSW release
Need to converge on a few things soon, toward the CEPCSW release
  Sensor chip dimension
    Narrow chip for inner layer
    Wider chip for middle and outer layer
  Ladder dimension
  Flexible PCB
  Carbon fiber support
  Support design for short barrel
  Channel number: 128 * X

## Slide 12: Decay length
for b-hardon:
: , ,
: , :
for c-hardon:
: , ,
: , :
: , ,
: , :
: , ,
: , :
: , ,
: , :

## Slide 13: Layout optimization: CEPCSW full simulation
MOST2 prototype layout has been implemented in CEPCSW
  Long barrel： can be optimized using CEPCSW
  Short barrel+ endcap: Need to implement Endcap disk geometry into CEPCSW
    Need to work with software group

## Slide 14: Weekly meeting
Group Meeting every Thursday afternoon (2nd meeting last Thursday)
  https://indico.ihep.ac.cn/event/21543/
From last meeting, Discussion about the choice of technology
  Discussion with L3 Stitching (Mingyi) and SOI (Yunpeng)
  Agree to focus CMOS pixel for reference TDR baseline

## Slide 15: Key parameters
  Single-point spatial resolution (now and in the next 5 years)
  Time stamp precision requirement (to be discussed with Shengsun Sun)
  Material budget
  Cost estimation
  Occupancy
  Max data rate that can be handled by this technology (now, and in the next 5 years)
  Radiation hardness (now, and in the next 5 years)
  Power dissipation (now, and in the next 5 years)
  Expected Technology availability in the future
  Technology Readiness

## Slide 16: Towards TDR
Aim to have a draft of TDR by the end of 2024.
  System level design, choose baseline technology
  Electronics, service and mechanics needs to be included
Major change from CDR to TDR
  Beam pipe diameter: 28mm (CDR)  20mm (TDR) (reduce 30%)
  Instant Luminosity per IP:
    Z pole: 32×1034 cm-2s-1 (CDR)  192 ×1034 cm-2s-1 (TDR, 50MW) (6 times increase)
    ZH: 5.6×1034 cm-2s-1 (CDR)  8.3 ×1034 cm-2s-1 (TDR) (~1.5 times increase)