## Slide 1: Spin-Polarized Proton-Boron (p-¹¹B) Fusion: Pathways to Clean Energy
LI Zhi
1 Hebei Key Laboratory of Compact Fusion, Langfang, China
2 ENN Science and Technology Development Co., Ltd., Langfang, China
3 Shandong University, Qingdao, China
*Email：lizhiz@enn.cn
2025.09.22-26, Qingdao, China

## Slide 2: Outline
Fusion approaches, fuel options, and critical conditions
Ideal ignition conditions and reaction rate enhancement for p-¹¹B fusion
Polarization research advances toward p-11B fusion energy applications

## Slide 3
3
Stars
Hydrogen bomb
Directions for Controlled Fusion
Inertial Confinement Fusion (ICF)
Magnetic Confinement Fusion (MCF)
NIF
JET
Achieved Fusion Approaches

## Slide 4: Zoo of Fusion Devices
聚变点火原理概述，H.S. XIE(2023)

## Slide 5: Fusion Reactions for All Candidate Fuels
D, T, 3He :
H, 11B :
H. Rider. LLNL High Energy Density Science Seminar
Advanced fusion fuels
Criteria for fusion fuel viability:
Reaction threshold
Reaction cross-section
Energy released
Notes: criteria is easy

## Slide 6
A Visionary Goal: Commercially Viable Fusion Power
Safe
Cost-effective
ENN Fusion
Aneutronic
Pollution-free
Low-cost power generation (cheaper than wind and PV)
Compact facility
High energy conversion rate
Abundant Fuel Resources
Abundant and accessible fuel
Suitable for distributed energy market
Notes: hardest, but the final solution

## Slide 7
ENN’s Roadmap for p-¹¹B Fusion Power Based on the Spherical Torus (ST)
EXL-50U
2022-
EXL-50
2018-2023
p-11B Reaction (EHL-2)
2023-
p-11B Burn （EHL-3A&3B）
2027-
Commercial demo
2035-
Develop key technologies for ST p-B fusion
2035
Fusion power
Experimental verification of high-temperature plasma technologies
Feasibility assessment of boosted p-¹¹B fusion reaction rates
Enhance plasma performance parameters
Achieve boron fueling and robust operation control
Initiation, ramp-up, sustainment
ST device design, assembly, and operation
Phys, engineering, tech. scale-up
Sustained energy gain (Q>3)
Established the basis of ST p-B fusion
Validate all critical aspects of p-11B fusion
Achieve p-¹¹B plasma ignition and demonstrate net electricity generation
Deliver commercially viable fusion energy at competitive cost

## Slide 8
ENN’s Roadmap for p-¹¹B Fusion Power Based on the Spherical Torus (ST)
EXL-50U
2022-
EXL-50
2018-2023
p-11B Reaction (EHL-2)
2023-
p-11B Burn （EHL-3A&3B）
2027-
Commercial demo
2035-
Develop key technologies for ST p-B fusion
2035
Fusion power
Experimental verification of high-temperature plasma technologies
Feasibility assessment of boosted p-¹¹B fusion reaction rates
Enhance plasma performance parameters
Achieve boron fueling and robust operation control
Initiation, ramp-up, sustainment
ST device design, assembly, and operation
Phys, engineering, tech. scale-up
Sustained energy gain (Q>3)
Established the basis of ST p-B fusion
Validate all critical aspects of p-11B fusion
Achieve p-¹¹B plasma ignition and demonstrate net electricity generation
Deliver commercially viable fusion energy at competitive cost
M. S. Liu, H. S. Xie, Y. M. Wang, et al., ENN’s Roadmap for p-11B Fusion Based on Spherical Torus, Phys. Plasmas 31, 062507 (2024)
Peng1986
Complementary advantages and disadvantages!

## Slide 9: EXL-50U （ENN Xuan Long-50U）Spherical Torus (ST)
✓ Generated 1 MA plasma current with hydrogen-boron fuel
✓ Sustained ion temperatures >40 million°C
✓ Demonstrated robust magnet performance:
150 kA toroidal field current
1.2 tesla central magnetic fields
✓ 18 months: From design to completed construction
✓ 3 months: From commissioning to physics experiments

## Slide 10: Theoretical Possibility of p-11B Fusion: Need for Enhanced Reaction Rates
Fusion Enhancement factor
Fraction of fusion energy carried by charged particles
fusion power
radiation power loss
Simplified ignition criterion
More precise cross-section data required.
Energy carried per reaction by charged particles.

## Slide 11: Theoretical Possibility of p-11B Fusion: Need for Enhanced Reaction Rates
Simplified ignition criterion
Fusion reactivity
p-11B fusion achieves ignition with new cross-section.
Moreau1977
Putvinski2019
More precise cross-section data required.
Energy carried per reaction by charged particles.
Higher fusion reaction rate needed.
Fusion Enhancement factor
Fraction of fusion energy carried by charged particles
radiation power loss
fusion power

## Slide 12: Theoretical Possibility of p-11B Fusion: Need for Enhanced Reaction Rates
Simplified ignition criterion
p-11B fusion achieves ignition with new cross-section.
Kulsrud1982, Perkins1997, Leotta1987, Wanatabe2003
Moreau1977
Putvinski2019
More precise cross-section data required.
Energy carried per reaction by charged particles.
Higher fusion reaction rate needed.
H. Rider. LLNL High Energy Density Science Seminar
Spin-polarization
Shave Coulomb barrier
Shape-polarization
Muon Catalysis
Velocity Differential
Non-thermal
Fusion reactivity
Fusion Enhancement factor
Fraction of fusion energy carried by charged particles
radiation power loss
fusion power

## Slide 13: Polarization Research Advances toward Fusion Energy Applications
International research directions in polarized fusion fuels:
Reduce T consumption in D-T fusion
Control neutron emission direction in D-T fusion
Enhance D-3He/D-D fusion performance
Suppress neutron emission in D-3He fusion
Global spin-polarized nuclear data status:
D-D: Scarce
D-3He: Deficient
p-11B: Virtually nonexistent
Heidbrink (SPIN2023)
A comprehensive and systematic research plan!
Lots of efforts in last 2 years!
Extremely groundbreaking and brilliant research initiative!
Ciullo (SPIN)

## Slide 14: Polarization Research Advances toward Fusion Energy Applications
Heidbrink (SPIN2023)
Lots of efforts in last 2 years!
Ciullo (SPIN)
International research directions in polarized fusion fuels:
Reduce T consumption in D-T fusion
Control neutron emission direction in D-T fusion
Enhance D-3He/DD fusion performance
Suppress neutron emission in D-3He fusion
Global spin-polarized nuclear data status:
D-D: Scarce
D-3He: Deficient
p-11B: Virtually nonexistent
A comprehensive and systematic research plan!
Extremely groundbreaking and brilliant research initiative!
Numerous advantages, research agendas, and experimental proposals
— yet why not p-11B?

## Slide 15: Polarization Research Advances toward p-11B Fusion Energy Applications
Polarized p-11B fusion research
Remains largely unexplored
priorities:
  Differential cross-section measurements of spin-polarized p-11B reactions
  Development of boron fuel spin-polarization techniques
  Sustenance of spin-polarized hydrogen-boron plasma
Theoretical efforts
Experimental contribution

## Slide 16: p-11B Reaction: A Complex Process
Multi-pathway process with excited intermediates (12C, 8Be)
p+11B12C*α0+8Beα0+α01+α02:
p+11B12C*α1+8Be*α1+α11+α12 :
p+11B12C*3α :
p+11B12C+γ0:
p+11B12C+γ1+γ* (4.439 MeV) :
Becker1987, Spraker2012
Ep=675 keV
Mazzucconi2023
He2016
Munch2020

## Slide 17: Key Challenges Demand Theoretical and Experimental Advances
Differential Cross-Section | proton-polarized | boron-polarized | Double polarized
1st resonance peat@148 keV | ？ | ？ | ？
2st resonance peat@620 keV | ？ | ？ | √
Non-resonant | ？ | ？ | ？
Polarization resistance
Reaction channel
Numerous known unknowns await exploration!
Polarization effects on reaction cross-section
Unpolarized spin
Spin aligned along the magnetic field
Compared with the unpolarized scenario
Polarized hydroboration shows ~60% enhancement in total cross-section vs. unpolarized case
Requiring experimental verification!
For further details, see the subsequent report by YANG Wei

## Slide 18: Proposes for p-11B Polarization Studies Towards Fusion Application
Proposes for p-11B fusion reaction experiments
EXL-50U (operational): experiment proposes before 2027
EHL-2 (next generation): start in 2027
NBI-ICRF synergy-driven energetic protons initiating p-11B fusion
Thermonuclear p-11B fusion platform
Non-uniform magnetic field
particle collisions
wall recycling
RF waves
Spin-polarization sustainment and polarized reaction experiments?
+
Zhi2024

## Slide 19: Summary
p-11B Fusion: The Most Promising Commercialization Pathway
Advantages: Neutron-free, abundant fuel, high safety
Challenge: High ignition requirements
Research Directions:
  Synergy with spherical torus configurations
  Enhancing p-11B reaction rates (60%↑@620 keV)
Proposals for polarized p-11B fusion research:
  Polarized p-11B database establishment
  Boron polarization techniques development
  Polarized hydrogen-boron plasma sustenance
Experimental exploration on EXL-50U and EHL-2 devices
  (Polarized) fusion reaction experiments
  Polarized plasma generation and sustainment

## Slide 20
20
Thank you for your attention!
Email：lizhiz@enn.cn
Research interests and collaborations are welcome!

## Slide 21
Fusion Fuel of Great Promise and Challenge
Fuel | Pros | Cons | Fuel Price (USD/g) | Proven Reserves
1. D-T | Lowest ignition temp (100-200MK), high energy yield, proven scientific basis | Tritium fuel scarcity, neutron radiation challenges, nuclear waste concerns | Tritium: 30,000 | 25 kg
2. D-D | Abundant deuterium, no tritium needed, lower neutron yield | Higher ignition temp (400MK), lower energy yield, neutron damage | Deuterium: 4 | 45 trillion tons
3. D-3He | Minimal neutrons, high energy yield, direct conversion | Rare ³He, higher ignition temp (400MK), side reactions | 3He: 13700 | ³He scarcity: Extremely rare on Earth, requiring lunar mining or D-D breeding
4. p-11B | Abundant boron fuel, direct energy conversion, environmentally safe | Highest ignition temp (>1000MK), low reaction rate, S&T challenges | 11B: 4 | 1 billion metric tons
Tritium (T), helium-3 (³He), and lithium-6 (6Li) are government-controlled materials that are not accessible to private companies in China.
Fuel options for commercial fusion energy