## Slide 1: The PREFER collaboration
Giuseppe Ciullo & University of Ferrara
on behalf of the
COLLABORATION
at present time.
Group (Responsible) | Institute
R. Engels et al. | IKP - FZJ @ Jülich & GSI- Darmstadt, Germany
M. Büscher et al. | PGI - FZJ @ Jülich & ILPP- HH University @ Düsseldorf
G. Ciullo et al. | INFN & University @ Ferrara
T.P. Rakitzis et al. | IESL-FORTH & University @ Crete

## Slide 2: Polarized fuel for fusion: benefits and open questions
From the point of view of the nuclear physics, the use of polarized fuel can help fusion reactions thanks to:
enhancement of cross sections,
control on the angular distributions of the reaction products,
possible neutron lean reactors.
Open questions need still answers:
higher polarization and higher density (orders of magnitude more than available in nuclear polarized targets).
Preparation and Manipulation of fuel for fusion environments.
Survival of polarization in fusion environments.
It’s a challenging deal providing, manipulating, and testing polarized fuel in order to gain from the benefits of it in FUSION environments, and answer to the open questions.
We’ll gain deeper insights on knowledge for still “better and better” polarized sources, targets and polarimetry.

## Slide 3: Polarized fuel: Benefits and open questions
Reaction generations sorted vs the relative energy (temperature) of reactants.
Generation: D + T ® 4He + n
1.a) Enhancement of total cross section!!
1.b) Differential cross section: control on product angular distribution!!
2. Generation: D + D ® T + p or 3He + n
Fuel available (30 g m-3 in ocean water) !!
2.a) Enhancement of total cross section??
2.b) Differential cross-section and angular distrib. control?!
Still missing data for a complete description.
2.c) Possibility to suppress the reaction 3He + n / QSF (Quintet Suppression Factor)??
3. Generation: 3He + D ® 4He + p
3.a) and 3.b) expected like 1.a) and 1.b)!!
3.c) Possibility of Neutron lean reactor ?? This is conditioned by 2.c):
D+D ® 4He* ® 3He + n suppressed (QSF)?
Missing data on D-D
spin-dependent cross-sections.
Challenge objectives for PREFER
Missing polarized fuel
for fusion tests.
!! proven in scattering experiments and theoretically models are available, but still to be proven in fusion environments
?? Data not available in order to constrain theoretical models.

## Slide 4: Fusion o f spin ½ + spin 1 - polarized fuel
May the differential cross section of the fusion reactions be controlled by polarized particles ?
dσ/dΩ (ϑ) = σ0/4π [1 – ½ PDV PT + 3/2 PDV PT sin2 ϑ + ¼ PDT (1 – 3 cos2 ϑ)]
Factor 0.5
Factor 1.5
Factor 1
Total cross section
R.Engels et al. Advantages of Nuclear Fusion with Polarized Fuel in PoS 423 (SPIN2018) 176.
3He(d, p)4He Reaction
Leeman et al. ANN. PHYS. 66 (1971) 810.
G. Hupin «Ab initio prediction for polarized deuterium-tritium fusion reaction»Nat. Comm. 10 (2019) 351.
.
.
.
.
.
.
.
.
T + D → 4He + n and 3He + D → 4He + p
Experimental confirmatio
from 1972
Theoretical transposition to DT
... from 1972 many
experiments and
pubblications on
measuments and
theoretical models

## Slide 5: Fusion of spin 1+ spin 1 – polarized fueld
The total cross section D + D in respect to the incoming polarization of the fusing particles:
D ↑ + D ↑ spin dependent cross-section (data set very poor), and stilll less data at lower energy (electron screening ?)
In the case of D+D also P-, D-wave, togheter with S-wave and their interferences!
Fusing D + D, then D + T can fuses (n)
3He does not contribute at the ignition energy of D-D.
D + D → T + p / 3He + n

## Slide 6: Fusion of spin 1 + spin 1 – polarized fuel
Question: spin alignements allows to enhance, or suppress, reaction channels?
Neutron lean fusion: QSF (Quintet Suppression Factor)
D↑ (d ↑ p) T and D↑ (d ↑ n) 3He suppressed
by choosing deuteron spin parallel each others
S 1 1 = 0 5S2 Quintet State Suppressed
S 1 -1 0 1S0 Singlet state allowed
D↑
D↑
4He*
=

## Slide 7: PSTP people trys to involve fusion community
The PREFER collaboration was signed in 2017 in Ferrara during a Workshop on Polarized Fuel for Nuclear Fusion.
COVID ended our meetings.
Russia-Ucraina conflict interrupted official collaborations and official contacts with the russian colleagues.
Contributions of the Workshops held in 2013 at Trento, and in 2015 at Ferrara, collected in “Nuclear Fusion with Polarized Fuel”
(ed.s G. Ciullo, R. Engels, M. Büscher and A. Vasyliev)
Springer Proceedings in Physics 187
(Springer - 2016 - Switzerland)
The PREFER collaboration (early stages)

## Slide 8: Challenging objectives of PREFER
  @IKP-FZJ - Production of polarized fuel: from pABS and new proposals.
  @PNPI - D-D spin dependent cross-section measurements officially before 02/2022.
  @BINP - Production of polarized fuel: from MBS officially before 02/2022.
  @ IESL-FORTH - Production polarized fuel: by Laser IR-Quantum Beat (QB) excitation and Ultra Violet (UV) dissociation, joined the collaboration a little bit later.
& officially before 02/2022
still now
  @PGI-FZJ/HHDU - Laser Induced Plasma LIP: production, acceleration and reaction studies.
  @FE - Magnets for holding, manipulating and transporting polarized fuel .

## Slide 9: D ↑ - D ↑ spin dependent cross-sections
Unpolarized with solid target
Unpolarized with gas target
Polarized beam with unpolarized solid target
Polarized beam with unpolarized gas target
A. Yu. Rozhdestvenskij et. al Phys. Atom. Nucl. 87 (2024) 224.
4 1016 atom/s
15 mA
Theoretical models and experiment settings: H. Paez gen Schieck
«Spin Physics and Polarized Fusion: where we stand» in Nuclear Fusion with Polarized fuel Ed.s. G. Ciullo et al. Spr. Proc. Phys. 187 (2016).
B. P. Ad'yasevich Czech. J. Phys. B 32 (1982) 1349.
P. Kozma et al. Czech. J. Phys. B 35 (1985) 1118.
  @PNPI – D-D spin dependent cross-section measurements, officialy before 02/2022.
1011 atom/s

## Slide 10: D ↑ - D ↑ demanding of measurements
4 1016 atom/s
15 mA
[9] A. Solovev et al., J. Instrum. 15, C08003 (2020)
A. Yu. Rozhdestvenskij et. al Phys. Atom. Nucl. 87 (2024) 224.
  @PNPI

## Slide 11: Production of polarized fuel by pABS
R. Engels et al. «Production of HD molecules in definite hyperfine substates» Phys. Rev. Lett. 124 (2020) 113003
Production
recombination
Polarimetry
R. Engels - Current developments of polarized sources and polarimeter at FZ Jülich and further applications,
this symposium.
and new proposals.
  @IKP-FZJ - Production of polarized fuel: from pABS, and new proposals.
S. J. Pütz - Polarimetry of pulsed H- /D- ion beams: extended applicability of the Lamb-shift polarimeter,
in this symposium.

## Slide 12: Condensation & transp. of pol. fuel
T= 3-10K
Cold
Head
D2 ice
Production of 1 day
(>1021 molecules) is enough to feed a Tokamak for seconds,
in pellets, or for tests in ICF !!
H2, D2, and HD hyperpolarized molecules can be produced with polarization of P ~ 0.8 ! For HD any spin combination is possible !
HD is a perfect training ground for the handling of TD !
The condenser is surrounded by a S.C. MgB2 cylinder,
which provides the holding field also for transportation.
The Target can be used for LIP fusion test and esperiments @PGI-FZJ/HHDU
A holding magnetic field is required, for its transportation: superconducting MgB2 hollow Bulk material under investigation @ Fe.
Production of polarized fuel
The super-conducting hollow bulk material is also useful for other techniques under R&D
for polarized fuel production, like the ones propose by the colleagues of @ IESL-FORTH .

## Slide 13
D. Toporkov Status of experiments with polarized deuteron target at VEPP-3 electron storage ring,
this symposium.
Production of polarized fuel from pMBS
Instrum. Exper. Tecn. 62 (2019) 56-61.
Instrum. Exper. Tecniques 66 (2024) 531-537.
Instrum. Exper. Tecn. 62 (2019) 56-61.
  @BINP - Production of polarized fuel: from MBS officially before 02/2022.

## Slide 14: Production of polarized fuel by laser manipulation
Sofikitis et a.; PRL. 118 (2017) 233401.
The idea: ‘‘Highly nuclear-spin polarized deuterium atoms
from the UV dissociation of Deuterium Iodide”
DI
D atoms
LSP of Jülich Type
Laser
Excitation
Laser
Dissociation
Electron-Polarization = 1
Deuteron-Polarization ~ 2/3
Proof-of-principle
(Univ. of Crete/FORTH, IKP/PGI in FZJ/HHUD).
(Proton-Polarization = 1)
Pulsed Nozzle
HI
Sofikitis et a.; Phys. Rev. Lett. 121 (2018) 083001.
1018 cm-3 SPD from DI
> 1019 cm-3 SPH & SPD
  @ IESL-FORTH – Production polarized fuel: by Laser IR-Quantum Beat (QB) excitation and Ultra Violet (UV) dissociation, joined the collaboration later.

## Slide 15: Production of polarized fuel by laser
  @ IESL-FORTH – Production polarized fuel: by Laser IR-Quantum Beat (QB) excitation and Ultra Violet (UV) dissociation, joined the collaboration a little bit later.
Notation: I1 (Y nuclear spin) I2 (H isotope nuclear spin) J (rotational angular momentum, Fi=J + I1 and F=Fi+I2.
H isotope -Y diatomic molecules
HBr excited with s+ IR.
HBr excited with s+ IR.
After the IR excitation the UV shooting after the trasfer of polarization to p, which can be «frozen» by a magnetic field.
C. S. Kannis et al. Mol. Phys. 120 (2022) e1975053.
HBr
I2 proton spin and Fi=J+I1
HI
I2 proton spin and Fi=J+I1
C. S. Kannis et al. Chem. Phys. Lett. 784, 139092 (2021)
SPH and SPD
> 1019 /cm3
SEOP and S-G ~1013 /cm3
vs
C.S. Kannis Spin manipulation in atomic and molecular systems for nuclear spin applications. This Symposium

## Slide 16: Laser Induced plasma (LIP)
  @PGI-FZJ/HHDU - Laser Induced Plasma LIP: production, acceleration and reaction studies.
There are various proposal to produce high intense
and pure polarized fuel for fusion, but ...
... still an question is pending:
... the polarization will survive in fusion environments?
... then let’s jump a step and start from polarized beam and test its survival in PW laser. As a result this will be a goal on providing polarized ion sources too.

## Slide 17: Polarized 3He gas-jet for LIP acceleration
Up to 80% nuclear polarization
magnetic holding field for storing pre-polarized 3He gas @3 bar
non-magnetic nozzle provides the desired gas-jet target
I. Engin et al.,
Plasma Physics and Controlled Fusion 61 (2019) 115012
compressor increases pressure of 3He gas to ~30 bar
Target @
Feasibility studies of laser induced acceleration on 4He
High density polarized 3He Gas-Jet Target 3/4 1019 cm-3
P. Fedorets et al.
Instruments 6 (2022) art.n. 18
Best Working points: + 90° Laser dir.
4He++ 4.65 MeV, 4He+ 3.27 MeV.
Gas Backing p= 30 bar, 40-60 J & 1.6-3.2 ps
jet of 4 10 19 cm-3
3He polarized @Jülich
FZJ
GSI
~ 250 km
3He polarized jet beam at @GSI

## Slide 18: Polarimetry for 3He ions for LIP
Employing the know analyzing power of the reaction
Transverse polarization () of the ions
↕︎
Measurable left/right & up/down rate : asymmetry of 𝛼 particles
3He polarization along z mantained with B ~ 1.3 mT (——), Helmoltz coils (10 A and 5 mT max) hallow to rotate the polarization along the x axis (+ 75.5°) relative to the 3He ion momenta (- - -).
Helmholtz coils
off
on
− on
CD2 foil
x
z
Polarimeter
Polarimeter
CR-39 stack
3He++ beam
CD2 foil:
CR-39 stack

## Slide 19: Observed (a-)symmetry for LIP
Change of 𝛼-distribution: modified kinematics for polarized 3He gas
In both cases no L/R (U/D) asymmetry ➔ polarimeter works as expected
Higher sensitivity on a particle.
😀
😮
x
z
Long. polarized 3He gas
Unpolarized 3He gas
3He-ion polarization conserved after acceleration
2x increased 3He-ion flux from pol. plasma
Our concept (polarized target @ PW laser) works
Plasma acceleration of polarized beams (e–, p, ions) feasible
Models/simulation codes seem incomplete (spin-dependent ionization?)
signal for unpolarized or longitudinally pol. ions
Asymmetry e
e=

## Slide 20: Superconducting Bulk magnets
  @FE - Magnets for holding, manipulating and transporting polarized fuel .
DB ~ 0.02 mT
on 970 mT
in 15 days
1- iron yoke, 2 –coils, 3-iron poles, 4- nylon support, 5A –Al Chamber, 5B-5C SS chambers, 6-cold-head, 7B -7A TM pumps, 8A-8B Penning gauges
We tested the tube in the so called ZFC (Zero Field Cooling) condition and it shielded 970 mT for more than 1480 h ~ 61.5 days.
We found the optimal MgB2 bulk tube and tested it in the so called
FC (Field Cooling) condition and keep useful fields for a long time more than the requirements for transportation.
M. Statera et al. NIM A 882
(2018) 17-21.
G. Ciullo et al. Front. Phys. 12
(2024) 1358369
A- Cu-can hosting
sensors and MgB2 tube.
B – Opening Cu-cover.
C- Extracting MgB2 tube
from the Cu-can.

## Slide 21: Estending framework and collaboration
SPINPOL: Novel Methods for Hyperpolarized electron and nuclear spin production for: hyperolarized magnetic resonance (MRI/NMR/ESR) and Polarized Laser Fusion.
(1) in vivo medical imaging, and (2) atmospheric chemistry (3) polarized nuclear fusion
Spin-polarized HD trapped at a surface is done in the following steps:
(1) production of cold HD beam, with all molecules in the J=0 rotational state. (2) IR excitation of all molecules in the ground J=0 state using STIRAP [42], producing polarization of HD bond rotation ; (3) transfer of rotational polarization to HD nuclear spin through hyperfine beating; (4) trapping of HD at a cold surface; (5) transport of trapped HD to measurement facility; (6a) (polarized) laser fusion at the PALS in IPP, which possesses the intensity to produce collision energies high enough to trigger fusion reactions, such as D-D fusion (and D-3He fusion, in the presence of both hyperpolarized D and 3He; the latter supplied by UDUS);
6b) Hyperpolarized MRI on animals using hyperpolarized hydrocarbons (instead of HD), at Aarhus.
(The main novelty of SPINPOL is to combine all 6 steps, and to produce spin-polarized molecules at a scaled up level (at least mmol quantities of SPMs). Given that each of these 6 steps has been demonstrated individually (references given in each case), the likelihood of success for SPINPOL is very high.
Foundation of Research Technology- FORTH-Hellas; University of Düsseldorf - UDUS ; University of Münster- UMU; Quamtum Diamonds - QD – Münich; Aarhus University – AU; Institute of Plasma Physics - IPP – Prague; SpinFlex Ashkelon; University of Creta-UOC-Hellas, University of Ferrara – UNIFE.

## Slide 22: The ARPA-E ad hoc workshop
ARPA_E involved the PREFER in a very workshop on polarized fuel for the improvement of fusion facilities.
https://arpa-e.energy.gov/news-and-events/events/spin-polarized-fusion-spf-workshop

## Slide 23: The SPF (Spin Polarized Fusion) program at DIII--D
A project is funded by the DOE in USA for the test at the DIII-D tokamak for the survival of polarization.
Feeding pellet of
3He and LiD with spin parallel
and antiparallel
with proper diagnostics of the angular
distribution of fusion products,
will provide evidence of the
survival of the polarization.
Also the D polarized +
D unpolarized reaction has to be considered, they compared
different beam pitch v||/v and
with the D+3H spin aligned reaction
and tensor polarized D + 3He unpolarized
reaction.
W. W. Heidbrink et. al. A research program to measure the lifetime of spin polarized fuel Front. Phys. 12 ((2024) 1355212.

## Slide 24: Conclusions
Interests and activities on fusion with polarized fuel are “boiling” around, involving fusion experts too. This is another good result, which will be surely fruitful.
The proposal SPINPOL, submitted to the European community, enlarged already our collaboration.
A program in USA has been funded, in which our collaboration was determinant.
The most impelling and determinant result is to provide useful and “easy to handle” polarized fuel,
but we engaged excellent teammates for our spin games.
Sebastiano Filippi (named Bastianino)
“The spin game”
A fresco on the cieling of the Games’s Hall of the
Este Castle in Ferrara,
dated after earthquake of 1570.