## Slide 1
Polarized beam studies for CEPC and BEPCII
Zhe Duan
Institute of High Energy Physics, CAS
on behalf of the CEPC Polarization Working Group
Sep 22-26, 2025, 26th International Symposium on Spin Physics, Qingdao, email: duanz@ihep.ac.cn

## Slide 2: Outline
Polarization studies at CEPC
R&D for polarized beams at IHEP
Concepts of longitudinal polarization at BEPCII
Summary

## Slide 3: Circular Electron Positron Collider (CEPC)
Circular Electron-Positron Collider (CEPC) as a Higgs (Z / W / ) factory in China
  45 ~ 180 GeV beam energy, ~100km circumference
  Higgs Factory (>1M Higgs, ~1% precision)
  Z Factory (~Tera Z)
  The W+W- pair and then pair production thresholds
  Higgs, EW, flavor physics & QCD, probe to new physics up to 10 TeV
Possible pp collider (SppC) of ~ 125 TeV (TDR spec.) in the far future.

## Slide 4: Progress and schedule
Now in the phase of Engineering Design Report
CEPC plan to submit a proposal to the central government to be included in 15th FYP

## Slide 5: Physics motivation of polarized beams @ CEPC
Precision beam energy calibration @ Z, W (~100keV)
  resonant depolarization with vertically polarized beams (> 10% pol)
Precision measurement of weak mixing angle @ Z
  Longitudinally polarized colliding beams for measuring ALR
  could resolve the tension between AFB & ALR, by measuring both in the same experiement
CPV with polarized beams in e+e- → HZ. H → ττ etc
L. Arnaudon, et al., Z. Phys. C 66, 45-62 (1995).
G. Moortgat-Pick’s talk on CEPC Workshop EU @ Marseille, 2024 April
ECFA meeting on e+e- to ZH angular measurements
Polarized beam applications @ ILC,
arXiv:2105.09691, 2111.06687, 2202.07385

## Slide 6: Self-polarization in the CEPC
CEPC CDR parameters | 45.6 GeV (Z, 2T) | 80 GeV (W) | 120 GeV (Higgs)
Polarization build-up time w/o radiative depolarization (hour) | 256 | 15.2 | 2.0
Beam lifetime (hour) | 2.5 | 1.4 | 0.43
CEPC CDR parameters | 45.6 GeV (Z, 2T) | 80 GeV (W) | 120 GeV (Higgs)
 | 256 | 15.2 | 2.0
 | 2.5 | 1.4 | 0.43
Beam polarization build-up rate much slower than the beam decay rate @ Z-pole
  Boosted with asymmetric wigglers in the Collider (FCC EPOL)
  Hard to achieve a high-level polarization
  In conflict with a high luminosity
e+/e- beams become “self-polarized” via the Sokolov-Ternov effect in a storage ring

## Slide 7: Injecting polarized beams for resonant depolarization
Polarized source
  Polarized electron gun w/ superlattice GaAs cathode (>85% polarization)
  Positron damping/polarizing ring(>20% polarization)
Linac & Transport lines
  no interleaved H & V bendings
  polarization loss is negligible
Booster
  free from intrinsic spin resonances
  polarization can be well maintained for Z & W
T. Chen, Z. Duan, D. H. Ji, D. Wang, Phys. Rev. Accel. Beams, 26, 051003 (2023).
Similar approach is now being studied for FCC-ee
J. Wenninger, Injecting polarized beams , FCC Week 2025, FCC-FS EPOL group meeting 40
> 70% polarization transmission in the injector chain for Z & W operation.

## Slide 8: Polarization Maintenance in the Booster
Concern
  Depolarization due to crossings of hundreds of spin resonances, during Booster acceleration
Finding
  Highly periodic lattice -> structural cancellation -> weak spin resonances
  Spin resonance crossings lead to negligible depolarization to Z
Resonance strength vs ramping rate:
CEPC-Z in the regime of negligible depolarization
T. Chen, et al., Booster free from spin resonance for future 100-km-scale circular e+e- colliders, Phys. Rev. Accel. Beams, 26, 051003 (2023).
Polarization transmission to Z, W and Higgs energies in Booster:
Z: over 99%, W: 77.5%~ 98%, Higgs: no better than 40%

## Slide 9: Dual-purpose e+ damping/polarizing ring
DR V4.0 | unpolarized e+ | polarized e+
Energy (Gev) | 1.983 | 
Circumference (m) | 144.2 | 
Number of trains | 2(4) | 
Number of bunches/trian | 1(2) | 
Total current (mA) | 12.4 | 
Dipole strength B0 (T) | 1.92 | 
U0 (kev/turn) | 397.9 | 
Damping time x/y/z (ms) | 4.8/4.8/2.4 | 
Momentum compaction | 0.0078 | 
Storage time | 20 ms | 10 min
0 (%) | 0.0917 | 
0 (mm.mrad) | 132 | 
injection z (mm) | 6 | 
Extract z (mm) | 6.7 | 6.6
inj (mm.mrad) | 2500 | 
ext x/y (mm.mrad) | 133/13 | 132/13
inj /ext (%) | 0.18 /0.092 | 
RF acceptance (%) | 1.85 | 
Longitudinal tune | 0.025 | 
Use self-polarization at the e+ damping ring
  polarization build-up time ~ 14.5 min
  extracted beam polarization @ 10min ~ 44%

## Slide 10: A high-level longitudinal polarization @ Z-pole
50%-70% longitudinal polarization for e- bunches is a reasonable goal
Unpolarized e+ is assumed
Over 70% injected e- beam polarization
Simulated equilibrium longitudinal polarization > 70%, leaving a large margin for effects not yet covered.
Simulated equilibrium polarization for an imperfect lattice w/ rotators after closed orbit correction
Implementation of the spin rotators adjacent to the IR
W. Xia et al., Investigation of spin rotators in CEPC at the Z-pole,
Radiat. Det. Tech. Meth. 6:490 (2022).

## Slide 11: Outline
Polarization studies at CEPC
R&D for polarized beams at IHEP
Concepts of longitudinal polarization at BEPCII
Summary

## Slide 12: Beam polarization R&D in the EDR phase
CEPC requirements, R&D items,
and required experiment demonstration
R&D, beam tests, and foreseen experimental demonstration at IHEP accelerator facilities
These activities will set the basis for polarized beam applications @ CEPC.

## Slide 13: A test facility for polarized electron source
Convert a HV DC gun to a polarized electron source
  Beamline physics design in progress, in particular the Wien filter and Mott polarimeter
  Beam commissioning scheduled in 2027
500kV photocathode DC gun @ PAPS
Li Xiaoping, V. Tyukin, Liu Wei, Meng Cai, Wang Jianli, Wang Haijing, Liu Jindong, Liang Zhijun, Liu Zhongtian etc
Wien filter
Mott polarimeter
Beamline for polarization measurement

## Slide 14: A test facility for polarized electron source
Domestic R&D on superlattice GaAs cathode
  cathode production: polarization > 85%, QE > 0.8%
  build a platform for cathode performance test (pol & QE)
  First cathode has been produced and will be tested soon
Platform for cathode test:
ESP & QE
First sample of superlattice GaAs/GaAsP cathode
component fabrication and tests under way

## Slide 15: Compton polarimeter @ BEPCII
15
CEPC vertex detector prototype
15
Su Mengyu, Duan Zhe, A. Martens (IJClab), Liang Zhijun, Tang Guangyi, Wang Jianli etc
A Compton polarimeter is under commissioning at BEPCII (see Mengyu Su’s talk)

## Slide 16: YBCO Superconducting solenoid spin rotator R&D
Design specs：
Peak field: 12 T
Integral field：10.34T.m
Length：1.018m
Working current：300A
Coil aperture：140mm
magnet aperture > 64mm
HTS with conduction-cooling
Coil design and experimental studies under way
Measurements scheduled in 2027
Beam tests at LPA-Ring TF foreseen
Zhao Ling, Xu Qingjin, Hou Zhilong, Zhou Jin, Liu Zhongxiu etc
Cryo-cooler
Solenoid
Vacuum Dewar
10.5 Tm Solenoid as a Siberian snake
Longitudinal polarization
LPA-Ring TF under design

## Slide 17: Outline
Polarization studies at CEPC
R&D for polarized beams at IHEP
Concepts of longitudinal polarization at BEPCII
Summary

## Slide 18: Status of BEPCII
2025-2030: BEPCII upgrade to higher luminosity (x3 @ 2.35 GeV) & higher energy (up to 2.8 GeV) with rich physics potential (see Haibo Li’s talk yesterday)
2024.7
2025.1
2025.5
2025.10
Start tunnel installation
Linac resumes operation
SR commissioning
Colliding beams at 1.84 GeV
Colliding beams at 2.35 GeV

## Slide 19: Motivation for longitudinal polarization at BEPCII
Upgrade to e- longitudinal polarization could further enrich spin physics studies at BESIII
  Spin entangled hyperon-antihyperon pairs for CP tests (see Hong-Fei Shen’s talk)
  Fragmentation function (see Yateng Zhang’s talk)
  ...
A test bed for e- longitudinal polarization in future colliders incl. CEPC
  simultaneous achievement of high luminosity and high longitudinal polarization
  swap-out injection applied to e+e- collider, already demonstrated at APS-U & HEPS
swap-out injection

## Slide 20: Polarization issues at 1.55 GeV
Sokolov-Ternov time is 10.5 hour, beam lifetime is 1~2 hour
Inserting a Siberian snake to attain longitudinal polarization at IP
  Depolarization time is 24 min for a spin matched snake (requirements on lattice design)
Frequent extraction of depolarized bunches & injection of fresh polarized bunches
  e.g. replace 1/12 of all 120 bunches every 20 seconds
  for an injected beam polarization 80%, time-averaged polarization ~ 70%
A single full snake

## Slide 21: Envisaged modification and research topics
150kV polarized DC gun
wien filter
Mott polarimeter
spin rotator
extraction to beam dump
Siberian
snake
Compton polarimeter
Issue #1： polarized e- source
Issue #2: polarization manipulation
Issue #4: Extraction to beam dump
Issue #3: Compton polarimetry
Detailed design study is under way.

## Slide 22: International collaborators
Spin dynamics studies
  D. Barber (DESY), E. Forest (KEK), S. Nikitin (BINP)
  contribute to FCC-ee EPOL collaboration
Compton polarimeter
  A. Martens (IJCLab, supported by France-China Particle Physics Laboratory/Network)
  Instructive discussions with I. Nikolaev, V. Kaminskiy (BINP)
  A laser-vacuum insertion was borrowed from BEMS @ BESIII for early commissioning, granted by N. Muchnoi and M. Achasov (BINP)
Polarized electron source
  V. Tyukin (JGU Mainz, supported by PIFI program of CAS)

## Slide 23: Summary
A scheme of injecting polarized beams is promising for CEPC
R&D of key technologies in progress
  Compton polarimeter at BEPCII
  Test facility for polarized electron source
  Prototype of a HTS solenoid spin rotator
Longitudinal polarization option is being studied for BEPCII
These activities will set the basis for polarization applications at CEPC
Thank you for your attention!