## Slide 1
Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
The 26th international symposium on spin physics (SPIN2025)
Reporter：Mengyu Su
Authors：M. Y. Su, Z. Duan, Z. J. Liang, Q. F. Han, D. H. Ji, G. Lei, Q. Li, Y. C. Li, X. J. Sun, G. Y. Tang, J. L. Wang, C. H. Yu, W. Zhang, Y. L. Zhang, N. C. Zhou, D. C. Zhu, A. Martens, F. Castellanos, C. Sandoval
Date：20250923

## Slide 2
Background
1
Design considerations
2
Implementation status
3
Summary
4
CONTENTS

## Slide 3
1
PART
Background

## Slide 4
1.1 Polarized lepton beams
Sokolov-Ternov effect drives the spontaneous buildup of vertical polarization in electron storage rings
Polarization degree:
Applications of polarized lepton beams
  Vertical polarization:
    Precision energy calibration via resonant depolarization technique (VEPP-4M: ~)
  Longitudinal polarization:
    Longitudinally polarized colliding beams help enhance the physics reach
Longitudinal polarized lepton beam collision
Achieved：SLC, HERA
Planning：CEPC, CCF, SuperTC, EIC, SuperKEKB
Synchrotron radiation photons can induce electron spin flips, with unequal probabilities for up→down versus down→up transitions.
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Require high precision polarimeter !
(Dokl. Akad. Nauk SSSR 153(5), 1052–1054 (1963))
(Blinov:Nuclear and Particle Physics Proceedings 273-275, 210–218 (2016)
(CCF study report,CEPC TDR, EIC design report)
(CLENDENIN19941,Moortgat-Pick:2008,PhysRevD.110.014035)

## Slide 5
1.2 Compton polarimeter
Compton polarimeter are commonly used in electron storage rings with GeV beam energies because of their advantages of accurate and nondestructive measurement.
Real-time polarization measurement is required by polarized beam applications
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Polarimeter | Direction | Type | Energy (GeV) | Systematic Uncertainty
CERN LEP (R. Assmann:CERN SL/93-02 (BI)) | Vertical | γ | 46 | 5%
HERA LPOL (hep/ex 1201.2894) | Longitudinal | γ | 27 | 2.0%
HERA TPOL (hep/ex 1201.2894) | Vertical | γ | 27 | 1.9%
SLD @ SLAC (PhysRevLett.84.5945) | Longitudinal | e | 45.6 | 0.5%
CREX@ JLAB Hall A (PhysRevC.109.024323) | Longitudinal | γ, e | 2 | 0.36%
JLAB Hall C | Longitudinal | γ, e | 1.1 | 0.6%
the above list of polarimeters is not exhaustive

## Slide 6
1.3 The principle of laser Compton polarimeter
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Asymmetry==
Helicity flips
Asymmetry along Y
Analyzing power
Can be calculated
Degree of circular Polarization of laser ~100%
Can be measured
Degree of vertical polarization of electron
For a circularly polarized laser and transversely polarized electron beam,
Eb=2.35 GeV, λlaser=532 nm
The differential cross section
(ginzburg_colliding_1984, SLAC-PUB-4656)

## Slide 7
2
PART
Design considerations

## Slide 8
2.1 Introduction to BEPCII
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Beijing Electron Positron Collider II (BEPCII), a double-ring electron positron collider operating in the tau-charm energy range.
Driven by increasing particle physics research interests at higher beam energies, it is undergoing an upgrade, BEPCII-U, to achieve a threefold increase in the luminosity at 2.35GeV and a higher beam energy up to 2.8 GeV.
The polarization build-up time is about 72.5 min at 2.35 GeV for BEPCII storage rings, and the electron beams are injected normally every 1.5 hour.
(Yu: 7th International Particle Accelerator Conference, p.01 (2016))

## Slide 9
2.2 A Compton polarimeter at BEPCII
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
4W2, a wiggler-based X-ray beamline of BEPCII has retired from operation under the upgrade
We propose to modify the front end and the hutch to set up a Compton polarimeter.
Close to head-on collision
LOOK HERE!

## Slide 10
2.3 The luminosity of laser Compton polarimeter
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Reduce beam size, increase luminosity
The laser frequency and single pulse energy,
need to adjust the time synchronization between the laser and the electron beam.
For electron beam bunches and pulsed lasers, the collision luminosity is

## Slide 11
2.4 Design parameters and MC simulation
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Laser can be synchronized with an arbitrary bunch by the timing system
Asymmetry of a simulation of gamma
[Guangyi Tang]
Assume 50% vertical polarization
Thickness of lead (mm)
[Guangyi Tang]

## Slide 12
2.5 Detection system
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
The TaichuPix-3 silicon detector, a CMOS pixel sensor prototype for the CEPC vertex detector with a sensitive area of 15.9 × 25.7mm2 and a pixel size of 25 × 25μm2.
Since the lepton detection efficiency is higher than that of γ photons for such a detector, a lead converter with a thickness of a few millimeters, subject to optimization, is placed just in front of the detector to convert γ photons into leptons.
Detector readout active pixels with a time resolution of 50ns
2 layers of chips
lead (~3mm)
Backscattering photon
Signal on Taichu-Pix 3

## Slide 13
3
PART
Implementation status

## Slide 14
3.1 Overall progress
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Background measured by lead preshower + scintilator + PMT
Laser optics
Visible light part of synchrotron radiation from the reflector mirror

## Slide 15
3.2 Modification of the photon beamline
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII

## Slide 16
3.3 Laser optics tuning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
To ensure a specific circular polarization state at the IP.

## Slide 17
3.3 Laser optics tuning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
To adjust the spot size at IP

## Slide 18
3.3 Laser optics tuning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Here we can see the visual part of synchrotron radiation light

## Slide 19
3.3 Laser optics tuning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
The spot on target

## Slide 20
3.4 Beam commissioning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Connected to an oscilloscope
~5mm lead + glass scintillator (~)+ PMT
Alignment of detector & electron beam based on background
~100 colliding bunches in storage ring
Online adjustment of the electron position at the IP by the local bump of the storage orbit.

## Slide 21
3.4 Beam commissioning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Connected to an oscilloscope
~5mm lead + glass scintillator (~)+ PMT
Scan the position of laser to find the collision signal
Online adjustment of the laser position at the IP by rotating along pitch and yaw axes.
The laser is configured in internal trigger mode (4.5 kHz) , asynchronized with the ring RF frequency, the straight section is 5m long, the laser pulse is likely to coincide with up to 3 bunches
We can disregard the longitudinal matching here
~100 colliding bunches in storage ring

## Slide 22
3.4 Beam commissioning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Connected to an oscilloscope
Temporal distribution of detected peaks of 1000 triggered waveforms
a 600ns window
laser Qout
internal trigger at 4.5kHz
Causality between laser and backscattered γ signal
Event rate increases with laser power in a narrow temporal window

## Slide 23
Timing system sends 4.508kHz trigger to laser, in synchronization with ring RF frequency
Laser is now synchronized with one pilot bunch
3.4 Beam commissioning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
18ns gap
6ns bunch spacing, ~108 colliding bunches
delay
delay + 480ns
delay + 485ns
delay + 495ns
BEPCII e- Ring Bunch current Monitor

## Slide 24
We have observed the gamma signals via Taichu-Pix 3.
The next step is to distinguish the collision signals from the background
3.5 Detector commissioning
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Taichu-Pix 3 detection system
Single bunch collision via BLM
Event timestamp
Time resolution = 50ns
Signal on Taichu-Pix 3

## Slide 25
4
PART
Summary

## Slide 26
4 Summary
A laser Compton polarimeter has been designed and implemented in the electron storage ring of BEPCII, for vertical polarization measurement via detection of the vertical asymmetry of the back-scattered γ.
First laser-beam collision has been observed (BLM), commissioning is underway to detect electron beam polarization (TaichuPix-3).
Such a polarimeter can enable tests of resonant depolarization and study radiative depolarization mechanism, and contribute to spin physics research at BESIII experiments.
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII

## Slide 27
THANKS
The 26th international symposium on spin physics (SPIN2025)
Reporter：Mengyu Su
Authors：M. Y. Su, Z. Duan, Q. F. Han, D. H. Ji, G. Lei, Q. Li, Y. C. Li, Z. J. Liang, X. J. Sun, G. Y. Tang, J. L. Wang, C. H. Yu, W. Zhang, Y. L. Zhang, N. C. Zhou, D. C. Zhu, A. Martens, F. Castellanos, C. Sandoval
Date：20250923

## Slide 28
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Backup
Type | Scattered γ | Scattered e-
Transverse | Calorimeter or pixelized detector | Pixelized detector
Longitudinal | Calorimeter | 
Accelerator implementation | 😀 | ~100m drift for spectrometer
Background | SR & bremstrahlung | 😀
Intrinsic issues | Limited resolution for calorimeter Sys. error due to converter for PD | only measure 2 components

## Slide 29
SPIN2025 Design and Preliminary Implementation of a Laser Compton Polarimeter for BEPCII
Backup
系统误差和统计误差受铅转换体的厚度影响
  取铅厚度3mm，则取数20s 统计误差~1%
  铅同时用来屏蔽同步辐射
背散射gamma事例率12.8MHz，康普顿边缘~180MeV
Location | beamline and experimental hall of 4W2 wiggler
Laser | 532nm, 4.5 kHz, 2 mJ, 1 ns, flippable circular polarization
Observable | Vertical asymmetry of backscattered γ (up to 180 MeV)
Detector | lead preshower + silicon pixel detector
Signal | backscattered γ ~ 20kHz/mA/W
Background | bremsstruhlung γ ~ 1kHz/mA