## Slide 1
From HIAF to EicC
a facility under construction and its future
Jiancheng Yang and Lijun Mao
on behalf of HIAF design group at IMP CAS
2025/09/26, Qingdao

## Slide 2
Scientific motivation
Introduction of HIAF
Challenges and key technologies of HIAF accelerators
From HIAF to EicC: collision, polarization and cooling
Conclusion
Outline

## Slide 3
Scientific motivation
Introduction of HIAF
Challenges and key technologies of HIAF accelerators
From HIAF to EicC: collision, polarization and cooling
Conclusion
Outline

## Slide 4
Scientific Motivation
Particle accelerators are devices that speed up the particles that make up all matter in the universe and collide them together or into a target. This allows scientists to study those particles and the forces that shape them.
——DOE explains
Gravitational force
Electromagnetic force
Strong force
Galaxy ~1021m | Solar ~109m | Neutron star ~104m | Crystal ~10-8m | Atom 10-10m | Atomic nucleus 10-15 - 14 m | nucleon（10-15m） | 
 |  |  |  |  |  | Quark | Gluon
High intensity HI beams
RIBs ~1.5-2 GeV/u
Relative. HI beams ~100 GeV/u
High Energy
High Intensity

## Slide 5
Scientific Motivation
More than 30 facilities are in operation in the world, with the energy range from MeV/u to TeV/u

## Slide 6
Scientific Motivation
Hypothetical island of stability
Science,
125 Top Questions
Energy frontier or Intensity frontier, that is the question
How to explore the limit of nuclear existence?

## Slide 7
Heavy ion research facility at Lanzhou (HIRFL)
Phys. Rev. C 100, 051203(R) (2019)
Phys. Rev. C 99, 064303 (2019)
Chin. Phys. C 39, 104001 (2015)
Phys. Rev. Lett. 109, 102501 (2012)
Astrophys. J. Lett., 766, L8 (2013)
Phys. Lett. B, 735, 327 (2014)
Phys. Rev. Lett. 117, 182503 (2016)
Phys. Lett. B, 767, 20 (2017)
Phys. Rev. C 98, 014319 (2018)
Phys. Rev. C, 102, 054311 (2020)
Phys. Rev. C 98, 014315 (2018)
94mRu
Phys. Lett. B 781, 358 (2018)
First measured in CSR
Accuracy improved in CSR
Stable nuclei
Phys. Rev. C 96, 031303 (R) (2017)
Phys. Rev. Lett. 106, 112501 (2011)
Ions | Energy (MeV/u) | Current (ppp)
238U74+ | 500 | ~108
78Kr26+ | 500 | ~109
12C6+ | 1000 | ~1010
Scientific Motivation

## Slide 8
94mRu
Precise mass measurement spectrometry of short-lived nuclides
Too many isotopes can not be produced, mainly because of very small cross-section
A high intensity heavy ion beam accelerator facility is needed
HIAF (High Intensity heavy-ion Accelerator Facility)
---proposed in 2011
---approved in 2015
---construction from 2018
---beam commissioning in 2025
Scientific Motivation

## Slide 9
Scientific motivation
Introduction of HIAF
Challenges and key technologies of HIAF accelerators
From HIAF to EicC: collision, polarization and cooling
Conclusion
Outline

## Slide 10
HIAF introduction
Budget ~3 billion CNY (including civil construction), start from Dec. 2018, installation finished in Sept. 2025, located in Huizhou.

## Slide 11
HIAF introduction
Budget ~3 billion CNY (including civil construction), start from Dec. 2018, installation finished in Sept. 2025, located in Huizhou.
December. 2018
September. 2025

## Slide 12
HIAF introduction
HIAF = 4th SECR + superconducting Linac + Fast ramping rate synchrotron+ Terminals
BRing
iLinac:
Superconducting linac
Length:100 m
Energy: 17-22 MeV/u(U35+-45+)
SRing:
Spectrometer ring
Circumference: 273m
Rigidity: 13-15 Tm
Electron/Stochastic cooling
Two TOF detectors
Four operation modes
L: 180m, Bρ: 25 Tm
Fast cycle ring
Circumference: 570 m
Rigidity: 34 Tm
Large acceptance (250/120)
Two planes painting injection
Fast ramping rate（3-10Hz）
HFRS: Radioactive beam line
SECR:
Superconducting
ECR source
Low energy nuclear structure terminal
High energy experimental terminal
High energy fragment separator HFRS
High precision spectrometer ring SRing
Electron ion recombination terminal
Radioactive ion beam physics terminal
1
2
3
4
5
6

## Slide 13
HIAF beam parameters: the highest heavy ion bunches in the world
 | SECR | iLinac | BRing | HFRS | SRing | FAIR
Length / circumference (m) | --- | 114 | 569 | 192 | 277 | 1080
Final energy of U (MeV/u) | 0.014 (U35+) | 17 (U35+) | 835 (U35+) | 800 (U92+) | 800 (U92+) | 2700 (U28+)
Max. magnetic rigidity (Tm) | --- | --- | 34 | 25 | 15 | 100
Max. beam intensity of U | 50 pμA (U35+) | 28 pμA (U35+) | 11011ppp (U35+) | ------- | (2~4)1011ppp (U92+) | 41011ppp (U28+)
Operation mode | DC | CW or pulse | fast ramping (12T/s, 3Hz) | Momentum-resolution 1100 | DC, deceleration | 0.5
HIAF introduction

## Slide 14
HIAF introduction
0.1 MJ
1 MJ
Total energy per pulse
HIAF
the average beam power is not competitive, the stopping power in materials is enough for high energy intensity physics.

## Slide 15
HIAF introduction

## Slide 16
Scientific motivation
Introduction of HIAF
Challenges and key technologies of HIAF accelerators
From HIAF to EicC: collision, polarization and cooling
Conclusion
Outline

## Slide 17
Challenges and key technologies
4th SECR: state of the art ECRIS
The goal of the stored particle number in HIAF needs a powerful ion source
1 emA U35+ is required
---L. Sun, ICIS’23
45GHz

## Slide 18
4th SECR: state of the art ECRIS
The goal of the stored particle number in HIAF needs a powerful ion source
1 emA U35+ is required
---L. Sun, ICIS’23
45GHz
1.016emA O6+
Challenges and key technologies

## Slide 19
Superconducting linac: CW and pulsed modes
3HB+RFQ
MEBT
QWR007
HWR015
To BRing with 3 Hz pulsed beam
To low energy terminal with CW beam
QWR 007
HWR 015
RFQ in tunnel
Cavities and Cryomodule
Challenges and key technologies

## Slide 20
RFQ entrance：0.23 π.mm.mrad
Primary commissioning of ESR and RFQ
Ion | Current | Pulse width | Energy | Trans. effy | Accel. effy
16O6+ | 1 emA | 1ms@1Hz | 12.86 MeV | 70.9% | 60.6%
84Kr19+ | 115 eμA | 1ms@1Hz | - | 94.6% | 86.4%
209Bi31+ | 52 eμA | 1ms@1Hz | 169.4 MeV | 93.0% | -
1 emA 16O6+ beam has been obtained from RFQ, Kr and Bi have been accelerated successfully
Efficiency as well as stabilities have to study in detail
RFQ entrance：0.07 π.mm.mrad
Commissioning results
Challenges and key technologies

## Slide 21
Booster Ring (BRing): Fast ramping rate synchrotron
Working point (oscillation frequency) for each particle is different
Beam loss due to resonance or dynamic vacuum effect
Fast ramping acceleration is a possible way to avoid the beam loss
Very high current ramping rate up to 38 kA/s for dipole PS
High acceleration voltage up to 240kV/turn
Thin wall vacuum chamber to avoid distortion with eddy current
0.6T/s @ HIRFL
10T/s @ SIS 18
12T/s @ BRing
Challenges and key technologies

## Slide 22
Fast ramping rate full energy storage power supply for dipoles and quadrupoles
Requirement of magnet power converters featured by fast ramping rate：12T/s, ±38000A/s,
the peak power reaches 230MW totally at full load
Energy capacitor is used to store energy during the falling, and provide the energy for next fast ramping
Challenges and key technologies
Power (MVA) | Conventional | Energy storage
BRing bendng magnet | 180 | 15
BRing quadruple magnet | 50 | 6
Total of BRing | 250 | 41
Total of HIAF | 297 | 88

## Slide 23
Magnetic ally core loaded RF system
To satisfy fast acceleration, the voltage for total RF system should be 240 kV
acceleration
Gradient of traditional ferrite is only ~10kV/m, long dispersion-free space is needed, challenges for beam optical design
Facilities | Voltage (kV) | Length (m) | Gradient (kV/m)
JPARC-RCS | 41 | 1.78 | 23
JPARC-MR | 46.7 | 1.78 | 26.2
SIS18 | 50 | 2 | 25
HIAF-BRing | 70 | 2 | 35
Amp. Error < ±1%
Cavities in tunnel
Challenges and key technologies

## Slide 24
Titanium alloy-lined thin-walled vacuum chamber
Vacuum system for HIMAC in 1993
Stainless steel-0.3mm
Rib-15mm,one side
Problem: fast ramping of the magnets induces eddy currents:
The chamber walls are heated
Generation of additional harmonics in field
Solution from GSI
Vacuum better than 710-12mbar
Rings inside @ IMP
Challenges and key technologies

## Slide 25
Scientific motivation
Introduction of HIAF
Challenges and key technologies of HIAF accelerators
From HIAF to EicC: collision, polarization and cooling
Conclusion
Outline

## Slide 26
EicC motivation
Rutherford experiment
5.3 MeV
Proton, neutron not discovered yet
Experimentally… we need to determine each of the above contributions

## Slide 27
From fixed target to collider
EicC motivation
---Y.Zhang, Jlab, EIC leture
Improve the energy, luminosity and polarization
Luminosity=current
Resolution=energy
unpolarized
polarized
Spin

## Slide 28
Electron cooler and electron target
EicC motivation
EicC
HIAF-U
Collider ring ~1149.07 m
电子对撞环eRing ~ 1151.20 m
Electron ring ~287.80 m
2.8 GeV ~ 5 GeV
BRing_N ~569.10 m
BRing_S ~ 574.54 m
Proton energy up to 24.85 GeV
eLinac
HIAF
---Max Klein, University of Liverpool，2014
EicC covers the kinematic region between JLab experiments and EIC@BNL
EicC focuses on moderate x and sea-quark region

## Slide 29
Electron cooler and electron target
EicC motivation
EicC
HIAF-U
Collider ring ~1149.07 m
电子对撞环eRing ~ 1151.20 m
Electron ring ~287.80 m
2.8 GeV ~ 5 GeV
BRing_N ~569.10 m
BRing_S ~ 574.54 m
Proton energy up to 24.85 GeV
eLinac
HIAF
Phase 1: HIAF for nuclear physics
Phase 2: HIAF upgrade for applied science
Phase 3: EiccC
HIAF
Parameter | electron | proton
Circumference (m) | 1151.20 | 1149.81
Kinetic energy (GeV) | 3.5 | 19.08
CM energy (GeV) | 16.76 | 
fcollision (MHz) | 100 | 
Polarization | 80% | 70%
Bunch intensity (x1011) | 0.44 | 0.27
(nm·rad, rms) | 12.5/3.75 | 25/12.5
(cm) | 10/4 | 5/1.2
RMS divergence (mrad) | - | 0.7/1.0
Bunch length (cm, rms) | 0.75 | 8
Crossing angle (mrad) | 50 | 
Hourglass | 0.52 | 
Luminosity (cm-2s-1) | 1.13 × 1033 | 
Parameter | electron | proton
Circumference (m) | 1151.20 | 1149.81
Kinetic energy (GeV) | 3.5 | 19.08
CM energy (GeV) | 16.76 | 
fcollision (MHz) | 100 | 
Polarization | 80% | 70%
Bunch intensity (x1011) | 0.44 | 0.27
 | 12.5/3.75 | 25/12.5
 | 10/4 | 5/1.2
RMS divergence (mrad) | - | 0.7/1.0
Bunch length (cm, rms) | 0.75 | 8
Crossing angle (mrad) | 50 | 
Hourglass | 0.52 | 
Luminosity (cm-2s-1) | 1.13 × 1033 | 

## Slide 30
High luminosity and quasi-full-acceptance
Collision
50 mrad
X
X’
High luminosity mode: large particle number, small betatron function, peak luminosity up to
Quasi-full-acceptance mode: large particle number, small betatron function, peak luminosity up to

## Slide 31
Rapid cycling operation mode
Higher integral luminosity
the collision bunches are replaced online and quickly enough, much higher peak and integral luminosity is feasible
Injection line
DUMP
Beam dump line
Collision ring
Kicker
Swap-out injection scheme
Rapid-cycling booster
9 s or 12 min (multi-EC)
Replace all in minutes or seconds
Collision

## Slide 32
Polarization
Constant-field solenoid Siberian snake
A constant field solenoid Siberian snake has been designed in the BRing-N
The required magnetic field ramp rate for a conventional constant-strength solenoid Siberian snake is 29 T/s, to control the depolarization loss below 10%;
The spin tune gap generated by a constant-field solenoid Siberian snake is sufficient to avoid the vertical tune (red line), which will significantly reduce hardware challenges;
Mingxiang Li, et al., PRAB, 28, 094002 (2025)

## Slide 33
Beam cooling
Beam cooling can be used for accumulation, improving beam quality and compensating the emittance growth.
Acc. ~ 0.1 s
E.C. ~ 120 s
6.8×1012 ppp
RMS ~
12/6 π mm·mrad
3 injections
2.03×1013 ppp
RMS ~ 200/100 π nm·rad
To replace all collision bunches ~ 12 mins
1 bunch
192 bunches
CW
9.3 GeV
Acc. ~ 4 s
2 injections, 384 bunches
1.05×1011 ppb
4.05×1013 ppp
RMS ~ 100/50 π nm·rad
Proton beams as an example!
2 GeV

## Slide 34
Beam cooling
lower energies, better cooling
 | E-cooling
energy（keV） | 450
current（A） | 2.0
Magnetized DC electron cooling can be used in BRing-N for beam accumulation.

## Slide 35
Beam cooling
Relativistic electron cooling will be used in collider ring for compensation
electron
E-gun
ion
ERL
Dump
Items | Value
energy | >11 MeV/u
charge/bunch | >1 nC
bunch length | ~ 4 cm
average current | >100 mA

## Slide 36
Scientific motivation
Introduction of HIAF
Challenges and key technologies of HIAF accelerators
From HIAF to EicC: luminosity, polarization and cooling
Conclusion
Outline

## Slide 37
Conclusion
As an injector of EicC, the HIAF accelerator complex (phase 1) has been installed completely
The upgrade project of HIAF will focus on the improvement of energies and intensities, in order to satisfy the requirement of EicC
The beam dynamics and technical challenges related to collision, polarization and beam cooling should be studied and solved in coming years

## Slide 38
Thanks for your attention!