## Slide 1: ECAL Digitization Overview
2023/05/17
Jiaxuan Wang

## Slide 2: Digitization
Flow chart
File : 40GeV e-
  Test beam data
  MC 40GeV e-
    Beam size : selected from energy gravity center distribution
    Mixed with 2.5% pion
Digitization format
  Same with test beam data

## Slide 3: Photon produce
Photon production
  Photon number
    = / 0.305 MeV
    p.e. = / light yield(p.e./MIP)
      SiPM gain (ADC/p.e.)
      MIP MPV (ADC/MIP)
    photon = p.e./PDE
  Poisson smear
  Non-uniformity of light output(~0.042)
SiPM
ADC conversion
yazhou

## Slide 4: Digitization : photon produce
The physics process during photon produce hardly affect the energy and hitNo
10K 40GeV electron events
Event cut
Hit cut : dead channel cut, 0.8 MIP cut

## Slide 5: SiPM pixel saturation
Hamamatsu SiPM S12571-010P, S12571-015P
  10000, 4489 pixels respectively
  ~ 8 , 22 p.e./MIP
SiPM saturation model
  100*100 ，67*67 pixel placement
  Uniform sampling a pixel from pixel array
  Binomial sampling for PDE
  IF NOT avalanche, then let it avalanche
  Get total fired pixel number
  Formula matches the SiPM saturation model very well

## Slide 6: Digitization : SiPM pixel saturation
Total deposited energy decrease after introducing saturation effect
HitNo also decreases slightly

## Slide 7: Digitization : SiPM pixel saturation
Get digitization file with SiPM saturation
Calibrate the digitization file and get hit energy

## Slide 8: SiPM Crosstalk
Hamamatsu SiPM S12571-010P, S12571-015P
  Optical crosstalk may not be ignored
  PCT = (N2p.e. + N3p.e. + N4p.e. + ...)/(N1p.e. + N2p.e. + N3p.e. + ...)
Crosstalk Model
  100*100 ，67*67 pixel placement
  Uniform sampling a neighboring pixel from eight directions
  Set PCT as probability of optical crosstalk occurs in one of neighboring pixel

## Slide 9: Crosstalk model : Scan crosstalk probability
10um SiPM
10um SiPM
P_ct : probability of crosstalk between adjacent pixels
P_tot : probability of crosstalk calculated by PCT = (N2p.e. + N3p.e. + N4p.e. + ...)/(N1p.e. + N2p.e. + N3p.e. + ...)
P_tot is slightly less than P_ct
  15um ~2.2%
  10um ~1.5%

## Slide 10: Crosstalk model : comparison
15um SiPM
15um SiPM
10um SiPM
Formula match SiPM saturation very well
Crosstalk would increase the n_fired
The discrepancy between with/without crosstalk model will decrease

## Slide 11: Digitization: crosstalk model
Saturation
Saturation
Energy mean value increases by 8%

## Slide 12: Digitization : ADC
ADC && gaussian smear
  ADC Mean = * SiPM Gain
  ADC Sigma = 3 * sqrt()?
High-low gain mode ADC
Pedestal fluctuation
High-low gain saturation
  High gain saturation: high adc > switch point , let high adc =4000
  Low gain saturation : low adc > 3000, let low adc = 3000

## Slide 13: Digitization : ADC
The spectrum of hit energy becomes lower and width due to ADC smear

## Slide 14: Summary && prospect
Digitization process finished and verified
Energy mean value could be explained by the digitization, energy sigma still unknown
HitNo mean value is still large than data
Muon MC Digitization check
  Reconstruct MIP spectrum

## Slide 15: Backup
ADC
Photon produce
SiPM
Model
ADC
Convert