## Slide 1: Beam Tests of the CEPC AHCAL Prototype
Hongbin Diao
State Key Laboratory of Particle Detection and Electronics
University of Science and Technology of China

## Slide 2: Motivation
Circular Electron Positron Collider (CEPC)
  Ecm  240 GeV (higgs mode)
  luminosity ~ 8.31034 cm-2s-1 (higgs mode)
  challenges: jet energy resolution <
Particle Flow Algorithm (PFA)
  High granularity
  Good track finding
  Good energy resolution

## Slide 3: AHCAL Prototype
Total layers | 40
Sensitive area | 72cm*72cm
Granularity | 4cm*4cm*0.3cm
Total channels | 12960
NIL | 4.6
Energy Resolution | <60%@ 1 GeV
Weight | 5.0T
AHCAL
Plastic
Glass
an Analogue readout Hadronic Calorimeter prototype has been developed

## Slide 4: Beam Tests
3 beam tests have been done at CERN
  muon position scan(100GeV/c)
  pion (1-120GeV/c)
  electron (1-120GeV/c)
2023 SPS H2
2022 SPS H8
2023 PS T9

## Slide 5: Outline
Parameters Calibration
Pedestal
High-low ratio
MIP
Single PhotoElectron
Non-uniform of Scintillator
SiPM response
Photon Flucturation
Electronic Flucturation
Event Selection
Energy Reconstruction
Simulation & Digitization
Energy Reconstruction

## Slide 6: Outline
Parameters Calibration
Pedestal
High-low ratio
MIP
Single PhotoElectron
Non-uniform of Scintillator
SiPM response
Photon Flucturation
Electronic Flucturation
Event Selection
Energy Reconstruction
Simulation & Digitization
Energy Reconstruction

## Slide 7: Pedestal Calibration
the mean of electronic offset is pedestal, its width is noise level
normally(HitTag=0), pedestal have multiple peaks due to crosstalk
use force-trigger-mode now to prevent this problem
hittag=0 mode
force trigger mode

## Slide 8: High-Lowgain Calibration
SPIROC2E chip has two gain modes to cover wider dynamic range
using beam test data, calibrate high-lowgain ratio
set fit range as (200,max highgain-500)
fit range
200
max-500
pi-
e-

## Slide 9: MIP Calibration
MIP is the key to reconstruct energy
MPV value is obtained by fitting 100GeV/c muon
need temperature correct
MIP
noise
MIP event

## Slide 10: SPE Calibration
SiPM is a photon-counting device using multiple APD pixels operating in Geiger mode
Its reponse is not linear strictly
to correct this effective, single photoelectron (SPE) calibration is necessary
muon data(MIP) are fitted with multi-gaussian to calculate SiPM gain for each channel

## Slide 11: Outline
Parameters Calibration
Pedestal
High-low ratio
MIP
Single PhotoElectron
Non-uniform of Scintillator
SiPM response
Photon Flucturation
Electronic Flucturation
Event Selection
Energy Reconstruction
Simulation & Digitization
Energy Reconstruction

## Slide 12: Digitization I
Scintillator
  energy to photon (poisson sampling)
  4.8% gaussian smear from non-uniformity of scintillator
  photon electron conversion (binomial sampling)
SiPM
scintillator
light yield uniformity in one scintillator

## Slide 13: Digitization II
SiPM response
  SiPM saturation and flacturation
  SiPM gain smear
fired pixels to data format ADC
data
MC digi

## Slide 14: Outline
Parameters Calibration
Pedestal
High-low ratio
MIP
Single PhotoElectron
Non-uniform of Scintillator
SiPM response
Photon Flucturation
Electronic Flucturation
Event Selection
Energy Reconstruction
Simulation & Digitization
Energy Reconstruction

## Slide 15: Energy Reconstruction
Focus on electron response mainly
Beamtest data need to be selected to improve purity
  hit number
  shower start position
  ...
e-
muon
energy deposite in sensitive volume of 20GeV e-

## Slide 16: Energy Linearity and Resolution
preliminary results show, at low energy level, the energy linearity and resolution is well
preliminary
preliminary

## Slide 17: Summary and Plan
Summary:
  based on the beam tests of AHCAL prototype
  carry out full-process analysis on high energy particle
    calibrate basic parameters
    reconstruct energy of electron
    optimize MC simulation and digitization
  preliminary results show, at low energy level, the aggrement between beamtest and MC is well
Plan:
  high energy electron and pion analysis
  using the high granularity, carry out research on particle identification and PFA method, lay the foundation for the deep study of CEPC
Thanks!

## Slide 18: Backup

## Slide 19: Motivation
PFA make use of the optimal detector subsystem to determine the energy/momentum of each particle in a jet.
photons (~30%)
neutral hadron(~10%)
ECAL
HCAL
charged particles (~60%)
Tracker
distinguish among energy deposits of individual particles
require
High, three-dimensional spatial granularity
require

## Slide 20: Calibration

## Slide 21: Simulation Based on Geant4
code is based on baohua(ihep colleague)
incident particles: electron, pion, muon
particle flow size: 20mm
Scintillator: polystyrene: 3 mm
Cu
PCB: FR4
gap: air
Absorber: steel: 18 mm
Absorber: steel: 2 mm
gap: air, 1.5m
front trigger detector: polystyrene
incident particle
geometry construct

## Slide 22: Digitization
4.8%(1.836/38.37) gassian smear caused by non-uniformity of light yield
energy to photon (poisson distribution)
photon to photoelectron (binomial distribution)
fill
True energy
photon
photoelectron
light yield smear
poisson sampling
binomial sampling

## Slide 23: Digitization SiPM Model
SiPM reponse is not linear strictly
4. SiPM response
  gaussian smear with sigma

## Slide 24: Digitization
5. phoelectron to ADC (times SPE)
6. gaussian smear (sigma of SPE peak )
7. ADC to highgain and lowgain using high-lowgain
ratio and pedestal (include pedestal fluctuation)
True energy
photon
photoelectron
ADC
high/lowgain
light output smear
poisson sampling
binomial sampling
SiPM reponse model
SPE smear
beamtest format

## Slide 25: SPE and mean of SiPM

## Slide 26: Event Select Criterion
set threshold as 0.5 MIP
hit number > f(beam energy)
shower start (the first layer that have >=5 hit) < 5
  the energy ratio of the last 5 layer < 5% to remove MIP
  find energy center of each layer and let the max distence of them < 200mm
  energy center of the first 30 layers are in the central chip, that is in (120,120)mm
  energy center of layer4 to layer6 are in (15,25)mm
  calculate energy in 5×5 cells around energy center in the first 30 layers

## Slide 27: Hitno and Hit layer
  f(x)=372.285*(1-exp(0.0064584*x))