## Slide 1
CEPC Detector Magnet
Stray field and yoke
Feipeng NING
2024.05
中国科学院高能物理研究所
Institute of High Energy Physics, CAS

## Slide 2: Outline
Latest size of the Magnet;
Yoke and stray field；
The magnetic field distribution required by the software.
Notes: Two changes: first, add yoke to reduce the range of stray field; second, the size of HCal increase, so size of the solenoid and the yoke increase accordingly.

## Slide 3: 1. Latest size of the magnet
Inner diameter | 7070 mm
Thickness | 700 mm
Outer diameter | 8470 mm
Length | 9050 mm

## Slide 4: 1. Latest size of the magnet
The gap between the barrel and the end: From 250 mm to 60 mm
250 mm
60 mm

## Slide 5: 2. Yoke and stray field
Yoke size：
 | V2.1 | V2.2 | V2.3 | V2.4
Barrel yoke (ton) | 2480 | 2590 | 2340 | 2080
Each End yoke (ton) | 839 | 879 | 771 | 669
Total Yoke (ton) | 4158 | 4348 | 3882 | 3418
Diameter(m) & length (m) | 11.29&12.07 | 11.29&12.07 | 11.09&11.87 | 10.89&11.67
Notes: Two changes: first, add yoke to reduce the range of stray field; second, the size of HCal increase, so size of the solenoid and the yoke increase accordingly.

## Slide 6: 2. Yoke and stray field
Magnet V2.3：
Yoke mass (ton) | 3882
Thickness of the yoke (m) | 1.3
Diameter(m) & length (m) | 11.09*11.87
Inner diameter | 7070 mm
Thickness | 700 mm
Outer diameter | 8470 mm
Length | 9050 mm
Inner diameter | 7300 mm
Operating current | 16717.5 A
Cable length | 33 km
Inductance | 11 H
Stored Energy | 1.54 GJ
Total mass | 220 tons
Magnet parameters:
Coil parameters:
Notes: Two changes: first, add yoke to reduce the range of stray field; second, the size of HCal increase, so size of the solenoid and the yoke increase accordingly.

## Slide 7: 50 Gauss and 100 Gauss distribution:
2. Yoke and stray field
50 Gauss and 100 Gauss distribution
Stray field |  | V2.1 | V2.2 | V2.3 | V2.4
50 Gs | R direction | 23.3 m | 23.0 m | 23.6 m | 24.3 m
 | Z direction | 29.3 m | 28.9m | 29.8 m | 30.6 m
100 Gs | R direction | 18.4 m | 18.2 m | 18.7 m | 19.2 m
 | Z direction | 23.2 m | 22.9 m | 23.6 m | 24.3 m
100 Gauss
50 Gauss

## Slide 8: 2. Stray field at the booster ring
The detector stray field can reach the booster and influences the beam dynamics of booster.
The current study shows that the correction to the detector stray field seems possible at low field (less than 50 gauss) level by orbit correction.
Dou Wang, Yuan Zhang, Daheng Ji, Feipeng Ning, Impacts of Detector Stray Field on Booster, AP NOTE, ACC-AP-NOTE-2020-001, Receive Date (October 15, 2020)
25m
V2.3
From 42.6 Gs to 30 Gs

## Slide 9: 2. Stray field at the booster ring
All versions meet the requirement of less than 50 Gauss
 | V2.1 | V2.2 | V2.3 | V2.4
Stray field (Gauss) | 40.7 | 39.0 | 42.6 | 46.2
Total Yoke (ton) | 4158 | 4348 | 3882 | 3418
V2.1
V2.2
V2.3
V2.4

## Slide 10
2. Yoke and stray field
At present B(1m) 0.16~0.18 T. Bigger than 0.12 T (CMS required)
1 m

## Slide 11
2. Yoke and stray field
Magnetic field at 1 m away on barrel yoke.
V2.2
V2.3
V2.4
V2.1
 | B (T)
V2.1 | 0.147~0.155
V2.2 | 0.14~0.146
V2.3 | 0.16~0.173
V2.4 | 0.18~0.2
Bigger than 0.12 T (CMS required)

## Slide 12
2. Yoke and stray field
Magnetic field saturation region

## Slide 13: 3. The magnetic field distribution required by the software.
Diameter and length: 3660mm*5860mm
1830
2930
软件部分最关注的是磁场的非线性，就是重建时两点之间磁场是怎样的，平均值和实际值之间的差值是多大，这个值不是梯度。
Different data acquisition intervals（10cm, 5cm, 1cm）
This work is currently in progress.
Magnetic field mapping is important.

## Slide 14
The size of superconducting magnet is confirmed.
The area of stray field is related to the design of the yoke.
The work of providing magnetic field distribution for the software part is still ongoing.
The mechanical design of the magnet has begun.
Conclusion