## Slide 1
Z-pole event pileup estimation
Suen Hou
suen@sinica.edu.tw
2024/04/30
1 Bhabha events on LYSO cells (3x3mm2)
pile-up rate ~1x10-4 at low-θ edge
2 Z lineshape Z → qq
pile-up rate (4π coverage) ~1x10-3
Resolve BCID, inner ECAL layers,
SiPM do High-gain + 3-bit (8 levels) comparator

## Slide 2: Cross-section
Z-lineshape
e+e− → Z → qq‾
Luminosity by Bhabha
e+e− → e+e−
σ = 41 nb
hep-ph/0411321 NPB 716 (2005) 280
Bhabha
at θ= 5o

## Slide 3: BHLUMI X-section, racetrack @CEPC
LAB ONE e+ or e− detected |  | LAB both e+, e− detected | 
θ>15 mRad | θ>15mR & ¦y¦>15mm | θ>15 mRad | θ>15mR & ¦y¦>15mm
395.3 | 255.9 | 257.8 | 245.9
θ>25 mRad | θ>25mR & ¦y¦>25mm | θ>25 mRad | θ>15mR & ¦y¦>25mm
133.5 nb | 81.8 nb | 85.4 nb | 78.0 nb
θ>30 mRad | θ>30mR & ¦y¦>30mm | θ>30 mRad | θ>30mR & ¦y¦>30mm
87.2 | 51.8 | 54.9 | 49.1
Acceptance @z=1m r>25 mm, |y|>25 mm
CDR
racetrack
e+, e− back-to-back
Symmetric to
out-going pipe center
at Z = 1000 mm
LAB frame
e+, e− detected
@ Z=1000 mm

## Slide 4
Bhabha smeared by
Multiple scattering
Detector resolution
OFFSET on the mean
Causing δN/N error
M.S. non-liner !!
dominant systematic
Si-strip detector
fiducial edge = central line between two strips
Multi.Scattering  events flow in/out Fiducial
+ geo error  event counting error
Systematics against δL/L ~10-4
δL/L ~ 2 δθ/θmin
δL/L < 10-4 for θmin= 20 mRad
 δθ = 1μRad dr=1μm @ z=1m
δN/N ~10-4
in fiducial θ window
1. Det. Position offset
Multi. Scattering, det. Resolution
B-field helix
3. Rad. Bhabha, preshower offset
δN/N ~10-4

## Slide 5: Bhabha pile-up rate @High-Lumi Z
High-Lumi Z (2021 design) Lmax/IP = 115 x 1034/cm2s
Bhabha both e+, e− detected, X-sec = 246 nb
Event rate = (246x10-33) x (115 x 1034) /sec = 115 kHz
Event rate / 25 ns bunch crossing = 0.003 events /b.c.
Pile-up: next b.c., @adjacent cell in peak region
Pile-up Fraction = 0.018*6cells/2sides = 0.054
Pile-up event rate = 0.003*0.054 = 1.6 x 10-4 in 3x3 mm2 cells
50 GeV e- shower in 3x3 mm2 cells
c.f. LEP
L= 1x1032
X-sec= 100nb
Rate= 10 Hz
25 ns
LYSO signal overlap
event fraction /(cell of 3x3mm2)
maximum at beampipe edge = 0.018

## Slide 6: Z → qq‾ pile-up rate @High-Lumi Z
High-Lumi Z (2021 design) Lmax/IP = 115 x 1034/cm2s
Z → qq‾ , X-sec = 41 nb
Event rate = (41x10-33) x (115 x 1034) /sec = 47 kHz
bunch cross = 40 MHz
Event rate / 25 ns bunch crossing = 0.001 events /b.c.
next b.c. having a Z → qq‾
Pile-up rate 4π coverage ~ 1x 10-3
if BCID not identified
pileup of two 2-jets  4-jet
rare decay precision ~1x 10-3
25 ns

## Slide 7: SiPM w. Comparator in MIP layers
25 ns
SiPM output
ECAL front 2Xo layers, LumiCal 2Xo decks
High-gain signal (ADC of multi BC)
3-bit (8 levels) comparator per BC