## Slide 1
CEPC Detector Magnet V0
Feipeng NING
2024.05
中国科学院高能物理研究所
Institute of High Energy Physics, CAS

## Slide 2: 1. The size of magnet
Inner diameter | 7070 mm
Thickness | 700 mm
Outer diameter | 8470 mm
Length | 9050 mm

## Slide 3: Detect Magnet
Barrel yoke (ton) | 2300
Each End yoke (ton) | 754
Total Yoke (ton) | 3808
Diameter(m) & length (m) | 10.97&11.75
The gap between each layer of yoke is 40 mm.
Yoke parameters：
Inner diameter | 7300 mm
Operating current | 16702 A
Cable length | 33 km
Inductance | 11 H
Stored Energy | 1.54 GJ
Total mass | 220 tons
Coil parameters:
Notes: Two changes: first, add yoke to reduce the range of stray field; second, the size of HCal increase, so size of the solenoid and the yoke increase accordingly.

## Slide 4: 50 Gauss and 100 Gauss distribution:
stray field
50 Gauss and 100 Gauss distribution
Stray field |  | 
50 Gs | R direction | 23.6m
 | Z direction | 29.8m
100 Gs | R direction | 18.7m
 | Z direction | 23.6m
100 Gauss
50 Gauss

## Slide 5: Stray field at the booster ring
25m
 | V0
Stray field (Gauss) | 42.7
Total Yoke (ton) | 3808
From 42.7 Gs to 29.7 Gs
V0

## Slide 6
Yoke and stray field
Bigger than 0.12 T (CMS required)
1 m
 | B (T)
V0 | 0.166~0.184

## Slide 7
Conclusion