## Slide 1
CEPC MDI EDR progress - cryomodule design
Xiangzhen Zhang, Xiaochen Yang, Penghui Li,…
Cryogenics Group, Accelerator Research Center Institute of High Energy Physics(IHEP)
2024.06.27

## Slide 2: Content
Introduction
Cryogenic scheme of the cryostat
Structural design of the cryostat
Calculation and simulation
EDR superconducting anti-solenoid
MDI alignment
Summary and plan

## Slide 3
  Introduction
In CEPC, there are two combined-function Superconducting magnets in MDI
Each combined-function magnet includes double aperture high gradient quadrupole (Q1a, Q1b, Q2) and anti-solenoid, around each side of the IP point.
The cryostat is used to provide the cryogenic environment for SC magnets, which is below 5.0 K.
From Yingshun Zhu
ITEM | Q1a | Q1b | Q2 | Anti-solenoid
Central field gradient (T/m) | 142.3 | 85.4 | 96.7 | 
Cooling type | LHe | LHe | LHe | LHe
Operating current (A) | 780 | 650 | 770 | 1300
Magnetic storage energy (KJ) | 11.5 | 11 | 33.2 | 630
Cross section parameter (mm) | Φ40~61 | Φ52~78 | Φ62~88 | 100 sections
Magnet length (m) | 1.22 | 1.23 | 1.53 | 5.1
Net weight (Kg) | 25 | 32 | 43 | 302
Total weight of magnets (Kg) |  |  |  | 402

## Slide 4
  Introduction
Design and optimization of the structure.
Heat and mass transfer of the cryostat.
PI＆D of the cryogenic system.
Scheme of the current leads.
Some other problems.
From Yingshun Zhu
Insufficient or unfinished works for the cryostat

## Slide 5
Superconducting magnets are immersed in the helium tank for the low temperature.
One thermal shield is set for the heat interruption from the ambient temperature.
The shield is extended between the helium tank and the beam chamber.
The 4K cold mass is cooled by supercritical or subcooled helium, and the shield is by liquid nitrogen.
Cryogenic scheme of the cryostat
Cryostat scheme

## Slide 6
Conventional helium cooling scheme: Liquid helium is directly provided by helium refrigerator. The flow rate is limited by the refrigerator. Liquid helium can be subcooled or supercritical type.
Helium circulation cooling scheme: A closed helium circulation is established depending on a pump. The flow rate can be increased largely. The system will be complex.
Superfluid helium(HeⅡ): Perfect cooling uniformity; Stable pressure; Higher magnet current; Higher cost.
Cryogenic scheme of the cryostat
Cooling system

## Slide 7
1985mm
1915mm
2885mm
Q1a
Q1b
Q2
Anti-solenoid
Structural design of the cryostat
Support of SC magnet
The superconducting magnets Q1a,Q1b and Q2 are supported on the inner wall of the solenoid.
The anti-solenoid is supported by a ring on the inner wall of the helium tank.
Vacuum
Thermal shield
LHe tank
Support
Anti-solenoid
Q1a
Beam chamber
Notes: 标注尺寸

## Slide 8
Outer cylinder of helium tank
Fluid domain
inlet
outlet
Cooling flow: One-way in and out
Without considering the magnetic support structure:
Heat conduction of support is 13.68 W; Heat flux of thermal radiation is 0.1 W/m2;
Helium inlet flow is 3.0 bar@4.2 K.
Chart: Coil number of anti-solenoid
| 1 | 2 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
4.0 g/s | 4.39 | 4.71 | 16.6 | 11.95 | 10.07 | 13.438 | 12.49 | 10.25 | 9.04 | 8.59 | 6.8 | 5.34 | 4.86 | 4.74 | 4.52 | 4.56 | 4.69 | 4.84 | 4.78
6.0 g/s | 4.295 | 4.297 | 12.81 | 9.592 | 8.624 | 9.58 | 9.492 | 8.457 | 7.56 | 7.25 | 6.37 | 5.49 | 4.65 | 4.61 | 4.39 | 4.36 | 4.37 | 4.46 | 4.54
8.0 g/s | 4.29 | 4.29 | 7.26 | 8.39 | 8.02 | 11.46 | 11.12 | 9.14 | 7.63 | 6.45 | 5.53 | 4.82 | 4.47 | 4.38 | 4.32 | 4.3 | 4.31 | 4.32 | 4.38
12.0 g/s | 4.262 | 4.262 | 8.301 | 6.94 | 6.31 | 5.96 | 6.18 | 5.83 | 5.5 | 5.26 | 4.78 | 4.42 | 4.4 | 4.42 | 4.35 | 4.34 | 4.33 | 4.32 | 4.43
Calculation and simulation
Cooling of anti solenoid
Not feasible！

## Slide 9
Cooling flow: Outer single-layer flow channel ：
Chart: Coil number of anti-solenoid
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
2g/s | 4.9018 | 4.9282 | 4.9373 | 4.9266 | 4.926 | 4.9229 | 4.9462 | 4.9511 | 4.9833 | 4.9767 | 5.0021 | 4.9386 | 4.9673 | 4.9463 | 4.9375 | 4.9436 | 4.9458 | 4.9556 | 4.972 | 5.0009
4g/s | 4.6213 | 4.6405 | 4.6486 | 4.6389 | 4.6412 | 4.6358 | 4.6493 | 4.6539 | 4.6883 | 4.6817 | 4.7157 | 4.6507 | 4.7019 | 4.6544 | 4.649 | 4.6522 | 4.6551 | 4.6621 | 4.6685 | 4.6788
6g/s | 4.5924 | 4.6094 | 4.6143 | 4.6077 | 4.6109 | 4.603 | 4.6196 | 4.6153 | 4.6559 | 4.6486 | 4.7045 | 4.6507 | 4.6786 | 4.6373 | 4.6307 | 4.6476 | 4.645 | 4.6522 | 4.6507 | 4.6525
10g/s | 4.4571 | 4.471 | 4.4757 | 4.4682 | 4.47 | 4.4629 | 4.4767 | 4.4715 | 4.5003 | 4.4955 | 4.5597 | 4.5019 | 4.547 | 4.4848 | 4.4695 | 4.4848 | 4.4896 | 4.4946 | 4.4868 | 4.4709
Chart: Coil number of anti-solenoid
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
2g/s | 4.6856 | 4.6678 | 4.6984 | 4.7036 | 4.7072 | 4.711 | 4.714 | 4.7202 | 4.734 | 4.7332 | 4.758 | 4.7424 | 4.7473 | 4.7652 | 4.7707 | 4.7721 | 4.7678 | 4.7749 | 4.7837 | 4.7986
4g/s | 4.4286 | 4.4316 | 4.4506 | 4.4592 | 4.4631 | 4.4701 | 4.4665 | 4.4708 | 4.4883 | 4.4882 | 4.5134 | 4.4833 | 4.504 | 4.5127 | 4.5204 | 4.5222 | 4.5155 | 4.5194 | 4.5257 | 4.5321
6g/s | 4.4004 | 4.4041 | 4.4091 | 4.41 | 4.4199 | 4.4211 | 4.4254 | 4.4275 | 4.4478 | 4.4484 | 4.4884 | 4.4452 | 4.4681 | 4.4731 | 4.4827 | 4.4916 | 4.4834 | 4.4857 | 4.4869 | 4.4931
10g/s | 4.3302 | 4.3328 | 4.3358 | 4.3342 | 4.3412 | 4.338 | 4.3468 | 4.3456 | 4.3607 | 4.3566 | 4.3936 | 4.3545 | 4.3801 | 4.3734 | 4.375 | 4.385 | 4.3844 | 4.386 | 4.3807 | 4.3802
Chart: Helium flow channel（single-layer）
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 20
进出口压差Pa | 0.8413 | 3.3359 | 7.4465 | 13.2656 | 20.9472 | 29.6841 | 40.5507 | 53.136 | 82.7403
Temperature distribution of the outer cylinder of the helium tank: 3bar@4.2K 10g/s
Calculation and simulation
inlet
outlet
Cooling of anti solenoid

## Slide 10
Optimized helium channel
Quadrupole flow channel:
Anti-solenoid flow channel :
Inner and outer double flow channel design：
Minimum gap is 4mm
Minimum gap is 2mm
inlet
outlet
inlet
outlet
Calculation and simulation

## Slide 11
Comparison of single-layer and double-layers cooling channels ：
A double-layers flow channel is more effective for cooling superconducting magnets compared to a single-layer flow channel, especially when the helium flow rate is low ；
Some other advantages, including the heat management, quench recovery or magnet cooling time.
Chart: Coil number of anti-solenoid
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
2g/s Single flow channel design Anti-solenoid Peak temperature | 4.9018 | 4.9282 | 4.9373 | 4.9266 | 4.926 | 4.9229 | 4.9462 | 4.9511 | 4.9833 | 4.9767 | 5.0021 | 4.9386 | 4.9673 | 4.9463 | 4.9375 | 4.9436 | 4.9458 | 4.9556 | 4.972 | 5.0009
10g/s Single flow channel design Anti-solenoid Peak temperature | 4.4571 | 4.471 | 4.4757 | 4.4682 | 4.47 | 4.4629 | 4.4767 | 4.4715 | 4.5003 | 4.4955 | 4.5597 | 4.5019 | 4.547 | 4.4848 | 4.4695 | 4.4848 | 4.4896 | 4.4946 | 4.4868 | 4.4709
2g/s Double flow channel design Anti-solenoid Peak temperature | 4.6173 | 4.6526 | 4.6609 | 4.6415 | 4.6379 | 4.6348 | 4.663 | 4.6674 | 4.7316 | 4.7112 | 4.7102 | 4.6389 | 4.6693 | 4.6463 | 4.6367 | 4.6397 | 4.6417 | 4.6514 | 4.6704 | 4.7153
10g/s Double flow channel design Anti-solenoid Peak temperature | 4.441 | 4.4609 | 4.4646 | 4.4531 | 4.4536 | 4.4477 | 4.4703 | 4.4697 | 4.5207 | 4.5111 | 4.5565 | 4.497 | 4.5315 | 4.4571 | 4.4533 | 4.467 | 4.4697 | 4.4763 | 4.4689 | 4.4536
Calculation and simulation
inlet
outlet
Cooling of anti solenoid

## Slide 12
Calculation and simulation
Cooling of quadrupole coils
Helium flows into the inner channel and out from the outer channel.
Q1-A
Q1-B
Q2
Thermal radiation 0.2 W/m2
Thermal radiation 0.2 W/m2
Surface emissivity:
Thermal radiation 17.055 W/m2
Inlet helium state:
3.0bar@4.5K
(Supercritical helium)
Fluid pressure difference diagram (Inlet flow rate 10g/s)
Chart: Mass flow rate of helium at the inlet （g/s）
| 4 | 6 | 8 | 10 | 12 | 14 | 16
压差Pa | 8.2361 | 16.772 | 28.1237 | 41.8732 | 58.0346 | 76.5527 | 97.2631

## Slide 13
Calculation and simulation
X
Temperature distribution of helium fluid
Inlet flow rate 10g/s, 3.0bar@4.5K
x=3.500 m
x=1.400 m
x=0.060 m
x=1.250 m
x=2.500 m
Helium fluid is heated in the inner channel.
The temperature of the fluid in the inner channel varies greatly near Q1-A
Cooling of quadrupole coils

## Slide 14
Calculation and simulation
X
Temperature distribution inside the inner channel
Temperature distribution on the outer side of the inner channel
Inlet flow rate 10g/s, 3.0bar@4.5K
The temperature of 10g/s subcooled helium increases by about 0.04K, after passing through Q2 and Q1-B.
When subcooled helium flows through Q1-A, its temperature risesrapidly, with a gradually increasing temperature difference at the same X position.
Cooling of quadrupole coils

## Slide 15
Calculation and simulation
Chart: Mass flow rate （g/s）
| 4 | 6 | 8 | 10 | 12 | 14 | 16
Maximum temperature: inside the inner channel | 4.9649 | 4.8373 | 4.7427 | 4.6902 | 4.6637 | 4.6387 | 4.6216
Maximum temperature: Outer side of inner channel | 4.8161 | 4.7071 | 4.6345 | 4.5947 | 4.5741 | 4.5615 | 4.5527
Maximum temperature: inside the outer flow channel | 4.7557 | 4.6667 | 4.632 | 4.602 | 4.5826 | 4.5696 | 4.5602
The static thermal radiation of a quadrupole focusing magnet is constant.
The higher the flow rate, the lower the temperature of the Q1-A magnet.
The flow rate of subcooled helium is determined based on the temperature of the magnet.
Cooling of quadrupole coils

## Slide 16
Possible Improvement
Application cases of large flow forced flow cooling ---- supercritical helium cycle pump:
The electron-proton collider HERA at the electron synchrotron laboratory (DESY) in Hamburg, Germany, uses a 45g/s helium circulating pump. （DESY）
The Atlas-LHC at CERN in Geneva, Switzerland, uses two 600g/s helium circulation pumps and two 1.2Kg/s helium circulation pumps.
The Superconducting magnet Test Facility at the Atomic Energy Research Institute of Japan.
TOSKA at the Institute of Technical Physics at the Karlsruhe Research Center in Germany.
Refrigerator
SC Magnet
LHe
Conventional helium cooling mode
Refrigerator
SC Magnet
LHe
Helium circulation cooling mode
helium circulating pump
Calculation and simulation

## Slide 17
Supercooled LHe Circulation
A tank is used to control the pressure.
The flow rate can be improved largely.
Temperature distribution can be more uniform.
The system is complicated.
Calculation and simulation

## Slide 18
EDR superconducting anti-solenoid
In order to reduce the magnet size, energy and cost, the anti-solenoid is divided into more than 100 sections with different inner coil diameters.
The coil radius of anti-solenoid in quadrupole region is smaller than that in TDR. ( radius reduction about 10 to 15mm)
Magnetic field calculation and optimization is performed using axi-symmetric model in OPERA-2D.
The central field of the first section of the anti-solenoid is the strongest, with a peak field of 8.7T @ r=0, and 10.7T in coil.
Combined field
Combined field @z <1.9m
Combined field @z >1.9m
Combined field of Anti-solenoid and Detector solenoid is fine tuned.
The total integral solenoid field is almost zero.
The net solenoid field inside quadrupole magnet at each longitudinal position is smaller than 170 Gs.

## Slide 19
MDI alignment
MDI alignment
cryostat module pre-alignment
Installation and alignment
Position inspection of superconducting magnet
cryostat module position monitoring
Existing issues:
  How to measure the front position after the cryostat module is inserted into the detector?
  Optional methods:
    Permanently place several tracker targets at the front of the cryostat module, with large openings at both ends of the detector to allow the tracker to measure the targets inside from the outside.
    To use laser collimation, it is necessary to open a through hole.
    Installing sensors

## Slide 20: Summary
Design status of cryomodule:
The cryostat has been updated as the optimization of the SC magnets.
Supercritical/ Suncooled liquid helium is used as the cold source.
Double cooling channels of SC magnets can be used, if the mechanical space is allowed.
A supercooled LHe circulation is designed, which can increase the flow rate largely.
Works to be done:
Optimization of the cryostat;
Thermal and mechanical analysis; (quench protection, energy storage , supports )
Current lead and cryogenic system;
Measurement requirements; (temperature/pressure/BPM)
Initial consideration of processing and manufacturing technology;

## Slide 21
EDR plan
EDR plan for MDI SC cryostat:
2024:
Update the design of the cryomodule
Thermal and mechanical analysis of the structure
Optimization of heat and mass transfer of the helium
Design of current leads
2025:
PI＆D scheme determination
Assembly process design and alignment considerations
2026:
Machine-finishing technological design
Cryogenic performance test of critical component

## Slide 22
Thanks for your attention!