## Slide 1: CEPC vertex detector towards TDR
Zhijun Liang,
On behalf of CEPC vertex working group

## Slide 2: Towards TDR
Aim to have a draft of TDR by the end of 2024.
  First review meeting in July 2024.
  System level design, choose baseline technology
  Electronics, service and mechanics needs to be included
Major change from CDR to TDR
  Beam pipe diameter: 28mm (CDR)  20mm (TDR) (reduce 30%)
  Instant Luminosity per IP:
    Z pole: 32×1034 cm-2s-1 (CDR)  192 ×1034 cm-2s-1 (TDR, 50MW) (6 times increase)
    ZH: 5.6×1034 cm-2s-1 (CDR)  8.3 ×1034 cm-2s-1 (TDR) (~1.5 times increase)

## Slide 3: Discussion with TowerJazz China
2nd time Met with TowerJazz management team at IHEP
  Jianchun, Wei wei, Yiming, Yunpeng, Zhou Yang, Zhang Ying, Zhijun
Support 65nm and 180nm CIS and modified process
There is some threshold to use 65nm technology
  More order to 180nm CIS is needed
  Need clear R & D and production plan towards to 65nm technology
In one of Tuesday TDR meeting, together with Yifang, we decide to use 65nm CIS as our baseline for reference TDR
  For Low lumi Z: 40mW/cm2

## Slide 4: Data rate estimation
2D pair production background from Haoyu
  Pairs: /cefs/higgs/shihy/work/cepc_bkg/Results/Ref-TDR/20240312/Higgs/Pairs.root
Z pole (high lumi)
ZH runs
Rate( Hz/cm2)
Rate( Hz/cm2)

## Slide 5: Data rate estimation from Haoyu
df

## Slide 6: Vertex detector design status
Reminder of last CEPC day
  Compare vertex detector design from other experiments
Update today
  Overview other vertex detector design
  “Short barrel + endcap” layout will come later
Short barrel + endcap
Example of Long barrel layout

## Slide 7: Update on long barrel Cooling design (preliminary )
The thermal conduct to beam pipe is important
  Assuming beam pipe temperature is 16 Celsius
To bring down temperature, a potential solution to add thermal conductive glue
  Thermal glue to Increase thermal conductivity to beam pipe
  Beam pipe has active cooling
  Air speed ~2.3 m/s
Barrel layer | # of ladder | Max temperature (Celsius)
 |  | 40mW/cm2
Inner layer w/wo beam pipe Temperature | 8 | ~25°C(w thermal glue) / 49 (wo thermal glue)
Middle | 16 | 28°C
Outer | 25 | 30°C
Total heat generation of the VTX is 337W, assuming 40mW/cm2

## Slide 8: Long barrel vs short barrel
Long barrel has more material in layer 2 and layer 3
  6 metal layer in flexible PCB (Compared to 4 layer PCB in layer 1)
  More material in support structure
Short barrel is marginally better than Long barrel in central region
  But no solution for endcap region yet

## Slide 9: Summary
Long barrel option is converging
  Plan to put them into CEPCSW release
Issue : No enough manpower for “short barrel + endcap” solution
  At least need one dedicated engineer and one student for layout optimization
  Air flow simulation and cooling design

## Slide 10: Electronics
DCDC：电源管理芯片
  TAICHU功耗0.8W（1.8V*0.42A）
  单个DCDC最多为10个TAICHU提供电源，效率按85%计算
  DCDC功耗为0.8*10*15% = 1.2W
  如果最外层需要20个芯片则需要2个DCDC
  lpGBT和VTRX+需要其他种类电源（1.2V，2.5V），总体功耗不高，~1W，则DCDC功耗为0.15W
lpGBT：数据汇总芯片
  0.75W@10.24Gb/s
VTRX+：光电转化芯片
  1发1收：0.193W（RX：2.5V*0.05A，TX：2.5V*0.02A，core：1.2V*0.015A）
说明：1：图中仅展示ladder一端一面，底面及ladder另一端有同样的配置
2：lpGBT及VTRX+的参数为CERN对应芯片手册得到，CEPC最终参数可能有所不同。
1.2W
0.75W
0.193W
lpGBT :
9mmX9mm
VTRX+:
10mmX20mm
DCDC:
50mmX20mm
1.2W
0.15W
DCDC:
50mmX20mm

## Slide 11: Reminder of long barrel design
The drawings show the option that pre-assembled halves barrels mounted onto the beam pipe(dedicated tooling required)
The support ring can be either glued/bolted to or pre machined on the beam pipe related parts. (for the inner most layer bolting and machining are too difficult)
The VTX on the tentatively modified beam pipe components
More consideration - different constraint on two ends?
From Jinyu Fu

## Slide 12: Material budget for long barrel
Geometry implemented in CEPCSW
Material budget is a factor of two higher than CDR.
  With realistic support material and realistic material for flexible PCB
Average Material budget
More material in layer 2 and layer 3
  6 metal layer in flexible PCB
    Compared to 4 layer
  More material in support structure

## Slide 13
VTX-Material Budget
the variation of X0 with theta in the corrected structure
in detail
Pick out the minimum value of phi in the first layer, which is 33.98

## Slide 14
VTX-Material Budget vs phi
Based on the requirements discussed last week, the variation of X0 with phi from 0 to 90 has been drawn.
After inspection, at a certain phi value, the larger material mass is due to passing through 7 layers of silicon

## Slide 15
随出射粒子动量的变化
The correct-TDR-full simulation and CDR, following from the single-point resolutions as CDR
the impact parameter exhibits similar performance as the momentum changes.
Full Simulation of different structures (CDR vs reference TDR long barrel design)

## Slide 16: CLIC vertex design
CLIC has vertex detector design with endcap
  Air speed 6-8 m/s ,
  Maximum temperature 40-45 °C
CLICdp-Note-2014-002

## Slide 17: SID and SLD vertex detector design
Liquid nitrogen cooling design with cryostat
  SLD operated at 190K
SLAC SLD vertex design
ILC SIDvertex design

## Slide 18: BELLE2 vertex detector
Strip tracker SVD operated at -25 °C
PXD operated at 15~20 °C, air cooling
  Active cooling at Support and Cooling Blocks

## Slide 19: FCC-ee vertex and tracker design
Air cooling for inner pixel detector
Active cooling for endcap and outer barrel

## Slide 20: Air Cooling of vertex detector
Barrel layer | # of ladder | Max temperature (Celsius)
 |  | 40mW/cm2
Inner layer w/wo beam pipe Temperature | 8 | ~25°C(w thermal glue) / 49 (wo thermal glue)
Middle | 16 | 28°C
Outer | 25 | 30°C
Beam pipe temperature is very important for vertex inner layer cooling
  With thermal conduct from beam pipe, it brings down temperature
  We now assume 16 Celsius as beam pipe temperature
Final goal: ~20°C
  Middle and outer layer are likely to reach the goal by further optimization
  Inner layer still need significant improvement
Total heat generation of the VTX is 337W, assuming 40mW/cm2
From Jinyu Fu

## Slide 21: Plan to improve cooling
The thermal conduct to beam pipe is important
To bring down temperature, a potential solution to add thermal conductive glue
  Thermal glue to Increase thermal conductivity to beam pipe
  Beam pipe has active cooling
Other options :
  Reduce temperature of beam pipe
  Increase the distance of first layer to beam pipe
  Higher air flow
  low material Active cooling

## Slide 22
Full Simulation of different structures (CDR vs reference TDR long barrel design)
随出射粒子动量的变化
The correct-TDR-full simulation and CDR, following from the single-point resolutions as CDR
the impact parameter exhibits similar performance as the momentum changes.
By CEPCSW

## Slide 24: VTX像素芯片功耗分布估算
 | Matrix | Periphery | DataTrans. | DACs | Total Power
太初3芯片 @ triggerless (CDR) | 304 mW | 135 mW | 206 mW | 10 mW | 655 mW
65nm 芯片 @ 1 Gbps/chip (TDR LowLumi) | 60 mW | 80 mW | 36 mW | 10 mW | 186 mW
估算说明：
太初3芯片：180 nm工艺，电源1.8 V;
65 nm芯片：电源1.2 V;
Data rate@Triggless-CDR: 4.48 Gbps /chip
bunch spacing (min.): 25 ns需要快前沿前端
Data rate@Triggless-TDR (Low Lumi):
1 Gbps/chip
Low Lumi@TDR: bunch spacing ~几百ns，像素前端不需要快前沿，Matrix功耗可降低到60 mW
(from Weiwi,Ying)

## Slide 25: Flex厚度和物质分布
6层柔性板基于国内Cu工艺（当前阶段）
4层柔性板基于国内Cu工艺（当前阶段）
国内工艺当前只能实现基于铜的PCB，如需采用铝材料，需要委托CERN进行加工（accessibility？）
(from Weiwi,Ying)

## Slide 26: backup: CEPCSW full simulation
50um Si
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
12um G4_Al
25um Kapton
12um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
250um CFPR
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
12um G4_Al
25um Kapton
12um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
50um Si
layer1
layer2、3 (for each ladder with more than 10 sensors)
50um Si
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
12um G4_Al
25um Kapton
12um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
250um CFPR
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
8um G4_Al
13um Kapton
12.5um Acrylicglue
12um G4_Al
25um Kapton
12um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
13um Kapton
8um G4_Al
12.5um Acrylicglue
12.5um Kapton
12.5um Acrylicglue
50um Si

## Slide 27: Summary
long barrel layout Mechanics design is in progress
“Short barrel + endcap” layout will come later
Next step is improving cooling simulation,
Look into material effect and its physics performance

## Slide 28: Backup

## Slide 29: VTX assembly
Support rings / Al alloy
Ladder can be glued / bolted to the support ring. Gluing will save space to make the ratchet teeth hollow, which helps ventilation, currently we prefer this method.
Two methods to assemble the VTX:
Assemble the barrel in advance (consisting of two halves), and then install the barrel on the beam tube.
Install (or machined) the support rings on beam pipe in advance, then directly install the ladders (preferred).
Notes: Ratchet shaped support ring The ratchet teeth is hollow, this is not only for reducing the materials due to the support ring is outside the acceptance. It is mainly used for air ventilation, the end of ladder is kind of blocked .

## Slide 30: VTX installation on the beam pipe
The drawings show the option that pre-assembled halves barrels mounted onto the beam pipe(dedicated tooling required)
The support ring can be either glued/bolted to or pre machined on the beam pipe related parts. (for the inner most layer bolting and machining are too difficult)
The VTX on the tentatively modified beam pipe components
More consideration - different constraint on two ends?

## Slide 31: Update on mechanics

## Slide 32: Cable and service
Optical fiber connector can not go through holes for fibers
Plan to re-do fibers connector after routing the cables

## Slide 33: Layout - long barrel
The VTX - section view
The VTX - side view
3 different sizes of ladders( section size and length ) for barrels.
Ladder support size