## Slide 1: CEPC Time of flight and outer tracker with LGAD
Yunyun Fan
Tuesday, June 11, 2024

## Slide 2: Outline
Optimize the geometric design of the barrel
The preliminary design of AC-LGAD endcap
Summary

## Slide 3: Re-estimate the Electronics Thickness
Detail thicknesses of different regions
The thickness of the region 1：4.6mm
  PCB：1.6 mm
  ASIC：3 mm
The thickness of the region 2:
  一级汇总供电：3 mm
  PCB：1.6 mm
The thickness of the region 3：14.6 mm
  电源模块：6 mm
  光电复合电缆：5mm
  弯折走线空间：2mm
  PCB：1.6 mm
The thickness of the region 4：6 mm
  柔性板厚度：1 mm
  二级汇总电缆：5 mm （高低压供电，光纤）
Region 2
Region 3
Region 1
Region 4
Thickness of electronics + sensor:
25 mm -> 15.1 mm
Total thickness of ToF:
85 mm -> 58 mm
Ladder 3D module
R
Y
Y
X
Ladder 2D module

## Slide 4: Optimization of the Barrel Design
Three arrangement of the ladder
R = 58 mm （The Best arrangement）
G2:R = 68 mm
G3: R = 65 mm
Sensor towards the IP
G1:
From：付金煜

## Slide 5: 3D module of the Barrel
d
Lower Ladder
Higher Ladder
From：付金煜

## Slide 6: Endcap design 1
Double layers to reduce the dead area
  24 petals/layer
  10 rows/petal，
  7.5o per row，
  Overlap 0.5o/petal
140 mm / row at R direction， same pitch （100 um）
The differences between the ASIC number of R10 and R1 ：20 ASIC /4 ASIC = 5
R1
4 ASIC
R10
20 ASIC
～52.4mm
235.5 mm
Sector Module per row
Petal
Disk
Double layers arrangement
70 mm
R0: 52.36mm-70.69mm

## Slide 7: Sensor Arrangement and the readout channel
 |  | Maxmum Arc（mm） | Readout channel number | Sensor number | Hit Rate Hz/cm2
R0（400-540） | 52.36 | 70.686 | 707 | 1 | 105
R1：540-680 | 70.69 | 89.012 | 891 | 1 | 103
R2：680-820 | 89.012 | 107.338 | 1074 | 1 | 102
R3: |  | 125.664 | 1257 | 1 | 20
R4 | 125.664 | 143.990 | 1440 | 1 | 20
R5 |  | 162.316 | 1624 | 2 | 20
R6 |  | 180.642 | 1807 | 2 | 20
R7 |  | 198.968 | 1990 | 2 | 20
R8 |  | 217.294 | 2173 | 2 | 20
R9：1660-1800 |  | 235.620 | 2357 | 2 | 20
位置分辨：10 um （最大pitch 100 um）
Sensor in the 8 inch wafer
Old number

## Slide 8: Endcap design
Need to consider the details of the mechanics
Need detailed electronics design （How different from the barrel？）
  Arc PCB
  Hit rate of each channel and ASIC
  Cluster size？
  TOA TOT
  Impedance matching
Arc LGAD sensor
  leakage current
  Different pitch
3D arrangement of endcap

## Slide 9: Summary and questions
Decrease the thickness of barrel from 85 mm to 58 mm
Get the preliminary design of the endcap.
Need to discuss about the longer TPC at the endcap(> 1800mm problem)
Need to know the spatial resolution in the z direction(beam direction) ?(important to the power density of electronics )
TPC

## Slide 10: Backup

## Slide 11: Geometric layout: Barrel-OTk
TPC is limited within R = 1.8 m
LGAD: minimum radial requirement is 85(58) mm (R1800-1858 mm) after comparing different deployments
  two layers of ladders
  ladder thickness 35 （25.1 mm） mm: 25 （15.1）mm of sensors and electronics, 10 mm of support embedded with cooling tubes
best option

## Slide 12: Need reasonable hit rate at endcap
Need reasonable hit rate at endcap
  The present rate 105 hit/cm2（from haoyu ） is too high to realize at ASIC side

## Slide 13: Arrangement of the ToF with strip LGAD：Barrel
One layer: 3780 modules
  90 ladders，45 ladders each side,
  42 modules/ladder，
  22 ASIC/module，128 Channel/ASIC
One layer ToF
R= 1800 mm
H～5800mm
Module
140mm x 160mm

## Slide 14: Arrangement of the ToF with strip LGAD ：Endcap
Petals： one petal each 8°× 45 = 360°
Total modules：~ 450 (14cm × )
R：400 mm - 1800 mm
8°
Module
Longest side：140mm

## Slide 15: Layout of the Electronic System for LGAD ToF & oTracker

## Slide 16: Re-estimate the Electronics Thickness
Y
Z
Detail thicknesses of different region
The thickness of the region 1：4.6mm
  PCB：1.6 mm
  ASIC：3 mm
The thickness of the region 2:
  一级汇总供电：3 mm
  PCB：1.6 mm
The thickness of the region 3：14.6 mm
  电源模块：6 mm
  光电复合电缆：5mm
  弯折走线空间：2mm
  PCB：1.6 mm
The thickness of the region 4：6 mm
  柔性板厚度：1 mm
  二级汇总电缆：5 mm （高低压供电，光纤）
Region 2
Region 3
Region 1
Region 4
Region 1
Thickness of electronics + sensor:
25 mm -> 15.1 mm
Total thickness of ToF:
85 mm -> 58 mm

## Slide 17: Detector Impact – Vertex -- Higgs
Preliminary results. Without any safety factor. Take the highest bin value as result.
  Pair Could be used as reference of design, Beam Loss could not. Further optimization/mitigation will be performed.
Result File link:
  Pairs: /cefs/higgs/shihy/work/cepc_bkg/Results/Ref-TDR/20240312/Higgs/Pairs.root
  BeamLoss: /cefs/higgs/shihy/work/cepc_bkg/Results/Ref-TDR/20240312/Higgs/BeamLoss.root(available when exists)
Layer | Hit Density() |  | TID(k) |  | 1 MeV equivalent neutron fluence () | 
 | Pair | Beam Loss | Pair | Beam Loss | Pair | Beam Loss
1 | 760 | 110.0634 | 185 | 75.28 | 1.8 | 0.20506
2 | 490 | 90.1943 | 112 | 62.51 | 1.75 | 0.16436
3 | 70 | 45.72336 | 6.4 | 12.63 | 0.01 | 0.030855
4 | 66 | 43.73305 | 5.4 | 12.08 | 0.01 | 0.030824
5 | 42 | 27.91237 | 1.1 | 3.15 | 0.004 | 0.007239
6 | 40 | 27.60218 | 1.0 | 3.34 | 0.004 | 0.010251
Layer |  |  |  |  |  | 
 | Pair | Beam Loss | Pair | Beam Loss | Pair | Beam Loss
1 | 760 | 110.0634 | 185 | 75.28 | 1.8 | 0.20506
2 | 490 | 90.1943 | 112 | 62.51 | 1.75 | 0.16436
3 | 70 | 45.72336 | 6.4 | 12.63 | 0.01 | 0.030855
4 | 66 | 43.73305 | 5.4 | 12.08 | 0.01 | 0.030824
5 | 42 | 27.91237 | 1.1 | 3.15 | 0.004 | 0.007239
6 | 40 | 27.60218 | 1.0 | 3.34 | 0.004 | 0.010251
 | Higgs
BXRate(Hz) | 1.34e6

## Slide 18: Detector Impact – Vertex – Z-pole
Preliminary results. Without any safety factor. Take the highest bin value as result.
  Pair Could be used as reference of design, Beam Loss could not. Further optimization/mitigation will be performed.
Result File link:
  Pairs: /cefs/higgs/shihy/work/cepc_bkg/Results/Ref-TDR/20240312/Z/Pairs.root
  BeamLoss: /cefs/higgs/shihy/work/cepc_bkg/Results/Ref-TDR/20240312/Z/BeamLoss.root
Layer | Hit Density(k) |  | TID(k) |  | 1 MeV equivalent neutron fluence () | 
 | Pair | Beam Loss | Pair | Beam Loss | Pair | Beam Loss
1 | 16200 | 316763 | 8613 | 12198874 | 35.61 | 1081.16
2 | 11400 | 253791 | 5353 | 7569336 | 34.60 | 1252.93
3 | 1490 | 133919 | 252 | 6819307 | 0.5 | 555.51
4 | 1410 | 161755 | 232 | 7585843 | 0.45 | 609.69
5 | 825 | 100452 | 67.0 | 3660636 | 0.16 | 318.95
6 | 786 | 102476 | 59.6 | 3408929 | 0.14 | 592.95
Layer |  |  |  |  |  | 
 | Pair | Beam Loss | Pair | Beam Loss | Pair | Beam Loss
1 | 16200 | 316763 | 8613 | 12198874 | 35.61 | 1081.16
2 | 11400 | 253791 | 5353 | 7569336 | 34.60 | 1252.93
3 | 1490 | 133919 | 252 | 6819307 | 0.5 | 555.51
4 | 1410 | 161755 | 232 | 7585843 | 0.45 | 609.69
5 | 825 | 100452 | 67.0 | 3660636 | 0.16 | 318.95
6 | 786 | 102476 | 59.6 | 3408929 | 0.14 | 592.95
 | Z
BXRate(Hz) | 3.93e7

## Slide 19
7.5度
10列，每列140mm 长, Asic 数量差：
最长弧度/最短弧度（282.6mm （3 strip sensors）/62.8mm（1 strip sensors））=4.5
9度
10列，每列140mm 长,
R10和R1 的Asic 数量差：
23 ASIC /5 ASIC 约 4.5倍差
R1
R10

## Slide 20: Endcap design 1
Double layer to reduce the dead area
  20 petals/layer
  10 row/petal，
  9o per row，
140 mm / row at R direction， same pitch （100 um）
The differences between the ASIC number of R10 and R1 ：23 ASIC /5 ASIC = ~ 4.5
R1
5 ASIC
R10
23 ASIC
62.8mm
282.6 mm
4 module，maximum arc < 140 mm
10 module, maximum arc > 140 mm

## Slide 21: CEPC TOF
Pair production background from Haoyu
Need to updated with new version of CEPCSW
Z pole (high lumi)
ZH runs
One layer ToF
R= 1800 mm
H～5800mm
Rate( Hz/cm2)
Rate( Hz/cm2)

## Slide 22: 7.5o
Radius | Arc (mm)
400 | 52.36
470 | 61.52
540 | 70.69
610 | 79.85
680 | 89.01
750 | 98.17
820 | 107.34
890 | 116.5
960 | 125.66
1030 | 134.83
1100 | 143.99
1170 | 153.15
1240 | 162.32
1310 | 171.48
1380 | 180.64
1450 | 189.8
1520 | 198.97
1590 | 208.13
1660 | 217.29
1730 | 226.46
1800 | 235.62

## Slide 23
Petal with 9o
5 single
5 double sensor