## Slide 1
CEPC Detector Magnet
Feipeng Ning
On behalf of SC magnet Team
Aug. 22, 2024, CEPC Mechanical workshop

## Slide 2: Content
Introduction of Detector magnet
Detailed design of the CEPC solenoid magnet
Cryogenic system
Mechanical design
Main Technical challenges
Research team
Summary

## Slide 3: Introduction of Detector magnet
How to analyze the shower of particles ? We need:
- Track reconstruction
- Energy measurement, in calorimeters
- Charge identification in magnetic field
Momentum measurement in magnetic field.
A detector magnet is in fact a “magnetic separator”.
Information yield:
- left turn > positively charged particle
- right turn > negative particle
- curvature > momentum
BESIII 2009

## Slide 4: Introduction of Detector magnet
•1969 CERN –BEBC, Big European Bubble Chamber (solenoid)
•1972 CERN –Omegamagnet (large aperture dipole)
•1977 CERN/ISR –Solenoid
•1978 DESY –CELLO (solenoid)
•1983 SLAC/PEP4 –TPC solenoid
•1985 KEK/TRISTAN –TOPAZ, VENUS (solenoids)
•1988 CERN/LEP –ALEPH, DELPHI (solenoids)
•1990 DESY/HERA –ZEUS (solenoid)
•1997 SLAC –BABAR (solenoid)
•2004 KEK –BESS-Polar (ultra-thin solenoid)
•2007 CERN/LHC –CMS (solenoid), ATLAS (Toroids, solenoid)
∙2009 IHEP/BES III (solenoid)
History of High Energy Physics Detector Magnets
T. M. Taylor, CERN Summer Student Lecture, 2006

## Slide 5: Introduction of Detector magnet
Detector Magnet needed in the future
 | Experiments | Site | B [T} | Size, ID x L [m] | Note | Fabrication Expected
Collider | EIC-Detector | BNL | 1.5~3 | 2.5~3.2 x 8.5 | Solenoid | 2025 ~
 | ILC-ILD | Japan | 4 | 6.88 X 7.35 | Solenoid | 2030 ~
 | ILC-SiD | Japan | 5 | 5 X 5 | Solenoid | 2030 ~
 | CLIC-ILD | CERN | 4 | 6.8 X 8.3 | Solenoid | 2035 ~
 | CLIC-SiD | CERN | 5 | 5.4 X 6.5 | Solenoid | 2035 ~
 | CLIC | CERN | 4 | 7 X 8.3 | Solenoid | 2035 ~
 | FCC-ee IDEA | CERN | 2 | 4.2 X 6.0 | Solenoid | 2035 ~
 | FCC-ee CLD | CERN | 2 | 7.4 X 7.4 | Solenoid | 2035 ~
 | FCC-hh | CERN | 4 | 10 X 20 | Solenoid | 2060 ~
 | ALICE-3 | CERN | 2 | 3 x 7.5 | Solenoid | 2027 ~
 | CEPC | IHEP | 3 | 7.07*9.05 | Solenoid | 
Others | Mu2e | Fermilab | 5 ~ 2.5 | 1.5 X 4 | Production | Under construction
 | Muon-g-2 | Fermilab | 1.473 | 0.09 X 14.22▪2 | Storage solenoid | Reuse after BNL
 | COMET | J-PARC | 5 ~ 3 | 1.3 X 1.6 | Capture Sol. | Under const.
 | Muon-g-2 | J-PARC | 3 | 0.66 X 0.33 | Solenoid | 2025 ~
 | BabyIAXO | DESY | 2 | 0.7 X 10 | D. Racetrack | TBD
 | IAXO | DESY | 5 - 6 | 5 X 25 | Toroid | TBD
 | Panda | GSI | 2 | 1.8 x 3.1 | Solenoid | TBD
 | Madmax | DESY | 9 | 1.35 x 1.2 | Dipole | TBD

## Slide 6: Detailed design of the solenoid magnet
Position and size
Magnetic field
Inner diameter | 7070 mm
Thickness | 700 mm
Outer diameter | 8470 mm
Length | 9050 mm
Energy | t | Higgs | W | Z
Magnetic field | 3T | 3T | 3T | 2T
Energy |  | Higgs | W | Z
Magnetic field | 3T | 3T | 3T | 2T

## Slide 7
Detailed design of the solenoid magnet
Design of the magnet
7
Central magnetic field | 3 T
Inner diameter | 7070 mm
Outer diameter | 8470 mm
Thickness | 700 mm
Length | 9050 mm
Cold mass | 140 tons
Yoke mass | 3752 tons
Magnet mass | 265 tons
Magnet parameters:
magnet

## Slide 8
Detailed design of the solenoid magnet
Yoke
8
Barrel yoke (ton) | 2184
Each End yoke (ton) | 784
Total Yoke (ton) | 3752
Diameter(m) & length (m) | 10.97&11.75
Yoke parameters：
In order to reduce the detection dead zone of the muon detector, the barrel yoke is designed as a spiral structure.
Barrel yoke
2184 tons
Single module of the barrel yoke
182 tons
End yoke
784 tons

## Slide 9
Detailed design of the solenoid magnet
Magnet parameters:
9
 | CEPC | CMS
Central magnetic field (T) | 3 | 4
Inner diameter (m) | 7.07 | 5.94
Outer diameter (m) | 8.47 | 7.6
Thickness (m) | 0.7 | 0.83
Length (m) | 9.05 | 14.4
Cold mass (ton) | 140 | 225
Yoke mass (ton) | 3752 | 10000
Yoke Diameter & Length(m*m) | 10.97*11.75 | 14.0*21.6

## Slide 10
Detailed design of the solenoid magnet
10
直径 | 3.35米
长征二号、三号、四号
长征九号重型运载火箭
任务规划于2030年前后实现首飞
一级直径/米 | 11 | 10.6 | 9.5 | 9.5 | 9.5
长征五号重型运载火箭
芯一级 | 5米

## Slide 11
Detailed design of the solenoid magnet
CEPC detector magnet dummy coil:
11

## Slide 12
Detailed design of the solenoid magnet
Physical design of the magnet
12
Material | Von Mises stress (MPa)
Coil at 4.2 K | 
Pure Aluminum | 12.8-96.5
SC cable | 188-246
Al alloy | 30.2-57.1
Coil at 4.2 K, energized | 
Pure Aluminum | 52.5-102
SC cable | 80-223
Al alloy | 46.7-125
Central magnetic field | 3 T
Inner diameter | 7300 mm
Operating current | 16702 A
Cable length | 33 km
Inductance | 11 H
Stored Energy | 1.54 GJ
Coil parameters:

## Slide 13
Cryogenic system
Cooling methods: Thermal siphon
13
Uniform temperature distribution;
High heat transfer efficiency, not limited by source pressure and pressure drop;
Low cost. No need for liquid helium circulation pump
Cooling process diagram
Verification experiment schematic diagram
Detailed calculations and process designs are currently underway.

## Slide 14
Mechanical design
2D
Completed the design of the 2D chain and the space occupied by each component.
3D
Completed the design of the 3D structure, added suspension system, cooling pipes, and connection structure.
coil
Thermal shield
suspension rod

## Slide 15: Main Technical Challenges
Aluminum stabilized superconducting cable;
Suspension system of the huge coil (140 tons);
High precision machining and assembly of large cylindrical dewar；
There are lots of welds in low-temperature pipes, including pipes and coil supports, pipes and liquid/gas helium tanks.

## Slide 16: Main Technical challenges
Aluminium-stabilized Nb-Ti/Cu conductor types
CMS
Now
Pioneer
Future

## Slide 17: Main Technical challenges
Aluminium-stabilized Nb-Ti/Cu conductor
The Superconducting Detector Magnet Workshop is organized by CERN and KEK, and is hosted at CERN in hybrid format
For the purpose of:
  Addressing the issue of commercial availability of aluminum-stabilized conductor technology for future superconducting detector magnets
  Informing the community of on-going and future projects
  To exchange ideas, concepts, best practices, and to advance superconducting detector magnet technology
  Fostering collaboration
With 88 participants (55 on-site and 33 online) from 36 institutes and companies
Welcome!
The aluminum-stabilized Nb-Ti/Cu conductor is the traditional workhorse that is used in nearly all superconducting detector magnets
For a given amount of mass, aluminum-based superconducting conductors give strong performance needed for superconducting detector magnets:
Significant heat capacity for a given amount of weight
Excellent electrical and thermal conductivity at 4 K (pure or nickel-doped aluminum)
Very good mechanical properties (nickel-doped aluminum or aluminum-alloy)
Affordable, in combination with superconducting Nb-Ti/Cu Rutherford cables
However, in recent years, commercial availability has been an issue
Can we obtain it? Do viable alternatives exist?

## Slide 18
Main Technical Challenges
Conductors
  Conductor is the foundation of the magnet development. Most of the detector magnets used or will use the Aluminum-stabilized Nb-Ti/Cu conductors.
18
The IHEP and Toly company have jointly established an aluminum coated conductor production line in 2015.
Rutherford Cable
Aluminum stabilized NbTi/Cu conductor
Extrusion machine

## Slide 19
Production line
Al-stabilized Conductors
19
1.5 km
100 m
LTS: Aluminum stabilized NbTi Rutherford cable
HTS: Aluminum stabilized Stacked REBCO Tape Cable
Aluminum coated conductor production line

## Slide 20
Main Technical Challenges
Suspension system
Thermal shield suspension system:
6 radial rods each end
Material: titanium alloy
Coil suspension system (140 tons):
8 axial rods each end
6 radial rods each end
Material: titanium alloy
Forces and torques resulting from axial and radial offset, and from angular tilt of the coil.
Axial displacement (cm) | 1 | 3 | 10
Axial force (kN) | 484 | 1498 | 5034
Radial displacement (cm) | 1 | 3 | 10
Radial force (kN) | 34.3 | 236 | 656
Angular tilt (angle) | 1/407.5 =0.14° | 3/407.5 =0.42° | 10/407.5 =1.41°
Torque (kN.m) | 1965 | 6170 | 19935
 | Diameter | Length | amount
Axial rods | 30 mm | 3530 mm | 16
Radial rods | 40 mm | 1700 mm | 8
Main pull rods | 48 mm | 1650 mm | 4

## Slide 21
Main Technical Challenges
High precision machining and assembly of large coil and dewar
21
Large scale superconducting coil winding platform
φ7.2m dummy coil
Coil winding, vacuum leak detection, epoxy impregnation curing.
vacuum leak detection
Dummy coil
4 layers*10 turns
The machining accuracy is controlled within ± 1mm

## Slide 22
Main Technical Challenges
Processing and assembly of large thin-walled cylinders.
22

## Slide 23
Main Technical Challenges
There are lots of welds in low-temperature pipes, including pipes and coil supports, pipes and liquid/gas helium tanks.
Good contact
Leak proof

## Slide 24
IHEP: staff 13; engineer 5; post doctor 1; students 3
Cooperative institutes and Universities: SJTU, SWJTU, NCEPU, TSINGHUA, IEE, IPC, IPP and so on.
Cooperative companies: Wuxi Toly (aluminum stabilized conductors), Hefei Keye ( coil winding platform and dummy coil development), Xinjiang Zhonghe ( Aluminum stabilizer), WST ( LTS wires), SSCT ( HTS tapes), and so on.
Welcome international cooperation.
Research Team

## Slide 25
Experience: BES III detector magnet
Research Team
Design, processing, manufacturing, and assembly experience of BES III detector magnet;
Safe, stable, and accident free operation for nearly 20 years.

## Slide 26: Summary
1. There are many challenges faced in the mechanical aspect.
2. We have achieved a leading position in aluminum-stabilized superconducting cable development.
3. We need the cooperation of large precision machining companies.

## Slide 27
Thank you for your attention!
Aug. 7th, 2024, CEPC Detector Ref-TDR Review