## Slide 1: CEPC vertex detector towards TDR
Zhijun Liang,
On behalf of CEPC vertex working group

## Slide 2: Introduction
CEPC L0 management decided to develop CMOS stitching baseline design
It is exciting development and cutting edge technology for vertex detector
  Layout & Physics design , then implementation in CEPCSW
  Background & Data rate
  Mechanics & cooling
  Service and cabling

## Slide 3: VTX像素芯片功耗分布估算
 | Matrix | Periphery | DataTrans. | DACs | Total Power
太初3芯片 @ triggerless (CDR) | 304 mW | 135 mW | 206 mW | 10 mW | 655 mW
65nm 芯片 @ 1 Gbps/chip (TDR LowLumi) | 60 mW | 80 mW | 36 mW | 10 mW | 186 mW
估算说明：
太初3芯片：180 nm工艺，电源1.8 V;
65 nm芯片：电源1.2 V;
Data rate@Triggless-CDR: 4.48 Gbps /chip
bunch spacing (min.): 25 ns需要快前沿前端
Data rate@Triggless-TDR (Low Lumi):
1 Gbps/chip
Low Lumi@TDR: bunch spacing ~几百ns，像素前端不需要快前沿，Matrix功耗可降低到60 mW
(from Weiwi,Ying)
Power consumption estimation is based on 25*25um pixel size

## Slide 4: What is stitching? (from Meng Wang)
df

## Slide 5: Top focus on stitching
Inner layer : background , data rate, power consumption
Middle layer and outter layer:
  refine stitching proposal and estimate yield, power consumption

## Slide 8: Data rate estimation of CEPC VTX
TDR raw hit density: Higgs 0.54，Z 0.3; Safety factor: TDR 1.5, CDR 10;
Cluster size: 3pixels/hit (@Twjz 180nm, EPI 18~25um)
Area: 1.28cm*2.56cm=3.27cm2 (@pixel size 25um*25um)
Word length: 32bit/event (@Taichu’s scale, 512*1024 array)
Trigger rate：20kHz@CDR，120kHz@TDR estimated
  Trigger latency: 3us(very likely not enough), Error window: 7 bins
  FIFO depth: @3us * hit rate/chip
  Data rate=pixel/bunch*trigger rate*32bit*error window
 |  | Hit density (Hits/cm2/BX) | Bunch spacing (ns) | Hit rate (M Hits/cm2) | Hit Pix rate (M Px/cm2) | Hit rate/chip (MHz) | Data rate@triggerless (Gbps) | Pixel/bunch | FIFO Depth @3us rg latency | Data rate@trigger (Mbps)
CDR | Higgs | 2.4 | 680 | 3.53 | 10.59 | 34.62 | 1.1 | 23.5 | 103.9 | 105.28
 | W | 2.3 | 210 | 10.95 | 32.86 | 107.44 | 3.4 | 22.6 | 322.3 | 101.248
 | Z | 0.25 | 25 | 10 | 30 | 98.1 | 3.1 | 2.4 | 294.3 | 53.76
TDR | Higgs | 0.81 | 591 | 1.37 | 4.11 | 13.44 | 0.43 | 7.96 | 40.4 | 213.9？
 | W | 0.81 | 257 | 3.16 | 9.45 | 30.90 | 0.98 | 7.96 | 92.8 | 213.9？
 | Z | 0.45 | 23 | 19.6 | 58.7 | 191.9 | 5.9 | 4.4 | 575 | 118
Assume data rate @1Gbps per chip for low lumi Z (20% of high lumi Z)
for triggerless

## Slide 9: Issue of stitching for large pixel matrix
Normal chip
Transmission:
  Each chip has a dedicated data transmission path for 1Gbps
  The transmission path is on PCB (ideal transmission line, high signal quality)
Buffering:
  On Periphery (on chip), for high hit rate
Pixel Matrix
Periphery
1Gbps on PCB
1Gbps on PCB
1Gbps on PCB
1Gbps on PCB
Ladder for Normal chip

## Slide 10: Issues of the dead area

## Slide 11: Preliminary thoughts
On chip & dimension
  NX+2Y scheme:
    Challenging but DO-able
    Inner layer VTX, a half layer: total data rate 10Gbps at one end on one “chip”
    Actually no fundamental change of chip, but save the mechanical
  NX+MY (M>2) scheme:
    Too ideal   
    Data transmission, power distribution, timing… all with big issues
    But maybe possible for outer-most layer – data rate greatly decreased
On mechanical
  Overall mechanical is easier than the normal scheme
  But dead area seems inevitable on the same layer and not small
Rough estimation
  Innermost layer: NX+2Y of (1024row*512col) can be bent to be a semi-circle

## Slide 12: Preliminary outline for Vertex section @ referenece TDR
3. Vertex detector (Zhijun & Meng Wang)
a. Requirements (position and vertex) Zhijun , Manqi
b. Technology survey and our choices (both baseline & backup options), Zhijun & Meng
c. R&D efforts and results
CMOS Stitching: Meng Wang
 CMOS normal chip: Zhijun, Wei Wei, Yupeng
 SOI: YunPeng
d. Detailed design including electronics, cooling and mechanics
 Layout: Zhijun & Meng Wang
 CMOS sensor design: Wei Wei，Ying Zhang, Yunpeng
Cooling and mechanics: Jinyu Fu
e. Readout electronics & BEC
Background estimation : Haoyu Shi
 Data rate and readout scheme: Jun Hu, Wei Wei
f. Performance from simulation (impact parameters). Chengdong Fu

## Slide 13: Testbeam in BSRF for vertex sensor digitization model
Testbeam in BSRF from June 1st to July 1st
Try to test different incident angle from 8° - 90°
  In last test beam at DESY, incident angle is about 70-90°
  Cluster size, efficiency vs incident angle

## Slide 14: News about TJ65nm CMOS design
Got design Kit for TJ 65nm technology. (Ying Zhang, Wei wei)
  Pixel cell dimension study
  Power consumption
Problem
  Design kit was N type low resistivity wafer
   should be p type high resistivity Epi wafer

## Slide 15: Issue of stitching for large pixel matrix
NX+2Y: still have Periphery region, for buffering & data transmission, almost the same as the normal chip scheme
NX+MY: the inner Pixel Matrix with no support of buffering & data link, can only go through others. Data rate accumulation effect reveals
Pixel Matrix
Periphery
Pixel Matrix
Periphery
Pixel Matrix
Periphery
Pixel Matrix
???
Pixel Matrix
Periphery

## Slide 16: ALPIDE parameters
From CERN-LHCC-2024-003/ALICE-TDR-021：Technical Design Report for the ALICE Inner Tracking System 3 - ITS3 A bent wafer-scale monolithic pixel detector