## Slide 1
The design, production and QC test of
GEM electronics board for CMS ME0 project
  Zhe Li (on behalf of PKU Group)

## Slide 2: Outline
Outline:
Introduction of CMS ME0 GEB
Requirements of CMS ME0 GEB
Design of CMS ME0 GEB
Production and QC test of ME0 GEB
Summary

## Slide 3: Introduction of CMS ME0 GEB
GEB: front-end electronics board of GEM detector for upgraded CMS muon system (GE1/1, GE2/1, ME0)
Function of GEB:
  Carrier of front-end and back-end electronics system
  Front-end signal transmission carrier
  Provide direct shielding for GEM detectors
Works of CMS China HEP group:
  Production and test of GE1/1 GEB
  Design、production and test of ME0 and GE2/1 GEB
  Development of automatic tester
GEM
DAQ system of CMS-GEM
CMS detector cross section
ME0
GE2/1
GE1/1

## Slide 4: Requirements of ME0 GEB
  Signal transmission:
    Ensure that the characteristic impedance is 100 Ohm for differential line, and small fluctuations in characteristic impedance to reduce signal reflections
    Ensuring that time delay of the signal lines are the same to meet isochronism requirement
    Low BER (Bit Error Rate) and noise
  Power Supply:
    Meet the different power requirements of VFAT and OH board
    Effective power distribution systems
    Power monitor, current, voltage and temperature monitor
    Prevent large voltage drop during transmission
    Validate the voltage to set value
  Mechanical performance:
    Total board thickness is less than 1.1mm, limited by installation space.
    Surface flatness lower than the IPC standard curvature 0.75%.
    standoffs (holding VFAT and OH boards) aligned and firmed mounted

## Slide 5: Design of CMS ME0 GEB
GEB with its function modules
A set of GEB connects to:
24 VFATs
4 ASIAGO boards (2 OH-CONN on each)
6 FEAST (1.2VA, 1.2VD and 2.5V)
VFAT Connector and standoff
FEAST Connector and standoff
OH Connector and standoff
The VFAT chip converts the signal on the readout strips into digital signal
Electrical components on OH board convert the signal from GEB into an optical signal on the optical fiber
FEASTs provide voltage to chips on VFAT and OH board
Narrow board
Wide board

## Slide 6: Stacks of GEB board
To meet characteristic impedance requirement:
  Choose proper dielectric constant: surface solder 3.5 medium 4.2
  Copper thickness for signal stack: 0.5Oz
  Mini number of vias for each differential line: 2 vias (Reduce the fluctuation of characteristic impedance)
To meet mechanical performance requirement:
  Board thickness: 1.05mm (within the requirement 1.1mm)
  Symmetrical arrangement and the same copper laying method (Reduce the curvature)
  Use halogen-free boards
Top layer
Bottom layer
For example, top layer and bottom layer are laid with the same copper arrangement, in order to reduce the board curvature
Stacks structure

## Slide 7: Characteristic impedance and routing
Characteristic Impedance
Set to 100Ohm for differential lines:
Factors that affects characteristic impedance:
W1,W2:Line width
S1:Differential line separation
D1:Ground strip separation
H1,H2:Stack thickness
Er1, Er2: Dielectric constant of the medium
Characteristic Impedance fluctuation: <10%
Routing:
(1) Differential signal lines: linewidth / gap / linewidth: 0.1/0.25/0.1 mm (Considering coupling effect)
(2) Other parameters: Minimum distance to another pairs / DGND: 0.55mm / 0.6mm.
(3) Simpler routing design: Reduce routing corner
Characteristic impedance fluctuation of most differential line is within 10%

## Slide 8: Signal
Signals introduction:
VFAT trigger unit outputs 9 differential signals: VFAT communication E-port has 3 pairs of differential signals
VFAT reset signal LVCMOS level signal: RESET
Signals are arranged on two layers:
Signal1 and signal2
Prevent crossover of signal lines as in GE1/1 case
Signal1 Layer
Signal2 Layer
To meet time resolution requirement of signals:
Equal length(CLK and RXD):
J1-J6,J7-J12 To ensure signal isochronism
Both signal layers have upper (Top layer or bottom layer) and lower shielding layers (DGND1 and DGND2) to reduce signal interference

## Slide 9: Power distribution system
GEB distribute the voltage from FEAST to VFAT and OH board through vias and power plane.
In addition, grounding operation is achieved through the DGND and AGND planes.
Different colors show different power supply areas and link to different FEAST
Chip of VFAT and OH requires a different FEAST power supply
3 FEASTs provides 3 voltages to the corresponding chips of VFAT and OH board
FEAST
Prevent voltage loss:
(1) The thickness of the power supply layer is 1oz
(2) For high current power supply, we provide large area power plane

## Slide 10: Power monitor
The output monitoring voltage show whether the FEAST is working properly.
To monitor the current output of each power supply, we use Monitor to detect the voltage drop through the current sensing resistor with a resistance of 0.01 Ohm.
The GEB power supply is designed with 2 sets of LED lights, corresponding to the main power input terminal and 2.5V power output seperately , which can display the power supply status of both in time.
Power monitor:
introduced to ensure that the voltage value of the supply is normal
Power monitor of 1V2DVFAT
LED
OH power supply；
  PWR1: 1V2DVFAT ---1.3A for one ASIAGO, total is 2.6A.
  PWR2: PWR2V5 --- 0.2A for one ASIAGO, total is 0.4A.
VFAT power supply:
  PWR1: 1V2DVFAT ---70mA for one ASIAGO, total is 840mA.
  PWR2: PWR2V5 --- <1mA for every VFAT
  PWR4: 1V2AVFAT ---140mA for one VFAT, total is 1.68A
Voltage measurement：
  Monitor1 and Monitor0 are 0.6V (1.2V × 0.5)
Current measurement:
  If Ir51 = 3.44A, voltage of Monitor0 –Monitor1 = 17.2mV
  (3.44A × 0.01Ω × 0.5)

## Slide 11: Grounding system and shielding system
Grounding system:
2 DGND layer(digital ground) and 1 AGND(analog ground) layer.
Split plane of AGND layer
Shielding system:
The signal layer is between top/bottom layer and grounding layers to avoid electromagnetic interference.
Shielding pads which connected to the external frame are added to reduce noise.
chimney
chimney
Shielding Pads
12 in total

## Slide 12: Cooling system and temperature measurement
Cooling system
Temperature measurement:
Temperature is measured by the pin of PTAT on the BPOL with divided resistors.
The output of the divider of PTAT is 0.45V --- 0.85V(2.425mV/℃).
PTAT output change with temperature shown as below picture.
Cooling system to cool down the DAQ system:
The cooling system is modified as the number of FEAST is from 4 to 3.
• Remove the 1.2VD FEAST which is located in the positions marked by the purple X
Temperature curve
Previous temperature measurement system

## Slide 13: Fiber routing
• Fiber fixing
5 KEYSTONE 5016 for narrow GEB
5 KEYSTONE 5016 for wide GEB
attach optical fiber to zipline
• In order to ensure it is firm, many through holes are placed on the keystone.
• In order to avoid signal interference ,
- 1. The keystone is not grounded
- 2. No signal routes through the occupied position

## Slide 14: Production site of ME0 GEB
  Sinofast in Shenzhen, China has long term collaboration with CMS-GEM team, has produced all GE1/1 & GE2/1 GEBs and ME0 GEB, including their prototypes
  Etching Machine CNC drilling machine
  Laminating Machine

## Slide 15: Production and QC test of ME0 GEB
Milestone of ME0 GEBs production:
  Designed finalized in June 2022, 1st batch of 15 sets of ME0 GEBs produced on Jan. 2023, completed test at CERN in Apr. 2024
  240 sets of the remaining GEBs production completed in Feb. 2024, 2nd batch of 95 sets of GEBs tested in China and shipped to CERN in April 2024
  3rd batch of 145 sets of GEBs tested at China completed in Nov. 2024, shipped to CERN ~15 Nov.
Test at GEB production site in Shenzhen Sinofast Ltd., China:
  Flying Probe test and characteristic impedance test (by the factory)
  Power module test
  Signal connectivity test and BER test (new tool)
  Bending degree test and mechanical compatibility test
Acceptance test at CERN:
  Similar as GE2/1 acceptance test at CERN, to make sure no damage caused by shipment.

## Slide 16: Power module test
Voltage and current test of 3 power modules:
  2.5V on OH board
  1.2V digital power、1.2V analog power supply on VFAT
→ The power test has been done with the ME0 GEB(wide & narrow) prototypes, the results meet the GEB design requirements, and the fluctuations are within a reasonable range
Load board

## Slide 17: Signal Connectivity Test: FPGA-computer based device
Connectivity test:
  all VFAT signal channels and power supply pins
BER test:
schematic diagram
  Device:
  using Xilinx Spartan-6 FPGA and LabVIEW
  Used in acceptance test of GE2/1 GEB
  The device was verified and successfully used in GE2/1 mass production
  Flow chart of the test device
Test Criteria:
No short and open circuit (connectivity)
No error occurs in one minute (BER)

## Slide 18: Characteristic Impedance test
Characteristic Impedance test results
(provided by Sinofast company)

## Slide 19: Mechanical Compatibility & Flying Probe Test
Mechanical compatibility test
Mount VFAT (Plugin Card), OH board, and FEAST to check the collimation of Standoff.
Test results of ME0 GEB prototypes: Standoff has good collimation
Flying probe test:
The factory performs automated flying probe test during GEB production.
Automated flying probe test machine

## Slide 20: Test At UCLA and FIT
Integration test with OH and VFATs
1. The goal:
6 ME0 GEBs (2N + 4W) arrived and underwent full-loaded test at UCLA
2. Test process:
• Check voltages with only FEASTs loaded onto GEB
• Load one ASIAGO (ME0 Optohybrid) and one VFAT
• Check ASIAGO is ready and can communicate with VFAT
• Fully load GEB and check communication with all VFATs (tests full communication chain and DAQ elinks)
• Take current measurements using current sensing chips + thermistors on ME0 GEB and reading out through ADC of ASIAGO
• Check uplink and downlink error rates and eye diagrams
eye diagram
Noise test
Test result of full-loaded test

## Slide 21: Summary
The design, production and test of all CMS-GEM GEB are completed (except the acceptance test of the last batch of ME0 GEBs at CERN)
We developed the GEB test criteria, procedure and automatic device, all GE1/1, GE2/1 and ME0 GEBs produced in China passed the test and shipped to CERN
The CMS-GEM upgrade project is on schedule, Chinese group completed its shared tasks on GEBs (GEM electronics boards).