## Slide 1: Consideration for CMOS tracker readout
JIANG Xiaojie, LI Yiming, SHENG Shuqi, WANG Jianchun,
XU Zijun, ZHOU Yang
22 Jul 2024

## Slide 2: Layout
Optimization ongoing; subject to change
https://indico.ihep.ac.cn/event/23036/attachments/80042/100091/geo_layout.pdf

## Slide 3: Key Specifications for CMOS chip
Parameter | Requirement / expectation
Pixel size | 34 150
Chip size | ~ 2 2 cm2.
Array size | 512 rows 128 columns
Spatial resolution | < 10
Timing resolution | ~3-5 ns
Power consumption | ~ 300 mW/cm2. (aiming for 200)
Data size per hit | 42 bit (14b BXID*, 7b+9b address, 6b TOT, 5b fine TDC, 1 polarity*)
Event rate / chip | ??? (background?) up to 1.28 Gbps
LV | 1.2V
HV | ~150 V?
Parameter | Requirement / expectation
Pixel size | 
Chip size | 
Array size | 
Spatial resolution | 
Timing resolution | ~3-5 ns
Power consumption | ~ 300 mW/cm2. (aiming for 200)
Data size per hit | 42 bit (14b BXID*, 7b+9b address, 6b TOT, 5b fine TDC, 1 polarity*)
Event rate / chip | ??? (background?) up to 1.28 Gbps
LV | 1.2V
HV | ~150 V?
* To be reduced

## Slide 4: Background rate
Latest estimation from Zhan Li on 20 July
  on Pair production only
  Fixing previous estimation by merging steps in GEANT4 into single hits
  Rate substantially dropped wrt bkg file provided by Haoyu in March
Assuming 42 bits/hit
Layer | Avg data rate [MHz/chip] | Max data rate [MHz/chip]
SIT1 / ITKB1 | 5.7 | 12
SIT2 / ITKB2 | 13 | 202
SIT3 / ITKB3 | 13 | 113
640 MHz /chip is enough

## Slide 5: Module concept (as proposed 05 July)
 | Thickness (mm) | Radiation Length [%X0]
Pixel Sensor | 0.150 | 0.18
HybridFlex | 0.200 | 0.28
Kapton Tape | 0.100 | 0.14
BareStave | 4.000 | 0.21
Optical connector | 1.250 | 0.13
lpGBTx | 4.000 | 0.07
Total |  | 1.01
Silicon + Al
Cu+ Kapton
142.16mm
42.76mm
lpGBTx: W=9, L=9
Optical connector: W=10, L=20
42.76mm + 10 mm + 2 sides/gaps
10 mm
1 lpGBT provides 280.32, 140.64, or 71.28 Gbps DATA links
=> 2 lpGBT needed for current bkg rate; may reduce to 1?

## Slide 6: Updated module concept
Key modification:
  Moving PCB from below the chip to above
  Common electronics & cables directly on top of PCB
Advantage
  Chip in direct contact with supporting, better cooling
  No need for inactive area to the side of module
  Minimal changes (simplification) to stave design
Cooling for common electronics needs study
Now assuming 1 lpGBT / module, if all chips reach ~1Gbps more fibres needed
142.16mm
42.76mm + 10 mm + 2 sides/gaps
42.76mm
10 mm
42.76mm + 10 mm + 2 sides/gaps
Optical convertor
Transmission (GBTx like)
DCDC
Optical fibre
Supporting & cooling to be optimized seperately
142.16mm
Power cable
Hybrid PCB
Data aggregation

## Slide 7: Barrel arrangement & counts
Layer | Modules/stave | Staves/layer | Modules/layer
B1 | 7 | 40 | 280
B2 | 10 | 58 | 580
B3 | 14 | 96 | 1344
* Numbers given by Qi & Yihan at 19th July rTDR tracker meeting
In total 2204 modules, 30856 chips needed
Total data rate for the whole barrel?
Assuming 640MHz/chip => upper limit 19.7 Tbps
Assuming dominated by background, 2 Zhan’s estimation (P4): ~0.7 Tbps
Total power: ~2.65 kW for sensors, ?? For common electronics?

## Slide 8
Double column schematics: two pixels
Pixel matrix:
512 rows
64 double columns
serializer
R/O
controller
R/O
controller
Up to 1.28Gbps
......
FIFO and FSM
DACs for biasing
LVDS
PLL
640 MHz
40 MHz
I2C slow control
Digital process & data formation
Periphery & IOs
Schematic of a HV pixel sensor
LE: Leading edge
TE: Tailing edge
Front-end electronics

## Slide 9: Electronics design
HVCMOS
chips
HVCMOS
chips
HVCMOS
chips
HVCMOS
chips
lpGBT (like)
Front-end
Module
Data
Control
DC convertor
1.2/?? V
BEE
HV
Data
Control
Clock
Clock
12V
HV system

## Slide 10: Cost estimation
Category 类别 | Item 名称 | Total (10k CNY) 小计（万元） | Unit cost (CNY) 单价（元） | Unit 单位 | Quantity 数量 | Note 备注
Sensor chip | Sensor chip | 1278 | 18,000 | Wafer | 710 | 3.3 MCNY for NTO + 18k/wafer; assume 50% yield
Common electronics | Hybrid PCB | 154 | 700 | Piece | 2204 | 
 | Optical fibre | 44 | 200 | 20m | 2204 | 
 | Optical connector | 441 | 2,000 | Piece | 2204 | 
 | PCB connector | 22 | 100 | Piece | 2204 | 
 | Power cable | 88 | 400 | 20m | 2204 | 
Total |  | 2027 |  |  |  | 
Note:
cost on mechanical support and cooling not considered yet
Assuming 2 fibre/module in innermost layer TO DO!

## Slide 11: backup