## Slide 1: Data issues found and tests
Tingxuan Zeng
TDAQ Group, Experimental Center, IHEP
2024.07.22

## Slide 2: Issues found during last data taking
1. GEMDC packet L1 count not increasing when working with dummy GEMROC data.
2. The first GEMDC packet length is wrong.
3. The GEMROC data format in the first GEMDC data packet is wrong.
4. Found DC buffer pile up, multiple DC packets has been read out in one DMARun.
5. GEMROC L1 counter not start from 0.
6. GEMROC L1 counter is increasing by 4 most time, sometimes by 3 or 5.
7. DAQ software is able to acquire data for 2 minutes, after that, no interrupts happened.
8. Sometimes data format of GEMROC 5 is wrong.(new found)
9. Link NO in DC packet is not corresponding to the GEMROC ID.(new found)
Our Analysis:
1 maybe cause to 2 different GEMROC data formats: confirming with Pawel if the DC firmware support two GEMROC data format .
2,3,5 maybe due to the same problem.
4 is correct according to current design of DC firmware.
6 ，7 still need to research.

## Slide 3: What I have tested in Hall 3 106
“No interrupt” issue
Data taking and testing
Feedback to Pawel to solve
Not yet solved
Test without interrupt to see if it can work out
When no interrupt happens, test DC buffer status and check if it can recover
“Buffer empty” happens, can not recover
Buffer not empty, can recover
Check buffer status, if buffer not empty, then read out
“Buffer empty” happens quickly
Reduce buffer register access and read out frequency
“Buffer empty ”also happens, but improved (can run for longer time, 1 hour).
Maybe high buffer register access frequency or small read out length has side effects in the FEE firmware implement?

## Slide 4: Test in experiment hall
STEP 1: Test Trigger signals
  Network of Angelo’s PC is connected.
  Make BESIII DAQ system worked with ZDD system.
    The L1/CHK/CLK signals are already seen in the Oscilloscope.
  Michela is testing the signals with the GEMROC
(TO DO)STEP 2: Data taking with BESIII Global trigger