## Slide 1: 202407

## Slide 2: Simulation on BEPCII polarization measurement
Simulation layout:
  10cm-long Iron beampipe (inner radius 2.8 cm), 1mm-thick glass-plate, 1cmto20cm-thick lead pre-shower, 20um-thick Si sensor.
Generator:
  Based on Prof. Muchnoi’ s GitHub project.
  Add dispersion & twiss paras. effects.
  Beam polarization: 50% Laser polarization: 100%
Generate 100M events for each samples
  Sample 1: beam 2.35 GeV, laser 515 nm;
  Sample 2: beam 4.73 GeV, laser 515 nm;
beampipe
Glass plate
Pre-shower
Si sensor

## Slide 3: Simulation & reconstruction
The truths of back-scattered photons (in 6D phase space) are recorded.
The positions at which back-scattered photons pass through the glass plate are recorded.
The energy depositions in Si sensor are recorded.
In reconstruction:
  The pixel size is assumed to be 25x25um^2.
  The number of scattered photon ~ Poisson distribution()
  If the energy deposition in one pixel is larger then 1440eV, the count in this pixel +1.
Fit procedure:
  Based on Aurelian’s function.
  Fit to the scattered photon positions on glass plate, or counts from Si sensor.

## Slide 4: Sample 1: on glass plate
Left hand polarization and right hand polarization
Polarization: on a 100x100 mm^2 area.

## Slide 5: Sample 1: on glass plate
The fit result varies as the plate area changes.

## Slide 6: Sample 1: in si sensor
Left hand polarization and right hand polarization
Polarization:
  on a 100x100 mm^2 area.
  on a 25x25 mm^2 area.

## Slide 7: Sample 1: in si sensor
The fit result varies as area of the sensor and the thickness of pre-shower change.

## Slide 8: Sample 2: in si sensor
The fit result varies as area of the sensor and the thickness of pre-shower change.

## Slide 9: Discrepancy between truth and construction
Truth – simulated position on glass
Fit to “truthdiscrepancy”
Truth – simulated position for each energy deposition step in Si sensor

## Slide 10: Fit to “truthdiscrepancy”
The fit result varies as area of the sensor and the thickness of pre-shower change.

## Slide 11: summary
Based on generator and Prof. Aurelian’s function, input/output check seems fine
Pre-shower and Si sensor enlarge the discrepancy between truth and“measurement”
  Should be solved.

## Slide 12: 20240808 progress

## Slide 13: Software scheme
Generation
Compton scattering generator
For each laser polarization, beam-laser collisions (serval-minute data taking)
For each laser polarization, 10^8 beam-laser collisions (serval-minute data taking)
Geant4 simulation
Reconstruction
In each pixel, count +1 if deposited energy >1.44 keV
Pseudo-measurement
Fit asymmetry pattern to obtain polarization
Generation
Geant4 simulation
Reconstruction
In each pixel, count +1 if deposited energy >1.44 keV
Pseudo-measurement
Fit asymmetry pattern to obtain polarization
beampipe
Glass plate
Pre-shower
Si sensor

## Slide 14: Fit results
Optimize thickness of pre-shower and sensor area.
  2mm lead seems well
Pile-up events affect measurement.

## Slide 15: backup

## Slide 16: Geant4 change-log
The production cuts (range cuts) are changed from 700 um (default) to 1 um for all material. Leads to the decreasing of energy thresholds for
  Pb: 94.6 keV -> 1.2 keV Si: 5.9 keV -> 990 eV Fe: 17.2 keV -> 990 eV glass: 5.2 keV -> 990 eV

## Slide 17: Bin maximum
10^8 events for each polarization data taking
In the bin with the highest number of events, one count is generated per events.
Qualitatively speaking, the pile-up event will affect the pattern when more than one count is generated, equally when pileup events are more than events .
 | 1mm | 2mm | 3mm | 4mm | 5mm | 6mm | 8mm
maximum | 59 | 97 | 122 | 148 | 168 | 185 | 211