## Slide 1: CGEM DAQ Status
Tingxuan Zeng
2024-09-02

## Slide 2: Outline
Test New Firmware
FEE configuration integration

## Slide 3: Test New firmware in DAQ lab
DC firmware had been updated by Pawel.
  Send out 1 event per interrupt
Use the python script write by Angelo to send out dummy GEMROC data packets.
  can set maximum 6KHz and 255 hits.
  Test with 6KHz periodic trigger, adjust the event size , 1 DC board with 1 GEMROC.
Can run continuously in interrupt mode , multiple events read out still exists, happened once at the beginning(<1min) of each run.
1e-5 Packet loss occurred of the GEMROC packets, telling from the UDP Sequence counter.
Single DC board the maximum throughput : 11.7MB/s , can meet the performance requirement.
event size (Byte) | Event rate (KHz) | Throughput (MB/s)
56 | 6 | 0.34
448 | 6 | 2.63
848 | 5.9 | 4.92
1648 | 5.8 | 9.38
1968 | 5.77 | 11.1
2088 | 5.76 | 11.7
Notes: Dummy GEMROC data has fixed format.
  The DC L1 count is fixed to 0xe0
  Hit number can not check

## Slide 4: FEE configuration integration
Summarized the configuration processes and steps from the code.
  Include 10 configuration steps .
Identify parameters that will be configured during operation with FEE experts together.
Use the final document as the basis for future integration and maintenance.
 | GEMROC DAQ | Tiger Global | Tiger Channel
Config Parameters need modify during data acquisition |  |  | 

## Slide 5: Summary
DC firmware has been updated twice, I have tested with new firmare in DAQ lab.
  Interrupt issue solved.
  Remaining some data format issues.
Draft a FEE configuration procedure to let the FEE expert confirm.
The HV test was successfully completed this morning:
  With the high pressure set to a safe value of 10V.
  All HV control and monitoring functions were tested without any errors.
Next to do
Flash the other 2 DC boards in Hall 3
Test new firmware in Hall 3
Set up the system and take data with real trigger in experiment hall
Thanks for the assistance from the Italian team!

## Slide 6
backup

## Slide 7: Firmware flash status
Board ID | DC board 1 | DC board 2 | DC board 3 | DC board 4
DIP switch (sw5-0) | 0000 01 | 0000 00 | 0000 00 | 0000 01
CSR Address | 0x04000000 | 0x00000000 | 0x00000000 | 0x04000000
Irq vec, irq line | 0x3f, 0x04 | 0x40, 0x03 | 0x40, 0x03 | 0x3f, 0x04
Jtag cable connected | no | no(updated) | no | Yes
Place | Hall 3 106 | DAQ lab | Hall 3 106 | DAQ lab
Latest firmware updated ? | no | yes | no | Being flashed. Register all 0xffffffff

## Slide 8: How does CGEM Sync with other subsystem?
FULL Signal: When DC buffer is almost full , How does it notify GEMROC fanout module ?
  Does DC board have connection to GEMROC Fanout Module?
  Or DC board notify the MCC module directly ?
When DC buffer is full , what will be done to protect the buffer?
  When read out is slow, will DC board ensure that one or several complete events will be thrown away?

## Slide 9: Issues found during last data taking
1. GEMDC packet L1 count not increasing when working with dummy GEMROC data.
2. The first GEMDC packet length is wrong.
3. The GEMROC data format in the first GEMDC data packet is wrong.
4. Found DC buffer pile up, multiple DC packets has been read out in one DMARun.
5. GEMROC L1 counter not start from 0.
6. GEMROC L1 counter is increasing by 4 most time, sometimes by 3 or 5.
7. DAQ software is able to acquire data for 2 minutes, after that, no interrupts happened.
8. Sometimes data format of GEMROC 5 is wrong.(new found)
9. Link NO in DC packet is not corresponding to the GEMROC ID.(new found)
Our Analysis:
1 maybe cause to 2 different GEMROC data formats: confirming with Pawel if the DC firmware support two GEMROC data format .
2,3,5,8,9 data format issue.
4 is correct according to current design of DC firmware.
7 interrupt issue
6 need my recheck.
Interrupt issue solved.
remaining some data format issues.

## Slide 10: ISSUE I : The generation of issue 1 is due to the difference in parsing L1 count between dummy data packets and real data packets. For dummy data packets, it is fixed at 0xe0, while for real data packets, it increases based on the trigger number.
GEMROC packet length is consistent with dummy and real data.
  Length: hit number * 2+3*2 word , hit number = (header >>16)&0xff
    For dummy GEMROC packet: Length is fixed: just 8 words.
    Hit num (0xc08765432001abcd >> 16)&0xff == 1 , length = 1*2+3*2=8 word
GEMROC Local L1 count has difference with dummy and real data.
  Dummy data : ((0x2001abcd>>24)&0x3f) + ((0xc0876543&0x3ffffff)<<6) , fixed, the low 8 bit is 0xe0(224)
  Real data : (((*(buffer+1))>>24)&0x3f) + (((*buffer)&0x3ffffff)<<6), is increasing
  When working with dummy gemroc ,the DC L1_count_LSB is not increasing, fixed to 0xe0.(issue 1 is explained.)