## Slide 1
Horizontal IP feedback system at SuperKEKB based on fast luminosity measurements
Philip Bambade IJCLab – Orsay
Acknowledgements: Y. Funakoshi, M. Masuzawa, H. Nakayama, Y. Ohnishi, S. Uehara (KEK – Tsukuba)
Dima. El Khechen (2013-2016), Cheng-Guo Pang (2016-2019), Salvatore Di Carlo (2017-2019), Meng Li (2023-present)
Mini-workshop on CEPC Fast Luminosity Feedback System September 14, 2024 Beijing - China

## Slide 2: The SuperKEKB/Belle II project
Damping Ring
Injector Linac
Main Ring
Belle-II
 | Electron | Positron
Energy (GeV) | 7 | 4
Current (A) | 3.6 | 2.6
Belle II (General purpose detector) Vertex detectors: Pixel Vertex Detector (PXD), Silicon strip Vertex Detector (SVD) Tracking: Central Drift Chamber (CDC) Calorimeter: Electromagnetic CaLorimeter (ECL) Particle ID: Aerogel Ring Image CHerenkov detector (ARICH) K-Long and Muon detector (KLM) Time-Of-Propagation counter (TOP)
SuperKEKB (Electron-Positron Collider) C.M.S. Energy: √s = 10.58 GeV Luminosity: L = 8 x 1035 cm– 2s–1 （Luminosity Frontier Machine）

## Slide 3: Luminosity Frontier
SuperKEKB  unchartered luminosity territory  new techniques
N = s x L
B-pair production rate (pair/sec) :
s = cross-section for B pair production = 1.1nb L = luminosity.  110 pairs of B mesons produced / second for L = 1035 cm–2s–1.
World’s history before SuperKEKB
Our history, current record: 4.7x1034 cm–2s–1

## Slide 4
KEKB ↔ SuperKEKB parameters
× 1/20 βy
× 2-3 beam currents
 up to × 40 peak luminosity
σy ≈ 50-60 nm
(similar as ILC/ATF2)
similar beam-beam strength
(tune-shift)

## Slide 5
Nanobeam collision scheme
Very small βy avoids “hour-glass” limitation (effective bunch length ≈ depth of field of the optics)
Collide more charge @ tiny vertical beam size with similar beam-beam tune-shift strength parameter
× 1/20 βy
× 2-3 beam currents
× 1/20 σy
1. Optical aberrations near IP must be cancelled to achieve / maintain tiny beam spots
2. Control beam-beam tune-shift with more complex IP beam-beam dynamics + optical aberrations
3. Continuously inject intense beams in strongly demagnified IP optics → injection backgrounds… beam tails…
Opportunities
Challenges

## Slide 6: Nanobeam scheme reduced bunch overlap visible on reconstructed track vertex Z distribution

## Slide 7
IP optical aberrations blowing up the beam size are unavoidable → reliable measurement for correction only possible at the IP…
+ higher order terms (geometric & chromo-geometric)
ideal spot waist shift linear x-y coupling linear dispersion
Optical functions in LER ±27 m around IP SC final focus system integration with Belle II
IP
matching quads to select β*
quad strength tolerance for waist shift < β* / L* ≈ 3 10-4
σIP ≈ 60 nm
σquad ≈ 0.2 mm
Δψ
π/2
π/2
≈ π/2 except near a waist
Propagate IP aberration in low-β insertion → no visibility (except, possibly, at a secondary waist)
Must tune directly at IP (luminosity…)
IP

## Slide 8: Two complementary techniques for fast luminosity measurements - compare / collaborate / mutually supporting - share simulation, mechanics, some data… - since 2012
LumiBelle2 / IJCLab
ZDLM (Zero Degree Luminosity Monitor) / KEK
single crystal CVD diamond sensors
Fast charge/current amplifiers
Digital electronics and processing
Cherenkov and scintillator detectors
LGSO non-organic scintillator and ES-crystal (quartz)
Photomultipliers
Analog & digital processing
Notes: LGSO (Lu2-xGdxSiO5)

## Slide 9: What for / specs ?
“Dithering” feedback
Bunch by bunch luminosity diagnostic
IP vertical beam size measurement + tuning at very low currents
Correct for few Hz horizontal motion
79 Hz orbit “dithering” + luminosity sampling @ 1 kHz  reconstruct baseline freq. + 2nd harmonic
Efficient separation from other “slow” variations
1% relative precision @ 1 kHz sufficient (cf. C.-G. Pang et al., J.Phys.Conf.Ser. 1067 (2018) no.7, 072023)
Provide analog signal as input to lock-in amplifier
Nominally 4 ns bunch separation  need short signal pulses, ideally < 4 ns
1% or better relative precision @ 1 Hz
Single beam orbit + optics corrections in two rings
Vertical e+ and e- beam size optical tuning  suppress local aberrations in nanobeam final focus
Control of beam-beam blowup  find best spot in tune diagram
Very low current  avoid confusion from beam-beam induced blowup
Dynamic range L ≈ 1032  1036 cm-2 s-1
Non luminosity scaling contamination < 1% (e.g. beam gas bremsstrahlung and Touschek losses)
Manage radiation damage at highest luminosity
Notes: LGSO (Lu2-xGdxSiO5)

## Slide 10
Large cross section for
    1) 𝑒+ rate in LER 10 m after IP (part of energy spectrum near E(𝑒+) ≈ 3.5 GeV after large bend)
    2) 𝛾 rate in HER 30 m after IP (part of 0.1-0.3 mrad IP beam angular spread due to geometry)
Bhabha process at vanishing scattering angle
a.k.a. Single Bremsstrahlung
𝑒+
𝛾
Only relative luminosity  with certain conditions…
Acceptance depends on choice of sensor / location
Also some variation with beam parameters…
𝜎Bhabha@zero-degree not precisely computed in QED
 OK for usage on “short” enough time-scales
 care for beam parameter dependence
Dima El Khechen et al., PRAB 22, 062801 (2019)
Notes: LGSO (Lu2-xGdxSiO5)

## Slide 11
Optimal position found at 10 m behind IP using SAD
Over-bent Bhabha positrons  vacuum chamber
Special beam pipe with window + Tungsten radiator
Start-to-end simulation (GuineaPig++, SAD, GEANT4)
POSITRON RING (measure e+)
IP
X(m)
0
28 m
Photon ray-tracing in detailed vacuum chamber geometry + GEANT4
Original position at 30 m (2018)
New optimal position found at 28 m with ≈ 10 times higher rate
ELECTRON RING (measure )
IP
0.4
Implementation in LER and HER
Cheng Guo Pang et al., Nucl.Instrum.Meth. A931 (2019) 225-235
loss position distribution
Notes: Radiation length of Tungsten is 0.3504 cm

## Slide 12
ADC Channels
HER
LER
CH1
CH2
CH3
CH4
IP
140 μm + current amp 2 GHz
500 μm + charge amp 10 ns
removed
present setup

## Slide 13: LumiBelle2 diamond sensor signals
High charge carrier mobility  fast signal formation
Wide band-gap (5.5 eV)  good radiation tolerance
SuperKEKB nominal collision spacing = 4 ns
Monitor bunch-by-bunch luminosity  easier with pulse width < 4 ns
140 thick diamond + fast 2 GHz current amplifier  2 ns FWHM
2 ns
FWHM
DIAMOND
AMPLIFIER
Notes: Radiation length of Tungsten is 0.3504 cm

## Slide 14: LumiBelle2 signal processing
2 / 10 ns FWHM signals from 140 / 500 μm with 2 GHz current / low noise charge amp sampled every 1 ns
Synchronized to RF clock  continuous monitoring, averaging at 1 kHz and 1 Hz (bunch by bunch and all bunches together)
Luminosity proportional to amplitude of signal peaks
  ADC is AC-coupled  record difference between peak and baseline  “TIL” & “BIL”
  Raw sum of all samples also ∝ luminosity and recorded  “RAWSUM”
  Number of peaks also recorded (constant fraction discriminator)  “COUNT”
E-HUT F-8
 EPICS broadcasting @ 1 Hz  “1 Hz, 1 KHz, bunch-by-bunch, bunch-current” data streams transferred daily for archiving
多学科122

## Slide 15: LER 400 mA single beam vacuum scrubbing – 17/02/2024 (beam gas Bremsstrahlung events)
On-line EPICS data plotter 140 μm diamond 500 μm diamond
2 GHz current amp 10 ns charge amp
E-HUT / lumi-diamond PC
E-HUT / Keysight digital scope
LER channel 2
LER channel 4

## Slide 16: Signal formation and DAQ simulation

## Slide 17: Background study
SIMULATION FEATURES:
  Bremsstrahlung, Coulomb, and Touschek scattering included
  Use of SAD for tracking and Geant4 for particle detection
  Detailed simulation of pressure profile and chemical composition of vacuum gas () from previous study (J.Carter, M.Ady)
HER (e- ring):
  Dominant rate from Bremsstrahlung photons
  Electron rates from Bremsstrahlung, Coulomb, and Touschek scattering are negligible()
LER (e+ ring):
  Dominant rate from Bremsstrahlung positrons
  of the rate from Touschek scattering
  Positron rate from Coulomb scattering is negligible
Touschek
e- ring
e+ ring
Simulated vacuum profile in IR
Jason CARTER (ANL) & Marton ADY (CERN)
Scattering position of Bremsstrahlung
particles detected in LumiBelle2 / LER

## Slide 18: Setting up and optimizing beam collision with LumiBelle2
Initial scanning of IP beam offset to enable Regularly optimizing IP beam offset
collisions at very beginning of the run… to maximize luminosity…

## Slide 19: Minimising electron and positron IP beam sizes with LumiBelle2…

## Slide 20: LumiBelle2 1Hz bunch-by-bunch luminosity 2346 bunches on 04-05-2024

## Slide 21: Fast & slow beam position variations at IP require feedback corrections
Beam-beam deflection for fast vertical motion
Luminosity feedback by “dithering” for slower horizontal motion
Dy at IP=  5nm  1/10sy*
BPM
IP
BPM
Dy at BPM=  1.3mm
x
Luminosity
Vertical vibration  25-100 Hz
Sampling (BPMs)  32 kHz
Horizontal motion  few Hz
Modulation freq. f0  79 Hz
Sampling (lumi. meas.)  1 kHz
- minimize f0 output component
- dithering  lumi. signal  phase


2f0
f0
LUMINOSITY
DITHERING
Dithering coil x 12

## Slide 22: Luminosity degradation with horizontal offset nanobeam collision geometry
Sensitivity similar to head-on collisions for βy → 0.3 mm

## Slide 23: Horizontal orbit dithering feedback simulation basic ingredients & setup
Inverse FFT of measured GM spectra
Cheng Guo Pang, Doctoral thesis, https://theses.hal.science/tel-03092297

## Slide 24: Horizontal dithering orbit feedback simulation response to fixed offset

## Slide 25: 1st dithering feedback test in Phase 2
e- beam artificially given an offset, while e+ beam was dithered
Compute beam offset magnitude to cancel magnitude [V] of luminosity FFT component at dithering driving frequency
Beams brought back to optimal position (remove unwanted offset o=0) applying this offset with
- sign set by relative phase of input dithering and induced luminosity variation
- damping factor (depends on precision / noise levels)
Corresponding bump parameters sent to magnet control system via EPICS
After first 2 attempts + PI algorithm parameter optimization, the 3rd feedback test could smoothly minimize the induced offset
e+
e-
Mika Masuzawa et al., “Early Commissioning of the Luminosity Dither Feedback for SuperKEKB ”, IBIC2018 MOPA13
Yoshihiro Funakoshi et al., “Early Commissioning of the Luminosity Dither Feedback for SuperKEKB ”, eeFACT2018 WEXBA04

## Slide 26: Horizontal dithering orbit feedback simulation response to ground motion
Luminosity precision 2-3% @ 1 kHz
 Luminosity loss < 1%

## Slide 27
Concluding remarks
First tests of horizontal IP orbit offset feedback at SuperKEKB indicate basic feasibility
Not currently operated but will probably be needed when βy reaches design value of 0.3 mm
Testing showed that interplay with operating beam-beam deflection based vertical IP orbit offset feedback will need to be taken into account…
Dithering technique based on luminosity may also be considered for vertical IP orbit offset feedback
Missing from the simulation  careful representation of transfer function between ground motion and IP offsets (including ground motion coherence length in IR, mechanical response of supports within final doublet cryostat, detailed ring beam dynamics,…)
Issue of radiation tolerance need further study
LumiBelle2 @ KEK operated by IJCLab partly remotely and with help from KEK, but very understaffed  contributions & improvements from IHEP would be highly welcome

## Slide 28
Thanks

## Slide 29: Extra slides

## Slide 30: 1Hz luminosity from ECL, ZDLM and LumiBelle2 LER 500/140 μm & HER 500 μm channels 04-05-2024

## Slide 31: Luminosity sampled history from ECL, ZDLM and LumiBelle2 LER 140 μm channel 26/03/2024  31/07/2024 Meng Li et al., “Status and performance of LumiBelle2 in the 2024 beam operation of SuperKEKB”, IBIC2024 THP16
LumiBelle2 / ECL
AI “forest method”

## Slide 32: Luminosity sampled history from ECL, ZDLM and LumiBelle2 LER 500 μm channel 26/03/2024  31/07/2024
LumiBelle2 / ECL
AI “forest method”

## Slide 33: First collisions (luminosity): 25 April, 2018
VERTICAL SCAN
VERTICAL SCAN
PHASE SCAN
PHASE SCAN
Vertical and phase (longitudinal) scans were performed to find the optimal position of the beams
The LumiBelle2 and ZDLM channels worked well and were in agreement
Successfully measured and provided the luminosity on-line from the first collision up to this date

## Slide 34
C. G. Pang et al.: Nucl.Instrum.Meth. A931 (2019) 225-235

## Slide 35: Beam size estimation with vertical offset scans
e+
e-
Analytical result integrating Gaussian distributions with vertical offset:
assumes rigid beams
estimation biased due to non constant beam-beam blow-up during the scan
Benchmark vs ECL
I × I (mA2)
beam-beam
simulation
(S. Di Carlo & D. Zhou)
Blow-up
Bias
S. Di Carlo, 2018

## Slide 36: LumiBelle2 bunch-by-bunch luminosities, folded vertical bunch sizes and relative offsets
8% spread mainly depends on bunch current differences
Bunch-by-bunch luminosity precision: 1-2% at 1Hz
dominated by spread in bunch-by-bunch currents
8nm RMS spread in bunch-by-bunch vertical offsets (2.3% of average bunch size)
2% RMS spread in bunch-by-bunch vertical beam sizes
C. G. Pang et al.: Nucl.Instrum.Meth. A931 (2019) 225-235