## Slide 1: Design of the Fast Orbit Feedback of HEPS
Huang Xiyang, Jiao Yi, Wei shujun
2024-9-14

## Slide 2: Main content
1
Introduction
2
Fast orbit feedback and related simulation
3
Conclusion

## Slide 3
1
Introduction

## Slide 4
2024.7

## Slide 5: The fourth-generation light source
Multi Bend Achromat, MBA
Third-generation
Fourth-generation
Emittance of third-generation light source：1000~5000 pmrad
Emittance of forth-generation light source ： 100 pmrad
lattice
ESRF -> EBS

## Slide 6: The fourth-generation light source
Multi Bend Achromat, MBA
Third-generation
Fourth-generation
Emittance of third-generation light source：1000~5000 pmrad
Emittance of third-generation light source ： 100 pmrad
lattice
ESRF -> EBS

## Slide 7: The fourth-generation light source
Multi Bend Achromat, MBA
Third-generation
Fourth-generation
Emittance of third-generation light source：1000~5000 pmrad
Emittance of third-generation light source ： 100 pmrad
lattice
ESRF -> EBS
HEPS FOFB Goal:
Frequency：>500 Hz
Time：<10% beamsize~300 nm@V

## Slide 8: FOFB of the light sources in the world
Third-generation | Feedback | Bandwidth
ALBA | Fast | DC - 130 Hz
BESSY II | Fast | DC - 10 Hz
DIAMOND | Fast | DC - 130 Hz
ELETTRA | Fast | DC - 150 Hz
ESRF | Slow + Fast | DC - 150 Hz
SLS | Fast | DC - 100 Hz
SPEAR3 | Fast | DC - 100 Hz
ALS | Slow + Fast | DC - 60 Hz
APS | Slow + Fast | DC - 100 Hz
TPS | Fast | DC – 100(v)/60(h) Hz
NSLS II | Fast （+ SC） | DC - 250 Hz
SOLEIL | Slow + Fast | DC - 250 Hz
SSRF | Slow + Fast | DC - 100 Hz
Fourth-generation | Feedback | Bandwidth
APS-U* | Fast + Slow | 1 kHz
Sirius | Fast + Slow | DC-1 kHz
ESRF-EBS | Fast + Slow | DC - 150 Hz
MAX IV | Slow | -
Based on Nicolas Hubert’s talk, DIPAC09

## Slide 9
2
Fast orbit feedback and related simulation

## Slide 10: FOFB system
576 BPM
16 FOC station
384 PS controller
12 BPM→1 station
3 station → 1 FOC
1 FOC → 24 PSC
Topology of FOFB system
Data collection : 3 BPM stations => 1 FOFB station to reduce latency of global data distribution.
Global data distribution : Bi-direction, multi-channel high speed serial transmission with redundancy.
Muti-Mode Fiber & optical transceivers used for BPM data collection to reduce cost.
Single-Mode Fiber & optical transceivers used for global data distribution to ensure long distance transfer reliability.
X-BPMs integration into nearby stations.

## Slide 11: Fast corrector and power supply
Courtesy of X. Sun& P. Liu
Prototype of the fast corrector magnet

## Slide 12: Fast corrector and power supply
Diagram of

## Slide 13: Fast corrector and power supply
(Left) Amplitude-frequency measurement data of the magnetic field in both planes and the fitting transfer function. (Right) Comparison of step response test data in the vertical plane and the fitting transfer function

## Slide 14: Vacuum chamber
requirement：Inconel 625，thickness = 0.5 mm， Bandwidth>30kHz
Courtesy of Y. Wei & N. Wang

## Slide 15: Feedback Control loop
System response for different PID
Closed loop: 22kHz sampling

## Slide 16: Feedback Control loop
System response for different PID
Closed loop: 22kHz sampling
The closed-loop bandwidth >500 Hz

## Slide 17: Simulation procedure
The subsystems’ time response can be modeled from the measurement results.

## Slide 18: Time domain simulation

## Slide 19: Time domain simulation
FOFB on/off w & w/o BPM noise.
Compare with the continues model

## Slide 20: The impact of noises
BPM noise
PS noise
BPM noise
PS noise
RM noise
…

## Slide 21
3
Conclusion

## Slide 22: Conclusion
To fulfill the stability requirements of the HEPS, we will adopt a fast orbit feedback system with a closed-loop bandwidth exceeding 500 Hz.
We have carefully designed the FOFB communication structure, as well as various hardware subsystems such as the fast corrector power supply, magnet, vacuum chamber, and optimized the system latency, although some hardware-related details are not mentioned in this talk.
Through frequency domain analysis and time-domain numerical simulations, we predict the performance of the FOFB system, and its impact of noises.

## Slide 23: Thank you！